**** DISSPOP.COM 
        **** OFFLINE.COM
        **** PLOTLABEL.FOR,PLOTLABEL.CMM


          The enclosed command and Fortran  files  were  designed  to  help
     users  more  easily access the DISSPOP graphics post-processor utility
     sold by Integrated Software Systems Corporation (ISSCO).  The  DISSPOP
     routines  allow  users  to  generate  a  common plot command file thru
     DISSPLA and to route their  final  graphics  output  to  any  hardware
     device available to them.

          Though the executable modules work well, there is no central core
     allowing  users  to easily direct their graphics output.  That was the
     basis for the creation of DISSPOP.COM.  Users are only required to use
     DISSPOP,  then  are  prompted  for  any  further input required by the
     command file.  Another requirement was the  fact  that  some  hardware
     translations  of  the  plot file use fairly healthy amount of CPU time
     and should really not be  run  in  an  interactive  environment.   The
     Versatec 1200A and the Printronix 300 LPM and 600 LPM graphics are two
     hardware devices that require large amounts of CPU and  I/O  resources
     to  obtain  their final outputs.  OFFLINE.COM was generated to process
     these jobs so that overall interactive response was kept at a  maximum
     level.

          Another factor in the OFFLINE.COM design was the evidence that  a
     Printronix 600  LPM  printer producing graphics uses from 40 to 60 per
     cent of a VAX11/780 just to handle the large amount of I/O operations.
     This  chunk  of  the  limited  resources available tended to seriously
     degrade the overall interactive thruput.  To eliminate  this  problem,
     we  have a PDP11/34A running RSX which shares a brand-X 300 Mbyte disk
     (mapped as 3 RP-04's) with our VAX which handles the  actual  printing
     of  the  graphics  output  only.  Thru a combination of DECNet and the
     shared disk, we are able to offload the  printing  load  generated  by
     Printronix printers.  The PDP11 is primarily a front-end processor for
     our VAX and handles no user load, so if its response is degraded it is
     of no real importance.

          PLOTLABEL.FOR is  a  program  which  uses  the  DISSPLA  graphics
     software  to  place  the user id, the DISSPOP source file and the date
     and time of the batch run on the Printronix and Versatec plot outputs.
     It  uses  some  features  of  version 9.0  of  DISSPLA  but  with  few
     modifications, will easily run on earlier versions of DISSPLA.

          If you need any further information or if you have problems, call
     or write the following individuals:

               Richard Olds or Capt. Randy Rushe
               Air Force Weapons Laboratory
               Laser Development Division AFWL/ARLB
               Kirtland AFB, NM 87117
               (505)844-4691

                                                                     Page 2


                                USER NOTES                                ____ _____



               1.  DISSPOP.COM                   ___________

                   a.  BASE_DIR, Logical variable  defining  the  directory
                       where the DISSPOP executables and command procedures
                       are located.

                   b.  SYS$DISSPOP, Logical variable defining  the  default
                       name used by the DISSPOP executables for their input
                       data file.  Set to DISSPOP.PLT at system startup.

                   c.  SCR_QUE, Symbol defining the batch queue to be  used
                       if  Printronix or Versatec output is required.  Will
                       be set  to  ONLINE,  PLOT$PNT  or  PLOT$VER.   These
                       queues  should be initialized to have a job-limit of
                       1 so that no file collisions occur.


               2.  OFFLINE.COM                   ___________

                   a.  SUBMIT, Clears  any  user  defined  values  for  the
                       SUBMIT command.

                   b.  DISK$SHARE:[200,1],  Directory   used   as   scratch
                       location  for  use  by  both  the  VAX11/780 and the
                       PDP11/34A.  The VAX is allowed  to  read  AND  write
                       into this mapped RP04, but the PDP11 is allowed only
                       to read.  This eliminates any disk  block  conflicts
                       generated  by  the  shared  drive.   This  directory
                       should be placed on a disk that does NOT  have  disk
                       quotas enabled as the plot files can get quite large
                       before they are finally deleted.

                   c.  SYS$PNTRNX, Logical variable  defining  the  current
                       status  of the printer on the PDP11.  If the printer
                       or DECNet link is down for some reason, OFFLINE will
                       not try to send it over to the PDP11 for printing.

                   d.  NETPLOT.CMD,  Command  proceedure  resident  on  the
                       PDP11.   Searches  for  a  print  file  in  a  known
                       location, copies it to the mapped disk that  it  can
                       write  AND read on, then sends a message back to the
                       VAX to delete the original copy of the  print  file.
                       Sends  its  copy  of  the  file  to its printer then
                       deletes its copy and is finished.  Due to a  crashed
                       PDP11, I cannot put a copy on the distribution tape.
                       However, if you will send me a  floppy,  I  will  be
                       glad to forward you a copy.


                                                                     Page 3


               3.  PLOTLABEL.FOR                   _____________

                   a.  Two logical variables must be defined to obtain info
                       for  this  program.   FILE_ID  defines  the original
                       DISSPOP plot data file name, including the  disk  id
                       and  directory.   DEVICE_ID  is  the actual graphics
                       hardware that the plot is being sent to.