[VAXF81.ROSS.REMOTE]AAAREADME.DOC

[remote]areadme.txt

	utility:	remote
	author:		Jim Sturtevant
			Ross Systems, inc.
			Palo Alto, California
			(415) 856-1100 x310
	edit date:	December, 1981

	abstract:	utility provides for terminal emulation through
			VAX port. In conjunction with a VENTEL 212-plus
			auto-dial modem this utility will allow interactive
			users to dial out.

	setup:		1. link remote with remotel.com
			2. set line characteristics for remote ports to be 
			   1200 baud, passall, fullduplex
			3. add logical remote_log to point to a sequential
			   file with world:RW protection
			4. add logical REMOTE0 thru REMOTEn to be equated with
			   the ports which your modem(s) are connected.
			5. create logfile with remote.com

	more info:	The remote program will begin by attempting to assign
			the first available port begining with REMOTE0 till it
			finds no more logicals. As it progresses it reports 
			who's using the busy ports and continues to rotor to 
			the next avaialable port. Once connected it outputs 2
			carriage returns to get the attention of the modem.
			At this point REMOTE is connected to the modem.

			From this connected point till the end of the session
			the user may type a control-F to request a remote 
			function.

			Once connected to a Ventel modem the user can type the
			desired phone number and operate as a remote terminal.

	features:	.ability to log terminal session to an ondisk log file
			.request input from a disk file on the local cpu
			.drops DTR (to hangup the modem) due to an exit from
			 program.
			.more efficient use of dial out modems...