The primary purpose of the BOOST procedures is to enable a user to
raise the base priority for a specified image name.  This, therefore,
allows the image process to run in a higher (than default) priority class.

	There are 3 types of input which are acceptable in the actual 
call to BOOST.  A brief step-by-step explanation of how to run the procedures, 
with each individual type of input, is given below...

	1. Input is a filename with a '.COM' extension

 	   a. Copy your LOGIN.COM file to a new filename.
	      (Note: the new filename's extension must equal '.COM')
	   b. Add the following two lines to the end of the newly
	      created file:

 		   $ASSIGN 'F$LOGICAL("SYS$OUTPUT")' SYS$INPUT
		   $RUN <program-image>

	      (where <program-image> specifies the name of the 
	       program which is to run in the higher priority class)
	   c. Run the BOOST main program by merely typing BOOST. It will
	      then prompt you for a base priority and an image name. The
	      base priority is a number between 1 and 6 (base priority=4
	      is the default).  The image name is the name of the newly
	      created file as specified in step a above.
	   d. Next, a password prompt will be displayed. Enter the BOOST
	      password.  The correct password is essential in order to
	      raise the base priority. (Note: ALL passwords should be
	      entered in upper case letters ONLY!). If the password is
	      typed correctly, a message indicating that the 
	      <program-image> has started execution is displayed.  If,
	      however, the password is typed incorrectly, the BOOST
	      main program exits with a 'Fortran Stop'. 

	2. Input is a filename with a '.EXE' extension

	   a. This type of input is used in the case where it is not
	      necessary to equate any of the logical symbols in the user's
	      LOGIN.COM file for the <program-image> which is to be run.
	      Thus, one wishes to directly call the <program-image> instead
	      of going through a command file. In order to do so, merely
	      type BOOST. It will then prompt you for a base priority 
	      and an image name.  The base priority is a number between
	      1 and 6 (base priority=4 is the default).  The image name
	      is the <program-image> name which is to run in the higher
	      priority class (Note: this file must have a '.EXE' extension).
	   b. Refer to step (1)d. above...

	3. Input is a filename WITHOUT an extension

	   a. In this case, the file extension '.EXE' is assumed and taken
	      as default.  Thus, the steps are the same as those described
	      in step (2) above.
	      *** However, when you type in the <program-image> name, it is
	          not necessary to type in the extension '.EXE' since it
	          is always the default when none exists.