;+++
;
; FACILITY
;	OAK RIDGE NATIONAL LABORATORY
;	FUSION ENERGY DIVISION
;	TOKAMAK SECTION
;
; ABSTRACT
;
;	This library contains a collection of procedures
;	designed to support list driven CAMAC operations on
;	the ORNL Fusion Energy Division VAX-11/780 computer 
;	system(s). These procedures are designed to conform 
;	to VAX linkage conventions and as such should
;	be callable from any VAX supported high-level language.
;	Specifically, this library contains the following 
;	procedures:
;
;	CAM$DCLST
;	-Declare a CAMAC command list buffer and initialize it,
;	CAM$LSTATE
;	-Allows user to set/modify default CAMAC states for a given
;	 command list(defaults taken from current CIB values),
;	CAM$LPIO
;	-Generates a command list frame to perform a single-action
;	 CAMAC operation(equivalent of CAM$PIO),
;	CAM$LQSCAN
;	-Generates a command list frame to perform a CAMAC Q-Scan
;	 operation(equivalent of CAM$QSCAN),
;	CAM$LSTOP
;	-Generates a command list frame to perform a CAMAC Stop mode
;	 operation(equivalent of CAM$STOP),
;	CAM$EXECUTE(W)
;	-Executes a previously generated CAMAC command list,
;	CAM$RDATA
;	-Extracts CAMAC read data for a specific command frame from
;	 the reply list,
;	CAM$WDATA
;	-Updates CAMAC write data for a specific command frame in the
;	 CAMAC command list.
;
;
;	A brief synopsis of each access procedure is included
;	in the preamble for that procedure.
;
; AUTHOR
;	E. T. Blair
;
; REVISION HISTORY
;	V02-000, E.T. Blair,12-AUG-1982
;	Modified CAMAC access procedures performing QIO(W) system services
;	to provide analogous entry points,i.e. CAM$XXX and CAM$XXXW calls
;	with consistent argument lists for both calls. In V01 the determination
;	as to whether a call was wait/proceed mode was based on the argument
;	list parameters specified, however, this approach posed some problems
;	when attempting to perform CAMAC calls from PASCAL.
;
;	V02-001, E.T. Blair,13-AUG-1982
;	Modified CAM$LSTATE procedure call argument list to be consistent
;	with the CAM$CSTATE procedure call for setting default CIB
;	CAMAC state values. Also, made changes to documentation in several
;	procedure preambles to correct errors and clarify intent.
;
;	V02-002, E.T. Blair, 8-SEP-1982
;	Incorporated changes to optimize the generation of list command
;	frames via a single internal routine(CAM_LFRAME). 
;
;---


;+++
;
;	Procedure:
;	CAM$DCLST(EXE_LIST,BLENGTH[,MEM][,EXE_FIBL])
;
;	Description:
;	The specified list buffer(EXE_LIST) is initialized as a CAMAC command
;	list. The first eight(8) words of the execute list buffer
;	are used by the list access procedures as a header block.
;	The format of this header follows:
;	FIELD		MEANING
;	WORD 0		Points to next available frame in execute
;			list,
;	WORD 1		Points to next available frame in the reply 
;			list,
;	WORD 2		Execute list buffer length(in units of words),
;	WORD 3		Execute list CAMAC status/state word(fields defined
;				below),
;	WORDS 4-5	Address of the execute list Frame Information
;				Block List(FIBL),
;	WORD 6		Current execute list frame number,
;	WORD 7		VMS I/O channel used to submit list for execution,
;	WORD 8		Execute list internal status word,
;	WORD 9		CAMAC controller ID<00:07>; CAMAC crate<08:15>.
;
;	The Frame Information Block List(FIBL) is a buffer intended
;	to receive Frame Information Block(FIB) entries(1 per
;	execute list command frame) that may be used to perform
;	subsequent random access to the list by command frame
;	number. The format of a FIB is as follows:
;	FIELD		MEANING
;	WORD 0		Execute list frame pointer,
;	WORD 1		CAMAC function code<00:07>; command size<08:15>(words),
;	WORD 2		Data frame pointer(0-relative) defining index of first
;				word of data(index into execute list for CAMAC
;				writes;index into reply list for CAMAC reads),
;	WORD 2		Execute list frame length(in words),
;	WORD 3		Data frame length(in words).
;
;	The list status/state word contains the following fields
;	FIELD		MEANING
;	LIP		List execution is in progress(modify interlock bit),
;	QDC		Q-Don't Care state for determination of
;				NORMAL/ERROR status,
;	QNE		Q Not Expected state for determination of
;				NORMAL/ERROR status,
;	XI		X-Ignore state for determination of
;				NORMAL/ERROR status,
;	M16		Memory format control(M16=1, MEM=16; M16=0,
;				MEM=24),
;
;	The execute list header is initialized with all pointers
;	and counts reset. If the FIBL is specified, it's address
;	is saved in the execute list header. If not, the FIBL address
;	pointer is reset. In either case, the current frame count
;	is reset.
;
;	The list status/state word may be subsequently modified 
;	by calling the CAM$LSTATE procedure.
;
;	Parameters:
;	EXE_LIST- address of buffer to be used as an execute
;		(command) list,
;	BLENGTH- address of a word containing the length of the
;		buffer in units of words,
;	MEM- address of a byte containing memory format for the
;		list being declared(MEM=16; MEM=24). If not specified,
;		the current CIB memory format state is used. Note
;		that 16 and 24 bit memory transfers may not be mixed
;		in a single execute list, i.e. ALL data transfers
;		must be 16 bit transfers or ALL data transfers must
;		be 24 bit transfers !!!!
;	EXE_FIBL- address of the Frame Information Block List
;		to receive command frame data that may be used
;		for subsequent random access/updates to the
;		execute list.
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$LSTATE(EXE_LIST[,XSTATE][,QSTATE][,MEM])
;
;	Description:
;	This procedure allows the state/status word of the
;	specified CAMAC execute list buffer to be updated.
;	The call parameters correspond to list state/status
;	and are briefly described below.
;	Parameter: XSTATE
;
;	Function:
;	Allows the user to influence the logic equation used by the
;	CAMAC branch driver in the determination of 'ERROR'/'NORMAL'
;	termination of a list PIO operation. This value initially 
;	defaults to CAMAC image block value.
;
;	Values:
;	CAM$XI-Ignores CAMAC X response in the determination of
;		ERROR status from the CAMAC branch driver.
;	CAM$_XE-Opposite of CAM$_XI.
;
;	Parameter: QSTATE
;
;	Function:
;	Allows the user to influence the logic equation used by the
;	CAMAC branch driver in the determination of 'ERROR'/
;	'NORMAL' termination of a list PIO operation. This value 
;	initially defaults to CAMAC image block value.
;
;	Values:
;	CAM$_QDC-Ignores CAMAC Q response in the determination of
;		ERROR status from the CAMAC interface.
;	CAM$_QNE-CAMAC Q response not expected. If received, the CAMAC
;		interface terminates with ERROR status on list PIO
;		operations.
;	CAM$_QE-CAMAC Q response expected. If not received, the CAMAC
;		interface terminates with ERROR status on list PIO
;		operations.
;
;	Parameter: MEM
;
;	Function:
;	Allows the user to change the default memory format state for
;	a given image. The memory format used determines whether 16 or
;	24 bit CAMAC data transfer operations are performed. This value 
;	initially defaults to the CAMAC image block value.
;
;	Values:
;	16-Sets default memory format to '16' bit format(1 CAMAC transfer =
;		1 word).
;	24-Sets default memory format to '24' bit format(1 CAMAC transfer =
;		2 words).
;
;	Parameters:
;	EXE_LIST- address of a CAMAC execute list buffer,
;	XSTATE- address of a word containing one of the symbolic values
;		CAM$_XI,CAM$_XE,
;	QSTATE- address of a word containing one of the symbolic values
;		CAM$_QDC, CAM$_QE, CAM$_QNE,
;	MEM- address of a byte containing one of the values 16 or 24.
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$LPIO(EXE_LIST,%DESCR(MODULE_NAME),A,F[,DATA][,EXE_FRAME])
;		Or
;	CAM$LPIO(EXE_LIST,%DESCR(KEY),A,F[,DATA][,EXE_FRAME])
;
;	Description:
;	This procedure inserts a single action command frame into
;	the specified execute list. If the optional frame number
;	(EXE_FRAME) is specified, that frame in the execute list
;	is updated with the specified parameters provided the
;	command frame and data frame lengths in the FIB for
;	the specified frame are consistent with the LPIO command
;	and data frame lengths. If the frame number is not specified,
;	the next available list frame(as determined from the list header).
;	is used to receive the LPIO command frame. If the
;	specified execute list has a FIBL attached, a FIB is
;	generated for this frame.
;
;	If the action performs a CAMAC write operation, the
;	write data is extracted from the specified data buffer
;	(DATA). If the action performs a CAMAC read operation, the
;	data will be inserted at the next available location in the
;	reply list. The transfer count is determined in both
;	cases by the memory format associated with the specified
;	list buffer(i.e. '16' bit=1 word transferred; '24' bit=
;	2 words transferred).
;
;	Parameters:
;	EXE_LIST - address of an execute list command buffer previously
;		declared via a CAM$DCLST procedure call,
;	MODULE_NAME- address of a CHARACTER variable containing an ASCII 
;		character string identifying the CAMAC module to be referenced,
;	KEY- address of a longword descriptor for the key value
;		previously computed for the CAMAC module via
;		calling the procedure CAM$ASSIGN,
;	A- address of a byte containing CAMAC subaddress,
;	F- address of a byte containing CAMAC function code,
;	DATA- address of CAMAC write data buffer. If omitted,
;		space is allocated in the execute list for
;		write data for CAMAC write function codes. CAMAC
;		read data is returned to the reply list,
;	EXE_FRAME- address of a word specifying the commmand frame
;		number to be updated by this LPIO request. If not
;		specified, the next available location in the execute
;		list will be used,
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$LQSCAN(EXE_LIST,%DESCR(MODULE_NAME),A,F,COUNT[,DATA][,EXE_FRAME])
;		Or
;	CAM$LQSCAN(EXE_LIST,%DESCR(KEY),A,F,COUNT[,DATA][,EXE_FRAME])
;
;	Description:
;	This procedure builds a Q-scan command frame into the 
;	specified execute list. If the optional frame number
;	(EXE_FRAME) is specified, that frame in the execute
;	list is updated with the specified parameters provided
;	the command and data frame lengths in the FIB for the
;	specified frame are consistent with the LQSCAN command
;	and data frame lengths. If the frame number is not specified,
;	the next available list frame(as determined from the list
;	header) is used to receive the LQSCAN command frame. If the
;	specified execute list has a FIBL attached, a FIB is generated
;	for this frame.
;
;	If the specified CAMAC function code indicates a
;	 write operation, data is cross-loaded from the
;	specified data buffer(DATA) into the execute list
;	as part of the command frame. For CAMAC read operations,
;	the data buffer need not be specified. Subsequent execution
;	of the specified list will result in a Q-scan block transfer
;	functionally equivalent to CAM$QSCAN. The memory format
;	associated with the specified execute list(MEM=16 or 24)
;	controls the interpretation of the transfer count(COUNT)
;	value(i.e. for MEM=16, 1 transfer = 1 word; for 
;	MEM=24, 1 transfer = 2 words).
;
;	Parameters:
;	EXE_LIST- address of an execute list buffer previously
;		declared via a CAM$DCLST procedure call,
;	MODULE_NAME- address of a CHARACTER variable containing an ASCII 
;		character string identifying the CAMAC module to be referenced,
;	KEY- address of a longword descriptor for the key value
;		previously computed for the CAMAC module via
;		calling the procedure CAM$ASSIGN,
;	A- address of a byte containing CAMAC subaddress,
;	F- address of a byte containing CAMAC function code,
;	COUNT- address of a word containing the CAMAC transfer
;		count(in units of the memory format).
;	DATA- address of data buffer that contains CAMAC write data
;		or that will receive CAMAC read data,
;	EXE_FRAME- address of a word specifying the command frame
;		number to be updated by this LQSCAN request. If not
;		specified, the next available location in the execute
;		list will be used.
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$LSTOP(EXE_LIST,(%DESCR(MODULE_NAME),A,F,COUNT[,DATA][,EXE_FRAME])
;		Or
;	CAM$LSTOP(EXE_LIST,(%DESCR(KEY),A,F,COUNT[,DATA][,EXE_FRAME])
;
;	Description:
;	This procedure builds a Stop On Transfer Count command frame 
;	into the specified execute list. If the optional frame number
;	(EXE_FRAME) is specified, that frame in the execute list
;	is updated with the specified parameters provided the
;	command frame and data frame lengths are consistent with
;	the LSTOP command and data frame lengths. If the frame number
;	is not specified, the next available list frame(as determined
;	from the list header) is used to receive the LSTOP command frame.
;	If the specified execute list has a FIBL attached, a FIB
;	is generated for this frame.
;
;	If the function code indicates a CAMAC write operation, data
;	is cross-loaded from the data buffer(DATA) into the
;	command frame. If the function code performs a CAMAC
;	read, the data buffer is not required. Subsequent execution
;	of the specified list will result in a stop mode
;	block transfer transaction functionally equivalent
;	to the execution of a CAM$STOP call. Data from
;	a CAMAC read operation is returned to the reply list
;	specified when the execute list is initiated.
;	The memory format associated with the specified execute list
;	(MEM=16 or 24) controls the interpretation of the transfer
;	count(COUNT) value(i.e. for MEM=16, 1 transfer = 1 word;
;	for MEM=24, 1 transfer = 2 words).
;
;	Parameters:
;	EXE_LIST- address of an execute list buffer previously 
;		declared via a CAM$DCLST procedure call,
;	MODULE_NAME- address of a CHARACTER variable containing an ASCII 
;		character string identifying the CAMAC module to be referenced,
;	KEY- address of a longword descriptor for the key value
;		previously computed for the CAMAC module via
;		calling the procedure CAM$ASSIGN,
;	A- address of a byte containing CAMAC subaddress,
;	F- address of a byte containing CAMAC function code,
;	COUNT- address of a word containing the CAMAC transfer
;		count(in units of the memory format).
;	DATA- address of data buffer that contains CAMAC write data
;		or that will receive CAMAC read data.
;	EXE_FRAME- address of a wordspecifying the command frame
;		number to be updated by this LSTOP request. If not
;		specified, the next available location in the execute
;		list will be used.
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$EXECUTE(W)(EXE_LIST,[REPLY_LIST,BLENGTH][,IOSB]
;		[,EFN][,AST][,ASTPRM])
;
;	Description:
;	This procedure executes the specified list of CAMAC command
;	frames built by calls to the list mode access procedures.
;	For this call to be successful, the specified execute list must
;	 have a nonzero execute list frame pointer value. 
;	The execute list frame pointer is contained in the list
;	header(an eight word reserved area at the beginning of the
;	execute list buffer) and is maintained by the list mode
;	access procedures. This pointer determines the length of
;	the execute list buffer for the execute list call.
;	If the specified list contains any CAMAC read command frames,
;	the optional reply list buffer(REPLY_LIST) and length
;	(BLENGTH) are required. The execute list header also contains
;	a reply list pointer that specifies the next available
;	word on the reply list(hence the length of the reply list
;	required to receive CAMAC read data from the execution of
;	the specified command list). If the buffer length specified
;	for the given reply list buffer is not sufficient to 
;	contain the read data resulting from the execution of the
;	specified command list, request is not allowed.
;
;	If the I/O status block parameter is specified, the status
;	of the CAMAC I/O operation is returned in that quadword
;	buffer. If not, a quadword in the CAMAC image block is
;	used to receive the status.
;	
;	If the proceed mode call(CAM$EXECUTE) is used, control returns
;	 to the caller as soon as the CAMAC request is queued to 
;	the system. If the wait mode call(CAM$EXECUTEW) is used, control 
;	is returned to the calling program only when the CAMAC I/O 
;	is complete. 
;
;	The I/O synchronization parameters(EFN, AST and ASTP) are used
;	in the same manner as their counterparts in the QIO and QIOW
;	system services. See the VAX System Services Reference Manual
;	for further discussion if needed.
;
;
;	Parameters:
;	EXE_LIST- address of an execute list buffer previously
;		declared via a CAM$DCLST procedure call and
;		containing CAMAC command frames built by calls
;		to the list mode access procedures CAM$LPIO,
;		CAM$LQSCAN, CAM$LSTOP,
;	REPLY_LIST- address of the buffer used to receive
;		CAMAC read data from the execution of the current
;		list,
;	BLENGTH- address of a word containing the length of the
;		buffer in units of words.
;	IOSB- address of a quadword buffer to receive I/O completion
;		status from the CAMAC request.
;
;	Optional I/O Synchronization Parameters:
;	EFN- value specifying the number of a local event flag
;		to be set upon I/O completion. If not specified, the
;		default process event flag from the CAMAC image block
;		is used,
;	AST- address of an AST procedure to receive an I/O completion
;		AST,
;	ASTPRM- address of a longword containing a parameter to
;		be passed to the specified AST procedure.
;
;
;	Return Status:
;
;---


;+++
;
;	Procedure:
;	CAM$RDATA(EXELST,FRAME,REPLST,READ_DATA)
;
;	Description:
;	This procedure provides a means of accessing CAMAC read data
;	resluting from the execution of a CAMAC command list(via the
;	CAM$EXECUTE call). The key for referencing the CAMAC read data is
;	the execute list frame number(FRAME). Successful use of this procedure
;	requires that a Frame Information Block List(FIBL) be associated with
;	the specified execute list(EXELST). The procedure verifies that the
;	specified frame in the execute list did indeed perform a CAMAC read
;	operation and if so, transfers the data read by the execution of that
;	frame from the specified reply list(REPLST) into the specified read
;	data buffer(READ_DATA). The number of words transfered is determined
;	from the FIB for the specified frame.
;
;	Parameters:
;	EXELST- address of an execute list buffer(assumed to have been
;		executed prior to this call),
;	FRAME- address of a word specifying the desired frame to be returned,
;	REPLST- address of a reply list buffer(assumed to contain CAMAC read
;		data as the result of executing the specified execute list),
;	READ_DATA- address of a buffer to receive the data resulting from the
;		execution of the specified frame from the execute list.
;
;---


;+++
;
;	Procedure:
;	CAM$WDATA(EXELST,FRAME,WRITE_DATA)
;
;	Description:
;	This procedure provides a means of updating CAMAC write data
;	in a CAMAC command list. The key for referencing the CAMAC read data is
;	the execute list frame number(FRAME). Successful use of this procedure
;	requires that a Frame Information Block List(FIBL) be associated with
;	the specified execute list(EXELST). The procedure verifies that the
;	specified frame in the execute list intends to perform a CAMAC write
;	operation and if so, transfers the data from the specified write data
;	buffer(WRITE_DATA) into the execute list to update the write data for 
;	the specified frame. The number of words transfered is determined
;	from the FIB for the specified frame.
;
;	Parameters:
;	EXELST- address of an execute list buffer(assumed to have been
;		executed prior to this call),
;	FRAME- address of a word specifying the desired frame to be returned,
;	WRITE_DATA- address of a buffer to containing the data to be written
;		into the specified frame of the execute list.
;
;---


;---