MAC80 is a TOPS-10 8080/8085 cross assembler written in MACRO-10, using
TOPS-10 monitor calls.  It also runs in "compatibility mode" (with PA1050)
under TOPS-20.  It will assemble most CP/M .ASM programs, generating a .HEX
file as output, with an optional listing file.  MAC80 was written by Bruce
Tanner at Cerritos College, Norwalk CA.

Most of the features of MAC80 are illustrated in the program TORTUR.M80, which
is reproduced below.  Some of the restrictions are:

o	Labels, macro names, etc., are limited to 6 characters. If more than 6
	characters are found, the extra characters are ignored, and a warning
        message "%Token overflow" is issued.

o	Labels must end with a colon.  Macro definitions and EQU statements
	must not.

o	A simple macro facility is available, similar to MAC and MACRO-80,
	except dummy labels are not supported.

MAC80 uses the standard TOPS-10 compiler command line syntax

*hex,list=source

Default filetype for the source is .M80.  Output filetypes are .HEX and .LST,
respectively.

Under TOPS-20, filenames must conform to TOPS-10 specifications (6.3).


* Implementation notes:

A feature test assembly switch will allow the generation of a somewhat obscure
hex file extension to support relocation and internal/external references.

TMP files are supported, so that the line

X MAC80,M80,MAC80,,HEX,,=

can be placed in COMPIL.MAC to invoke MAC80 like any other assembler. SFDs are
not supported.  Under TOPS-20, an equivalent modification to the Exec might
support MAC80 under the load-class commands.

(Note from the author...)

MAC80: I wrote MAC80 in 1976 when the only alternative was to toggle in
programs with the Altair 8080 front panel switches. It had a (since removed)
BOOT option that would write a paper tape bootstrap loader and program
combination on our KA10 paper tape punch.  It was patterened after the Intel
assembler in the Intel 8080 reference manual (the ONLY 8080 documentation at
the time). Anyway, it should bear a strong resemblance to Digital Research MAC
or Microsoft MACRO-80; all came from the same root. There are no command line
options except for listing.  There is a pseudo op OPT which has four arguments
OCT,HEX,SMAC,LMAC; OCT prints all data in octal (it may inhibit hex file
output, I don't remember).  HEX is the default. SMAC inhibits printing the
macro expansion. LMAC is the default.  The program TORTUR (short for touture
test) pretty much exercises every feature of the assembler.  Someday I may
convert MAC80 into a Z80 assembler, but not soon.  You may distribute MAC80 in
the public domain, except for commercial (for profit) use, etc. etc.  If
anybody can use it, feel free.


* TORTUR.M80 -- MAC80 Torture Test:


	TITLE	Instruction set program

	SUBTTL	/This goes in .HEX file/

STAT	EQU	2		;PORT 2 HAS SYMBOLIC NAME STAT
FALSE	EQU	0
TRUE	EQU	NOT FALSE
THIS	EQU	TRUE
THAT	EQU	FALSE

	ORG	100H		;TELL MAC80 TO PLACE CODE AT 100 HEX

;	OPT	HEX		;HEX OUTPUT (THE DEFAULT)

START:	ACI	1		;ALL THE INSTRUCTIONS IN ALPHABETICAL ORDER
	ADC	C
	ADD	B
	ADI	123
	ANA	M
	ANI	20
	CALL	MACROS
	CC	START+1		;EXAMPLES OF ADDRESS CALCULATIONS
	CM	START-10H
	CMA
	CMC
	CMP	B
	CNC	START/2
	CNZ	(START*3)/3
	CP	(START/3)*3
	CPI	2+3*4
	CPE	START MOD 10
	CPO	START AND 0FFH
	CZ	LOW START
	DAA
	DAD	H
	DB	"Hello ","There",(RIM),(ADD C),(MOV A,M)
	DCR	C
	DCX	H
	DI
	DS	(STAT*10)-1
	DW	1,2,3,(RET)
	DZ	"Hello There
"
	EI
	HLT
	IN	STAT
	INR	A
	INX	H
	JC	-START
	JM	START AND 0FF00H
	JMP	HIGH START	;SAME AS (START AND 0FF00H)/100H
	JNC	NOT START
	JNZ	#START		;MEANS "NOT START" SEE DODATA ROUTINE
	JP	-(START * STAT)
	JPE	START
	JPO	START-STAT
	JZ	START!77Q
	LDA	START OR 3FH
	LDAX	B
	LHLD	START
	LXI	H,"ab"
	MOV	A,M
	MVI	B,(START-$-1) AND 0FFH
	NOP
	ORA	B
	ORI	LOW (START-$-1)	;SAME AS "AND 0FFH"
	OUT	5
	PCHL
	POP	B
	PRINTX	This is the instruction set test
	PUSH	H
	RAL
	RAR
	RC
	RET
	RIM
	RLC
	RM
	RNC
	RNZ
	RP
	RPE
	RPO
	RRC
	RST	5
	RZ
	SBB	D
	SBI	"A"
	SHLD	START SHR 2
	SIM
	SPHL
	STA	START SHL 3
	STAX	D
	STC
	SUB	L
	SUI	'"'		;QUOTES CAN BE ' OR " (AND IS REMEMBERED)
	XCHG
	XRA	C
	XRI	4
	XTHL

	IFE	THIS		;IF ELSE ENDIF TESTS
	DB	1
	ELSE
	DB	2
	ENDIF

	IF	THIS		;'IF' IS THE SAME AS 'IFN'
	DB	3
	ELSE
	DB	4
	ENDIF



MAC1	MACRO			;MACRO TESTING
	DB	"THIS IS A MACRO WITH NO ARGS"	;AND A COMMENT
	ENDM

MAC2	MACRO	A,B
	CALL	B		;A COMMENT
	DB	"2 ARGS"	;;AND A SUPPRESSED COMMENT
	ENDM

MAC3	MACRO	INSTR,TEXT	;...
	INSTR			;DO INSTR
	DB	TEXT
	ENDM

MACROS:	MAC1
	MAC2	FOO,START
	MAC3	<MVI B,(STAT*3)>,<"ANGLE BRACKETS
DELIMIT ANYTHING">

	OPT	SMAC		;SUPPRESS MACRO EXPANSION
	MAC1

	OPT	LMAC		;LIST MACRO EXPANSION
	MAC1

TABLE	MACRO		;CLASSIC TABLE GENERATION MACRO
	X	ABC
	X	AAA
	X	JKL
	X	C90
	ENDM

X	MACRO	ARG
	DB	"ARG"
	ENDM

VALUES:	TABLE

X	MACRO	ARG
	DW	ADR'ARG
	ENDM

ADDRES:	TABLE

X	MACRO	ARG		;BE LAZY & MAKE ADDRESSES ALSO
ADR'ARG:	JMP	START
	ENDM

	TABLE

	END	START		;START ADDRESS OPTIONAL


[End of MAC80.DOC]