FOR RECIPIENTS OF ANSI LABELED TAPES:


ANSI labeled tapes are provided to KERMIT requestors who:

  (a) asked for them;
  (b) didn't mention tape format specifically, but have VAX/VMS;
  (c) asked for a tape in a format we cannot provide; or
  (d) did not specify a system or tape format.

All systems are supposed to be able to read ANSI labeled tapes, which,
according to ANSI standard X3.27-1978: "Magnetic Tape Labels and File
Structure for Information Exchange", should be the universal medium
for exchange between mainframe computers.  If your system can't read
this kind of tape, it might be a good idea to get hold of the standard
and implement it.

The tape is written as follows:

Tracks:   9
Density:  1600 bits per inch
Parity:   Odd

ANSI labels:
  Volume label: KERMIT
  File header labels give name of each file.

ANSI Format: "D" -- variable length records with length fields at the beginning
  of each record, line terminators stripped, and no record crossing a block
  boundary.  "F" (fixed length record) format, although simpler to read, was
  not used because the KERMIT distribution would not fit on a standard 2400'
  reel of tape if written in this way because of the space wasted by padding.

Character Encoding:  ASCII (ANSI X3.4-1968)

Record Length:  Variable, maximum 200 (no lines of text or program source in
  the Kermit distribution are more than 200 characters long; very few are
  longer than 100).

Block Length:  2000

Only printable files (text, program source, text formatter source, or hex) are
included on this tape.

[End of <KERMIT>ANSI-TAPE.DOC]