In the process of fixing a problem in VMS Kermit that cropped up under
VMS V4 I found that the format of the Parity Flags field in the IOSB of the
Terminal Driver's Set/Sense Mode/Characteristics I/O functions was not
documented.  Initially, I assumed that the format of the Parity Flags field
was the same as the P5 argument to the Set Mode/Characteristics I/O functions 
which is used to set the parity flags.  However, the P5 argument has bit
settings that are outside of the low order byte, namely TT$M_ALTDISPAR and
TT$M_DISPARERR.  Therefore, the format of the Parity Flags field in the IOSB
of the Set/Sense Mode/Characteristics I/O functions must be different than the
format of the settings in the P5 argument of the Set Mode/Characteristics I/O
functions.  With the help of DEC's Customer Support Center and some microfiche
reading I was able to determine the format of some of the information returned
in the Parity Flags field.  The format of that information is shown below. 
Bits 3 and 4 somehow indicate the terminal's frame size.  As legal frame sizes
are between 5 and 8 -- four different values -- I thought that the two bits
would simply represent the four possible frame sizes, but I have not been able
to nail down the relationship.  The information could probably be found in the
microfiche for the Terminal Driver but I have not had time to get that far. 


IOSB for Terminal Driver Set/Sense Mode/Characteristics I/O Functions
    (IO$_SETMODE, IO$_SETCHAR, IO$_SENSEMODE, IO$_SENSECHAR)

    +--------------+--------------+-----------------------------+
    |              |              |                             |
    |   Receive    |   Transmit   |           Status            |
    |    Speed     |    Speed     |                             |
    |              |              |                             |
    +--------------+--------------+--------------+--------------+
    |              |              |              |              |
    |      0       | Parity Flags |   LF Fill    |   CR Fill    |
    |              |              |    Count     |    Count     |
    |              |              |              |              |
    +--------------+--------------+--------------+--------------+


Parity Flags	Meaning					Symbolic Mask
 Bit Number						Name (if any)
------------	-------					-------------
	0	?

	1	0 - Parity errors are not dismissed
		1 - Parity errors are dismissed

	2	?

	3	} Something to do with 
	4	}  the frame size

	5	0 - One stop bit in use
		1 - Two stop bits in use

	6	0 - Parity is not in use		TT$M_PARITY
		1 - Parity is in use

	7	0 - Parity in use is even		TT$M_ODD
		1 - Parity in use is odd