NAME:		FTCOPY

TYPE:		Main program.

PURPOSE:	Provides an efficient means of copying data files between
		foreign (non-labeled) tapes, labeled tapes, and disk files.
		Allows code translation (EBCDIC, ASCII, etc.), data editing,
		and padding of output records and blocks.

MACHINE:	VAX

SOURCE LANGUAGE: VAX-11 MACRO.

DESCRIPTION:	FTCOPY provides users with an efficient means
		of handling foreign tapes on the VAX computers.  It allows
		deblocking and blocking of data records on input and output,
		translation of character codes (EBCDIC, ASCII, 7 bit ASCII,
		etc.), padding output records and/or blocks to specified length,
		making output blocks an even number of bytes in length, and
		keeping data which remains in an input block after deblocking.

INPUT		FTCOPY copies from foreign (non-labeled) tapes, ANSI standard
		labeled tapes, and all RMS disk files.  (Indexed and relative
		files are accessed sequentially.)

OUTPUT:		FTCOPY writes to foreign (non-labeled) tapes, ANSI standard
		labeled tapes, and RMS sequential disk files.  Information,
		warning, and error messages are written to SYS$OUTPUT and
		SYS$ERROR.

USAGE:		FTCOPY operates like the VMS utilities. The user enters
		the command, the input file designation, the output
		file designation, and any command qualifiers.  The command
		format is shown below along with a brief outline of the command
		parameters and qualifiers.  A full discussion of the parameters
		and qualifiers is given in Appendix 1.

	Format:

	FTCOPY	input_file_spec	    output_file_spec


	Command qualifiers			Defaults

	/[NO]TRANS=translation_code		/NOTRANS


	Input file qualifiers			Defaults

	/BLOCK_SIZE[=n]				(see appendix 1)
	/FILES[=n]				/FILES=1
	/RECORD_SIZE[=n]			(see appendix 1)
	/[NO]TRAILING_DATA=([RECORD[:y],BLOCK[:y]])	(see appendix 1)


	Output file qualifiers			Defaults

	/BLOCK_SIZE[=n]				(see appendix 1)
	/[NO]EVEN[=x]				/NOEVEN
	/RECORD_SIZE[=n]			(see appendix 1)
	/[NO]PAD=([RECORD[:x],BLOCK[:X]])		(see appendix 1)

RESTRICTIONS:	FTCOPY cannot write blocks of less than 14 bytes to a foreign
		tape.  This restriction mostly affects source code files and
		data  files with short records being copied to foreign tape.
		The restriction will be removed in a future release.  Until
		then, we suggest that files with records shorter than 14 bytes
		be padded to a fixed length, large enough to accommodate the
		largest record expected.

		FTCOPY will copy data on disk and tape devices as well as
		terminals, printers, and the null device (NL:).

		The /FILES qualifier may only be used with foreign tape input
		files.

		Blocks of data on a foreign tape which produce a parity error
		will have the block copied to the output medium as is and a
		warning message will be issued.

		The input files must be able to be opened for sequential assess.
		Indexed and relative files will be read sequentially.  Output
		RMS files are created as sequential access with variable length
		records and list carriage control.

		When an end-of-volume (the logical end-of-tape marked by a
		double end-of-file) is found on a foreign input tape, the copy
		operation will terminate, the files will be closed, and a
		message will be issued.

		When a physical end-of-tape is found on either input or output
		foreign tapes, the copy operation will be terminated and a
		message issued.  Data which have been read at the end-of-tape
		mark are not transferred to the output file.  Likewise, FTCOPY
		will not attempt to write data or an end-of-file mark after
		the end-of-tape condition is detected.

		If an output block size is not an even multiple of the output
		record size,  the /PAD qualifier must specify a block pad byte.
		Likewise, if the output record size is larger than
		the input record size, /PAD must be used to specify a byte for
		padding the output record.  In either case, if the /PAD
		qualifier is not specified FTCOPY will abort the copy operation 
		and issue an error message.

		Input and output block size restrictions are listed below.
		Any block outside these sizes will result in a fatal error.
		All sizes are in bytes.
			disk  	      input  - 1-32767
				      output - 1-32767

			ANSI tape     input  -  1-9991
				      output -  1-9991

			foreign tape  input  - 14-65535
				      output - 14-65535

	During its execution, FTCOPY may issue information, warning, and error
	messages to inform the user about conditions found in the data or
	command.  If an informational or warning condition is found, FTCOPY will
	continue execution; however, if the condition is an error or severe
	error, FTCOPY will immediatly terminate.  All messages are written to
	the SYS$OUTPUT and SYS$ERROR logical devices.

	If you get numerous warning messages and wish to avoid them at your
	terminal, reassign the logical name SYS$OUTPUT to device NL: and
	reassign logical name SYS$ERROR to a file which you can examine after
	the execution to check for errors.  These assignments should be made
	in the user_mode so that the output and error logical names will
	revert to your terminal after FTCOPY is done.  For example

		$ ASSIGN/USER_MODE NL: SYS$OUTPUT
		$ ASSIGN/USER_MODE ERRFILE.TMP SYS$ERROR

	These assignments will suppress all messages on your terminal or batch
	log file but will save them in the file ERRFILE.TMP so they may be
	examined later.



SUBPROGRAMS REQUIRED:
	FTCOPY requires a large number of subroutines written for its
	own use as well as a number of VMS system subroutines. 
	The FTCOPY specific routines are: FT_BLANK, FT_COP_MSG,
	FT_CREATE, FT_OUTPUT, FT_PADEVEN, FT_PCOPY, FT_STOP, and FT_TRANS.
	The TAPESUBS package (on the Spring 1982 VAX SIG tape in directory
	[VAX82A.TAPESUBS]) is used for the foreign tape I/O.  The VMS
	Run-time library routines include LIB$TPARSE, LIB$CVT_DTB,
	LIB$AB_ASC_EBC, and LIB$AB_EBC_ASC.  The command line interface
	routines include CLI$PRESENT and CLI$GET_VALUE.  VMS system
	services include $FAO, $GETDVI, $WAITFR, $PUTMSG, and $EXIT.
	RMS I/O routines are $OPEN, $CLOSE, $PARSE, $GET, $PUT, and
	$CONNECT.

OPERATIONAL ENVIRONMENT:
	FTCOPY requires 296 virtual pages of memory on a VAX 11.

PROGRAM LOGIC:	This program initializes its internal data structures and
	then analyzes the command line to establish the parameters for the
	copy operation.  It next gets the user translation table if required
	for the copy.  Once all of the parameters are established, FTCOPY opens
	the input and output files and starts the copy.  The data are read into
	an input buffer one block at a time and deblocked as necessary.  The
	logical records are copied into an output buffer. If code translation
	is specified, the translation is done during the copy as well as any
	padding of records and keeping of trailing record or block data. Once
	the output block is full, it is written to the output file.  The cycle
	of reading, copying from input to output buffer, and writing is
	continued until all of the input data has been read.  At this time the
	input and output files are closed and FTCOPY starts the copy over again
	if another file is specified.

ERRORS & DIAGNOSTICS:	Messages are sent to the SYS$ERROR device as necessary
	to inform the user of the progress of the copy operation.  A discussion
	of the error messages and possible fixes is contained in Appendix 2.

PROGRAMMER: Thomas W. Danforth

DATE:	1 May 1984 - Version 01.d.
	13 June 1983 - Version 01.B.