RD Controls Software Release 4.0
    
                Procedures to Simplify Remote Printing via DECnet
    
                                  Frank J. Nagy
    
                               September 21, 1986
    
    
     DECnet file copies permit  one  to  use  printers  attached to a remote
system (i.e. the  FNAL  VAXCluster).    This  is  a relatively primitive and
painful operation, usually involving copying the  files to a logical name or
to a node and device.  The system  manager has to have setup the printer for
spooling to allow  output  operations  to  be  done  directly to the printer
device.  Such files are spooled onto  a disk file and then implicitly queued
when the file is closed.
    
     A major disadvantage of this  scheme  is  the  lack of control over the
output format for  programmable  printers  like  the Talaris laser printers,
particularly when the default setup  is  not  adequate for the user's needs.
The best solution would be  for  network-based  print queues in which a file
PRINT'ed on one system would  be  transparently moved across the network and
printed on another system, retaining  all the print job parameters specified
via qualifiers on the PRINT command.
    
     Network print queues are  not  available  yet,  but  most of the user's
needs can be satisfied by a  pair  of  DCL command procedures.  The first of
these procedures I call RMTPRINTER.COM and  is  the remote system end of the
DECnet links.  This  procedure  must  be  placed  in  your login area on the
remote system (i.e., the FNAL VAXCluster).  You must also have a proxy login
between your "home" system and the remote  system.  You can test for this by
just doing a "DIRECTORY  node::"  operation.    If  the directory is of your
files on the remote system, you have  a  proxy  login.  If you do not have a
proxy login, contact your system manager for assistance.
    
     RMTPRINTER.COM  is   the   remote   end   of   a   DECnet  task-to-task
communications  link  setup   between   our   pair  of  command  procedures.
RMTPRINTER proceeds to read 3 records from  over the DECnet link.  The first
record gives the disk and directory location of the files on the originating
system.  The second record is the list  of files to be printed.  These files
must all be in the  same  directory  but  may  include wildcards.  The third
record is a set of qualifiers  for  the  PRINT command to be executed on the
remote system.   After  receiving  the  information  across  the DECnet link
(which is then  closed),  RMTPRINTER  proceeds  to  COPY  the files from the
originating system to  the  remote  system  on  which  the  procedure is now
running.  This copy is done into  your  login area on the remote system; you
can change this by replacing "SYS$LOGIN:" in RMTPRINTER.COM.  Once the files
have been copied, a PRINT command  is  done  on the files (now on the remote
system) with the qualifiers received across  DECnet.  In addition, the PRINT
command always includes "/DELETE"  since  the  files  being printed are just
copies of the  originals  and  are  presumably  not  needed once printing is
completed on the remote node.






              
     The second procedure, REMOTEPRINT.COM, is used on the local system as a
replacement for PRINT.  The format of a call to REMOTEPRINT is:
    
        @REMOTEPRINT  node::queue[/quals]  file[,...][/quals]
    
The first parameter to the  procedure  specifies  the remote system name and
the print queue on that system to which the files are submitted.  The second
parameter is a list of one or  more files (wildcards allowed) to be printed.
Qualifiers for the PRINT command  can  be  appended to either parameter, but
cannot be embedded in the file  list.   All the qualifiers are collected and
used as command qualifiers on the  PRINT command which ultimately results on
the remote system.   The  file  selection  qualifiers (such as /SINCE, etc.)
cannot be used with REMOTEPRINT.   In general, those qualifiers which affect
the print job (such as /SETUP or /FORM) are the only ones acceptable for use
with REMOTEPRINT.
    
     The easiest  way  to  use  REMOTEPRINT  is  to  define  symbols in your
LOGIN.COM as analogues to the PRINT  command.   For instance, the command to
print a file in "line  printer"  mode  on the Talaris-800 printer on 13-west
might look like:
    
        FPR*INT :== @RDCS$COM:REMOTEPRINT  FNAL::WH13W_PRINT/SETUP=S814L
    
where the /SETUP selects the module  to  print in landscape mode such that a
full page of printout will fit on an 8-1/2 by 11 page.
    
     The procedures REMOTEPRINT.COM and RMTPRINTER.COM  can be found on node
BSNDBG (at this time) under  the  logical  name  RDCS$COM of the RD Controls
Software group.  These procedures can also be found on the ALMOND VAXCluster
under the FERMI$EXE logical name.
    
    
    
Keywords
    
  Controls, EPICURE, remote, printing