W A T C H D O G



    This directory contains the WATCHDOG program.  The original was
taken from a DECUS tape (unknown authors) and was rewritten.  The
purpose of this program is to monitor interactive processes and log
processes off that have been inactive for a specified period of time. 
A interactive process is a process that is attached to a terminal. 
The process can be network process, a spawned process, or an
interactive process.  WATCHDOG does not care as long as it is
connected to a terminal. 

    A command file is included to build the program called
WATCHDOG.BLD.  To build WATCHDOG type the following command : 

	$ @WATCHDOG.BLD
	(Then answer the questions as they appear.)

    To start WATCHDOG you may use WATCHDOG.COM command file.  This 
command file should be modified to reflect your desired options and 
default values.  The following command should be added to your 
computer's startup command file SYS$MANAGER:SYSTARTUP.COM:

	$ @SYS_UTILITY:WATCHDOG.COM

    The following privileges are required to run WATCHDOG

	CMKRNL	- may change mode to kernel
	SYSNAM	- may insert in system logical name table
	DETACH	- may create detached processes
	PSWAPM	- may change process swap mode
	TMPMBX	- may create temporary mailbox
	WORLD	- may affect other processes in the world
	OPER	- operator privilege

    There are several logical names needed to run to WATCHDOG which
are explained below. 
     
	WATCHDOG_OPER_FLAG - Specifics which operator terminal types are
			     to receive WATCHDOG operator messages.  The
			     $OPCDEF macro defines symbolic names for
			     the operator terminal types.  The bit
			     encoded vector is constructed by specifying
			     the desired symbolic names in a logical OR
			     operation.  The list of the symbolic names
			     and their functions are given below for each
			     operator terminal type.  Symbols are setup
			     in the WATCHDOG.COM so symbol name need just
			     be logically OR together.  Typical value is
			     OPC$M_NM_CENTRL.

		OPC$M_NM_CENTRL   - Central Operator
		OPC$M_NM_PRINT    - Printer Operator
		OPC$M_NM_TAPES    - Tape Operator   
		OPC$M_NM_DISKS    - Disk Operator
		OPC$M_NM_DEVICE   - Device Status Information
		OPC$M_NM_CARDS    - Card Device Operator
		OPC$M_NM_NTWORK   - Network Operator
		OPC$M_NM_CLUSTER  - VAXcluster Operator
		OPC$M_NM_SECURITY - Security Operator
		OPC$M_NM_OPER1    - System Manager Defined Operator Function
		OPC$M_NM_OPER2    - System Manager Defined Operator Function
		OPC$M_NM_OPER3    - System Manager Defined Operator Function
		OPC$M_NM_OPER4    - System Manager Defined Operator Function
		OPC$M_NM_OPER5    - System Manager Defined Operator Function
		OPC$M_NM_OPER6    - System Manager Defined Operator Function
		OPC$M_NM_OPER7    - System Manager Defined Operator Function
		OPC$M_NM_OPER8    - System Manager Defined Operator Function
		OPC$M_NM_OPER9    - System Manager Defined Operator Function
		OPC$M_NM_OPER10   - System Manager Defined Operator Function
		OPC$M_NM_OPER11   - System Manager Defined Operator Function
		OPC$M_NM_OPER12   - System Manager Defined Operator Function

	WATCHDOG_INTERVAL  - Defines the Interval that WATCHDOG should
			     wake up and look for idle processes.  This
			     value must be specified in whole minutes.  A
			     typical value is 5 minutes ("0 00:05:00.00").

	WATCHDOG_START_MSG - Defines the system wide default at which time
			     WATCHDOG will start taking idle action and
			     at every interval after that until the process
			     it no long idle or the process is stopped.
			     WATCHDOG_START_MSG value should be a whole
			     number greater than 0.  A value of 0 means bypass
			     any idle action.  A value greater than 0
			     means start taking idle action at the
                             specified value (WATCHDOG_START_MSG)
                             multiplied by the wake up interval
                             (WATCHDOG_INTERVAL).  A typical value is 3,
                             which means if the WATCHDOG_INTERVAL is set to 5
                             minutes that WATCHDOG will begin warning idle
                             processes starting at at 15 minutes and
                             every interval after that until the user is
                             logged off or until CPU time or buffer I/O is
                             done by the process.

	WATCHDOG_STOP_PROC - Defines the system wide default at which time
                             WATCHDOG should perform the stop action on idle
                             processes.  WATCHDOG_STOP_PROC value should be
                             a whole number greater than 0.  A value of 0
                             means do not stop action.  A value greater
                             than 0 means take stop action at specified
                             value (WATCHDOG_STOP_PROC) multiplied by the
                             wake up interval (WATCHDOG_INTERVAL).  A
                             typical value is 6, which means if
                             WATCHDOG_INTERVAL is set to 5 minutes then
                             WATCHDOG will take stop action on users that
			     have been idle for 30 minutes.

	Before continuing lets understand terms:

                option flags - Are single bit flags to enable or disable
                               special options.  These options are explained
                               with the logical name they are associated with
                               set/cleared in.

                idle action  - The action WATCHDOG take when a process is
                               idle.  The default idle actions that WATCHDOG
                               takes are listed below.

                stop action  - The action WATCHDOG take when a process is
                               stop.  The default stop actions that WATCHDOG
                               takes are listed below.
                               
			Watchdog Default Actions:
                               1.  Put Header Messages on Warning and Stop
                                     Messages to the User.
                               2.  Do Not Notify Operator When Idle Action
                                     is Taken on User.
                               3.  Do Not Notify Operator When Stop Action
                                     is Taken on User.
                               4.  Tell User Idle Action is Taken.
                               5.  Tell User Stop Action is Taken.
                               6.  Do Not Log in Log File When Idle Action
                                     is Taken.
                               7.  Do Not Log in Log File When User Action
                                     is Taken.
                               8.  Attempt to Disconnect User If Possible on
                                     Stop Action

          WATCHDOG_FLAGS     - Defines the system wide default option flags
                               for users.  Specifics which options will be
                               on by default when WATCHDOG is running. The
                               USERDEF macro from WATCHDEF.MLB defines
                               symbolic names for flag.  The bit encoded
                               vector is constructed by specifying
                               the desired symbolic names in a logical OR
                               operation.  The list of the symbolic names
                               and the function are given below. Symbols are
                               setup in the WATCHDOG.COM procedure so symbol
			       names can be logically ORed together.  Typical 
			       value is 0.

           $ FLAGS = USER_M_NO_DISCONNECTIONS .or. USER_M_NOTIFY_OPER_LOGOFF
           $ DEFINE/SYSTEM/NOLOG WATCHDOG_FLAGS     "''FLAGS'"

           USER_M_NO_OPER_TIMESTAMP       1 ! No Operator Timestamp
           USER_M_NO_HEADER_MSG	          2 ! No Header Message on Terminal
           USER_M_NOTIFY_OPER_WARNING     4 ! Notify Operator When Warning User
           USER_M_NOTIFY_OPER_LOGOFF      8 ! Notify Operator When Logoff User
           USER_M_NO_NOTIFY_USER_WARNING 16 ! No User Warning Message
           USER_M_NO_NOTIFY_USER_LOGOFF  32 ! No User Logoff Message
           USER_M_LOG_WARNING            64 ! Log File Message When Warning User
                                            ! (The Above Option is Not
                                            !            Yet Implemented) 
           USER_M_LOG_LOGOFF            128 ! Log File Message When Logoff User
                                            ! (The Above Option is Not
                                            !            Yet Implemented) 
           USER_M_NO_DISCONNECTIONS     256 ! Not Disconnect User
           USER_M_FORCEX                512 ! Use Forcex Before Logging Off User

          WATCHDOG_FORCEX    - Defines the system wide decimal value to be
                               issued by $FORCEX system service before the
                               users to be logged off (only applied if the
                               FORCEX flag is set in their options.  A typical
                               value is 268444028 or %X10002172 which is
                               SS$_FORCEDEXIT (8572 dec or 2172 hex) logically
                               ORed with STS$M_INHIB_MSG (268435456 dec or
                               10000000 hex) to suppress an extra message when
                               force exiting a process.

          WATCHDOG_TIMESTAMP - Defines the frequency timestamp messages
            (Optional)         should be send to the operator.  If the flag
                               USER_M_NO_OPER_TIMESTAMP is set in system default
                               options then no logical name need be defined.

          WATCHDOG_EXCEPTION_FILE
            (Must be Comment Out If Not Used)
                             - Defines file containing the exceptions to
                               override the default start message, stop
                               process, and option values. Exceptions record
                               format is as follows :

          recordtype entity [{startmsg!DEFAULT} [{stopproc!DEFAULT} [{flags}]]]

                 where recordtype -> ACCOUNT    - Account Name
                                    !USERNAME   - User Name 
                                    !PROCESS    - Process Name
                                    !TERMINAL   - Terminal
                                    !IDENTIFIER - Rights Identifier or UIC

                 where entity     -> A fixed or single wildcard string or
                                     a fixed or wildcard identifier/UIC value
                                     or named the process may own or hold.

		 where startmsg   -> See definition logical WATCHDOG_START_MSG.
                                     This value overrides the logical's value.
                                     If the logical's value is desired use the
                                     keyword "DEFAULT".

		 where stopproc   -> See definition logical WATCHDOG_STOP_PROC.
                                     This value overrides the logical's value.
                                     If the logical's value is desired use the
                                     keyword "DEFAULT".

		 where flags      -> See definition logical WATCHDOG_FLAGS.
                                     With the exception instead of default of
                                     0 the default is value of WATCHDOG_FLAGS.

    Example of Exception Records :

	ACCOUNT BOSS			! Never Logoff User With The Account
					!   Name.
	ACCOUNT USER   5		! Warn these Accounts starting at the
					!   5th idle Interval But Never Log
					!   Them Off.
	ACCOUNT SYS*   2 10		! Warn any Account Name starting
					!   with "SYS" at 2nd idle Interval
					!   and log them out at 10th idle
					!   Interval.
	ACCOUNT DB*USER DEFAULT 7 512	! Warn any Account Name starting 
					!   with "DB" and ending with "USER"
					!   at the system wide default interval
					!   and log then out at the 7th idle
					!   interval.  There options flag
					!   says they should be logged off
					!   first by trying a disconnect, if
					!   that does not work then by using
					!   FORCEX assuming the default flags
					!   do specify NO_DISCONNECTIONS.
	ACCOUNT *TST DEFAULT DEFAULT 12 ! Any Account Name Ending with "TST"
					!   should be send warning messages 
					!   and logged out using the system
					!   wide startmsg and stopproc
					!   defaults.  The Options Flag
					!   Instructs Watchdog to Notify
					!   the Operator when a user is 
					!   send a Warning Message
					!   or a Log out Message.
	  !
          !  Same Type of Syntax May be used for All Other Record Types
	  !  Except for entity specification for Terminal, Identifier.
          !
	  !  Terminal Must Been with One significant Letter and End with
          !  a colon

          TERMINAL OP*:                    ! Never Log Any One off of Consoles

          !
          !  Identifier Entities May be Expressed in the Following Syntax
          !         [n,m]          <n,m>
          !         [name1,name2]  <name1,name2>
          !         [name]         <name>
          !         name
          !         %Xhex-value
          !         (any above of number or name may also be *)
          !

          IDENTIFIER [1,4]                ! Never Logoff Any One holding this
                                          !   Identifier
          IDENTIFIER <1,*>                ! Never Logoff Any One holding this
                                          !   Identifier
          IDENTIFIER [SYSTEM,MANAGER]     ! Never Logoff Any One holding this
                                          !   Identifier
          IDENTIFIER [MANAGER]            ! Never Logoff Any One holding this
                                          !   Identifier
          IDENTIFIER MANAGER              ! Never Logoff Any One holding this
                                          !   Identifier

	Any further improvements/wishlist can be made to the author below.	

	Finally note if Watchdog does disappear, messages are usually displayed
	on the console and a file WATCHDOG.DMP is created.  Or if your system
	crashes due to Watchdog the system dump will in SYSDUMP.DMP.  Save
	theses files and contact the author below if you want further a
	correction made.

        George H. Walrod III
        8150 Lakecrest Drive #402
	Greenbelt, MD  20770		(301)474-2971