DISK_REO.COM DOCUMENTATION


The purpose of DISK_REO.COM is to create a copy of a RA81 disk. The copy will:


     1. Be defragmented.

     2. Have most of its directories placed in the center of the disk.

     3. Have selected data files placed into 3 zones to minimize head 
	contention:

	0-------------------------------445536--------------------------891071
	33333333333322222222222222211111111111122222222222222333333333333
	-----------------------------------------------------------------

	Zone 1:	Center of the disk. On a RA81 logical block number (LBN) 445536
		is the center LBN. Included in this zone are:

		     a.	All files from the [SYSTEM] directory, such as page and 
			swap files.

		     b.	Files from selected directories. These files will be
			positioned in order by a parameter file.

		     c.	Places one half of the free space on each side of 
			this zone.

	Zone 2:	LBN's around zone 1. This zone is for short life files. Program 
		ZONE.BAS determines which files are included in zone 2 and zone
		3. Zone 2 will have .LIS files for example. The files are copied
		in sorted order by file extension and size.

	Zone 3: LBN's around zone 2. Places long life, low access files around 
		zone 2.

DISK_REO.COM was created because BACKUP/IMAGE does not:

     a.	Center directories. Directories are created as the first file within
	the directory is copied.

     b.	Evenly distribute the free space on the the disk. Backup places the 
	free space on the low LBN side of the disk. This was discovered by 
	running HEAD_ANAL2.COM after several BACKUP/IMAGE operations. Each try 
	used a different input disk with the same result.

     c.	Place the most active files in the center of the disk. Backup placed the
	files in unpredictable locations. Usually, the most important files were
	spread all over the disk.




			DISK_REO.COM DOCUMENTATION


Installation:
------------

     1.	Create a captive account with sufficient privileges to access all of
	the files on the input disk and to create the output.

     2. Copy all of the files into the captive accounts directory. This 
	directory needs to be secured.

     3.	Review all of the procedures. 

     4. Modify/create:

	     a.	Modify SET_DATA_DIR.COM to define data directories used by 
		ZONE.BAS and COPY.COM.

	     b. Create a file for each input disk containing the file 
		specifications for each file to be positioned in zone 1 by
		COPY.COM. The file name is the volume label, see example file: 
		WORK1.DAT. Note: do not specify the node or disk.

	     c.	Review/modify QUE_CHECK.COM. Our batch que names start with
		the system node name.

 	     d. Modify system node names and valid input disks in LOGIN.COM.

	     e. Setup a logical "SPARE_DISK" in LOGIN.COM or your 
		SYSTARTUP.COM to define the output disk.

	     f. Edit the list of file extensions in ZONE.BAS and DISK_REO.COM,
		see DISK_REO.COM Logic steps 25 to 27, which define the zone 3 
		files.

     5.	Warnings and notes:

	     a.	Group logicals REO_IN and REO_OUT are defined.

	     b. The procedures are intended for a mature disk. If you think
		that the number of files will more then double you should to
		modify the logic to calculate the correct number of files for 
		the output disk initialization.

	     c.	This procedure is not intended for a system disk. If the input
		disk has a [SYSTEM] directory with page and swap files, you must
		insure they are closed during reorganization.

	     d.	The input disk cluster size must be equal to the output. Other-
		wise you will need to add cluster rounding to the file position
		and size calculations.
	     



			DISK_REO.COM DOCUMENTATION


	     e.	You may want to modify or eliminate the sorting of the zone 2
		command file. The intent of the sort is to get large files, such
		as .LIS files, in adjacent positions to reduce fragmentation as
		each type of file is deleted.

             f.	Not all of the files will be defragmented. This is due to VMS 
		space allocation. Less than two percent of the files will be 
		fragmented and all within zones 2 and 3, which should not 
		present a large problem. Just insure that you most active files
		are copied by COPY.COM.

	     g.	The captive LOGIN command file does not provide functions to 
		shutdown DECNET, close page and swap files, stop all interactive
		jobs and queues. You may want to modify all of the procedures 
		for a partial shutdown. See DISK_REO_OPER.DOC for the operator
		instructions.

	     h.	Be sure that any file with a .DIR extension is really a 
		directory and each *.DIR has only one version.

	     i.	DISK_REO.COM sets WORLD:RE access on the output disk 000000.DIR.

	     j. Consider placing known images in the center of the disk.

	     k. Consider doing converts on indexed files before the 
		reorganization.

	     l. Volume sets are NOT supported. The modification should not be 
		difficult.

     6.	Speed. Using a VAX 8600:

		 1900 files / 650000 blocks under 1 hour

		10600 files / 685000 blocks under 3 hours

     7.	Related files which effect to operation of DISK_REO.COM:

	ASCII.FDL	      -	Used to create a file on the output disk to
				distinguish the input from the output disk
				when the plugs are exchanged by the operator.

	COPY.COM              -	Performs the copying of zone 1 data files.

	DEFINE_REO_IN.DAT     - Used by LOGIN.COM to save the definition of
				the input disk. Accessed by the dismount 
				function.

	DISK_REO_MOUNT.COM    - Leads the operator through the plug swap and 
				remount.




			DISK_REO.COM DOCUMENTATION


	DISKREO_IN_USE.NO     -	File set by LOGIN.COM to prevent more than one
				reorganization being done at the same time.

	DISMOUNT.COM          -	Called by LOGIN.COM to dismount the input disk.

	DISMO_CHECK.COM       - Makes sure that the input and output disks are
				dismounted.

	FILE_SIZE.COM         -	Returns total allocated blocks for a wild card 
				file spec in global S_FILE_SIZE.

	GEN_DUMMY.COM         -	Performs a CREATE/FDL to create a dummy indexed
				file at an exact position.

	GEN_DUMMY2.COM        -	Called by COPY.COM to create a dummy indexed
				file.

	GEN_DUMMY3.COM        -	Used to create a dummy file to allocate all the 
				available blocks on the output disk.

	GET_LBN.COM           -	Used to obtain the first retrieval pointer LBN
				of a given file.

	LOGIN.COM             -	Captive command for the operator account. Per-
				forms functions: 

					LOGOUT
					DEFINE INPUT DISK ADDRESS
					DISMOUNT INPUT DISK
					REORGANIZE

	QUE_CHECK.COM         -	Makes sure that batch queues are stopped.

	REMOUNT_INPUT.COM     -	Remounts the input disk when DISK_REO.COM fails.

	REO_DIRECT_DIF.COM    -	Performs a check to see that the directory and
				file counts on the output are equal to the input
				disk.

	SET_DATA_DIR.COM      -	Called by LOGIN.COM to define the directories to
				be processed by COPY.COM. i.e. the directories 
				where the Zone 1 centered file will be selected
				from.

	WORK1.DAT             -	Used by COPY.COM to select and position the 
				files to be placed in Zone 1. See WORK1.DAT
				for an example.

	ZONE.BAS/EXE          -	Reads a directory of the input disk and creates
				all the command files and global information 
				required to perform the reorganization.




			DISK_REO.COM DOCUMENTATION


     8.	Related files which help support the operation of DISK_REO.COM:

	DISK_REO_DATA_CHECK.COM	- This procedure will help determine if the zone
				  data sequence file specifications (WORK1.DAT)
				  will result with a balance of data on both 
				  sides of the directories and INDEXF.SYS.

	DISK_REO_DATA_CHECK.DOC - How to use DISK_REO_DATA_CHECK.COM.

	DISK_REO_OPER.DOC     -	Operator documentation for using the captive
				account.

	HEAD_ANAL2.COM        -	Performs a brief DUMP/HEADER, showing the
				file spec and all LBN's.

	HEAD_ANAL_DUMP2.COM   -	Called by HEAD_ANAL2.COM to do the DUMP/HEADER.
				The resulting .TMP file can exceed 40,000 
				blocks.

	HEAD_ANAL.BAS/EXE     -	Run by HEAD_ANAL2.COM to do the brief list.



 
			DISK_REO.COM DOCUMENTATION


DISK_REO.COM Logic:
------------------

0.	DISK_REO.COM is started after the operator has:

	a. Stopped DECNET.

	b. Stopped all interactive jobs.

	c. Stopped all queues.

	d. Defined which disk to reorganize. 

	e. Closed page and swap files on the input disk.

	f. Dismounted the input disk on each system.

	g. Note, if at any time DISK_REO.COM detects an error it will abort and 
	   remount the input disk.

1.	Input parameters:

		P1	Input disk - must have colon.
		P2	Output disk - must have colon.
		P3	Data directories on the input disk: "DATA1/DATAA/".

2.	Defines group logicals for input and output disks: REO_IN and REO_OUT.

3.	Check that the input and output disks are dismounted.

4.	Mounts the input disk for read/write and checks that the write protect 
	switch is depressed. The operator will be instructed to set the write
	protect switch.

5.	Dismounts and remounts the input disk for /NOWRITE.

6.	Obtains the input volume label and makes sure the disk does not have
	a [000000]<volume-label>.NEW_REO file which will be created on the 
	output to distinguish the input from the output. 

7.	Runs a warning routine to check for unusual files on [000000].

8.	Runs ZONE.EXE.

9.	Sorts and purges the ZONE command files.




			DISK_REO.COM DOCUMENTATION


10.	Initialization of the output disk:

	a. Obtains the input cluster size.

	b. Computes the size of [000000] directory.

	c. Computes the number of file headers to create.

	d. Initializes the output disk. The following diagram shows the output 
	   disk after initialization (RA81):
	
   LBN: 0-------------------------------445536--------------------------891071
	I I  			        0BIII
	-----------------------------------------------------------------

	I 	INDEXF.SYS
	
	0B	[000000], BITMAP.SYS.
	
	spaces	Unallocated space.


11.	Mounts the output.

12.	Sets NOHIGHWATER and NOERASE on output.

13.	Sets WORLD:RE access on the output 000000.DIR.

14.	Creates output:[000000]<volume-label>.NEW_REO file to distinguish the 
	input from the output. 

15.	Defines symbols for constants used for all positioning calculations.

16.	Creates a dummy, [000000]DRO_DUMMY_16.DAT to fill up the fragmentation
	of INDEXF.SYS between LBN 15 and 760.

17.	Performs housekeeping on the file DUMMY.FDL.

18.	Computes the size of, and creates a dummy file DRO_DUMMY_768.DAT to fill
	the LBN's from 768 to n blocks below [000000], where n is equal to the 
	number of user directories and subdirectories times the cluster size.

19.	Run BACKUP to copy all user directories and subdirectories to the
	output disk. When complete, one additional directory marks the end
	of the directories: [000000.DUMMY_DIR_END.DAT. This MUST be on the high
	side of INDEXF.SYS and is used to locate the free space on the high end
	of the disk.
	
   LBN: 0--768--------------------------445536--------------------------891071
	I-I****************************D0BIIIe
	-----------------------------------------------------------------

	I-I	INDEXF.SYS + filler (DRO_DUMMY_16.DAT) + INDEXF.SYS.
	
	*...*	DRO_DUMMY_768.DAT to fill 768 to the start of the directories.
	
	D0BIII	Directories, subdirectories, [000000], BITMAP.SYS, INDEXF.SYS.

	e	DUMMY_DIR_END.DIR to mark the end of the directories.



			DISK_REO.COM DOCUMENTATION



20.	Obtains the LBN of and deletes DUMMY_DIR_END.DIR. 

21.	Creates DUMMY_DIR_END.DIR to allocate all the blocks from INDEXF.SYS
	to 891071. Makes sure all blocks are allocated. 
	
   LBN: 0--768--------------------------445536--------------------------891071
	I-I****************************D0BIII############################
	-----------------------------------------------------------------

	#...#	DUMMY_DIR_END.DAT to fill up the disk.


22.	If the input disk has a [SYSTEM] directory:

	     a.	Computes the size of, deletes and creates a dummy file 
		DRO_DUMMY_768.DAT to fill the LBN's from 768 to n blocks below 
		the directories, where n is equal to the number of block uses 
		by the [SYSTEM] files.

	     b.	Calls COPY.COM to copy the [SYSTEM] files defined in file: 
		ZONE_SYS.DAT.

   LBN: 0--768--------------------------445536--------------------------891071
	I-I***************************SD0BIII############################
	-----------------------------------------------------------------

	S	[SYSTEM] files.





			DISK_REO.COM DOCUMENTATION


23.	Copy zone 1 data files:

	     a.	Computes the size of, deletes and creates a dummy file 
		DRO_DUMMY_768.DAT to fill the LBN's from 768 to n blocks below 
		the directories or system files, where n is equal to the number 
		of blocks used by the data files divided by two and rounded down
		to the last file requirement. The object is to create a free 
		space which will be equal to the total size of the first n files
		with space a total size equal to or less than one half of the 
		total zone 1 data blocks. COPY.COM will not split a file between
		the lower and higher areas and will dummy over any lower side
		space which is not large enough for the file it is attempting
		to copy. See COPY.COM for additional documentaion.

   LBN: 0--768--------------------------445536--------------------------891071
	I-I************		      SD0BIII############################
	-----------------------------------------------------------------


	     b. Creates symbols S_FIRST_DATA_FILE and S_LAST_DATA_FILE. The 
		first and last data file name is passed to DISK_REO by COPY.COM.
		These are used to create the dummy file to reserve free space 
		next to the data files.

	     c.	Calls COPY.COM to copy the [SYSTEM] files defined in file: 
		ZONE_DATA_<volume-label>.DAT.

   LBN: 0--768--------------------------445536--------------------------891071
	I-I*******************11111111SD0BIII11111111
	-----------------------------------------------------------------

	1...1	Centered data files. 


24.	Creating the dummy file to reserve the actual free space next to the
	data files.

	     a.	Computes the free space for the output disk.

	     b. Creates dummy files: DUMMY_FREE_LOW.DAT and DUMMY_FREE_HIGH.DAT
		with a size of 1/2 the output disk free space.

   LBN: 0--768--------------------------445536--------------------------891071
	I-I              LLLLL11111111SD0BIII11111111HHHHH
	-----------------------------------------------------------------

	LLLLL	1/2 free space DUMMY_FREE_LOW.DAT.

	HHHHH	1/2 free space DUMMY_FREE_HIGH.DAT.





			DISK_REO.COM DOCUMENTATION


25.	Zone 2 part 1 - copy all zone 2 files with block sizes of 400 or 
	more:

	     a. Create dummy files: DUMMY_LOW.DAT and DUMMY_HIGH.DAT to force
		data around the reserved free space.

   LBN: 0--768--------------------------445536--------------------------891071
	I-I*********     LLLLL11111111SD0BIII11111111HHHHH      #########
	-----------------------------------------------------------------

	*...*	DUMMY_LOW.DAT.

	#...#	DUMMY_HIGH.DAT.


	     b. Execute ZONE2.COM to copy the 400+ block files.

   LBN: 0--768--------------------------445536--------------------------891071
	I-I*********22222LLLLL11111111SD0BIII11111111HHHHH2222 2#########
	-----------------------------------------------------------------

	2...2	The zone 2 files with 400+ blocks. Note, a few files will be 
		fragmented. Note, the free space left is a result of some over 
		compensation of the space required. This space may not 
		necessarly be at the high LBN's.


26.	Zone 2 part 2 - copy all zone 2 files with block sizes of 400 or less:

	     a. Delete and create dummy files: DUMMY_LOW.DAT and DUMMY_HIGH.DAT
		to force data around the reserved free space.

   LBN: 0--768--------------------------445536--------------------------891071
	I-I****     22222LLLLL11111111SD0BIII11111111HHHHH2222 2     ####
	-----------------------------------------------------------------

	*...*	DUMMY_LOW.DAT.

	#...#	DUMMY_HIGH.DAT.


	     b. Run BACKUP to copy all the files on the input disk except thoes
		that are considered zone 3. This step will produce a 
		"RMS-E-FEX, file already exists, not superseded" message for 
		each file that has been copied to the output in previous steps.

   LBN: 0--768--------------------------445536--------------------------891071
	I-I****2222222222LLLLL11111111SD0BIII11111111HHHHH222222222 2####
	-----------------------------------------------------------------





			DISK_REO.COM DOCUMENTATION


27.	Copy zone 3:

	     a. Delete dummy files: DUMMY_LOW.DAT, DUMMY_HIGH.DAT and
		DRO_DUMMY_16.DAT to allow the remaining data to fill in the 
		remaining free space.

   LBN: 0--768--------------------------445536--------------------------891071
	I I    2222222222LLLLL11111111SD0BIII11111111HHHHH222222222 2
	-----------------------------------------------------------------


	     b. Run BACKUP to copy all the files on the input disk that are 
		considered zone 3. This step may produce a "RMS-E-FEX, file 
		already exists, not superseded" messages for each file that has 
		been copied to the output in previous steps.

   LBN: 0--768--------------------------445536--------------------------891071
	I3I33332222222222LLLLL11111111SD0BIII11111111HHHHH2222222223233 3
	-----------------------------------------------------------------

	3...3	Zone 3 files.


28.	Delete the dummy files in [000000] to complete the output disk.

   LBN: 0--768--------------------------445536--------------------------891071
	I3I33332222222222     11111111SD0BIII11111111     2222222223233 3
	-----------------------------------------------------------------

	I 	INDEXF.SYS
	
	SD	[SYSTEM] files, directories, subdirectories.

	0B	[000000], BITMAP.SYS.
	
	spaces	Unallocated space.

	1...1	Centered data files. 

	2...2	Zone 2 files.

	3...3	Zone 3 files.


29.	List directory totals for the input and output disks.

30.	Compares the input and output directory totals. The number of 
	directories and files must match to proceed with the placing of the
	output disk into production. Note, forget comparing the block counts
	because of the differences in [000000] size, number of headers defined, 
	and output size of some files.

31.	Execute DISK_REO_MOUNT.COM to lead the operator through exchanging disk
	address plugs and placing the reorganized disk into production.