WHAT

   A FAST Cluster and network-wide SHOW USERS (and Much more) type command.

	Authors:

	Pete Portante, (most of the work)
	Andrew W. Potter
	David Mulvihill
	Rochester Institute of Technology

	Distributed and supported by:

        Andrew W. Potter
        Systems Programmer
        Information Systems and Computing
        Rochester Institute of Technology
        Rochester NY, 14623  PH (716) 475-6994
        Email:    awpsys@ritvax.BITNET
                  awp8101@ritcv.UUCP

WHAT is a very fast utility that uses DECnet non-transparent communications
to produce three different displays.

	WHAT is distributed in Source (PASCAL, VAX C and MACRO 32 needed),
	object and executable form.  WHAT must be relinked to run under
        VMS V5 Executables are in the subdirectory [.V5]. 

	Relinking:

	WHAT may be relinked to run under V5 by setting default to
        the [.source] directory and typing:

		$ @BUILD_WHAT LINK


	Features:

	$ WHAT
	   Produces a SHOW USERS like display of users on this system

	$ WHAT/NODE=(node1[,node2...])

	  Same as above except it generates the display from all of the
          specified systems


	   /FULL Generates a full display of (somewhat like Unix FINGER)

	   /ALL  Lists ALL processes (only for use with /FULL)

	   /USER=(user1,[user2,...])
               Qualifies the list to only report on the specified users.
	       /USER can also translate the logical name WHAT_USER_list
               for a list of preferred users.  See Help WHAT

	   /OUTPUT=filename  Redirects output from SYS$OUTPUT

	   /SILENT   Directs what to not report an error of failure
                     to connect to a remote node.

	   /NOHEADER Eliminates the header line.
	   And more

	$ WHAT/NODE=(node1[,node2...])/STATUS

	  Prints a one line status line for each system

	The above command can be qualified with the following qualifiers

	   /OUTPUT=filename  Redirects output from SYS$OUTPUT

	   /SILENT   Directs what to not report an error of failure
                     to connect to a remote node.

	   /TOTAL   Generates a total line for the systems reported

	As an alternative to /NODE=(list) users can set up
        logical names to list preferred groups of nodes that run WHAT
	for use with the /SELECT qualifier

	EG.

	$ define WHAT_CLUSTER FOO,BAR,ZOT

	$ what/select=cluster [/any other what qualifiers]

	Will give the same result as
	  WHAT/NODE=(FOO,BAR,ZOT)


	WHAT uses some of the following techniques for speed.

	1) Looks at process state BEFORE calling $getjpi to retrieve
           information in P1 space.  This allows WHAT to NOT request
           that information if doing so would require a inswap.

	2) Does NOT use DECnet to retrieve information from the local
           node.  For example assume the user is logged on to
           LARRY and he issues the command:
		$ WHAT/NODE=(CURLY,LARRY,MOE)
	   What would connect to the non-transparent object only to
           retrieve the info from CURLY and MOE.

	3) Sends the qualifying information (/USER=userlist) to the
           remote node for remote subsetting.  This prevents having
           to transmit over the net large data buffers of ALL users
           just to filter it all out locally.


                       	Installation:


	NOTE:  If you wish you may perform the complete installation with
	       INSTALL.COM.

	1)Create a WORLD executable directory somewhere.  (Assume
	  Sys$sysdevice:)

		$ CREATE/DIR/prot=w:e/own=system -
                    	sys$sysdevice:[net_what]

	2) Define an exec mode logical name to point to that directory

		$ define/sys/exec WHAT_DIR sys$sysdevice:[what_dir]

	3) Copy all the files in this directory to WHAT_DIR:

	4) Modify if desired the logical names in WHAT_DIR:WHATLOG
           to define site specific node groups for WHAT/SELECT

	5) Apply the CLD WHAT_DIR:WHAT.CLD to the system dcltables.

	   SET COMMAND/TABLES=SYS$COMMON:[SYSLIB]DCLTABLES -
                      /OUTPUT=SYS$COMMON:[SYSLIB]DCLTABLES -
                      WHAT_DIR:WHAT.CLD

	   Use install to replace the DCLTABLES (need about 300 GBLPAGES free)

	   $ INSTALL == "$INSTALL/COMMAND"
	   $ INSTALL REPLACE SYS$LIBRARY:DCLTABLES

	   (Or you put the command SET COMMAND WHAT_DIR:WHAT.CLD in
           the users login.com files...Slow...Ugh)

	6) Apply the file WHAT_DIR:WHAT.HLP to your favorite help library.

	   $ LIBRARY/HELP SYS$HELP:HELPLIB WHAT_DIR:WHAT.HLP

	7) Add to your site specific startup command file
           SYS$MANAGER:SYSTARTUP.COM the following lines:

		$ DEFINE/SYS/EXEC WHAT_DIR sys$sysdevice:[net_what]
		$ @what_dir:start_what

	8) Start WHAT with the command @WHAT_DIR:START_WHAT

	Note:   All cluster members CAN run WHAT from the same directory

	Now go do the same thing on all other systems with reach to
        make it a useful network wide utility

=========================================================================