EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 1


OUTLINE

    INTRODUCTION

    SCRIPT LANGUAGE
         General
         Conditional Logic
         Text Strings
         Script Language Commands

    PROGRAM OPERATION
         Menu
         Script Interpreter
         Character Transfer Loops
              Output Loop
              Input Loop

    PERFORMANCE

    ADDING PORTS AND MODEMS
         Naming Modems
         Connect and Disconnect Scripts
         Adding the Modem to the Port File
         Adding the Class to the Menu File

    ADDING NEW FACILITIES
         Investigating the New Facility
         Writing the Script
         Adding the Facility to the Menu File
         Authorizing Users for the New Facility

    APPENDICES
         A.   List of Data Files
         B.   Data File Details
         C.   List of Modules
         D.   Input Loop Flowchart
         E.   Performance Graph
         F.   User Documentation
















EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 2


INTRODUCTION

EXTERNAL  is  a  utility  program  which  provides  dial-out  access to external
facilities.    It  is  intended  for use by unsophisticated users, and therefore
omits some of the more advanced capabilities of other communications packages.

EXTERNAL  allows  users  to be authorized for specific external facilities.  The
user  selects the desired facility from a menu which shows only those facilities
which he or she is authorized to access.  The menu is controlled by a menu file,
which defines the facilities available, and the rights required to access them.

The  allocation  of  communications  ports  is controlled by a ports file.  This
file, in conjunction with the menu file, determines which ports are available to
the user for the selected facility.

When  the  user  selects  a  facility,  the  dialling and login process is fully
automatic,  being driven by a script file, written in a special script language.
This  allows  the  telephone  numbers and passwords of the facilities to be kept
confidential,  and  saves the user from having to learn multiple different login
procedures.    Once a connection has been established with an external facility,
the  entire session is recorded into a session log file in the user's directory,
allowing the user to retrieve the information at a later time.

EXTERNAL  does not yet provide any file transfer protocols.  Users seldom have a
need  to  upload  data,  and downloading text can be accomplished by editing the
required information from the log file.

The  script  program referred to above controls the dialogue between the program
and the external facility.  The script is kept hardware-independent by confining
hardware-dependent  code  to  subroutines  called connect or disconnect scripts.
Each  type  of  modem  on  the system has its own connect and disconnect script.
When  the  main  facility  script  requires any modem-dependent action, EXTERNAL
determines  which type of modem is being used, and calls the appropriate connect
or disconnect script.

In  addition  to allowing a mix of different modem types, EXTERNAL allows modems
to  be  assigned to classes.  For each facility, one can specify which class(es)
of  modem is (are) valid for it.  Thus, for example, if there is a PAD connected
to  a  particular network, those facilities which are accessible via the network
can  request  a  port connected to the PAD, while other facilities can request a
public-dial  modem.  There are no restrictions on modem or class names, provided
that  they are unique.  Any number of modem types can be assigned to each class,
and any number of classes are permitted.

All  use  of EXTERNAL is logged into a permanent log file.  This is not the same
as  the  session  log file referred to above.  The permanent log file is created








EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 3


automatically  at  the  beginning of each calendar year, and contains one record
for  each  attempted  access,  whether  successful or not.  In the event that an
attempted  access fails, the input buffer at the time of the failure is saved in
a buffer dump file, allowing debugging and adjustment of facility script files.


















































EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 4


SCRIPT LANGUAGE

General

All  scripts,  whether facility scripts, connect scripts, or disconnect scripts,
are  written  in  a special script language.  This language provides for two-way
communication  between  the  program  and  the  assigned  port,  and for one-way
communication  from  the  program to the user's terminal.  There is no provision
for  accepting input from the user's terminal to the program.  A CONNECT command
provides two-way communication between the user's terminal and the port.

Each  facility  script, connect script, or disconnect script, is a separate text
file.    The  scripts  are  interpreted, rather than compiled, allowing for easy
adjustment and maintenance.

Each  command  line consists of a keyword followed by (zero or more) parameters.
Command  parameters  may  be  separated  by  spaces,  tabs,  or  commas.  Excess
parameters  will  be ignored.  There is no provision for continuing over several
lines: each command must be contained on a single line of the script file.

Conditional logic

Conditional  logic  provides  the  ability  to  detect certain specific run-time
conditions, as well as identifying strings received from the port.

The  identification  of  input strings is based on four Boolean condition flags,
numbered  1  through  4.   These flags are set by the INPUT statement, which can
search  for  up to four text strings.  Each condition flag corresponds to one of
the  four  text  strings.   After executing the INPUT statement, only one of the
four  flags  will  be set, corresponding to the first string which was detected.
If  none  of  the  specified  strings were found in the input, a fifth flag, the
TIMEOUT flag, will be set.  See the IF and INPUT commands for more details.

Text strings

Text  strings  should  (but  don't  have  to) be enclosed in quotes.  Quotes are
required  if  the  string  contains  embedded  blanks  or  commas.   In the SEND
statement, a numeric string must be enclosed in quotes to distinguish it from an
ASCII constant.

An  up-arrow  (caret,  "^")  in a string will be converted to a carriage return.
All  carriage  returns  must  be  explicitly  included  in  strings; there is no
automatic return at the end of a string.











EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 5


Script Language Commands

ABORT ["text"]   - stops execution of scripts
                 - runs disconnect script then exits from program
                 - may not be used in disconnect script
                 - 'text' is optional
                 - prints  'text'  on  screen  and  on  permanent  log (carriage
                   control is removed from 'text' when output to log)

CONNECT          - connects terminal to port for two-way communication: displays
                   incoming  text  on  the  screen,  and transmits text from the
                   keyboard to the port
                 - enables logging of received text to the log file
                 - returns to script when user enters disconnect code (CTRL\)
                 - may not be used in connect or disconnect script
                 - will usually (but not necessarily) be the last command in the
                   script
                 - if  omitted,  the user will be unable to type anything to the
                   external facility

DIAL number      - calls the connection script to dial the 'number' according to
                   the protocol for the modem on the port in use
                 - 'number'  is  required,  and  is passed as a parameter to the
                   connect script
                 - may not be used in connect or disconnect script

GOTO label       - goes to LABEL command with specified 'label'
                 - 'label' is required

IF condition [GOTO] label
                 - checks  for  specified  condition  and branches to 'label' if
                   true
       GOTO      - optional keyword; may be omitted
       label     - label to which control passes if condition is true
                 - 'label' is required
       condition - 'condition' is required
                 - several   different   types   of  condition  can  be  tested,
                   effectively   making   several   different  varieties  of  IF
                   statement: these are discussed below:

IF CLASS "class" [GOTO] label
                 - branches if the modem in use is of the specified class

IF condition-flag [GOTO] label
                 - 'condition-flag' may be 1, 2, 3, or 4
                 - branches if the specified flag is set








EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 6


                 - no  more  than  one  of the four flags will be set at any one
                   time,  corresponding to the string (if any) that was found by
                   the most recent INPUT command

IF ECHO [GOTO] label
                 - branches if the echo flag is set; the echo flag is set by the
                   SET ECHO command

IF MODEM "modem-type" [GOTO] label
                 - branches if the modem in use is of the specified type

IF NODE "node-name" [GOTO] label
                 - branches if the modem is on the specified node

IF PORT "port-name" [GOTO] label
                 - branches if the modem is on the specified port

IF TIMEOUT [GOTO] label
                 - branches if the most recent INPUT command timed out
                 - the  TIMEOUT  flag  is set if the most recent INPUT statement
                   did not detect any of the specified strings

IF VIEW [GOTO] label
                 - branches if the view flag is set; the view flag is set by the
                   SET VIEW command

IFNOT condition [GOTO] label
                 - same  as  IF (including all the varieties of conditions), but
                   branches if condition is false
                 - note: no space between IF and NOT

INPUT [interval [count]] ["text1" ["text2" ["text3" ["text4"]]]]
                 - waits for input from the port
                 - if input matches 'text1', flag 1 is set and the command exits
                 - if input matches 'text2', flag 2 is set and the command exits
                 - etc.
                 - if  input  does  not  match  any  of  the text strings within
                   ('interval' * 'count') seconds, flag 'TIMEOUT' is set
       interval  - number of seconds to wait before checking for reply
                 - checks for reply every 'interval' seconds
                 - default is 1
       count     - maximum number of attempts to wait for reply
                 - default is 1
       textn     - text  string to check; if none specified, waits ('interval' *
                   'count') seconds, then continues with TIMEOUT flag set









EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 7


LABEL name       - defines the label 'name' as target for GOTOs
                 - 'name' is required

SEND value [value...]
                 - sends data to port
       value     - may be any of:
                 - an ASCII code: sends the specified character
                 - a  '#'  sign: sends the string specified in the most recently
                   executed DIAL command
                 - a quoted string: sends the specified string

SET DATABITS value [parity]
                 - sets the number of databits and parity for the port
                 - note  that parity on incoming data is not checked, regardless
                   of the value of this parameter
       value     - may be one of: 7, SEVEN, 8, EIGHT
                 - default is 8 bits
       parity    - may be one of: ODD, EVEN, NONE, NOPARITY
                 - NONE and NOPARITY are synonymous
                 - default is NONE

SET ECHO         - enables keyboard echo for half duplex
SET NOECHO       - disables keyboard echo for full duplex (default)

SET PAUSE tenths
                 - causes  a  delay  of  ('tenths'  /  10)  seconds  after  each
                   character transmitted by a SEND command (default = 0)
                 - 'tenths' is required

SET SPEED value
                 - sets the speed of the modem port
       value     - may be one of: 110, 300, 1200, 2400, 4800, 9600, 19200
                 - default is 1200

SET VIEW         - allows user to see scripted dialogue
SET NOVIEW       - prevents user from seeing scripted dialogue
                 - if  the user possesses the EXT_SUPPORT rights ID, the default
                   setting  of  the VIEW flag depends on the DCL Verify flag: if
                   SET  VERIFY  is in effect, the view flag is on by default; if
                   SET NOVERIFY is in effect, the view flag is off by default
                 - for ordinary users, the view flag is off by default

TYPE "text"      - sends 'text' to screen

WAIT tenths      - waits  the  specified  time  before  proceeding  to  the next
                   command








EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 8


                 - 'tenths' is an integral number of tenths of seconds
                 - 'tenths' is required

!                - comment; remainder of line is ignored


















































EXTERNAL                                                       October 12, 1988
System Documentation                                                    Page: 9


PROGRAM OPERATION

This  section  describes  the  operation of the major portions of EXTERNAL.  You
should  have available a copy of the source listings of the various modules when
reading the following descriptions.

Menu

The  menu  selection  routine  (EXT_MENU)  starts  by  reading  the  ports  file
(PORTS.DAT)  to determine which ports are available on the current node.  If the
ports  file does not include any ports on the current node, a message is printed
indicating which nodes do have ports, and the program exits to DCL.

The routine then reads the menu file (MENU.DAT), and for each facility listed on
the  file,  determines if the current user possesses any of the required rights.
If  so,  the name of the facility is displayed on the menu screen.  The user can
select  any  of the displayed facilities by number, or can exit to DCL by typing
EXIT  or  <CTRL/Z>.    For compatibility with previous versions of EXTERNAL, the
number 99 is also accepted as a valid exit command.

Once the user has selected a facility, the program uses the information obtained
from  MENU.DAT  to  choose  a modem class.  It attempts to allocate ports in the
order  in  which  the  modem  classes  are listed on the record in MENU.DAT, and
within  each class, in the order in which the ports are listed in PORTS.DAT.  If
any  ports of a specified class exist, but cannot be allocated, the program will
ask  the user if he/she wants to use a different class.  If no ports exist for a
specified  class,  the program will select the next class without asking.  If no
port was allocated, the program will exit to DCL.

Once  a  port  has  been  successfully  allocated, EXTERNAL will call the script
interpreter to read and execute the script for the selected facility.

Script Interpreter

The   script   interpreter   (EXT_SCRIPT_INTERP)   is  a  simple  keyword-driven
interpreter for the script language described elsewhere (see "Script Language").
The  source  code  should  be  fairly  self-explanatory,  except for a couple of
points: some subroutines within the module are re-entrant, and the module itself
is called recursively.

The  re-entrant  subroutines  allow  the  interpreter  to perform a forced ABORT
command  if  a  syntax  error  is  encountered while processing a command from a
script.    There  is  no  conflict  in  variable  names  between  the  different
invocations  of  the  subroutines because of the limited use of the re-entrancy.
If any changes are made to these subroutines, great care must be taken to ensure
that no such conflicts arise.








EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 10


The  interpreter  is called recursively when it encounters a DIAL command in the
script.   The second invocation of the interpreter processes the connect script,
then  returns  to  the first invocation, which continues processing the facility
script.    The  depth of recursion is limited to two levels by the fact that the
DIAL command is not permitted within a connect script.

Character Transfer Loops

EXTERNAL  uses  two loops to transfer characters between the user's terminal and
the  modem.   A synchronous loop (the output loop) runs when the facility script
executes  the CONNECT command, and transfers characters from the keyboard to the
modem.  An  asynchronous loop (the input loop), consisting of four AST routines,
runs  for  the  duration  of  the facility, connect, and disconnect scripts, and
transfers characters from the modem to the terminal and to the log file.

Output Loop

The  output  loop  consists  of  routine  EXT_CONNECT_LOOP, which is called from
EXT_SCRIPT_INTERP (the script interpreter) when the facility script executes the
CONNECT command.  If the CONNECT command is never executed, this loop will never
be  run,  and  the  user  will  never  be  able to type anything to the external
facility.  This loop performs a single-character QIOW to read from the terminal,
followed  by  a  single-character  QIOW  to  send the character to the port.  It
continues doing this until the user presses <CTRL\>.

Input Loop

The  input  loop  is  totally  asynchronous,  and  consists  of  four  routines:
EXT_READ_PORT_AST,  EXT_PROC_BUF_AST, EXT_UNSOL_MBX_AST, and EXT_WRITE_TERM_AST.
In  order  to maximize throughput, the input loop uses multiple input buffers in
addition  to  the  alternate  typeahead  buffer.  For a flowchart explaining the
following discussion of the input process, refer to Appendix D.

The input loop is initiated by executing EXT_READ_PORT_AST.  This routine checks
for  the  availability of an input buffer, allocates a buffer, and queues a read
from  the port.  If no input buffer is available, the routine reschedules itself
to run again in 0.5 seconds.  Normally, the 0.5 sec pause will allow enough time
for one or more of the buffers to be released.

While  the  routine  is  waiting  for  a  buffer,  any  incoming characters will
accumulate in the typeahead buffer.  Eventually, the typeahead buffer could fill
up,  in which case the terminal driver would send an XOFF to the port.  Provided
the  external  facility  recognizes  the  XOFF, it will stop transmission of the
text.    If  the  external  facility does not respond to XOFF, some text will be
lost.   Transmission will resume when EXT_READ_PORT_AST is able to get a buffer;
gradually, the typeahead buffer will clear, and the terminal driver will send an








EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 11


XON.

The  read  queued  by  EXT_READ_PORT_AST specifies a timeout of 0 seconds.  This
means  that  it will trigger EXT_PROC_BUF_AST immediately, regardless of whether
or  not it has read any text.  If the typeahead buffer was empty, it will return
no text; if there was text in the typeahead buffer, some of it will be returned.
EXT_PROC_BUF_AST checks the buffer count to see if it has received any text from
the  read.    If not, it assumes that transmission of text has stopped.  It then
queues a read from the mailbox associated with the port.  This will be discussed
later.

If  the  read from the port has returned some characters, EXT_PROC_BUF_AST sends
the   text   to   the   terminal,   provided   that   the  VIEW  flag  was  set.
EXT_WRITE_TERM_AST  is initiated either by the write to the terminal if the VIEW
flag  was  set,  or by a $DCLAST system service if the VIEW flag was clear.  The
EXT_WRITE_TERM_AST routine will be discussed later.

EXT_PROC_BUF_AST  then reschedules another EXT_READ_PORT_AST routine to continue
the loop, after a variable delay.  The delay is 0.0 sec (i.e. immediate) if more
than  5  characters  were  received,  and  0.05 sec if 5 or less characters were
received.    The  assumption here is that if text is arriving slowly, we want to
allow  enough  time for some text to accumulate before reading it, whereas if it
is  arriving  fast,  we want to read it immediately, so as not to lose it.  This
allows  the  input  loop  to  provide a high throughput when required, while not
using an excessive amount of CPU time when idle.

The  routine  EXT_WRITE_TERM_AST  is triggered by EXT_PROC_BUF_AST, as described
above.    It  packs  the  received text into a buffer which has two purposes: it
serves  as  an  output  buffer  for  the  log file, and it is read by the script
interpreter  when checking for received text.  After the text has been packed to
the log file buffer, the input buffer is released for re-use.

If  the  routine  EXT_PROC_BUF_AST receives an empty buffer, indicating that the
incoming  text  stream  has  stopped,  it  queues  a  read  from the mailbox, as
described  above.  When the mailbox receives a message, EXT_UNSOL_MBX_AST starts
up.  Although several types of message are possible, the only one of interest is
"unsolicited  input";  all  other  messages  cause  another  mailbox  read to be
initiated.    The  unsolicited input message indicates that the input stream has
resumed, so it queues EXT_READ_PORT_AST again to restart the input loop.

The  input  loop  continues as described above until the CONTINUE flag is set to
false  as  the  program  runs  down.    When  this  flag is cleared, it prevents
EXT_PROC_BUF_AST  from requeueing either EXT_UNSOL_MBX_AST or EXT_READ_PORT_AST,
thus ensuring that the loop terminates.










EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 12


PERFORMANCE

Performance  tests were carried out on a VAX 11/750 under VMS V4.6, using a null
modem cable between two ports on the VAX as the "external" facility.  Throughput
was  measured  in  characters  per  second  (c/s).    Efficiency was measured in
characters per CPU second (c/sCPU).

EXTERNAL showed a measured throughput of approximately 440 c/s at 4800 baud, and
about  700 c/s  at 9600 baud.  This compares well with SET HOST/DTE, which gives
440 c/s  at  4800  baud  and  750 c/s  at  9600  baud.  For comparison, the best
throughput  possible  using  single-character  QIOs under the same conditions is
150 c/s, for any speed above 1200 baud.

As  described  under Program Operation, the input loop includes a 0.05 sec delay
if  less  than 5 characters are received in any one read operation.  The purpose
of  the delay is to ensure that CPU utilization is not excessive.  The effect of
changing  the  length  of  the  delay was measured, and the results are shown in
Appendix E.  As the length of the delay was increased, the efficiency increased,
but  the  throughput decreased slightly at 9600 baud.  The value of 0.05 sec was
chosen  as  a  compromise  between  throughput and efficiency.  This is the same
length of delay used in SET HOST/DTE.

































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 13


ADDING PORTS AND MODEMS

Because  EXTERNAL's  allocation of ports is controlled by simple sequential text
files,  it is easy to add new modems and to mix dissimilar types of modems.  The
following section describes the steps required to add a new type of modem to the
system.   If you wish to add a new modem that is identical to an existing modem,
all the following steps can be omitted except "Adding the modem to PORTS.DAT".

Naming Modems

Every  distinct  type  of  modem in the EXTERNAL system must have a unique name.
Modems  that  are  functionally  identical  may have the same name.  The obvious
naming  convention is to use the name or model number of the modem (for example:
DF03,  DF112, HAYES, RIXON) as the modem type.  There is no restriction on modem
names,  except  that  different  names  should  be  unique  in  their  first  10
characters,  for  ease  of  identification on the permanent log file.  The modem
name  will  be used as the file name for the connect and disconnect scripts.  It
will  also  be  specified  in the modem_type field of the PORTS.DAT file.  Modem
type  can  be  determined  within  a  script by the IF MODEM variation of the IF
command (described under the heading "Script language").

Modems  must  also  be  given a class name.  Each external facility requests (by
means  of  the  MENU.DAT  file) one or more classes of modem.  Therefore, modems
should  be  assigned  to  classes  based on which facilities they are capable of
accessing.    Normally, all modems capable of dialling into the public telephone
network can be assigned to one class (which you could call, for example: MODEM).
However,  you  may  wish  to  have separate classes of modem based on speed (for
example:  MODEM_1200,  MODEM_4800).    If  you  have access to a packet-switched
network, you would probably want the PAD to have a different class (for example:
PAD),  because  it  is  capable  of  accessing  different  facilities from those
available  to  public-dial  modems.  The deciding factor for assigning modems to
classes  should be which facilities are accessible by each modem type.  There is
no  restriction on class names.  The modem class is specified as the modem_class
field in the PORTS.DAT and MENU.DAT files.  Modem class can be determined within
a  script  by  the  IF  CLASS  variation  of the IF command (described under the
heading "Script language").

Connect and Disconnect Scripts

If you add a new type of modem to the system, you will have to provide a connect
script  and a disconnect script for it.  If the new modem is of the same type as
an existing modem, you can use the existing scripts, otherwise, you will have to
write a new pair of scripts.  The connect script should get the attention of the
modem  and send it the appropriate dial command.  Use the SEND # script language
command  to send the number to be dialled.  If for any reason the connect script
is  unable  to complete the dialling operation and establish a phone link to the








EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 14


external  facility,  it  should execute an ABORT command, providing a meaningful
message to the user.

The  disconnect  script  is  used  to  drop the phone connection to the external
facility,  and to reset the modem to a suitable state for the next user.  If you
are certain that the modem recognizes the DTR signal from the port, and performs
the  necessary  hangup  and reset when DTR is dropped (most "dumb" modems are in
this  category),  there  is  no  need  for the disconnect script to do anything.
However,  if  the  modem does not recognize DTR (some "smart" modems are in this
category),  or if you are in doubt, the disconnect script should force the modem
into  command  mode and perform a hangup command.  Be sure to allow for both the
possibility  that  the modem may already be in command mode, and the possibility
that it may still be in online mode.

Adding the Modem to the Port File

Once  the  connect  and  disconnect  scripts  are  written,  the  modem  must be
physically  connected  to  a  port,  and a corresponding record must be added to
PORTS.DAT.    The new record must specify the name of the node in the cluster on
which  the  port  resides,  the name of the port, the modem class, and the modem
type.    These items are separated by commas.  The records on this file need not
be  in  any  particular  order, except that for a given node and class, the port
allocated will be selected by the order in which the ports are listed.

Adding the Class to the Menu File

If  you  have created a new class of modem, you must modify MENU.DAT to have all
appropriate  facilities specify the new class.  If a facility can be accessed by
more  than one class of modem, separate the classes by "+" signs.  EXTERNAL uses
the  list  of classes specified for a facility to select an appropriate port, as
described                under                "Program               Operation".























EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 15


ADDING NEW FACILITIES

Adding  a  new  external  facility to EXTERNAL requires writing a script for the
facility  and adding a new record to MENU.DAT.  The following section gives some
guidelines for doing this.

Investigating the New Facility

The  first  step  in  setting  up  a  new  facility  is to investigate its login
procedure.    For this purpose, it is useful to have a "dummy" script which does
nothing more than a CONNECT command, allowing you to perform the login manually.
Using  this  dummy script, log in to the new facility, paying close attention to
the  sequence  of prompts and responses, and the time intervals between entering
your  response  and receiving the next prompt.  Be careful to record the prompts
exactly, since the INPUT command is case-sensitive.

Writing the Script

Once  you know the login sequence, you can write the script.  See the section on
"Script  Language"  for  details  on the various commands available.  The script
will normally consist of blocks of code such as:
         LABEL     label
         SEND      "response to previous prompt^"
         TYPE      "Waiting for xxxx prompt^"
         INPUT     2 5 "xxxx"
         IF        1 GOTO next_label
         ABORT     "Did not get xxxx prompt"

It  is  a  good idea to include TYPE commands at frequent intervals, as shown in
this  example, so that the user knows what is happening.  Alternatively, you can
start  the  script with a SET VIEW command, and allow the user to see the entire
login  process,  although  this  is  not recommended if you wish to keep account
numbers and passwords confidential.

In  the  INPUT  statement,  you  should specify a length of time to wait for the
input,  and  the  number of attempts to make.  In the example above, the program
will  wait  2 seconds before checking for the input, and will repeat this wait 5
times,  for  a total of 10 seconds before it gives up.  Note that it will wait a
minimum of 2 seconds (or whatever time you specify), even if the string(s) being
searched for is (are) available immediately.  Therefore, it is usually better to
wait  for a short length of time and increase the number of attempts than to try
only  once  for a long period of time, since the user will be forced to wait for
whatever length of time you specify.

When  you specify the string to wait for in the INPUT statement, you should keep
it  as  short  as  possible,  and  as  near as possible to the end of the prompt








EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 16


string.    For example, if the prompt is "Enter your password:", you should have
the  INPUT  statement  look  for  "password:",  or even just "word:".  This will
ensure  the  maximum  chance of finding the string, since the input buffer wraps
from  time  to time, potentially splitting the received text.  However, don't go
to  the  extreme  of looking for a single character, since there would be a high
probability  of  finding  the  character  in  the  wrong place.  Also, pay close
attention  to  blanks,  and  to  whether the characters are upper or lower case,
since the string must match exactly.

Adding the Facility to the Menu File

Once  the  script  is  written,  you must add the facility to the MENU.DAT file.
This  will  make  it available to authorized users.  Each record on the MENU.DAT
file  specifies  one  facility.  The order of the records is not important.  The
various fields of each record are separated by commas.

The first field on the record is a code for the facility.  This code must be the
same  as  the  name  of  the  script  file.  It is also used as the name for the
session log file created in the user's directory for each session.

The  second  field  is  the  display  name  of  the  facility.  This is the name
displayed to the user on the menu.  It should be in quotes.

The  third  field  is a list of the classes of modem which can be used to access
this  facility.   If there is more than one class, separate the classes with "+"
signs.    The list of classes is read from left to right, so the second class in
the  list  will  not  be  used  unless there was no port available for the first
class,  etc.    (See under "Program Operation" for details of the port selection
process.)

The  fourth field is a list of rights identifiers which will authorize a user to
access  this  facility.    If  there  is  more than one identifier, separate the
identifiers  with  "+"  signs.   If a user has any of the specified identifiers,
he/she  will  be  authorized  to use this facility.  If the user has none of the
identifiers, the facility will not even be displayed on the menu screen, and the
user will not be able to select it.

Authorizing the Users for the New Facility

For  a  user to access the new facility, he/she must possess at least one of the
rights  identifiers  listed  on the facility's record in MENU.DAT.  These rights
must  be  granted  by  the  UAF  at  login  time, not granted dynamically by the
SYS$GRANTID  system service.  The choice of identifiers is totally unrestricted,
but  one  identifier,  EXT_SUPPORT,  has a special effect: it allows the user to
switch on the view flag (see the SET VIEW command) for testing purposes by using
the  SET  VERIFY  command in DCL.  It is intended that this identifier should be








EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 17


held  by  whoever is responsible for maintaining the script files, and that each
facility should include this identifier on its record in MENU.DAT, thus allowing
the maintainer to access all facilities.



















































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 18
APPENDIX A: List of Data Files

Name                 File Spec        Description

Menu file            MENU.DAT         List  of  external  facilities,  including
                                      requested   modem   classes  and  required
                                      rights  identifiers.  Sequential text file
                                      created by text editor.

Port file            PORTS.DAT        Information   about   ports   and  modems.
                                      Includes   node  name,  port  name,  modem
                                      class,  and  modem  type.  Sequential text
                                      file created by text editor.

Facility script      xxxx.SCR         Script file for facility xxxx.  Sequential
                                      text  file created by editor.  Must follow
                                      Script Language syntax.

Connect script       mmmm.CSCR        Script  file  for dialling out using modem
                                      type  mmmm.    Must follow Script Language
                                      syntax.

Disconnect script    mmmm.DSCR        Script  file  for disconnecting modem type
                                      mmmm.  Must follow Script Language syntax.

Permanent log file   EXTERNAL_yy.LOG  Permanent  record  of  all EXTERNAL usage.
                                      Sequential  file, created automatically at
                                      start of each year.  yy is year.

Session log file     xxxx.LOG         Log file created in user's login directory
                                      containing   entire   online  session  for
                                      facility xxxx.

Buffer dump file     EXT_yymmddhhmmss.LIS  Buffer  dump  file,  created  when  a
                                      script  aborts.   It contains the contents
                                      of  the  input  buffer  at the time of the
                                      failure.



















EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 19
APPENDIX B: Data File Details

MENU FILE

     - name is MENU.DAT
     - sequential, variable length record
     - created and maintained by text editor
     - defines which external facilities are available: a script file must exist
       for each record on this file
     - four fields per record, separated by commas:
            - unique  code  identifying  the  facility: this code is used as the
              file name for the associated script file
            - display  name  for  the  facility,  in  quotes:  this  is the name
              displayed to the user
            - classes  of  modem  requested:  if  more than one class permitted,
              separate  classes  with  a  "+" sign; the class chosen will be the
              first available class, reading left to right
            - rights  identifiers  required:  if  more  than  one  ID  is valid,
              separate  IDs  with  "+"  signs;  if  the  user  holds  any of the
              specified rights, he/she is allowed to access this facility
     - blanks and tabs are permitted
     - any record starting with a "!" will be ignored
     - example:

ARIS,     "DEC Professional ARIS",  MODEM,                 EXT_SUPPORT
DBCAN,    "D & B Canada",           DP3000 + MODEM,        EXT_DBCAN
DIALOG,   "Dialog",                 DP3000 + MODEM,        EXT_DIALOG





























EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 20
APPENDIX B: Data File Details

PORT FILE

     - name is PORTS.DAT
     - sequential, variable length record
     - created and maintained by text editor
     - defines  which  ports  are available for dialling out, and identifies the
       corresponding modem classes and types
     - each  record  defines one port, and what type of modem is attached to the
       port:  there  must be a connect and disconnect script for each modem type
       referred to on this file
     - four fields per record, separated by commas:
            - name of the node on which the port exists: do not
              include the double colon
            - name of the port: include the colon
            - the class of the modem connected to this port: the class
              name must match the requested class of those facilities
              which are expected to use this port/modem
            - the type of modem connected to this port: this name is
              used as the file name for the connect and disconnect
              scripts
     - blanks and tabs are permitted
     - any record starting with a "!" will be ignored
     - example:

       BETA,         TTA4:,         MODEM,        SPORTSTER
       GAMMA,        TXA4:,         MODEM,        DF112
       GAMMA,        TXA5:,         DP3000,       PIN
       SIGMA,        TXA2:,         DIRECT,       NONE


























EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 21
APPENDIX B: Data File Details

PERMANENT LOG FILE

     - name is: EXTERNAL_yy.LOG, where yy is current year
     - sequential, fixed length record
     - created automatically by the first use of EXTERNAL of each calendar year
     - each use of external appends a new record to this file
     - record format:
        START_TIME          X(12)   date/time the connection was established.
        END_TIME            X(12)   date/time  the connection was terminated, or
                                    the connection attempt failed.
        FACILITY_NAME       X(10)   Abbreviated  name  of  facility  -  same  as
                                    facility name on MENU.DAT
        USER_NAME           X(12)   VMS Username of user
        ACCOUNT_NAME        X(12)   VMS Account of user
        NODE_NAME           X(10)   Node  of  VAXCluster  on  which EXTERNAL was
                                    run.
        PORT_NAME           X(5)    Name of port to which modem was connected.
        MODEM_TYPE          X(10)   Type  of  modem used - same as modem type on
                                    PORTS.DAT
        MESSAGE             X(50)   Error message if connection failed - message
                                    is taken from ABORT command.

































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 22
APPENDIX B: Data File Details

SCRIPT FILES

     - sequential text file, variable length records
     - created and maintained by text editor
     - three types of script:
            - facility script
            - connect script
            - disconnect script
     - these types are discussed below
     - the script language is discussed separately (see "Script Language")

Facility script

     - name of file is ffff.SCR, where ffff is the facility name from MENU.DAT
     - purpose  is  to control dialogue between program and external facility in
       order to perform log in sequence
     - will normally contain at least a DIAL command and a CONNECT command
     - the  remaining  statements  in  the  script  will  depend  on  the  login
       requirements of the particular facility
     - if  unable  to  log in, the script should execute an ABORT command with a
       meaningful message explaining the problem

Connect script

     - name of file is mmmm.CSCR, where mmmm is the modem type (from PORTS.DAT)
     - purpose  is  to  get  the attention of a particular type of modem, and to
       dial a specified telephone number
     - if  the  call  can not be completed, the connect script should execute an
       ABORT command with a meaningful message explaining the problem
     - should normally contain one SEND # command
     - connect script must not contain DIAL or CONNECT commands
     - called as a subroutine of a facility script by the DIAL command

Disconnect script

     - name of file is mmmm.DSCR, where mmmm is the modem type (from PORTS.DAT)
     - purpose is to disconnect the call, and to restore the modem to a suitable
       state for the next user to dial out
     - called by the ABORT command, or at the end of the facility script
     - may not contain DIAL, CONNECT, or ABORT commands.
     - if  the  modem  automatically  drops  the telephone connection and resets
       itself  when  the DTR signal is dropped (which happens automatically when
       the program exits), the disconnect script need not do anything
     - if  the  modem  does not reset itself when DTR is dropped, the disconnect
       script  should  get the attention of the modem, place it in command mode,
       and perform a hangup on the telephone line








EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 23
APPENDIX B: Data File Details

SESSION LOG FILE

     - name is ffff.LOG, where ffff is code for facility, from MENU.DAT
     - created  in  user's  default  directory for every successful or attempted
       access to a facility
     - format is a stream file with variable length records, and CR/LF as record
       terminator
     - contains  all  bytes  received from the port while the CONNECT command of
       the  facility  script  was  in  effect, except NUL (ASCII 0) and DC3/XOFF
       (ASCII 19)
     - contains  echo of text typed on keyboard by user only if echo is provided
       by  external facility (i.e. SET ECHO command provides echo to screen, but
       not to session log file)


BUFFER DUMP FILE

     - name is EXT_yymmddhhmmss.LIS, where yymmddhhmmss is current date/time
     - created any time script encounters an ABORT command
     - format  is  a  single  record  whose length is the length of the log file
       buffer (i.e. 512 bytes)
     - contains  the  contents  of  the  log  file  buffer at the time the ABORT
       command  was  executed    (The  log file buffer is what the INPUT command
       reads to search for the specified strings.)






























EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 24
APPENDIX C: List of Modules

     EXTERNAL.BAS                 main  program  to  communicate  between user's
                                  terminal and external facility

     EXT_UNSOL_MBX_AST.BAS        AST   routine  to  receive  unsolicited  input
                                  messages from the modem port

     EXT_READ_PORT_AST.BAS        AST  routine to initiate a read operation from
                                  the modem port

     EXT_PROC_BUF_AST.BAS         AST  routine  to  process  characters received
                                  from the modem port

     EXT_WRITE_TERM_AST.BAS       AST  routine  to  write received characters to
                                  the  log  file,  and  perform  buffer  cleanup
                                  operations

     EXT_SCRIPT_INTERP.BAS        subprogram to interpret and execute scripts

     EXT_SCREEN_HDR.BAS           subprogram  to  display a screen header with a
                                  message

     EXT_MENU.BAS                 subprogram  to display the customized menu and
                                  accept a selection by the user

     CHKRDB.BAS                   subprogram to check rights identifier

     EXTERNAL.COM                 DCL command file to run EXTERNAL.EXE.

     EXT_COMPILE.COM              DCL  command  file  for  compiling and linking
                                  EXTERNAL.EXE.
























EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 25
APPENDIX D: Input Loop Flowchart




















                             flowchart page 1


































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 26
APPENDIX D: Input Loop Flowchart





















                             Flowchart page 2

































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 27
APPENDIX D: Input Loop Flowchart





















                             Flowchart page 3

































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 28
APPENDIX D: Input Loop Flowchart





















                             Flowchart page 4

































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 29
APPENDIX D: Input Loop Flowchart





















                             Flowchart page 5

































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 30
APPENDIX E: Performance Graph





















                             Performance graph

































EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 31
APPENDIX F: User Documentation

Procedure:      EXTERNAL

Purpose:        Connects  you  to  one of several external facilities.  Performs
                automatic  log-on  to  the external facility, then connects your
                terminal to the facility.  Logs the entire online session into a
                file in your default directory.

Authorization:  Anyone can enter the External system, but specific authorization
                is  required to connect to each external facility.  The facility
                is  chosen  from a menu which displays only the facilities which
                you personally are authorized to access.

Called by:      typing EXT at system prompt

Aborting:       EXTERNAL  can be aborted in several different ways, depending on
                the current stage of the connection process:

                   STAGE                   ABORT PROCEDURE
                   Menu                    EXIT
                   LOGGING IN              <CTRL/C>
                   Connected to facility   <CTRL\>  (see note below)
                   Logged off facility     <CTRL\>  (see note below)

                Once  you  have  selected  a facility from the menu, the current
                abort  procedure  is  displayed at the upper right corner of the
                screen.

                NOTE: Most external facilities require that you log out when you
                are finished.  The procedure for doing this varies from facility
                to  facility,  and must be done prior to typing <CTRL\> to exit.
                Failure  to  log out can result in excessive connection charges.
                Once  you  log out of the facility, you must still press <CTRL\>
                to exit from EXTERNAL

Operation:      EXTERNAL is started by typing EXT at system prompt.  A menu will
                be  displayed,  showing  the  external  facilities  that you are
                authorized to access.  Enter the number of the facility you wish
                to access, or EXIT to exit.

                Once  you  have selected a facility, EXTERNAL will automatically
                dial  the facility and log on to it.  While this is occurring, a
                series  of  messages  is  displayed  at the bottom of the screen
                indicating which step of the process is currently in progress.

                The  message  "Connected  to  xxxx"  (xxxx  is  the  name of the
                facility)  at the top of the screen indicates that the login was








EXTERNAL                                                       October 12, 1988
System Documentation                                                   Page: 32
APPENDIX F: User Documentation

                successful,  and that you may proceed with whatever transactions
                you wish to make.

                To log off, you must first follow whatever logout procedures are
                required  by  the  facility  you  are  using.  Once the facility
                indicates  that  the  session has been terminated, press <CTRL\>
                (Hold down "CTRL" while pressing "\") to exit from EXTERNAL

Output:         Everything  which  appears on your screen from the time EXTERNAL
                completes the login until you log out is saved in a file in your
                login  directory.    The  name  of this file is displayed on the
                screen when you exit.