Host Process to FDDRV for VMS

1. GENERAL
   How an FDDRV host process connects to FDDRV to emulate a disk...

FDDRV uses only one I/O code, IO$_FORMAT, for its' interface to a host
process, while looking like a normal disk to whatever process is trying
to access the "disk". (There MUST be a modifier set also (128 or another
higher power of 2).

The IO$_FORMAT code requires two parameters.
	P1  is a buffer address describing what to do, etc.
	P2  is the length in bytes of the buffer in P1.

Write access to the buffer is required.

The buffer format is in longwords:
	Word 1 is a code number. Codes used in FDDRV are:

	0 - Declare or undeclare a host process (has the effect of
		setting disk max size and setting it online, or of
		declaring FDn: offline. Only one host process per
		unit of FD: should be declared. While this is not
		enforced, confusion and nonsense will result if it
		is not followed. It is expected that the host process
		will un-declare itself on image exit. However, if FDDRV
		detects nonexistent process when notifying a unit's control
		process of a transfer to be done, it will attempt to
		take itself offline and clean up.
	1 - Finish I/O on the packet currently in process by whatever
		is trying to read/write the disk (call this on behalf of
		the "client" process).
	2 - Copy data from the host process TO the driver's internal
		buffer (including the 20 byte header).
	3 - Copy data from the driver's internal buffer TO the host
		process (including the 20 byte header).
	4 - Copy data from host to driver internal, EXCLUDING the 20
		byte header.
	5 - Copy data from driver internal to host, EXCLUDING the 20
		byte header.

	The format of the buffer header is:
		Transfer direction, 0=read, 1=write. As seen by CLIENT.
		Block number
		Bytes to transfer
		I/O Status Block longword 1
		I/O Status Block longword 2

	All the buffer header fields are longwords.

	The IO$_FORMAT argument's buffer has a format that depends
	on the code used.

For declare Process:
	Code (=0)
	PID of host process (internal)
	Max number of blocks on disk (0 signals UNdeclare process)
	UCB address of a mailbox used to communicate to host.
	# Tracks (assembly option of fddrv) (goes into byte)
	# sectors/track (assembly opt) (goes into byte)
	# cylinders (assembly option) (goes into word)

For Complete I/O
	Code (=1)
	Function (0=read, 1=write)
	Block number
	Bytes in buffer
	I/O Status block longword 1
	I/O Status Block longword 2

For Copy data from Host process to Driver buffer
	Code (=2)
	Buffer address (in host process)
	Length of buffer in bytes (including 20 byte header)

For Copy Data from Driver Buffer to Host Process
	Code (=3)
	Buffer address (in host process)
	Length of buffer in bytes (including 20 byte buffer)

Note the copy subfunctions do NOT have to always grab all data from
the driver; repeated copies are legal.

	When FD: has some work for the host process, it sends
the buffer header contents (5 longwords) to the mailbox given
in the initial setup call. It is expected the host process is waiting
for a read on this mailbox and that it will then begin processing
the I/O. If there are errors in sending this data, FDDRV will abort
the I/O and take itself offline.
	An assembly option sends a 6th longword also, the address in
FDDRV of the data buffer header being used for this unit, in the mailbox
message. This can be used for access via $CMKRNL if desired.
	The host process is expected to do a QIOW type read on the
mailbox, which will then deliver the initial data to tell whether
it needs to perform a read or write. It should transfer data, then
issue its terminate I/O functions to tell the client process the
I/O is done. the driver takes care of moving data between driver
and client process.

The sequence should be something like this:


Create mailbox and get its UCB address.
Declare exit handler to run Cleanup code on exit

(Set up size in cylinders of drive as needed)
Register with fd: to indicate we're the server process.

loop:
Read mailbox channel, waiting till data appears.

If a read function
  Get data from wherever it lives and make it look reasonable
  Write data into driver's buffer with iosb valid...include the
	header.
Else if a write function
  Read whole driver buffer into host process
  Send to wherever it must go
  Formulate 20 byte header and write it to driver's buffers
end if

Terminate the I/O

Go back to loop

Cleanup code:
  Register with FD: driver that we're going out of business.


2. SPECIFICS
	The FDHOST program supplied is an initial implementation of a
host process for FDDRV. It uses a built in, static array to hold data
for the emulated disk as part of its' virtual address space. This is
largely done for initial tests to prevent any problems from corrupting
disk file structures on a hard disk. However it illustrates the
principle. Notice that since FDHOST has to copy data twice, the
implementation is somewhat inefficient. It is expected that where
storage is on a disk file or another node, this will not be an issue,
as data would be copied directly to/from the buffer used to
communicate with FDDRV. While the functions within FDDRV which copy
data only could be used, it is expected that FDHOST will be easier
to modify into a network or other type virtual storage host in the
form in which it is currently. The changes needed to support using
functions 4 or 5 instead of 2 or 3 for copying are fairly small in
any case; it is hoped this will not cause difficulties.
	To be more general, FDHOST also needs to be able to modify
more of the device characteristics of the driver; that is, things
like the physical layout must be specifiable somehow. Currently the
setup does some of this, but FDHOST can and should modify this for
cases where other geometries are desired. Most of FDDRV doesn't
really know or care about device geometry.

  Alternate FDHOSTs:

FDHOSTMEM.mar is a more efficient memory disk. It copies data between
the driver and the "disk" data area directly rather than making an
intermediate copy in a buffer. This makes it more efficient than
the original FDHOST and more suitable as a "production" memory
disk.