CHAPTER 1

                     DISM32 - GENERAL INFORMATION




                             LEGAL NOTICE

        This program is supplied "as-is" in the public domain,
        and  neither  the  author  nor  the  author's employer
        accept any liability for the function or lack  thereof
        of  the  program, or the uses to which the program may
        have  been  placed.   Any  acts  (legal  or   illegal)
        committed  by a user with this program are solely that
        user's responsibility.


Now that that's out of the way....




DISM32 is a program that runs on VAX/VMS systems and has the  function
of  converting executable, shareable, and system images created by the
VAX/VMS Linker back into symbolic MACRO-32 source files.

It can be run with the DCL RUN command or (preferably)  defined  as  a
foreign command:

        $ DISM32 :== $dev:[dir]DISM32

and invoked with a  parameter.   The  one  parameter  (which  will  be
prompted for if forgotten) is the file specification of the image file
to disassemble (default file  specification  is  defdev:[defdir].EXE),
with  optional qualifiers to modify the disassembler's operation.  The
disassembler will attempt to open the image file, determine the  image
type,  and  convert it into a MACRO source file located in the current
default directory with the same file name as  the  image  file  and  a
filetype  of  .MAR.  The disassembler may also create auxiliary output
files in the current directory.

The command qualifiers that may be specified with the input file are:

DISM32 - GENERAL INFORMATION                                  Page 1-2


         /[NO]ASCII  -  whether  or  not  byte,  word,  longword,  and
         quadword  data  items should be optionally displayed as ASCII
         strings in the .MAR file; (default is ASCII only in character
         string type data)

         /[NO]DRIVER - attempt to force interpretation of an image  as
         a   device  driver  or  old-style  loadable  executive  image
         (default is to only recognize a driver or loadable  image  if
         it has no transfer addresses)

         /[NO]STRING  -  attempt  to  convert  long  byte  arrays   to
         printable ASCII strings and re-type as such

         /[NO]TRACE - report one-line progress messages as DISM32 runs
         (default is to report progress)


The  disassembler  will  only  work  on   native   mode   images   (no
compatibility  mode),  but  will  handle normal executables, shareable
images, executable  files  containing  device  driver  images,  images
linked  /SYSTEM,  and  VMS V5.x loadable executive images.  The images
may have been built under any version of VAX/VMS  from  V1.0  to  V5.x
(although for images linked against the system symbol table, they must
be disassembled on a system of the same major version in order to  get
the proper SYS.STB file).

The disassembler generates symbolic  output,  filling  in  labels  and
procedure names for its symbol table from:

     1)  the VMS system symbol table file SYS$SYSTEM:SYS.STB,

     2)  the Run-Time Library system service entry definition  modules
         SYS$P1_VECTORS and RMS$GLOBALS,

     3)  the Debug Symbol Table (DST) and Global Symbol Table (GST) of
         the  image  file  (except  for certain DST records that would
         only occur in an image compiled and linked /DEBUG anyway),

     4)  the GST's of any shareable images the image is linked to,

     5)  any embedded CLI command tables found in the image,

     6)  a user-defined symbol table  file  in  disassembler  internal
         form,

         and, finally, if no other definitions occur,

     7)  it makes them up from the data/code type and address  of  the
         label.


The disassembler determines how to process the labels it discovers  on
pass  1  by how they are referenced, i.e.  if a label is referenced as
the address of a F_floating variable,  it  will  be  tagged  as  being
F_floating  type  (possibly among other types for the same label).  On

DISM32 - GENERAL INFORMATION                                  Page 1-3


pass 2, the disassembler uses the most important type for each  symbol
in determining how to process image data following the symbol.  Symbol
types recognized, along with their bit-mask values for the  .SYM  file
the disassembler outputs, are, in order of importance:

        00000001        CALLS/CALLG procedure entry mask
        00000002        JSB/BSBB/BSBW subroutine entry
        00000004        JMP/BRB/BRW label
        08000000        device driver FDT entry
        04000000        device driver reinitialization table
        02000000        device driver initialization table
        01000000        device driver DDT
        00800000        device driver DPT
        00400000        FORTRAN precompiled FORMAT statement
        00200000        RMS control blocks (FAB, RAB, etc.)
        00100000        shareable image transfer vectors
        00080000        extended data attributes, see explanation below
        00040000        <not yet defined, reserved for expansion>
        00020000        octaword
        00010000        EDITPC instruction pattern
        00008000        table (MOVTC, SPANC, CRC, etc. instructions)
        00004000        trailing numeric string
        00002000        leading separate string
        00001000        packed decimal (BCD) string
        00000800        ASCII character string
        00000400        H_floating value
        00000200        G_floating
        00000100        D_floating
        00000080        F_floating
        00000040        quadword (also some descriptors)
        00000020        longword (also address pointers)
        00000010        word
        00000008        byte

Some of these may not be completely supported yet; the disassembler is
still growing as need requires its functions to increase.

If the extended data attributes bit is specified in the  symbol  table
type  mask,  it indicates that the data type is of a complex type that
couldn't fit in the normal type mask because  it  required  additional
context  (and  also because we ran out of bits in the type mask).  The
additional  context  consists  of  an   extended   attribute   number,
indicating  the  data type, and a value associated with the attribute.
The attributes currently supported and  the  meaning  of  the  related
values are as follows:

     1.  LIB$TPARSE state table (value is  address  of  keyword  index
         table)

     2.  LIB$TPARSE keyword index table (value started at  zero,  will
         be count of number of keywords when done)

     3.  LIB$TPARSE state table entry (value  is  address  of  keyword
         table)

DISM32 - GENERAL INFORMATION                                  Page 1-4


     4.  SYS$GETDVI item list (value is not used)

     5.  SYS$GETJPI item list (value is not used)

     6.  SYS$GETQUI item list (value is not used)

     7.  SYS$GETSYI item list (value is not used)

     8.  SYS$SNDJBC item list (value is not used)

     9.  SYS$CHANGE_ACL item list (value is not used)

    10.  SYS$CHKPRO, SYS$CHECK_ACCESS item list (value is not used)

    11.  SYS$CRELNM, SYS$TRNLNM item list (value is not used)

    12.  SYS$CREPRC quota list (value is not used)

    13.  SYS$FILESCAN item list (value is not used)

    14.  SYS$GETLKI item list (value is not used)

    15.  SYS$GETUAI, SYS$SETUAI item list (value is not used)

    16.  SYS$MOUNT item list (value is not used)

    17.  BASIC-PLUS-2/VAX module argument list (value is not used)

    18.  CALLG  instruction  argument  list  (value  is   address   of
         procedure called with this argument list)

    19.  License Management Facility system services  item  list  (VMS
         V5.x only) (value is not used)

    20.  FORTRAN NAMELIST data structure (value is not used)

    21.  SYS$PROCESS_SCAN item list (value is  not  used)  (VMS  V5.2+
         only)

    22.  SYS$DEVICE_SCAN item list (value  is  not  used)  (VMS  V5.2+
         only)

    23.  LIB$TPARSE keyword text (to be used internally only; value is
         address of keyword index table)

    24.  terminal driver vector table (value is not used)

    25.  full VMS descriptor data structure (value is not used)

    26.  old-style loadable  executive  image  header  (SCSLOA,  etc.)
         (value is not used)

    27.  SYS$DCLEXH exit control block (value is not used)

DISM32 - GENERAL INFORMATION                                  Page 1-5


    28.  PL/I file control block (value is not used)

    29.  CRFSHR  library   routine   cross-reference   control   table
         ($CRFCTLTABLE macro) (value is not used)

    30.  BASIC file open option block (value is not used)

    31.  old-style loadable executive image (CPULOAxxx, SCSLOA,  etc.)
         initialization list (value is not used)

    32.  $XABITM RMS control block's item list (value is not used)

    33.  CRFSHR library routine cross-reference field definition macro
         ($CRFFIELD) (value is not used)

    34.  FAO control strings embedded in $CRFFIELD macros  but  stored
         separately  in  memory  (symbol type internal to disassembler
         only; value is address of corresponding $CRFFIELD macro)

    35.  bound-procedure-value (BPV) data structure (used  by  certain
         odd high-level languages; value is not used)

    36.  bound-label-value (BLV) data structure (used by  certain  odd
         high-level languages; value is not used)

    37.  generic item list (3-longword type),  where  type  codes  are
         unknown (value is not used)

    38.  embedded CLI command definition table block  (block  type  is
         determined implicitly from the virtual memory contents and is
         not stored in the symbol table;  value  is  address  of  base
         block in the table for all blocks except the base block; base
         block extended value is zero)


The auxiliary output files the disassembler generates in  the  current
default directory are:

     1)  filespec.SYM - the final version  of  the  symbol  table  the
         disassembler     uses.      format     is     (in    FORTRAN)
         FORMAT(Z8,X,Z8,X,I4,X,Z8,X,A), one  symbol  entry  per  line,
         where  the  first  Z8  field  is the hexadecimal value of the
         symbol, the second Z8 field is the  hexadecimal  bit-mask  of
         all  standard data types (see table above) the symbol is used
         with, the I4 field is the extended attribute number, the last
         Z8  field is the extended attribute associated value, and the
         A field is the symbol name (up to 31 characters).

     2)  filespec.DST - the Debug Symbol Table dump, only  for  images
         that  have  a  DST.  This is an ASCII text file narrating the
         contents of the DST.

     3)  filespec.MOD_LIN - the module/line number accounting  of  the
         image,  only  for  images  with a DST, and/or with procedures
         compiled  with  VAX  BASIC.   This  is  an  ASCII  text  file

DISM32 - GENERAL INFORMATION                                  Page 1-6


         describing the module and line number structure of the image.

     4)  filespec.GST - a copy of a shareable  image's  global  symbol
         table,  in  standard  VAX/VMS Linker binary .STB file format.
         Only created if file being disassembled is a shareable  image
         with a GST.

     5)  filespec.OPT - the linker options file that would  be  needed
         to  re-create  the image; specifies shareable image universal
         symbols, non-standard base address or image name, etc.


The disassembler looks for a .SYM file in the current directory before
it begins processing the image file.  This file is in exactly the same
format as the output .SYM file, and it is used to pre-load the  symbol
table  with  values,  types,  and  names;  generally, this is good for
forcing a meaningful symbol name when an image does not have a DST  to
define  the symbol, or for changing the type of a symbol (for example,
a procedure is referenced by a PUSHAB in a CALLS argument list and may
be  treated  as  BYTE type instead of PROCEDURE type; see below sample
session for an example).  If an old .SYM  file  does  not  exist,  the
disassembler  ignores  the  condition  and  goes  on without one.  The
disassembler then looks at the image transfer vectors,  the  DST,  and
the  GST, and uses those to pre-load the symbol table.  During pass 1,
any code-type symbols (PROCEDURE, SUBROUTINE, or JUMP/LABEL) are  used
as points to start disassembling code from in the hope of finding more
symbols.  This repeats until  the  disassembler  can't  find  any  new
code-type  symbols it hasn't already started disassembling from.  Thus
ends pass 1.

In the symbol table analysis phase, the module table and  line  number
table  are  sorted  into  ascending  address  order  (symbol  table is
implicitly sorted by entry insertion method),  and  attempts  to  find
names  for  symbols  begins,  in the order described earlier (although
some names were already inserted under the assumption they might  have
been needed to prime the disassembler's pass 1 operation).  Also, data
structures that might contain pointers to other  data  structures  (or
even  code)  are  analyzed to add the additional entries to the symbol
table; if new code symbols are found, pass 1 is rerun to  analyze  the
new symbols.  Among the data structures analyzed are the beginnings of
procedures which look like  they  might  have  been  compiled  by  the
BASIC-PLUS-2/VAX compiler with their appropriate setup code, and CALLG
argument lists which may be connected to system  service  or  Run-Time
Library  calls  (where the argument list entries have known meanings).
Argument list descriptions for Run-Time Library procedures (which  are
also used in pass 1) are stored in files located in the same directory
as DISM32.EXE (again,  not  necessarily  the  user's  current  default
directory),  where the files have the same name as the shareable image
and a filetype of .OFFSET.  Not having an .OFFSET file is not a  fatal
error; the disassembler will continue to run without type-checking the
called procedure arguments.

In pass 2, the disassembler just runs from beginning  to  end  of  the
image,  changing  processing  types  as  it reaches a new symbol table
entry with a different most-important data/code type.

DISM32 - GENERAL INFORMATION                                  Page 1-7


For device driver images, the  disassembler  recognizes  them  because
they  (usually)  have no transfer addresses and the first few bytes of
them look like a Driver  Prologue  Table  (DPT),  as  checked  by  the
DPT$B_TYPE and DPT$W_SIZE fields.  The disassembler will announce when
it is assuming that an image is a device driver, and will then process
all  data  found  in the driver's DPT, initialization tables, DDT, and
FDT in an attempt to initially build the symbol  table.   If  somebody
forgot  to  specify the linker options file with BASE=0 for the driver
when the driver was built, the disassembler will continue to run,  but
will  report  appropriate  warnings  and  add  the BASE= option to the
generated  .OPT  file.   Similar  processing  is  done  for  old-style
loadable  system  images (for example, SCSLOA), although they have the
LOADCODE header rather than a DPT.

For compatibility mode images, the disassembler  recognizes  that  the
image  header  type  specifies  TKB instead of LINK-32 and rejects the
image.  For other strange  but  native-mode  image  types  (CLI,  BPA,
etc.),  the  disassembler accepts them, but displays a warning message
and adds the undocumented Linker option  IMAGE_TYPE=  to  the  options
file.

For system images, the disassembler recognizes them because the  image
header type word is no value known to VAX/VMS.  The disassembler gives
the user the option of quitting or treating  the  image  as  a  system
image.   If  a  system  image, the user must enter the base address in
hexadecimal when prompted.  Note that, since a  system  image  has  no
mechanism  for  locating  any  initial  symbols,  a .SYM input file is
generally required to disassemble a system image into something  other
than  a  stream  of  longwords.  Note that, other than SYS.EXE and the
primary bootstraps, very few VMS images are of /SYSTEM type.

For normal executables and shareables linked on version V3 or  earlier
of  VAX/VMS, the disassembler will attempt to open a V3 copy of VMSRTL
to resolve shareable image references if such occur.   A  file  called
VMSRTL_V3.EXE  is  expected  to be in the same directory as DISM32.EXE
(not necessarily the user's current  default)  and  will  be  used  to
resolve such references; this file is a renamed copy of the VMSRTL.EXE
file found in SYS$LIBRARY on a V3 system.  This file is not  used  for
images linked at VMS V4.0 and higher.

The disassembler works best when  processing  code  that  follows  the
normal  rules of civilized programming, as defined by DEC.  However, a
fair amount of DEC (and third party) code does not  follow  the  rules
that  DEC  gave  to  everyone  else,  so  some  images  may  break the
disassembler or require careful manipulation of the .SYM file  to  get
meaningful  output.  Also note that for device driver images built for
a major version of VAX/VMS other than  the  one  the  disassembler  is
running   under   (which   is   supplying  SYS$SYSTEM:SYS.STB  to  the
disassembler),  the  references  to  the  executive   probably   won't
disassemble properly in regards to executive entry point symbols.













                              CHAPTER 2

                    A TYPICAL SESSION WITH DISM32



Typically, the disassembler is used in a multi-run session, where  the
first  run gets the image roughly disassembled, and, after analysis by
a human being,  a  final  run  is  made  with  erroneous  disassembler
assumptions  corrected  by  manually editing the disassembler's symbol
table.  Such a session is performed by the following steps:

     1.  run DISM32 on the image file with no previous .SYM  file  and
         with  the /ASCII qualifier specified; optionally, the /STRING
         qualifier can also be specified.

     2.  examine the .SYM and .MAR files returned to see if  any  data
         types have been mis-assigned (due to the limited intelligence
         of  the  disassembler).   Such  cases  could   include   (not
         all-inclusively):

         a)  local procedures passed as data items (PUSHAB  proc_name)
             to other local procedures;

         b)  procedures,  subroutines,  and  code  labels   referenced
             through  an indirect jump table array or addresses loaded
             previously into a register (often done by some compilers;
             hence  the  %DISM32-I-INDCALJSB  message, to alert you of
             such cases);

         c)  character data  types  referenced  as  numeric  and  vice
             versa;

         d)  device-dependent extensions to the  VMS  standard  device
             driver structure, or multiple symbols given the same name
             for different driver FDT routines (because they  work  on
             the same sets of I/O function codes).

         Such symbol entries can have their type, extended  type,  and
         extended  value  fields  modified to change the processing of
         that symbol entry.  This is done by editing the .SYM file  to
         change  the  stored typing of the entry; such entries will be
         used   as-modified   when   the   disassembler   next   runs.
         Additionally,  new symbol entries could be manually made with
         a text editor to cause additional disassembly to occur  (most
         frequently useful when a CALLx, JSB, or JMP occurs indirectly

A TYPICAL SESSION WITH DISM32                                 Page 2-2


         through  a  register  or  an   indexed   table,   where   the
         disassembler  does  not  properly  pick up the actual routine
         entry  points),  or  symbol  names  can   be   changed   from
         disassembler default names to more meaningful ones.

     3.  while scanning for disassembler errors, look for places where
         you  can  put in more meaningful symbol names.  Various cases
         where this is applicable include (but  are  not  limited  to)
         cases like this:

         a)  the  third  argument  to  the  SYS$PUTMSG  service  is  a
             procedure  that  is  passed a string by descriptor and an
             arbitrary user value.  SO, I can arbitrarily  change  the
             name    of    said    procedure    to    something   like
             "P_$PUTMSG_actrtn".

         b)  the first argument to SYS$ASSIGN is  a  descriptor-passed
             device  me  string,  and  the  second  argument is a word
             buffer for the returned channel.  Hence, you can go  look
             at the device name string pointed by that descriptor, and
             change  the  symbol  on  the  descriptor   to   something
             meaningful (i.e.  DSC_input_devnam_str) and similarly for
             the device channel word (i.e.  W_input_dev_chan).

         c)  some of the fields in RMS control blocks (most often, the
             FAB)  point to strings; the contents of these strings may
             help you determine what files those RMS blocks  are  used
             for   (and   then,   recursively,  the  function  of  the
             procedures that call  RMS  services  with  those  control
             blocks).

         d)  look for CALLS instructions to known procedures, and note
             where  register  values  are  pushed  for  the arguments.
             Knowing the  function  of  the  arguments,  and  scanning
             manually  backwards  through  the  .MAR file to where the
             register was loaded  (probably  with  a  MOVAB  or  MOVAL
             instruction),  you  can  find what to fix the symbol type
             and/or name to.  For example:

                            MOVAB  B_00001234,R5
                            PUSHAB (R5)
                            CALLS  S^#1,@#SYS$OPEN
             implies that B_00001234 is actually an  RMS  File  Access
             Block  (FAB)  instead  of  just a byte stream; therefore,
             edit the .SYM file to set the  type  field  bit  for  RMS
             control  blocks  for  entry 00001234, and change the name
             appropriately.


     4.  re-invoke the disassembler on the same image  file  with  the
         modified  symbol  table  file  in  the current directory; the
         disassembler will read the symbol table file and use it as  a
         starting  point  for  this disassembly run.  On such a second
         run, usually the /ASCII  qualifier  is  not  needed,  but  if
         several  new  code  symbols were defined, it may be useful to

A TYPICAL SESSION WITH DISM32                                 Page 2-3


         specify it again (or even use the /STRING option).

     5.  after exame output, you may wish to  repeat  steps  2  and  3
         again until the image has been arranged to your liking.  This
         may be repeated several times.














                              CHAPTER 3

                       FILES MAKING UP DISM32:



The disassembler consists of  a  set  of  source  files  defining  the
disassembler itself and two support utilities, and a set of data files
used  by  the  disassembler  to  help  direct  it  in  its   automatic
processing:

        DISM32.FOR      - source files for disassembler (just
        DISMINSTR.MAR     compile each by its proper translator
        DISMMEM.MAR       and link only these all together)
        DISMEXTEND.FOR
        DISMMSGPROC.FOR
        DISMCMDPRS.MAR
        DISMMSG.MSG

        DISMISDTBL.INC  - FORTRAN INCLUDE files used by the source
        DISMLINTBL.INC    code, defining local COMMON's
        DISMMISC.INC
        DISMMODTBL.INC
        DISMMSGTBL.INC
        DISMOBJDEF.INC
        DISMSHLTBL.INC
        DISMSYMTBL.INC

        DISM32.EXE      - the actual executable image file

        VMSRTL_V3.EXE   - copy of VMS V3.x VMSRTL.EXE Run-Time Library
                          shareable image, used to disassemble
                          pre-V4.0 images linked against the RTL

        *.OFFSET        - V4.0+ Run-Time Library shareable image
                          procedure entry point argument list
                          description files (currently supplied):
                         *ACLEDTSHR.OFFSET - ACL editor callable interface
                         *ADARTL.OFFSET    - VAX Ada RTL routines
                         *BASRTL.OFFSET    - BASIC support routines
                         *BASRTL2.OFFSET   - BASIC support routines
                         *CMSSHR.OFFSET    - VAX CMS callable interface
                         *COBRTL.OFFSET    - COBAL support routines
                          CONVSHR.OFFSET   - CONV$xxx routines
                          CRFSHR.OFFSET    - cross-reference RTL routines
                          DCXSHR.OFFSET    - DCX$xxx routines

FILES MAKING UP DISM32:                                       Page 3-2


                          DISMNTSHR.OFFSET - SYS$DISMOU system service
                         *DTKSHR.OFFSET    - DTK$xxx routines
                          EDTSHR.OFFSET    - callable EDT
                          FDLSHR.OFFSET    - File Definition Language
                                                routines
                         *FDVSHR.OFFSET    - VAX FMS Form Driver routines
                         *FORRTL.OFFSET    - FORTRAN support routines
                         *FORRTL2.OFFSET   - FORTRAN support routines
                          LBRSHR.OFFSET    - Librarian routines
                          LIBRTL.OFFSET    - general LIB$xxx, OTS$xxx,
                                                STR$xxx routines
                          LIBRTL2.OFFSET   - special LIB$xxx routines
                          MOUNTSHR.OFFSET  - SYS$MOUNT system service
                          MTHRTL.OFFSET    - MTH$xxx routines
                         *NCSSHR.OFFSET    - NCS$xxx routines
                         *PLIRTL.OFFSET    - PL/I support routines
                          PPLRTL.OFFSET    - parallel processing
                                                support routines
                          RPGRTL.OFFSET    - RPG-II support routines
                          SCRSHR.OFFSET    - obsolete screen control routines
                          SECURESHR.OFFSET - security system services
                          SECURESHRP.OFFSET- security system services
                         *SMBSRVSHR.OFFSET - print symbiont support
                         *SMGSHR.OFFSET    - Screen Management Routines
                         *SORTSHR.OFFSET   - callable SORT/MERGE
                          SPM$ETFSHR.OFFSET- VAX SPM Event Trace Facility
                                                support routines
                          UVMTHRTL.OFFSET  - MTH$xxx routines (should never
                                                be referenced explicitly)
                         *VAXCRTL.OFFSET   - VAX C support routines
                        Note that the files preceded by * are not full
                        descriptions of the corresponding files because of
                        lack of documentation of some of the entry points.

        DISM_OFFSET_MAKER.* - unsupported and unfriendly utility for
                                creating .OFFSET files from .SYM files
                                of the shareable images (it links
                                against itself and the RTL only)

        DISM_OFFSET_EDIT.FOR - much friendlier screen-oriented 
        DISMEDMSG.MSG           .OFFSET file editor (works from 
        DISMEDITSYMTBL.INC      old .OFFSET file and/or shareable
        DISMEDITMENU.INC        image file GST to generate updated
                                .OFFSET file; also links against
                                DISMMEM and DISMMSG)

        DISM.COM            - procedure to compile and link all of
                                DISM32 and its utilities

        DISM32.RND          - Runoff source for documentation
        DISM32.DOC          - printable documentation

The disassembler .OFFSET files  supply  descriptions  of  the  calling
arguments  for  the  named  shareable image libraries; this allows the
disassembler  to  more  intelligently  interpret   CALLG   and   CALLS

FILES MAKING UP DISM32:                                       Page 3-3


instruction sequences that call the Run-Time Library.  These files are
binary indexed and are created with one of the DISM_OFFSET_* utilities
listed above.

If you wish to support  a  shareable  image  not  supplied  above,  or
correct  any  errors found in one of the existing files (some of these
could be out of date, because of additional routines or new  arguments
added  to  existing  routines  since  the files were generated), it is
recommended to use the program DISM_OFFSET_EDIT  on  a  suitable  ANSI
video  terminal  (VT100,  etc.).   It  will prompt for the name of the
shareable image to analyze (default  file  name  SYS$SHARE:.EXE;  will
translate  logical names just like the image activator does, which can
cause problems in naming the output  .OFFSET  file)  and  assumes  the
corresponding  old  .OFFSET  file  (if  any) is in the current default
directory.  It will merge the information in the .OFFSET file and  the
shareable  image  GST  and  display  it  in  a scrollable video window
(similar to EDT or an FMS application).  You may then use  the  cursor
keys to move around the different fields; the fields are, from left to
right:

     a)  symbol name (read-only, picked up from GST)

     b)  entry point offset (read-only)

     c)  number of procedure arguments (negative  if  variable,  where
         the  absolute  value  is  the  minimum  number  of  arguments
         required;  positive  if  all  arguments   required;   maximum
         absolute value of 12)

     d)  mnemonics of argument type for the  first  12  arguments  (if
         that many are defined)


The editing keys are:

         cursor keys    - move around the window

         RETURN, ENTER  - move to arg count field on next line down

         PF2, F15 (HELP)- display HELP screen

         PF3, FIND      - find symbol  matching  user-entered  string,
                          using current search direction

         PF4, REMOVE    - delete  the  current  symbol  row  from  the
                          offset file

         KP8            - move one screen length in current direction

         KP4            - set current direction to forward

         KP5            - set current direction to backward

FILES MAKING UP DISM32:                                       Page 3-4


         KP2            - move to next last argument field in  current
                          direction

         KP3            - move  to  next  uninitialized  row  (unknown
                          count,  all  data  types unknown) in current
                          direction

         KP0            - move to next  arg  count  field  in  current
                          direction

         KP-            - erase the current field to default

         ctl-R, ctl-W   - refresh the screen

         SPACE          - move to the next field to the right

         TAB            - move to the next field to the right

         BACKSPACE      - move to the next field to the left

         LINEFEED       - move to the next line in the current  column
                          (skewing left if the next line does not have
                          that many columns)

         0-9, -         - insert a new value into the  argument  count
                          field  (note  that the first character typed
                          will be snatched  to  invoke  field  editing
                          mode,  and  will not actually be inserted in
                          the field)

         M, C           - select the argument type menu; highlight the
                          desired  data type by using the cursor keys,
                          then press SPACE or  RETURN  to  change  the
                          type in the main window

         ctl-Z          - exit and save all changes

         ctl-E          - exit and discard all changes (does  a  check
                          to verify this was really intended)

         ctl-L, F16 (DO)- invoke EDT editor in read-only  screen  mode
                          on   the  .MAR  file  corresponding  to  the
                          .OFFSET file being edited (if  such  a  .MAR
                          file exists)

         PREV SCREEN    - move one screen length backward

         NEXT SCREEN    - move one screen length forward














                              CHAPTER 4

                     DISASSEMBLER ERROR MESSAGES



The following section describes each disassembler error  message  that
can  be reported under normal (and most abnormal) circumstances.  Some
of  the  errors  are  due  to  operator  input;  others  are  due   to
disassembler  limitations  or  errors.   Some  of  the  latter  can be
field-corrected; in such cases, the correction is given  as  the  user
Action  to take.  For the problems that cannot be field-fixed readily,
it is requested that you inform the author of the  problem.   Many  of
the  fixes  appearing in later versions of the disassembler were found
by other users who reported  the  problem  as  found  in  the  earlier
releases.   When  making  a  report to the author, please specify what
image file you were attempting to disassemble  and  what  versions  of
VAX/VMS  and  DISM32  you  were using (if the image file was part of a
layered product or a third-party product, describe  what  product  the
file was a component of).



4.1  DISM32 Error Messages


                                                        ________     1.  %DISM32-I-BADARGLEN, bad argument list length @xxxxxxxx, used
               __           ________         len=^Xxx, actual=^Xxxxxxxxx

             Meaning:  in analyzing an argument list  data  structure,
             the  high bytes of the length longword were not zero; the
             high bytes have been ignored

             Action:  verify if that data structure is supposed to  be
             an argument list by examining the .MAR file


                                                   ________        __     2.  %DISM32-I-BADCLITBL, invalid CLI  block  @xxxxxxxx,  type=xx,
                 __         subtype=xx

             Meaning:  in deciphering a CLI command definition  table,
             certain  entries  were found to be nondecipherable.  Note
             that, due to  not-yet-determined  reasons,  this  happens
             frequently  with  a block type of 01 and a subtype of 01;
             please ignore these messages.

DISASSEMBLER ERROR MESSAGES                                   Page 4-2


             Action:   For  all  occurrences  except  those  described
             above,  ensure  that  manually  inserted  CLI  block type
             symbol table entries are correct.  If such  entries  were
             ALL  inserted correctly, please report the problen to the
             author.  The type/subtype 01/01 error will  be  corrected
             in a future release.


     3.  %DISM32-I-BADDRVRBAS, bad device driver  base;  image  linked
                   ________         with BASE=xxxxxxxx

             Meaning:  a device driver image was not  linked  with  an
             options  file  specifying  BASE=0;  the  disassembler  is
             attempting to compensate for  the  problem  but  may  not
             succeed

             Action:   examine  the  .MAR  file  after  completion  to
             determine  if  the  disassembler  was  able  to  properly
             compensate and if this image really is a device driver or
             not


     4.  %DISM32-F-BADDRVVER,  unrecognizable  driver  version:    V4-
              __          __         vers=nn, V5 vers=nn

             Meaning:  DISM32 interpreted the image file  as  being  a
             device  driver,  but  could  not find a valid VMS version
             number in DPT$W_VERSION (either the version 4-and-down or
             the  version  5 location) to tell it how to interpret the
             data structures

             Action:  analyze the image file to verify that  it  is  a
             valid  device  driver  image  that  is not corrupted, and
             correct any damage to the .EXE file; alternatively,  stop
             using   the   /DRIVER  qualifier  to  try  to  force  the
             disassembler to treat the  image  as  a  standard  device
             driver.


                                                     __     5.  %DISM32-E-BADSHRIMG,  FORTRAN  I/O  error  #nn   on   opening
                          ______         shareable image 'xxxxxx'

             Meaning:   an  error  occurred  when   the   disassembler
             attempted  to open a shareable image file that was linked
             to the image being disassembled

             Action:  correct  the  reason  (specified  as  a  FORTRAN
             IOSTAT code) why the file could not be opened


                                                     __     6.  %DISM32-E-BADSYSSTB,  FORTRAN  I/O  error  #nn   on   opening
         SYS$SYSTEM:SYS.STB

DISASSEMBLER ERROR MESSAGES                                   Page 4-3


             Meaning:   an  error  occurred  when   the   disassembler
             attempted to open the system symbol table file

             Action:  correct  the  reason  (specified  as  a  FORTRAN
             IOSTAT code) why the file could not be opened


     7.  %DISM32-F-BADTBLSIZ, ISD table built bigger than Psect  table
         - disassembly aborted

             Meaning:  Someone enlarged the ISD table  size  (per  the
             directions   for  the  %DISM32-F-ISDTBLOVF  message)  but
             didn't enlarge the PSECT table size correspondingly.

             Action:  edit the file  DISMISDTBL.INC  to  increase  the
             value  of  the parameter PSECT_TBL_SIZE to be larger than
             ISD_TBL_SIZE, then recompile and relink the disassembler.


                                                 __     8.  %DISM32-E-BADUSRSFL, FORTRAN I/O error #nn  on  opening  user
                            ______         symbol table file 'xxxxxx'

             Meaning:   an  error  occurred  when   the   disassembler
             attempted to open the .SYM file (other than that the file
             does not exist)

             Action:  correct  the  reason  (specified  as  a  FORTRAN
             IOSTAT code) why the file could not be opened


     9.  %DISM32-E-COMPATIMG,  compatibility  mode  (PDP-11)  image  -
         cannot be disassembled

             Meaning:  the executable image file you are attempting to
             disassemble is an RSX-11 image created by TKB, and cannot
             be handled by this native mode disassembler

             Action:  give up trying to analyze the  image  with  this
             disassembler, and find a PDP-11/RSX-11 disassembler to do
             it instead


    10.  %DISM32-F-CORDTSTRUC, internal disassembler  data  structures
         corrupted

             Meaning:  somehow, the master instruction  format  tables
             defined  in  the file DISMINSTR.MAR have become corrupted
             and no longer make sense

             Action:  try running  DISM32  again  with  process  image
             dumping  enabled,  and  then  send  a  bug  report to the
             author, including the process crash dump  file  (this  is
             extremely  serious, and implies severe errors in DISM32's
             internal operation).

DISASSEMBLER ERROR MESSAGES                                   Page 4-4


                                                              ________    11.  %DISM32-I-CREOPTFIL,  image  requires  .OPT  file;   filespec
         created

             Meaning:   the  disassembler  detected  image  attributes
             which  can  only be specified with a linker options file;
             the options file is being created

             Action:  none.  This is merely informational in case  you
             wish to rebuild this particular image.


                                               ___    12.  %DISM32-I-DIFINTNAM, executable file 'aaa' has internal image
               ___         name 'bbb'

             Meaning:  the image name embedded  in  the  image  header
             does not match the executable image file name

             Action:  none.  this merely  informs  you  that  somebody
             renamed this executable image after it was linked


                                                __    13.  %DISM32-F-FORTIORD, FORTRAN I/O error #nn  on  reading  input
         file

             Meaning:  an error occurred upon attempting to  read  the
             input  .EXE  file  (the  error number is a FORTRAN IOSTAT
             code)

             Action:  look up the IOSTAT  code  and  correct  whatever
             problem was causing read errors


                                       _____        ___    ___     ___    14.  %DISM32-I-IDCREC, obj IDC rec:-aaa- entity=bbb id=ccc obj=ddd

             Meaning:   an  entity-ident-consistency-check  sub-record
             was found in a shareable image's GST

             Action:  none


                                                  _____            ___    15.  %DISM32-I-IDCRECB,    obj    IDC     rec:-aaa-     entity=bbb
               ________        ___     ___         id=%X'xxxxxxxx' match=nnn obj=ddd

             Meaning:   an  entity-ident-consistency-check  sub-record
             was found in a shareable image's GST

             Action:  none


                                            ______    16.  %DISM32-E-INCITMLST, inconsistent $xxxxxx item list entry  at
         ________        ________         xxxxxxxx, value=xxxxxxxx

             Meaning:  in  interpreting  a  data  structure  that  the
             disassembler  was  told  was an item list for some system
             service, it found an item code undefined  for  that  item

DISASSEMBLER ERROR MESSAGES                                   Page 4-5


             list type in the list

             Action:  examine the  .MAR  file  to  see  if  that  data
             structure  is  supposed  to be an item list of that type,
             and correct the .SYM file if not


    17.  %DISM32-E-INCTPARSE, inconsistent LIB$TPARSE keyword index to
         text area
                             ________       ________                       index=xxxxxxxx, text=xxxxxxxx

             Meaning:  a  LIB$TPARSE  keyword  text  pointer  did  not
             specify   a  LIB$TPARSE  keyword  index  pointer  as  its
             extended value.

             Action:  if the symbol table file  was  edited  manually,
             check the edits applied.  if not, please report the error
             to the author.  Note that keyword text symbols should not
             be  inserted into the disassembler symbol table manually;
             they are intended to be a reserved internal  DISM32  data
             type.


    18.  %DISM32-I-INDCALJSB, indirect CALLx, JSB or  JMP  instruction
            ________         at xxxxxxxx

             Meaning:  the disassembler found a CALLS, CALLG, JSB,  or
             JMP  instruction  where  the  procedure  operand  was not
             addressed   by   absolute,   PC-relative,   or    general
             addressing,  and  therefore  the  disassembler  could not
             determine  what  procedure/subroutine  was  being  called
             during pass 1

             Action:  examine  the  .MAR  file  after  disassembly  is
             complete  and  determine  how the procedure or subroutine
             address is calculated, and insert the manually calculated
             procedure/subroutine address into the .SYM file to permit
             proper  disassembly  of  the  procedure/subroutine  being
             called


    19.  %DISM32-E-INVADRMOD,  invalid  addressing  mode  at  location
         ________         xxxxxxxx - operand ignored

             Meaning:  an  operand  of  an  instruction  was  invalid,
             probably   due   to   disassembling   data   as  code  or
             disassembling starting at the wrong address

             Action:  edit the .SYM file to correct the problem


                                                                   ___    20.  %DISM32-E-INVBASARG, invalid BASIC  argument  block;  len=nnn
            ________         LC=xxxxxxxx

DISASSEMBLER ERROR MESSAGES                                   Page 4-6


             Meaning:  a symbol was  marked  as  the  BASIC  procedure
             argument  block (not related to general procedure calling
             arguments), but the corresponding  data  structure  could
             not be deciphered.

             Action:  if the symbol table file  was  edited  manually,
             check the edits applied.  if not, please report the error
             to the author.


                                                       ________    21.  %DISM32-F-INVBOFSET, invalid  offset  (loc.   xxxxxxxx)  into
         disk sector buffer, null value returned

             Meaning:  the disassembler's  pseudo-"pagefault"  handler
             (which  calculates  which  block  of  the  image  file  a
             particular virtual address maps into) was unable to  find
             the  contents of the requested location, due to either an
             error in the image header or (more likely) a bug  in  the
             disassembler's  image  header  or  special  image section
             handling.   Note  that   this   exception   occurs   VERY
             frequently  inside DISM32 (a warning if you want to debug
             DISM32 yourself); it should only reach DCL level  if  the
             internal exception handlers can't deal with it.

             Action:  please report the error  to  the  author.   Note
             that  this  problem  is common for image files with large
             embedded message sections if you are using a  version  of
             DISM32  before V4.5; get a more recent version to fix the
             problem.


    22.  %DISM32-I-INVCRFCTL, invalid  cross-reference  control  table
          ________         @xxxxxxxx

             Meaning:  the disassembler detected  invalid  data  in  a
             data  structure purported to be a cross-reference routine
             control  table   (run-time   initted   fields   non-zero,
             out-of-range field values, etc.)

             Action:  verify that the specified symbol is supposed  to
             be  typed  as  a cross-reference control table; if it is,
             find why the image has corrupted the table, or report the
             problem to the author


    23.  %DISM32-I-INVCRFFLD, invalid cross-reference field definition
          ________         @xxxxxxxx

             Meaning:  the disassembler detected  invalid  data  in  a
             data  structure purported to be a cross-reference routine
             field definition macro (pointed  from  a  cross-reference
             routine control table)

DISASSEMBLER ERROR MESSAGES                                   Page 4-7


             Action:  verify that the specified symbol is supposed  to
             be  typed as a cross-reference field definition macro; if
             it is, find why the image has  corrupted  the  macro,  or
             report the problem to the author


    24.  %DISM32-E-INVIMMTYP,  variable-length   immediate   data   in
                           ________         instruction at LC=xxxxxxxx

             Meaning:  the disassembler attempted  to  disassemble  an
             instruction   specifying   short   literal  or  immediate
             addressing of  a  variable  length  data  type  (such  as
             character  string  or  packed  decimal),  probably due to
             starting disassembly at the wrong address

             Action:  edit the .SYM file to cause disassembly of  this
             section of code to start at the correct address


    25.  %DISM32-F-INVIMMTP2,  variable-length   immediate   data   in
                           ________         instruction at LC=xxxxxxxx (pass 2)

             Meaning:  on pass 2, the disassembler apparently found an
             instruction   specifying   short   literal  or  immediate
             addressing of an operand of variable length,  such  as  a
             character string or packed decimal string

             Action:  edit the .SYM file to not have the  disassembler
             begin  disassembly  in the middle of an instruction (such
             as specified for the pass 1 version of this error)


    26.  %DISM32-E-INVINITAB,  invalid  driver  initialization   table
                  ________         __         entry at xxxxxxxx - block=xx

             Meaning:  the disassembler was attempting to interpret  a
             DPT_STORE macro's code and the code was inconsistent

             Action:  verify that the code should be interpreted as  a
             DPT_STORE  macro  and  correct  the  .SYM file to fix the
             problem


                                                             ________    27.  %DISM32-E-INVLOAVEC, invalid  LOAVEC  header,  addr=xxxxxxxx,
                 __         subtype=xx

             Meaning:  in disassembling a loadable system  image,  the
             LOAVEC header was inconsistent.

             Action:  If the symbol table file  was  edited  manually,
             check  the  edits applied.  if not, verify that the image
             actually is an old-style loadable system  image  such  as
             SCSLOA,  CLUSTRLOA,  etc.   If  the  image  is  a  proper
             loadable system image, please report  the  error  to  the
             author.

DISASSEMBLER ERROR MESSAGES                                   Page 4-8


                                                   __    28.  %DISM32-I-INVOPCODE,  undefined  opcode  'xx'   at   location
         ________         xxxxxxxx

             Meaning:  occurs usually during pass 1  while  attempting
             to  build  a  valid  symbol  table, or either pass when a
             device driver  (since  the  IOC$WFIKPCH  and  IOC$WFIRLCH
             subroutines   have  a  word  of  data  rather  than  code
             immediately after the JSB and  the  disassembler  expects
             code);  this  may  also occur if a CASEB, CASEW, or CASEL
             instruction was actually coded erroneously in the  image,
             where  the disassembler interprets instructions following
             the CASE table as being more offset words or instructions
             (depending on whether the table length is too long or too
             short)

             Action:  ignore, but check the output .MAR  file  at  the
             specified  location  after  disassembly  is  complete  to
             verify that output code is valid and sensible,  and/or  a
             CASEx instruction is coded correctly or incorrectly


    29.  %DISM32-W-INVSTATBL, invalid  state  table  keyword  pointer,
               ________    ________      ________ ____         state@xxxxxxxx, >@xxxxxxxx, typ=xxxxxxxx(nnnn)

             Meaning:  a symbol table  entry  of  type  "TPARSE  state
             table  start" or "TPARSE state table entry" was specified
             without a valid extended value specifying the address  of
             the associated keyword table

             Action:  edit the .SYM file to fill in the missing value


    30.  %DISM32-F-ISDTBLOVF,  overflow  of  disassembler  ISD  table,
         rebuild disassembler

             Meaning:  the image being  disassembled  has  more  image
             sections  than  the disassembler has space for in its ISD
             table

             Action:  edit the file  DISMISDTBL.INC  to  increase  the
             value of the parameter ISD_TBL_SIZE to be large enough to
             hold all the  ISD's  in  the  desired  target  image  (or
             larger),  then recompile and relink the disassembler.  If
             you do this, make sure that the value  of  PSECT_TBL_SIZE
             remains    larger   than   the   size   of   ISD_TBL_SIZE
             (PSECT_TBL_SIZE  <  ISD_TBL_SIZE  is  a  data   structure
             inconsistency  inside  the disassembler and will cause it
             to abort).


    31.  %DISM32-F-LINTBLOVF, overflow of line number  table;  rebuild
         disassembler

DISASSEMBLER ERROR MESSAGES                                   Page 4-9


             Meaning:  the image  being  disassembled  has  more  line
             numbers  than  the disassembler has space for in its line
             number table

             Action:  edit the file  DISMLINTBL.INC  to  increase  the
             value of the parameter LIN_TBL_SIZE to be large enough to
             hold all the line numbers in the desired target image (or
             larger), then recompile and relink the disassembler


    32.  %DISM32-F-MODTBLOVF,  overflow  of  module   table;   rebuild
         disassembler

             Meaning:  the image being disassembled has  more  modules
             than the disassembler has space for in its module table

             Action:  edit the file  DISMMODTBL.INC  to  increase  the
             value of the parameter MOD_TBL_SIZE to be large enough to
             hold all the modules in  the  desired  target  image  (or
             larger), then recompile and relink the disassembler


    33.  %DISM32-F-MSGTBLOVF,  overflow  of  message  facility  table;
         rebuild disassembler

             Meaning:  the image being disassembled has  more  message
             facility   numbers  in  its  message  sections  than  the
             disassembler has space for in its message section table

             Action:  edit the file  DISMMSGTBL.INC  to  increase  the
             value  of  the parameter ICP_NUMMSGFAC to be large enough
             to hold all the modules in the desired target  image  (or
             larger), then recompile and relink the disassembler


    34.  %DISM32-I-NOIMGHDR, image file has no image header

             Meaning:  the image header could not be deciphered at all

             Action:  this message will be followed by the  query  "Is
             this  a  system  image  (Y/N) ?".  answer NO to abort the
             disassembler run, or YES to tell  the  disassembler  that
             this   is   an   image   linked   /SYSTEM/NOHEADER;   the
             disassembler will then prompt for the base virtual memory
             address  for  the  image  so  it  can build a dummy image
             header for its own internal use


    35.  %DISM32-I-NONSTDIMG, non-standard native mode image  of  type
          ___         'ccc'

             Meaning:  the  image  being  disassembled  looks  like  a
             native-mode  image,  but  has  a  funny image type in the
             header

DISASSEMBLER ERROR MESSAGES                                  Page 4-10


             Action:  ignore,  but  verify  that  the  image  file  is
             supposed  to  have  the  strange attribute; note that the
             disassembler will create a linker options file  with  the
             IMAGE_TYPE= option corresponding to this


    36.  %DISM32-E-NOSUCHSYM, no symbol found in pass 2  corresponding
                  ________         to value xxxxxxxx

             Meaning:  during pass 2, the disassembler could not  find
             a  symbol  table entry matching an item referenced in the
             code being disassembled

             Action:  if the symbol table file  was  edited  manually,
             check the edits applied.  if not, please report the error
             to the author.


                                                __    37.  %DISM32-W-OBJSYMERR, errors to  level  nn  were  reported  in
         symbol table information

             Meaning:  the shareable  image  being  analyzed  reported
             compile-time or link-time errors in its GST

             Action:  find why there are errors in the shareable image


                                                             ________    38.  %DISM32-I-OBSDESCR, obsolete descriptor type found @xxxxxxxx,
               __         class=xx

             Meaning:  in processing a descriptor-type data structure,
             the  disassembler  discovered  the  descriptor  class  is
             obsolete (per the 1981 VAX Architecture Handbook)

             Action:  examine  the  image  to  verify  that  the  data
             structure   is  supposed  to  be  a  descriptor;  if  so,
             determine why the specified class of obsolete  descriptor
             is being used


    39.  %DISM32-F-OFSFILOVF, overflow of shareable image offset  file
         table; rebuild disassembler

             Meaning:  the shareable image table has overflowed;  more
             shareable images are referenced by the .EXE file than the
             disassembler can handle

             Action:  this is a difficult fix, as the shareable  image
             arrays  have  not  been  parameterized  yet;  however, by
             editing the size of  the  arrays  in  DISMSHLTBL.INC  and
             finding   where  the  array  indexes  are  calculated  in
             DISM32.FOR,  it  might  be  possible  to  field-fix   the
             disassembler


DISASSEMBLER ERROR MESSAGES                                  Page 4-11


    40.  %DISM32-I-P0IMAGE, image created with /P0IMAGE

             Meaning:  the disassembler is  processing  an  executable
             image linked with /P0IMAGE

             Action:  none.  This is merely informational in case  you
             wish to rebuild this particular image.


    41.  %DISM32-I-SHRIMAGE,  image   is   shareable   (created   with
         /SHAREABLE)

             Meaning:  the  disassembler  is  processing  a  shareable
             library image (rather than an executable or system image)

             Action:   none  (but  expect  .GST  and  .OPT  files  for
             auxiliary output)


    42.  %DISM32-F-STKOVF,  auxiliary  stack  overflow  -  disassembly
         aborted

             Meaning:  there were more nested levels  of  DST$K_RTNBGN
             records  in  the  DST  of  the  specified  image than the
             disassembler could handle

             Action:  Try running the problem-causing image file under
             the  debugger  or  running ANALYZE/IMAGE on it.  If these
             don't report an error in the image's DST, please  send  a
             bug report to the author.


    43.  %DISM32-E-STKUDF, auxiliary stack underflow -  residual  data
         discarded

             Meaning:  in analyzing  the  Debug  Symbol  Table  of  an
             image,  there  were  more  DST$K_RTNEND  directives  than
             DST$K_RTNBGN for a module

             Action:  run ANALYZE/IMAGE on the image to see where  and
             why the DST is corrupted


    44.  %DISM32-F-SYMTBLOVF,  overflow  of  symbol   table;   rebuild
         disassembler

             Meaning:  the image being disassembled has  more  symbols
             than the disassembler has space for in its symbol table

             Action:  edit the file  DISMSYMTBL.INC  to  increase  the
             value of the parameter SYM_TBL_SIZE to be large enough to
             hold all the symbols in  the  desired  target  image  (or
             larger), then recompile and relink the disassembler


DISASSEMBLER ERROR MESSAGES                                  Page 4-12


                                                          ________    45.  %DISM32-I-SYSIMAGE, image created with /SYSTEM=%Xxxxxxxxx

             Meaning:  the disassembler is processing an image  linked
                       ________             /SYSTEM=%Xxxxxxxxx  and  /HEADER,  rather than a standard
             executable image, a  shareable  image,  or  a  headerless
             system image

             Action:  none


    46.  %DISM32-I-TOOMANYTYP,    too    many    data    types     for
                  ________         symbol=^Xxxxxxxxx
                                        ________      ___                      old        type=^Xxxxxxxxx,attr=nnn;         new
                ________      ___         type=^Xxxxxxxxx,attr=nnn

             Meaning:  the disassembler attempted to add a new type to
             an  already-existing symbol table entry, but the new type
             does not logically fit with the old data types;  the  new
             typing  was  not  added.  Incompatible types are all code
             types versus any extended data type

             Action:  examine the .SYM file to determine  why  symbols
             are  being  defined  as  both executable code and complex
             data  types,  correct  the  problem,   and   re-run   the
             disassembler


    47.  %DISM32-F-UNKIMGTYP, image type unknown - output file deleted

             Meaning:  the disassembler could not interpret the  image
             header and was told that the image is not a system image

             Action:  verify that the specified input file is actually
             an image file


    48.  %DISM32-W-UNKOBJREC,   unknown   Object    Language    record
               __         __         (type=xx,subtype=yy) - record ignored

             Meaning:  an Object Language record in a shareable  image
             GST  could  not  be  interpreted  because the type is not
             known  to  the  disassembler,  possibly  because  an  old
             version  of  the  disassembler  is  being used with a new
             version of VMS

             Action:  this will not affect your output (we hope),  but
             please  report  the  error  to  the  author if you have a
             current version of DISM32 according to the release  notes
             (V4.3  and  up  of DISM32 should work with VMS V5.x, V4.5
             and up support VMS V5.x system services)


                                                           __      __    49.  %DISM32-E-UNRECVEC, unrecognized vector type, ISD nn, VBN nn,
            ________        ________         LC=xxxxxxxx, typ=^Xxxxxxxxx

DISASSEMBLER ERROR MESSAGES                                  Page 4-13


             Meaning:  n image section with the VECTOR  attribute  did
             not  contain  a  vector  prologue  looking  like either a
             message vector or a privileged image change mode vector

             Action:  find why the image  section  in  the  executable
             image  file  is  marked  as  VECTOR type when it does not
             contain a valid vector


    50.  %DISM32-W-UNSPDATYP,   unsupported   extended   data    type;
             ________      ________           ____         val=xxxxxxxx, typ=xxxxxxxx, ext attr=nnnn

             Meaning:  an entry was found in the  disassembler  symbol
             table  specified  as being an extended data type, but the
             extended type number is not a recognized type

             Action:  examine that entry in the .SYM file to make sure
             it  makes  sense, or correct manually inserted changes to
             the .SYM file; also make sure you are not  using  a  .SYM
             file created with a newer version of DISM32 with an older
             version


    51.  %DISM32-I-UNTRMSTAT,  possible  unterminated   state   table,
               ________         state@xxxxxxxx

             Meaning:   the  disassembler   detected   an   apparently
             erroneous  transition  in a LIB$TPARSE state table, where
             repeated occurrences of $TRAN 0  appeared;  this  usually
             implies  that  the  last  state of a table didn't have an
             explicit transition state for  each  transition,  so  the
             disassembler   continued  on  into  unused  (and  zeroed)
             storage

             Action:  read the generated .MAR file to confirm that  an
             oddly  constructed  state  table does exist; if the state
             table ends normally  (all  last  state  transitions  have
             explicit  transition  states),  report the problem to the
             author


    52.  %DISM32-I-UNTRMSTAT2,     unterminated      state      table,
               ________         state@xxxxxxxx (pass 2)

             Meaning:   the  disassembler   detected   an   apparently
             erroneous  transition  in a LIB$TPARSE state table, where
             repeated occurrences of $TRAN 0  appeared;  this  usually
             implies  that  the  last  state of a table didn't have an
             explicit transition state for  each  transition,  so  the
             disassembler   continued  on  into  unused  (and  zeroed)
             storage.  This version of the message should  only  occur
             if the symbol table analysis pass processing was not able
             to come up with a work-around (previous error message).

DISASSEMBLER ERROR MESSAGES                                  Page 4-14


             Action:  read the generated .MAR file to confirm that  an
             oddly  constructed  state  table does exist; if the state
             table ends normally  (all  last  state  transitions  have
             explicit  transition  states),  report the problem to the
             author


    53.  %DISM32-I-WRNGDATYP,  invalid   data   type   in   descriptor
          ________        __       __         @xxxxxxxx, class=xx, type=xx

             Meaning:  in processing a descriptor-type data structure,
             the  disassembler discovered the descriptor data type was
             undefined

             Action:  examine the image to determine why the specified
             unknown data type is being used





4.2  DISM_OFFSET_EDIT Error Messages


     1.  %DISMED-S-EXIT, nnnn records written to filespec

             Meaning:  DISM_OFFSET_EDIT successfully exited and  wrote
             the  specified  number  of  .OFFSET  file  records to the
             specified output file

             Action:  none


                                                    _____  ___________     2.  %DISMED-I-INVARGTYP, bad type for  offset  xxxxx  xyz$aaaaaaa
             _      ________         arg#n type=xxxxxxxx

             Meaning:  somehow, a corrupted  entry  got  into  an  old
             .OFFSET file, and the editor does not know how to display
             it

             Action:  get a valid copy of the .OFFSET file


                                    _____     3.  %DISMED-I-MISOFS,  offset  xxxxx  missing  from   old   file;
                  ____________         inserted xyz$aaaaaaaa

             Meaning:  in scanning the shareable image  Global  Symbol
             Table,  DISM_OFFSET_EDIT  found  a  procedure entry point
             that did not exist in  the  old  .OFFSET  file;  the  new
             symbol  has  been  added  to  the editing buffer with all
             defaults for argument typing.

             Action:  none


DISASSEMBLER ERROR MESSAGES                                  Page 4-15


                                              _____     4.  %DISMED-I-OBSOFS,  obsolete  offset  xxxxx  not  declared  in
         shareable image

             Meaning:  an entry was found in an old .OFFSET file which
             had no corresponding entry in the shareable image GST.

             Action:  verify that the old .OFFSET file was valid  (you
             may  wish  to  create  a  new  .OFFSET file from scratch,
             rather than updating an old one; on the other hand,  such
             entries  may  be  because  DEC moved the entry to another
             shareable image and left only an undeclared stub for  old
             executable images to vector through [example:  VMSRTL.EXE
             under VMS 4.0 and up]).





4.3  VMS Error Messages Reported by Disassembler


     1.  %FOR-F-OPEFAI, open failure

             Meaning:  generally means that  the  input  filename  was
             specified incorrectly or one of the output files couldn't
             be opened due to  directory  protection  or  insufficient
             disk space

             Action:   fix  the  input  filespec  spelling,  get  more
             available  disk space, or correct the protection problem,
             based on which file FORTRAN is complaining about and what
             the associated system message is


     2.  %SYSTEM-F-BADIMGHDR, bad image header

             Meaning:  (DISM32) the user answered "NO"  to  the  query
             "Is   this   a   system   image   (Y/N)   ?"   after  the
             %DISM32-I-NOIMGHDR message.

             (DISM_OFFSET_EDIT) the specified  file  did  not  have  a
             decipherable image header.

             Action:  (DISM32) none.

             (DISM_OFFSET_EDIT)  check  that  the  correct  file   was
             specified to the editor.


     3.  %SYSTEM-F-NOSHRIMG, privileged shareable  image  cannot  have
         outbound calls

             Meaning:  DISM_OFFSET_EDIT found that the specified image
             existed,  but it was either not a shareable image, or the
             image had no Global Symbol Table.

DISASSEMBLER ERROR MESSAGES                                  Page 4-16


             Action:  verify that the correct image was specified.


     4.  %SYSTEM-F-NOSUCHFILE, no such file

             Meaning:  DISM_OFFSET_EDIT could not find  the  specified
             shareable image file.

             Action:  check the spelling of the shareable  image  name
             entered to verify that the named image actually exists.















                              APPENDIX A

                           REVISION HISTORY



A.1  Enhancements for V4.6


     1)  add logic to decipher embedded CLI  command  tables  (concept
         swiped  from  whatever  fine  gentleman  wrote the DECUS VERB
         utility on the Spring '90 tape)




A.2  Enhancements for V4.5-2A


     1)  change  FORTRAN   OPEN   statements   to   prevent   unwanted
         translations  of  logical names (the system-wide logical name
         MTHRTL, for example)

     2)  force disassembly of a device driver FDT to be limited to the
         length specified in the DDT




A.3  Enhancements for V4.5-2

Note that some of these fixes were due to the reports from the  people
at Baioni SPA, Italy.

     1)  change .MSG section processing to produce message definitions
         in  standard  format  [except  for leading semicolon] (former
         format used continuation lines  which  the  MESSAGE  compiler
         does not accept)

     2)  allow for 5-digit line numbers

     3)  allow for larger VMS V5 global section and P-sect  names  (up
         to 43 characters)

REVISION HISTORY                                              Page A-2


     4)  clean up /OPTIONS file writing (eliminating  excess  COLLECT=
         entries);   produce  additional  /OPTIONS  file  records  (as
         needed) for undocumented linker options

     5)  fix format of exit control  blocks  (formerly  had  procedure
         referenced by a .LONG pseudo-op instead of .ADDRESS)

     6)  fix .BLKx compression at end of image sections

     7)  add new peripheral adapters for I/O drivers

     8)  correct sizing of FDT element

     9)  add new I/O function codes (READCHUNK, WRITECHUNK)

    10)  look  up  bugcheck  code   mnemonic   names   directly   from
         SYS$SYSTEM:SYS.MAP

    11)  handle MOVZxL/CVTxL x,-(SP)  instructions  for  stack  unwind
         (prevents  premature  termination  of stack scan and improper
         parsing of $QIO  and  $GETDVI  calls),  handling  almost  all
         variations of first operand addressing

    12)  recognize  additional  reserved-to-DIGITAL  subroutine  entry
         vectors   in   driver   CRB's  1st  VEC  block  (VEC$L_START,
         VEC$L_UNITDISC) (VMS V5+ drivers only)

    13)  properly decode LOAVEC image initialization lists

    14)  report device type info for  drivers  to  terminal  in  trace
         information   (adapter,   device  class,  device  type,  both
         numerically     and     symbolically     looked     up     in
         SYS$LIBRARY:STARLET.MLB's $DCDEF module)

    15)  allow potential non-fatality of table overflows on module and
         line  number  tables  (still defaultly fatal, but severity of
         xxxTBLOVF messages could be lowered for module table and line
         number  table, with loss of some unessential symbol data; the
         ISD table and main symbol table must  be  able  to  hold  all
         entries)

    16)  fix DST code for DST$K_MODBEG where module table size was not
         checked (a table overflow could occur and not be detected)

    17)  verify that ISD table is not larger than PSECT table

    18)  add  new  extended  data   types   for   item   list   XAB's,
         cross-reference library routine macros, bound-procedure-value
         and bound-label-value structures,  and  generic  item  lists;
         finish  filling  in  code to process BASIC file options block
         and PL/I file control block

    19)  add additional RMS block fields

REVISION HISTORY                                              Page A-3


    20)  report potential "typos" in  LIB$TPARSE  state  tables  which
         might cause erroneous "run-ons" in symbol table analysis

    21)  correct and update required  macro  processing  for  extended
         data types

    22)  clean up symbol naming for fields in exit control blocks

    23)  improve DISM_OFFSET_EDIT  to  allow  searching  for  specific
         named  entry  points and invoking the EDT editor in read-only
         mode on the .MAR file corresponding to the .OFFSET file being
         edited




A.4  Enhancements for V4.5-1


     1)  support the V5.x image header system version array (displayed
         as comments in the disassembler output prologue)

     2)  fix .ASCID processing errors

     3)  support automatic processing  of  old-style  loadable  system
         images  [SCSLOA, etc.] using the same mechanism as for device
         drivers

     4)  support all defined types of descriptors as  a  new  extended
         data type

     5)  support executive image extended linker /OPTIONS  file  stuff
         (such as COLLECT= optionally with /ATTRIBUTES qualifier)

     6)  clean up handling of  symbols  in  undefined  virtual  memory
         areas

     7)  add new I/O function code names, add  intelligence  based  on
         UCB$B_DEVCLASS  value to select which of multiple names for a
         single I/O function code  should  be  used  within  a  driver
         disassembly

     8)  correct backwards references in complex data structures

     9)  add automatic recognition  of  exit  handlers  and  exception
         handlers  (add  exit  control  blocks  as a new extended data
         type; look for MOVAB and MOVAL instructions with (FP) as  the
         destination,  and retype the source argument [if PC-relative]
         to PROCEDURE type)

    10)  created user-friendly .OFFSET file editor


REVISION HISTORY                                              Page A-4


A.5  Enhancements for V4.5

Note:  several of these fixes are courtesy of or suggested by  Gerhard
Thallinger and other folks whose names, alas, I have misplaced.

     1)  support additional adapter types in device  drivers  (for  BI
         device  drivers), fix incorrectly-specified length values for
         DPT's, generate symbolic offsets for driver DPT_STORE  macros
         (where  the corresponding data structure modules can be found
         in SYS$LIBRARY:LIB.MLB), fix assorted typos in disassembly of
         DPT  and  DDT,  decode  terminal class and port driver vector
         tables

     2)  correct some bugs in XAB processing

     3)  add new V5.x  system  services  (including  undocumented  and
         unsupported services that are not yet active)

     4)  compress runs of identical .BYTE, .WORD, .LONG,  or  .ADDRESS
         pseudo-ops with .REPEAT and .BLKx pseudo-ops

     5)  augment message section processing to support  sections  with
         more   than   one   facility  and/or  more  than  64  message
         definitions

     6)  allow optional recognition of long byte arrays  as  character
         strings (the /STRING qualifier)

     7)  fix up BASIC arglist processing to extract BASIC line  number
         labels  and  convert  them to symbol names on the appropriate
         symbol table entries

     8)  allow  multiple  independent  LIB$TPARSE  state  and  keyword
         tables  in  the same image by accounting for the separateness
         of keyword indexes and actual text strings




A.6  Enhancements for V4.4

Note:  several of these fixes are courtesy of or  suggested  by  David
Deley.

     1)  break   extremely   long   .ASCID   strings   into   multiple
         continuation   lines   in   the   .MAR  file,  and  represent
         unprintable  characters  as  hexadecimal  numeric   constants
         embedded in the strings

     2)  if the .EXE file being disassembled was  linked  against  the
         system  symbol  table  file  SYS$SYSTEM:SYS.STB,  add a .LINK
         pseudo-op to the .MAR file to indicate the reference

REVISION HISTORY                                              Page A-5


     3)  handle device drivers that were not linked /NOTRACE (or  V5.x
         drivers   with   initialization  entry  points)  by  properly
         ignoring or working around defined transfer vectors

     4)  generate a linker /OPTIONS file for the image to hold
                        BASE=%Xxxxxxxxx
                        GSMATCH=x,y,z
                        IOSEGMENT=n[,NOP0BUF]
                        NAME=aaaa
                        STACK=n
                        UNIVERSAL=aaaa
         directives if such directives would be  needed  to  re-create
         the image

     5)  add certain missing H_floating  instruction  opcodes  to  the
         disassembler core instruction tables

     6)  handle  the  case  where  a  device  driver's  DDT  does  not
         immediately     follow    the    DPT    initialization    and
         reinitialization  table  (as  in  TTDRIVER,  for  some  weird
         reason)

     7)  use  the   CALLS   stack-windback   data   to   correct   the
         %DISM32-I-INDCALJSB  message  to  report  the  address of the
         instruction opcode,  rather  than  of  the  target  routine's
         operand

     8)  add  command  qualifiers  for  forcing  the  disassembler  to
         perform alternate disassembly operations




A.7  Enhancements for V4.3


     1)  handle nested routine definitions in modules listed in DST

     2)  analyze argument lists pushed on stack for CALLS instructions
         for  some  cases  of  calls  to  system services and Run-Time
         Library functions

     3)  optimize use of symbol table in pass 1

     4)  add new VMS V5 symbolic  names  for  I/O  function  code  and
         system service itemlist definitions

     5)  support new Object Language features for VMS V5.0

     6)  support programs that do nasty things like  put  RMS  control
         blocks in demand-zero image sections

     7)  support VMS V5.0 device drivers

REVISION HISTORY                                              Page A-6


     8)  unsupported utility (very user-UNfriendly) to  build  .OFFSET
         files  for  describing  shareable image procedure entry point
         argument lists




A.8  Enhancements for V4.2


     1)  recognition of CALLG argument lists,  and  interpretation  of
         same  for  system service calls (only when both argument list
         and  procedure  address  are   specified   as   absolute   or
         PC-relative).

     2)  support of non-standard device driver linking

     3)  supports more types of GSD records in an image Global  Symbol
         Table.

     4)  completed support of all currently known RMS control blocks




A.9  Enhancements for V4.1


     1)  recognition and analysis of BASIC procedure argument lists to
         supply  procedure labels, line numbers, and a more meaningful
         interpretation  of  the  definition  list   data   structures
         themselves  (see  the  VMS  V3.x  Language Support Procedures
         Reference Manual, section  on  BASIC,  for  more  information
         about BASIC procedure prologues).

     2)  recognition of shareable image transfer vectors  as  transfer
         vectors  instead  of the original procedure entry points, and
         insertion  of  the  .TRANSFER  and  .MASK   pseudo-ops   with
         appropriate  moving  of  labels  from  the image's GST to the
         actual procedures as well as the .TRANSFER/.MASK pseudo-ops.

     3)  default label  naming  conventions  for  RMS  control  blocks
         changed  to be of the form blktyp_xxxxxxxx, where xxxxxxxx is
         the hexadecimal address and blktyp is the type of  RMS  block
         (FAB,  RAB,  XABDAT,  etc.)  instead  of just RMS_xxxxxxxx as
         before.

     4)  fix assorted minor typos.

     5)  recognize in certain limited cases when a symbolic  condition
         code  defined  by  a resident message vector section is being
         referenced by code, and filling  in  the  symbolic  condition
         code name automatically when recognized.


REVISION HISTORY                                              Page A-7


If you have any suggestions, bug reports, or comments, please  let  me
know.  This product's capabilities will increase as people request new
capabilities.  Happy (and ethical) hacking!

                                Andrew Pavlin
                                General Electric Company
                                Government Electronics Systems Division
                                Court Street Plant
                                P.O. Box 4840
                                Syracuse, NY 13221   U.S.A.

                                phone: (315)456-1875
                                Internet: PAVLIN@c5vr.dnet.ge.com
                                          ACPAULIN@sunrise.acs.syr.edu
                                GE DECnet: RSD::PAVLIN