SPECTRAL

To compile:
     $ FORTRAN SPECTRAL
     $ LINK SPECTRAL

Performs the spectral test for a linear congruential random number generator.
Consider linear congruential generators of the form:
	SEED = (A*SEED + C) mod M

Given A, and M, the spectral test calculates NUSQ (NU**2), LOGNU (base 2),
and MU.  As a guide, Knuth suggests a multiplier A may be considered
adequate if the values of MU returned by the spectral test are > 0.1 .
For an exceptionally good multiplier, these values will all be greater
than unity.

The spectral test may be applied if:
   1.  The sequence has maximal period, or
   2.  M is prime and C = 0 and the period length is M-1, or
   3.  M = 2**e and A mod 8 = 5 or A mod 8 = 3.
       In this third case the spectral test is applied using
       A = A and M = 2**(e-2).  For example, in analyzing RANDU,
       use A = 65539 and M = 536870912 (2**29).

Further information on the spectral test is in:

  Knuth, Donald E.  "The Art of Computer Programming Vol. 2: Seminumerical
    algorithms, 2nd edition.  Reading, Mass.: Addison-Wesley. 1981

 This program adapted from:

    ALGORYTHM  AS 193 APPLIED STATISTICS, (1983) VOL. 32, NO.3 PG. 328-335
    T. R. Hopkins

Example:
   MTH$RANDOM is defined as

            SEED = (69069*SEED + 1) MOD 2**32

    Here A = 69069
     and M = 2**32 = 4294967296

   $ RUN SPECTRAL
   INPUT A: 69069
   INPUT M: 4294967296

   A=                          69069.0
   M=                     4294967296.0
   BIGT=           6
   NUSQ=
     NUSQ (           2)=                4243209856.000000
     NUSQ (           3)=                   2072544.000000
     NUSQ (           4)=                     52804.000000
     NUSQ (           5)=                      6990.000000
     NUSQ (           6)=                       242.000000
   LOGNU=
     LOGNU(           2)=                        15.991254
     LOGNU(           3)=                        10.491486
     LOGNU(           4)=                         7.844180
     LOGNU(           5)=                         6.385538
     LOGNU(           6)=                         3.959432
  MU=
     MU=  (           2)=                         3.103734
     MU=  (           3)=                         2.909942
     MU=  (           4)=                         3.203639
     MU=  (           5)=                         5.006469
     MU=  (           6)=                         0.017052

Now examine the MU values.  All values are above 1 except the very last
value MU(6) is 0.01, indicating MTH$RANDOM may not perform as well in a
6-D test.


Run spectral again this time trying the values for the bad RANDU generator:

   MTH$RANDOM is defined as

            SEED = (65539*SEED) MOD 2**31

    Here A = 65539
     and M = 2**31 but we use M = 2**29 for reasons discussed above


   $ RUN SPECTRAL
   INPUT A: 65539
   INPUT M: 536870912   !(2**29)

   A=                          65539.0
   M=                      536870912.0
   BIGT=           6
   NUSQ=
     NUSQ (           2)=                 536936458.000000
     NUSQ (           3)=                       118.000000
     NUSQ (           4)=                       116.000000
     NUSQ (           5)=                       116.000000
     NUSQ (           6)=                       116.000000
   LOGNU=
     LOGNU(           2)=                        14.500088
     LOGNU(           3)=                         3.441322
     LOGNU(           4)=                         3.428990
     LOGNU(           5)=                         3.428990
     LOGNU(           6)=                         3.428990
   MU=
     MU=  (           2)=                         3.141976
     MU=  (           3)=                         0.000010
     MU=  (           4)=                         0.000124
     MU=  (           5)=                         0.001421
     MU=  (           6)=                         0.015025

Notice here the MU values for dimensions 2 through 6 are all extremely
small.  This generator does horribly on these dimensions.  The spectral
test noticed it right away.