Excerpt from INETDRIVER.MAR, Copyright (C) 1992 TGV, Inc.

INETDRIVER's DPT table:

	.Subtitle	Driver Prologue Table
;+ ---
;
; DRIVER CHARACTERISTICS
;
;- ---

	DPTAB	       -			;Driver prolog table
			END=IN_END,-		;End of driver (size)
			ADAPTER=NULL,-		;No hardware
			UCBSIZE=UCB$K_INET_LENG,-;UCB size
			FLAGS = DPT$M_NOUNLOAD,-;Can't unload this driver
			NAME=INETDRIVER,-	;Driver name
;
; Both of these lines are REQUIRED for Alpha/VMS device drivers
;
			SMP=YES,-		;SMP ready
			STEP=1  		;Alpha preliminary


The DPT's initialization remains the same as well as the DDTAB.
Also, the FDT is still the same.  The only remaining thing is convert all
entry points (internal and external) using the .JSB_Entry macro.  Also, 
we found it was better to use the Digital supplied offsets for internal
data structures as opposed to using our own or hardcoding them.


LINK/Alpha/Native/BPage=16/Section/NoTrace/NoDemand-
    /Share/SysExe=Select/NoSysShr driver.opt/opt

The "/SysExe=Select" takes place of the SYS.STB/SEL option.

Some other changes:
1. Some structures have changed, mostly fields of IRPs, UCBs etc.
that were words, now are longs. A few are just gone.
2. You can put a psect=$$$105_prologue stmt into the DPTAB call.
Put your separate ".psect $$$105_prologue" after it.
3. All data must be in separate .psects.

Read the macro32 porting info carefully; all those caveats
apply!

To load a driver, use SYSMAN:
        $ MCR SYSMAN
        SYSMAN> IO LOAD MULTINET:INETDRIVER
        SYSMAN> IO CONNECT INET0:/NOADAPTER/DRIVER=INETDRIVER
        SYSMAN> EXIT