TPC - Fast Tape Copy
		     ====================

			Users' Guide
			============

 This  program  will copy a complete magtape to a Files-11 disk
 and  store it there in a special image mode, from which it can create
 one or more copies of the tape (must faster than FLX ever could).
   BIGTPC is able to do this, but also will handle any block size on
 tape up to 4200. bytes (big enough for BRU tapes). By going from 4
 to 3 buffers for tape and smaller numbers of disk blocks per read/write
 still larger tape block sizes can be handled. Also, several additional
 switches are supported. (If conditional $VAX is defined, the block size
 on tape may be up to 11000. bytes, big enough for VMS Backup or Unix
 TAR tapes.)
   If it is desired to support larger BIGTPC block sizes, it is possible
 to reduce the number of BIGTPC buffers (and the buffer headers) and to
 reduce the disk buffer count of blocks. This works well with the number
 of disk blocks reduced to 8., the number of BIGTPC buffers reduced from
 4 to 3, and the size increased to 11000. bytes, supporting image copies
 of such formats as VMS BACKUP or UNIX TAR tapes. Note however that where
 these counts are changed, BIGTPC may not terminate correctly when writing
 a container file from another version. You may have to abort and write
 EOFs with another utility. If you have a tape and recreate container files,
 there will be no trouble.

 The command format is:-

	TPC Output-filespec=Input-filespec<switches>

 where one  of the 'filespecs' must be a magtape device (e.g. MT:) and
       the other the name of an image file on disk.

 Legal switches are:-

       /BL:nnnn - Specifies  an  initial  allocation specification for
                  the image file if a disk is the output device.
		  Defaults to 200.
       /SA:nnnn - Specifies  a  secondary allocation specification for
                  the image file if a disk is the output device.
		  Defaults to 50.
       /CO      - Specifies that the disk file is to be contiguous
       /HD      - Indicates High Density (1600 BPI) tape is to be
		  written. (For TE16, tape is read at the proper density
		  automagically.) This permits a container file from one
		  density to be written out in another.
       /NR	- Specifies NO positioning of the tape prior to the
		  start of copying. This will allow TPC to merge
		  several backup collections on a single output tape
		  if used with care.
		After the end of a copy, TPC will write 4 EOF records and
		backspace so that it will be positioned after the first
		EOF on tape. This will ensure that a second backup
		done with the /NR switch will correctly copy onto a FLX
		tape in readable fashion.
       /SC:nnnn - Sets tape characteristics to nnnn  (octal), to allow read or write
		of tapes with even parity, 556BPI, etc. If the /HD switch is
		used, the high density bit is ORed in with the nnnn value
		specified in the /SC switch.
       /AN	- Specifies possible ANSI format tape. If TPC sees this switch
		it will look for ANSI label records and permit copies
		even where the tape has null files and hence double EOF
		before the real end of tape. Only 80 byte records are
		examined and EOFs are treated specially only between
		HDR2 and EOF2 (or EOV). The headers are assumed to be in
		ASCII unless the switch /EB is given, in which case they
		are assumed to be in EBCDIC. If the tape is not really
		an ANSI format tape, the TPC copy operation is not
		changed. Thus the /ANsi switch may be used on a tape of
		unknown format.
			The default is /AN, and to force BIGTPC NOT to
		look for ANSI labels (looking normally only at 80 byte
		records unless the /RT subswitch is used), use the /-AN
		switch.
       /EB	- This subswitch of the /AN switch forces on ANSI label
		checks but causes TPC to look for EBCDIC header labels
		rather than ASCII. Note that TPC looks for either ASCII
		or EBCDIC, not both. The default is not to look for
		ANSI labels and end copy at double EOF; the /AN or /EB switch
		settings allow some modifications to this.
       /RT	- Use RT11 type "ANSI" labels. RT11 may not make label
		records  80. bytes long, and if you have RT11 tapes, the
		ANSI checks will normally ignore the RT11 ANSI labels
		unless you use this switch. It causes BIGTPC to ignore
		length of records and checks everything to see if it is
		an ANSI label record. It is not a very good default because
		it probably can be fooled easily but may be needed for
		RT11 tapes.
       /ER	- Specifies that TPC will ignore errors on tape. This
		  specifically means that all errors except EOT/EOV/EOF
		  will be ignored. This is quite useful for recovering
		  data from tapes which are old and full of errors, or for
		  writing an output to a tape with bad spots (though
		  it won't cure bad spots and this method of writing
		  anyway is not necessarily a good idea...).
       /FR	- Rewind the tape after copying to it. Note the /NR switch
		applies to BEFORE the tape is used and inhibits positioning
		at that time. The /FR switch will rewind the tape AFTER
		writing to it.
       /TR	- This switch allows BIGTPC to read a disk to a container
		file as though it were a tape. It implies BIGTPC should
		act as though the input device were a tape even if it
		is not. BIGTPC will need to know the size to copy (defaults
		to 494. blocks, the size of an RX01) and the start block
		number (defaults to 0,0) as octal numnbers in the form
		low:high (see /SZ and /LO switches). The input device is
		copied 1 block at a time. The normal "control" features
		like density, rewind, etc., are suppressed UNLESS the
		/CT switch is used. Their effect is not likely to be
		meaningful.
       /TW	- This switch allows BIGTPC to write a container file to
		a disk as though the disk were a tape (on the output side
		of the command line). It is the inverse of the /TR switch
		and needs the /SZ and /LO information too.
       /MI	- Magtape In. Overrides device name recognition and lets
		BIGTPC consider the input device to be a tape.
       /MO	- Magtape Out. Overrides device name recognition and lets
		BIGTPC consider the output device a tape. NOTE that both
		/MI and /MO should not be used at one time and operation
		is NOT guaranteed if the device specified to be a tape
		really isn't one. This is a simple fix to let BIGTPC
		work with VAX/RSX again even on clustered disks, regardless
		of weird device names. There may be other uses for it
		not known to us. These switches differ from the /TR
		and /TW ones chiefly in that NO effort will be made
		with these to change the block numbers on the QIO$s to
		tape and no size limitation applies. If the input device
		won't generate two consecutive IE.EOF errors, the copy
		will never terminate. Note that tape can do this. Also
		control QIO$s for things like rewind and density are
		left alone by /Mi and /MO.
       /SZ:low:high - This switch sets the device size for /TR, /TW, and
		/IM copies, in 2 words of block counts. Note the number
		of blocks is given, not the last block number, so a disk
		with 494 blocks is specified as /SZ:494., the high size
		defaulting to 0. Default value is /SZ:494.:0.
       /LO:low:high - This switch specifies the starting physical block
		of the disk to begin transfer from in /TR and /IM, or
		transfer to in /TW cases. This allows you to move blocks
		around or to copy only parts of a disk. The default is
		0:0, so you won't need to use /LO often unless you intend
		to copy partial volumes.
       /CT	- This switch allows control-type QIO's to occur even if
		/IM, /TR, or /TW are specified. These QIO's do things
		like rewind, write endfile, space forward or back,
		and set density as well as attach the LUNs. It is not
		very meaningful for /TR or /TW unless you have a strange
		device that nevertheless is really a tape (and it's not
		certain you can emulate it properly this way anyhow). For
		/IM copies, it allows a tape to be the output device
		and to receive a blocked copy of a device in format
		independent ways while still setting density, rewinding,
		etc. Note the control QIOs are not error checked so if
		you try to rewind a disk, it'll not hurt you.
       /IM:low:high:blkfactor - This switch allows BIGTPC to copy data
		in image mode directly from one device to another. It
		does not operate AST driven in this mode as it does in
		all others, but uses all buffers as one large I/O buffer
		permitting I/O transfers of up to about 72. blocks at
		a time. The low:high arguments are the block number
		to begin the output transfer to on the output device
		(/SZ specifies the length in blocks to move), and the
		"blkfactor" argument is the number of blocks to
		be transferred at each QIO$ to the output device.
		This defaults to 8. so that if the output device is
		tape, the buffers will be 4096. bytes long. If you
		specify a bigger blocking factor than BIGTPC can
		handle, it will just use its maximum. Normal operation
		will not issue any "write-EOF" operations, but if tape
		is the output device, the /CT switch will permit
		these controls to be done so the resulting tape will
		work (and the /FR switch, the /HD switch, and the
		/SC switch will work).
       /FL:filnam	-This  switch works only with the /IM and /CT
		switches and will have no effect unless BOTH of these
		are specified. It causes BIGTPC to write a standard
		DOS format (FLX format) label record before it writes
		an image file on tape, using "filnam" (up to 6 characters)
		as the filename. The full file specification is
		[1,1]filnam.OLB with standard DOS protection and a creation
		date of 00-JAN-70. This permits the image file to co-exist
		on a FLX tape (.OLB is the extension chosen since FLX will
		copy it in image mode). FLX can skip the nonstandard
		file and make directories, read, or write on the tape,
		allowing it to contain other interesting programs (perhaps
		a copy of BIGTPC to read the images with, for instance).
		Also, multiple files may be more easily kept on the tape.
		On input, you must skip this record on tape prior to
		inputting the file.
		  If /ER is specified, zero byte reads will NOT terminate
		copies (so sizes better be right!) and lengths copied will
		be calculated from given block factors, not from returned
		actual byte counts.
       /NI	- This switch ("Nibble In") allows /IM copies to read a
		disk 1 block at a time instead of using big QIOs of "blkfct"
		blocks at a time. Thus, if there is a bad disk block, data
		on following blocks will not be lost. See the /IM switch doc.
		for interaction with /ER.
       /NO	- This switch ("Nibble Out") allows /IM copies to write a
		disk 1 block at a time. It is supplied also to aid in writing
		to a disk with bad blocks, guaranteeing that not more than 1
		block's data will be lost. Its interaction with /ER is as that
		of /IM. The /NI and /NO switches apply only to the /IMage
		mode copies of BIGTPC.
       /HE	- This switch causes BIGTPC to print a help message
		summarizing the action of all of its switches and
		giving the defaults for the more important ones.


 So that, for instance,

		TPC BACKUP=MT:

 will create the file BACKUP (.DOS by default) from the magtape on MT:, and

		TPC MT:=BACKUP

 would then create an exact copy of the original magtape onto the tape
 now mounted on MT:.

 Note that TPC will only handle one tape at a time and cannot handle
 block sizes of greater than 4200 bytes without edit and rebuild. If
 the tapes are FLX format tapes, however, the TPCDIR program ([312,315])
 may be used to list directories or extract copies of files in the
 container file, though in a fairly cumbersone way. Otherwise, BIGTPC
 acts as a format-independent tape copy to EOT (signalled by 2 consecutive
 EOFs).
  CAVEAT:
   It is possible for a FILES-11 tape to have 2 EOFs in a row where a zero
 length file is copied, yet not be at EOT.
  If the tape you are copying may be of this sort, use the /ANSI
switch while copying (or the /EBCDIC switch if it came from an IBM site using
EBCDIC labels). This will allow TPC to correctly handle double EOFs in the
middle of a file. If your tape does not have this pathology, TPC will function
correctly also, so the /ANsi switch is a good one to set most all
the time unless you have some sort of pseudo-ANSI tape that may have
records starting with HDR2, EOV, or EOF.
  If your tape was produced by RT11 PIP (possibly also under RSTS), you may
need the /RT switch to successfully handle null files. The /ANsi switch is
now on by default; use /-AN to turn it off if you must.


 TPC can report the following errors:-

 1.  TPC - DISK I/O ERROR.  CODE = n

     TPC encountered an error while reading from/writing to the disk.

 2.  TPC - MAGTAPE I/O ERROR.  CODE = n

     TPC encountered an error while reading from/writing to the magtape.

 3.  TPC - COMMAND LINE INPUT ERROR

     TPC encountered an error in reading the commandline.

 4.  TPC - COMMAND LINE SYNTAX ERROR

     TPC encountered an error when trying to parse the command line.

 5.  TPC - INVALID SWITCH

     The  commandline contained a switch that TPC could not recognise,
     or a file specification that it could not parse.

 6.  TPC - OPEN ERROR ON OUTPUT FILE

     A file was specified as output, but TPC encountered an error when
     it tried to open it.

 7.  TPC - OPEN ERROR ON INPUT FILE

     A  file was specified as input, but TPC encountered an error when
     it tried to open it.

 8.  TPC - SPECIFY 1 FILE & 1 MAGTAPE DEVICE

     The commandline either specified magtape as both input and output
     device, or a disk file as both input and output device.

   TPC tends to crash when it has an allocation failure while reading
 tape to disk.


	If BIGTPC is built with the $$$PRO conditional defined, it can
 be built on PRO 350 (should be linked /PR:0 to get at nonmounted disks)
 and used. The /SZ defaults there to 800. (the size of an RX50) then.
	While BIGTPC's tape handling is useless on the PRO, it can copy
 floppies in image mode and its error ignoring ability may allow recovery
 of floppies in which errors have developed. If built privileged, it
 should be able to access the floppies regardless of mount status. It
 can be used as a full or partial floppy copy program then. This allows
 copy of data on floppies before it can modify itself. This is a useful
 thing to do on commercial packages that modify their installation disks.
 Copy them before installing and install the copies. You will then always
 have a reliable virgin backup and if you blow something away during an
 install, you can restart. Floppy errors during installs CAN ruin diskettes
 if you aren't careful, so protect your investment.