Error Avoider

This is a software "wedge" system which uses an intercept driver to
do extra error recovery for disks. It was originally found to be useful
for certain optical disk models, since optical disks have very frequent
errors and some were exceeding error limits that a patched DKdriver would
allow. It may also be that there are circumstances where unusual load
conditions or problems with generic disk firmware can produce errors
which may disappear if retried, but which are not retried (or not retried
enough) by VMS disk drivers. Most such errors on normal SCSI disks
indicate impending drive failure, but on some occasions they may indicate
simply firmware which reports too many errors, or media (as in an old
floppy disk) which is approaching end of life, but which can be read with
very large retry counts. For these purposes, this wedge can spell the
difference between being able to use a device and not being able to. It
is a matter for experimentation whether this system will actually help,
but it is easy to install and use, and has no effect on operation save
that, FOR THE PARTICULAR DISK(s) INTERCEPTED, it allows a number
(currently 8) retries on read or write before giving up.

The driver, JGdriver, is an intercept driver furnished to provide
extended error retry for a VMS device (usually a disk, but any device can
be used). Note that this code is directed at disks primarily or at other
similar devices where the UCB does NOT GET DELETED. 

The intercept driver will cause erroneous read or write operations on its
target device to be (invisibly) retried up to a settable number of times
(8 as it currently stands...this is assembled into jgdriver) in the event
of error. Its use is otherwise invisible to users and it operates by
intercepting driver start_io and using the IRP$L_PID hook to get access
to the IRP after I/O but before the user app sees it.

The AXP version of JGdriver just uses the IRP space from IRP$Q_QIO_P3 on
through IRP$Q_QIO_P5 (in VMS 7.0 and up) for storage of information about
how many times (if at all) the IRP has been retried, and some bits of
extra information needed to finish it up. Since this information should
by start-io time have been fully encoded into the IRP it is expected this
will not cause problems.

The VAX version uses the IRP$L_KEYDESC field (so long as this is not
already in use) to point to a small block it allocates from pool to hold
this information, because there is not room for it in the VAX IRP.

Operation otherwise is the same. At start-io, for r/w,the intercept code
looks for a magic number in its data storage and if it finds it, assumes
that it has already set the IRP up. If it does not find it, it sets it up
and sets the IRP field IRP$L_PID to cause I/O post to go to a routine
within the intercept driver on completion. It then calls the original
start-io and returns. (If the operation is not read or write, it just
calls the original start-io without touching the IRP.)

The completion code examines the I/O status about to be returned to the
user. If the low bit is 1 (success) it just uses com$post to postprocess
the IRP (since the driver has already called REQCOM) If the low bit is 0,
it decrements the error retry count it has and requeues (via insioqc) the
I/O (from fork level!) to the intercepted driver again. If the retry
count is exhausted it just cleans up and calls com$post (actually, for
axp, the step2 replacement) to return the final status to the user.

This operation has proven handy for some types of disk storage where the
retry operation of the native drivers has been inadequate. In particular,
the VAX DKdriver is not as careful as it might be to retry potentially
retriable operations, so that using this intercept provides an invisible
yet highly effective way of ensuring that an error is repeatable before
the user code sees it. Where timing or other transient conditions cause
problems, this gives a large advantage. On optical media it has been
dramatic on VAX. The Alpha DKdriver is more careful, but even there, this
driver will ensure that errors due to timeouts under heavy load are
retried before being returned. Since this approach requires NO driver
code changes it is attractive; it can be applied for those disks needing
it, and not applied for others. The intercept is device unit specific,
unlike one which might patch a class driver in memory or something of
that sort. Units not intercepted operate EXACTLY as before.

The intercept here is one published by Glenn Everhart in 1992 as a
candidate standard. It works by replacing the victim DDT with its own and
allows the intercept to be removed completely with a single store of a
longword. It further allows the intercept to be intercepted, and
interception and removal can occur in any order. The reason for proposing
this scheme was precisely that interception and removal become order
independent, so that any third parties using the intercept can freely use
it without risk of crashes due to pool reuse, as occurs where the
interception code is not standardized and an entry is intercepted by
intercept A, then intercept B, and then intercept A is removed. If this
scheme is used, removal of intercept A results in the chain being
reconstituted so that intercept B no longer relies on intercept A's
presence. (In passing, it should be noted that switching has always been
on fairly idle systems, so there may be some cache invalidation needed to
perform such switches safely during load. Setup is done in "safe order"
though, and this intercept is expected to be used where normally it is
not needed to remove it.)

Installation is accomplished via VMSINSTAL. It asks whether to compile
from sources or just link prebuilt object files. Best advice is to
compile if possible. This needs the MACRO assembler on VAX, or the
MACRO32 compiler on alpha; the sources for VAX will work on VMS from
version 5.5 on, and the AXP sources will work from version 7.0 on.

Once you install the kit, you must run the procedure

sys$manager:EA_SETUP.com

which will give a manu which allows the option of doing error avoidance
on all mounted disks or of removing a disk from a previously selected
configuration. If you do not select extra error recovery for all mounted
disks (and you generally will not), the system allows you to go on to
select which disk or disks to do extra error recovery on. You select
disks from a menu until done, then finish. 

This produces a file

SYS$MANAGER:EA_START.COM 

which should be run at boot to enable the error reduction.

Should you want to turn off this feature for a disk, see in EA_START.COM
what the JGAn: unit number is that is associated with the disk and use
the command 

JGCTL/DEASSIGN JGAn: disk:

(This assumes you have cmkrnl privileges). This will restore disk
operation to exactly its normal configuration.