BASHDK 

BashDK is an in-memory driver patcher that is designed to patch
DKDRIVER in memory so that DKDRIVER will properly control jukebox
disks as normal VMS disks. The patches are minimal and do not
interfere with normal operation on normal VMS disks on SCSI
busses.

The BASHDK program is VMS version specific, so that it works
correctly only where DKDRIVER does not change. It does some testing
to ensure it has the correct DKDRIVER version and will do nothing
if it finds out it has the wrong version. 

Use:

Suppose you have an HP jukebox connected to SCSI unit 0 of
bus A.

1. Boot VMS normally.
2. Run BASHDK from a fully priv'd account (needs and uses $cmkrnl)
3. Issue SYSGEN connect commands like

$ sysgen:==$sysgen
$ sysgen connect dka0:/driver=dkdriver

Now the DKA0: device is connected and can be used as a normal VMS
disk.


Internals:

Several locations in DKdriver are patched.

In routine MODE_SENSE:

The instruction
        BITB    #<ERR_RECOV$M_AWRE!-    ; The following four flags must have
                  ERR_RECOV$M_ARRE!-    ; default values of zero: automatic
                  ERR_RECOV$M_RC>,-     ; write relocation, automatic read
                UCB$B_RECOV_PAR+2(R3)   ; disable correction
is patched so it is a bicb2 followed by changing the branch to always
act as though the bits are zero,

disabling these checks.

;In the early version,also the instruction
;
;        BICL2   #<UCB$M_NOREASSIGN!-    ; Assume REASSIGN_BLOCK supported,
;                  UCB$M_FLOPPY!-        ; Assume not a flexible diskette,
;                  UCB$M_FORMAT>,-       ; Assume FORMAT unsupported
;                UCB$L_DK_FLAGS(R3)
;
;was edited so that it does NOT clear the ucb$m_noreassign flag (which is
;set by the patch to INQUIRE).
   This is not done in the production version.

Also in mode_sense:

; If this is a read-only device such as a CDROM, it may not have real tracks,
; sectors, and cylinders. If this is the case, READ_CAPACITY will set up a
; dummy values for the geometry parameters. For now, assume success.

92$:    BBS     #DEV$V_SWL,-            ; If this is a read-only device, it's n$
                UCB$L_DEVCHAR(R3),75$   ; required to have non-zero values of

The above instruction is changed to test the DEV$V_IDV bit (input device)
which is basically always set. This allows any device to get its geometry
later on instead of giving up with an error.


Other things called from io_packack: are patched.

Subroutine INQUIRY:

        BNEQ    40$                     ; Branch if not, illegal device type
        BISL    #UCB$M_CDROM,-          ; Indicate CDROM-like device
                UCB$L_DK_FLAGS(R3)      ;
        BISL2   #UCB$M_HWL,-            ; This a read-only device so set
                UCB$L_DK_FLAGS(R3)      ; the hardware write-lock bit
        BBSS    #DEV$V_SWL,-            ; This a read-only device so set
                UCB$L_DEVCHAR(R3),10$   ; the software write-lock bit


	This has been changed to:

	blss	40$		; if type < 5 (5=cdrom), not a disk.
		; leaves types 5, 6, and 7 treated as disks
		; 5 = cdrom, 7 = jukebox.
	bisl #<ucb$m_cdrom>,-
		ucb$l_dk_flags(r3)	; Set cdrom type (in case true),
			; don't support block reassign and say no host based
			; shadow support so no read-long gets tried
	bisl	#0,ucb$l_dk_flags(r3)	; disable read-only set
	bbss	#dev$v_idv,ucb$l_devchar(r3),10$	; set idv bit which
			; basically is always set anyway; no-ops this inst.


Also we change the movb #3,<somewhere-ucb-retry-byte>(r5)
to a CVTFB #63,<somewhere-ucb-retry-byte> to change the retry
count from 3 to 120, and we clear the err_recov$m_rc but from
the error recovery ignore mask so that that bit IS cleared
during error recovery and treated as a don't care bit. This bit
is removed from a location in the mode_sense routine also.

The retry count patch is that we change:

IO_RW_RETRY:

        MOVB    #RW_RETRY_CNT,-         ; Initialize read/write retry count
                UCB$B_RW_RETRY(R3)      ;
to
IO_RW_RETRY:

        CVTFB   #63,-         ; Initialize read/write retry count
                UCB$B_RW_RETRY(R3)      ;


The two err_recov$m_rc patches are:

One in MODE_SENSE_CHANGABLE where we add the err_recov$m_rc
bit to the instruction:

        BICB    #<ERR_RECOV$M_EEC!-     ; Clear don't cares
                  ERR_RECOV$M_DCR!-     ;
                  ERR_RECOV$M_DTE>,R2   ;

and again in mode_select:
we remove the bit from the instruction:

        BICB3   #^C<ERR_RECOV$M_TB!-    ; Get the error recovery flags of
                    ERR_RECOV$M_DTE!-   ; interest (the other flags are either
                    ERR_RECOV$M_PER>,-  ; don't cares or have already been
                UCB$B_RECOV_PAR+2(R3),- ; checked for zero values in
                R1                      ; MODE_SENSE)



These changes allow the optical disks to be tested for support for
revectoring, but greatly increase the error retry count before
this happens and causes the driver not to treat the err_recov$m_rc
flag, common on opticals, as a fatal error condition. Should the
error result in no data being transferred in the first sector
however, the driver will still report an error. It is for that
reason that the jgdriver intercept function exists, to reissue the
IRP to the DKdriver again when this happens to recover. Once this
happens, opticals will have some errors logged when ECC recovery
happens, but this is essentially always recovered from. The optical
disk signal is noisy, so ECC errors on optical are common, but disabling
reporting of them for optical disk would interfere with reporting
this class of errors for other SCSI disks, where they are serious.
Accordingly, customers need to understand that the error count on
their optical disks will be usually nonzero, but that it is not
meaningful, and their applications will not see these errors. If we
had a hardware board, or a totally new driver, we could avoid
these bogus error reports, but as we're using the DEC driver in order
not to mess up access to other SCSI devices, these error reports
will occur and just need to be ignored.


Note however that a second test in mode set will still set the readonly
bits (dev$m_hwl and dev$m_swl) so long as the SCSI config reading
commands return writelock. My tests show this happening for CDroms.

Even if this isn't done, one can still use mount/nowrite to prevent
attempts at write access to CDs, though it will (obviously) do no harm.


These changes can obviously be made on future DKdriver versions.

While this change means dkdriver could attempt to access type 6 SCSI
devices, in fact this doesn't generally happen because one must
use the sysgen connect DKcnnn:/driver=dkdriver command to connect
disks. So long as one doesn't do something stupid like command to
connect one's scanner as a disk, this latent (mis)feature will
cause no harm.

As things now appear, it isn't clear to me that any further patches are
needed. I could place a bit of code out of line in there, but the
few error paths changed are basically operational errors, causing
no more problems because other errors a bit later will be seen (as
in the case of no geometry...mount will just fail a bit later if
no geometry is finally available, for example).


Glenn C. Everhart
2/15/1994
3/2/1994