This document is supposed to describe as11, the PDP-11 cross-assembler.

Command line: as11 [options] assembly-file

Options:
	-l listing-file
		Writes a listing, including generated code, into the
		named file.

	-o output-file
		Writes the generated code into the named file.

No filename extensions are enforced; the convention I have been using
is .s11 for assembly source, .l11 for listings, and .o11 for output
files.  Either (or both, if you feel weird) of the options can take the
name -, which means to write the corresponding thing to as11's standard
output.  This is really useful only with the -l option; looking at
output files is not very interesting.  They are not intended to be read
by anything but the simulator.

The assembly-file must be a real file.  (Actually, it must be something
on which rewind(3) works.)

The assembly language tries to stay moderately close to the DEC
assembler syntax; in particular, it uses # and @ where the UNIX
assemblers typically use $ and *.

The assembler processes each line of the source file in turn.  An
assembly source line takes one of the following forms.  Whitespace is
ignored except where noted, though it does serve to separate tokens
from one another.

conditional
[label] [comment]
[label] pseudo-op
[label] opcode [operand[,operand]] [comment]
assignment [comment]

where []s indicate that the thing enclosed is optional, and the names
represent things as follows.  Keywords, which appear in upper case in
the descriptions below, are literal values; other things are terms to
be described further.  Alphabetic case is ignored for such keywords,
and also for opcode and register names, but not for symbol names or in
character constants or strings.

comment

	A ; together with everything following it, up to the end of the
	line.

conditional

	One of
		.IF	condition	expression
		.IF	DF		symbol
		.IF	NDF		symbol
		.IFT
		.IFF
		.IFTF
		.ENDC
		.ENDIF
	where "condition" is one of EQ, NE, LT, GT, LE, or
	GE.  These provide conditional assembly.  When a .IF
	directive is encountered, if the condition is true, assembly
	continues as normal up to the matching .ENDIF; if false, all
	lines in between are ignored, except for further conditionals.
	This can be further modified by the .IFF and .IFT directives,
	which assemble code if the original condition was false or
	true, respectively, or .IFTF, which assembles code
	unconditionally (but does not terminate the conditional).
	Conditionals can be nested to an arbitrary depth and take no
	notice of include file boundaries (though a .INCLUDE directive
	is not executed if code is not being assembled at the time it
	is seen).  .ENDC and .ENDIF are synonyms.

	The condition of an if is considered true for the first form if
	the expression bears the indicated relation to 0; for example,
		.IF	GE	foo-bar
		...
		.ENDC
	will assemble the contained code if foo-bar >= 0.

	.IF DF and .IF NDF test whether a symbol is defined and
	assemble code if it is or is not defined, respectively.

	Note that conditionals look like pseudo-ops but, unlike
	pseudo-ops, cannot carry labels.

	Code inside a false conditional is not inspected, except to
	determine whether it is a conditional, and thus can include
	illegal opcode names, invalid expression syntax, or indeed
	anything that cannot be parsed as a conditional.  This can be
	dangerous, because a conditional with a syntax error will not
	be taken as a conditional if it occurs inside (another) false
	conditional.

	When inside a false conditional, the normal octal number giving
	the value of dot at the left hand side of the listing is
	replaced with six dashes.

symbol

	Any sequence of characters drawn from the set !$%&.?^_~ plus
	the digits and letters, but not beginning with a digit or a $.
	Any character can be part of a symbol name if it is preceded
	with a backslash; except for this, whitespace cannot be part of
	a symbol name.  Some symbol names beginning with a . have
	reserved meanings.  Currently, these are

		.	The current address.  This is updated only
			between lines; within any given line it is
			constant.  Assigning to it performs the
			function of the .org pseudo-op in some other
			assemblers.

		.base	The default base, used to interpret numbers
			where no other base can be determined.  Can
			range from 2 through 36.  See the description
			of an expression for more details.

assignment

		symbol = expression [comment]
	or
		symbol == expression [comment]

	Both forms cause the symbol to be given a value equal to the
	value of the expression.  The difference between the two forms
	is that the form with the double equal sign produces a warning
	if you change the value of a symbol; it is intended for
	manifest constants, such as device register addresses, whereas
	the first form produces no message if you change the value of
	the symbol with it; it can be used like an assignment in a
	programming language.  (Note, though, that the assembler is not
	intended as a general-purpose programming language!)

	A symbol's value can have any type; they are not restricted to
	16-bit integers.  Any expression's value can be store in a
	symbol with an assignment and will reappear, type and value
	unchanged, when that symbol is used in an expression.

label

	A symbol followed by a colon.  There may be whitespace between
	the symbol and the colon.  Doing this causes the symbol to be
	given a value equal to the value of . for the line on which it
	was seen.

pseudo-op

	One of the following:

		.ASCII	string
		.ASCIZ	string
		.EVEN
		.ODD
		.ALIGN	expression [comment]
		.SPACE	expression [comment]
		.BLKB	expression [comment]
		.BLKW	expression [comment]
		.BYTE	[expression[,expression[,expression...]]] [comment]
		.WORD	[expression[,expression[,expression...]]] [comment]
		.LONG	[expression[,expression[,expression...]]] [comment]
		.QUAD	[expression[,expression[,expression...]]] [comment]
		.FLOAT	[expression[,expression[,expression...]]] [comment]
		.DOUBLE	[expression[,expression[,expression...]]] [comment]
		.LIST	{ON|OFF|PUSH[{ON|OFF}]|POP}
		.INCLUDE filename [comment]
		.END	[expression]
		.DB	[expression[,expression[,expression...]]] [comment]
		.DW	[expression[,expression[,expression...]]] [comment]
		.DL	[expression[,expression[,expression...]]] [comment]
		.DQ	[expression[,expression[,expression...]]] [comment]
		.DF	[expression[,expression[,expression...]]] [comment]
		.DD	[expression[,expression[,expression...]]] [comment]

	These have semantics as follows:

	.ASCII
	.ASCIZ
		These assemble a string of ASCII characters.  See the
		entry for "string" for a description of what they
		accept.  The difference between .ASCII and .ASCIZ is
		that .ASCIZ automatically appends a null byte, as if
		the string ended with <0>.

	.EVEN
	.ODD
		These test whether . is even or odd, respectively, and
		skip forward by one if not.  (.EVEN is, thus,
		equivalent to .ALIGN 2.)

	.ALIGN
		This advances . until it's an exact multiple of the
		expression.  This is not needed often; .EVEN is all
		that's usually required.

	.SPACE
		This advances . by as many bytes as the value of the
		expression.  Thus, these two are equivalent:
			.SPACE	expression
			. = . + expression

	.BLKB
	.BLKW
		These reserve space for the specified number of bytes
		or words, respectively.  (.BLKB is thus equivalent to
		.SPACE.)

	.BYTE
	.DB
		These reserve bytes of memory and initialize them to
		the listed expressions.  One byte is reserved for each
		expression listed.  Both forms are completely
		equivalent.

	.WORD
	.DW
		These reserve words of memory and initialize them to
		the listed expressions.  One word is reserved for each
		expression listed.  Both forms are completely
		equivalent.

	.LONG
	.DL
		These reserve longwords of memory (32 bits each) and
		initialize them to the listed expressions.  One
		longword is reserved for each expression listed.  Both
		forms are completely equivalent.

	.QUAD
	.DQ
		These reserve quadwords of memory (64 bits each) and
		initialize them to the listed expressions.  One
		quadword is reserved for each expression listed.  Both
		forms are completely equivalent.

	.FLOAT
	.DF
		These reserve and initialize single-floats (32 bits
		each) in memory.  One float is reserved for each listed
		expression.  Both forms are completely equivalent.

	.DOUBLE
	.DD
		These reserve and initialize double-floats (64 bits
		each) in memory.  One double is reserved for each
		listed expression.  Both forms are completely
		equivalent.

	.LIST
		This controls the listing of lines.  If the argument is
		ON or OFF, listing of lines is turned on or off,
		respectively.  A stack of listing state is maintained;
		the arguments PUSH and POP control this stack.  POP
		pops it, setting the listing state to the state thus
		uncovered; PUSH alone duplicates the current state and
		pushes it on the stack, whereas PUSH ON and PUSH OFF
		push the stack and set the new state as specified.

	.INCLUDE
		Includes a file.  When a .INCLUDE directive is read,
		further lines are taken from the named file until
		end-of-file or a .END directive is reached, at which
		point assembly continues with the line after the
		.INCLUDE directive.  Includes can be nested arbitrarily
		deeply (or at least until the assembler runs out of
		open files; typically this limit will be at least
		fifteen or so, and often as much as 50 or 60).

	.END
		No further lines are read from the current input file.
		If it is being read because it was named in a .INCLUDE
		directive, processing resumes with the line after the
		.INCLUDE; if it is being processed because it was named
		on the command line, assembly terminates as if
		end-of-file had been reached.  Nothing after a .END
		directive is examined by the assembler, except in one
		circumstance: when the .END is inside a false
		conditional, in which case it is ignored like all other
		pseudo-ops.

string

	A sequence of quoted-strings and ASCII-codes.  A quoted-string
	is any string of characters surrounded by matching delimiters,
	provided the delimiter is not a less-than sign.  Such a string
	produces one byte in memory for each character between
	delimiters.  An ASCII-code is an expression inside <>, and
	assembles as one byte, whose value is that of the expression.
	Whitespace is significant inside quoted-strings, but not
	elsewhere (except possibly for character constants in the
	expression - see the description of expressions).

	Note that it is not possible to put a trailing comment after a
	string, because the leading semicolon would be taken as the
	leading delimiter of a quoted-string.

filename

	Any string of characters between matching delimiters.  The
	delimiter is taken to be the first non-whitespace character
	after the directive; the filename is everything from there up
	to the matching delimiter.  Unlike a string (above), a comment
	can appear after a filename.

opcode

	One of the recognized opcode names.  As of this writing, they
	are:

	ABSD	BICB	CLNV	CSM	LDF	NOP	SETF	STST
	ABSF	BIS	CLNVC	DEC	LDFPS	RESET	SETI	SUB
	ADC	BISB	CLNZ	DECB	MARK	ROL	SETL	SUBD
	ADCB	BIT	CLNZC	DIV	MFPD	ROLB	SEV	SUBF
	ADD	BITB	CLNZV	DIVD	MFPI	ROR	SEVC	SWAB
	ADDD	BLE	CLR	DIVF	MFPS	RORB	SEZ	SXT
	ADDF	BLO	CLRB	EMT	MFPT	RTI	SEZC	TRAP
	ASH	BLOS	CLRD	HALT	MODD	RTS	SEZV	TST
	ASHC	BLT	CLRF	INC	MODF	RTT	SEZVC	TSTB
	ASL	BMI	CLV	INCB	MOV	SBC	SOB	TSTD
	ASLB	BNE	CLVC	IOT	MOVB	SBCB	SPL	TSTF
	ASR	BPL	CLZ	JMP	MTPD	SCC	STCDF	TSTSET
	ASRB	BPT	CLZC	JSR	MTPI	SEC	STCDI	WAIT
	BCC	BR	CLZV	LDCDF	MTPS	SEN	STCDL	WRTLCK
	BCS	BVC	CLZVC	LDCFD	MUL	SENC	STCFD	XOR
	BEQ	BVS	CMP	LDCID	MULD	SENV	STCFI
	BGE	CCC	CMPB	LDCIF	MULF	SENVC	STCFL
	BGT	CFCC	CMPD	LDCLD	NEG	SENZ	STD
	BHI	CLC	CMPF	LDCLF	NEGB	SENZC	STEXP
	BHIS	CLN	COM	LDD	NEGD	SENZV	STF
	BIC	CLNC	COMB	LDEXP	NEGF	SETD	STFPS

	The convention some assemblers support, allowing what looks
	like bitwise or applied to opcodes, to combine multiple
	condition-code manipulation instructions into one, does not
	work.  Instead, each of the 15 possible combinations has its
	own opcode, formed by listing the affected bits in the order
	NZVC, or SCC/CCC for the instructions affecting all four bits.

operand

	Precisely what is legal in the "operand" field depends on the
	instruction.  Some take no operands at all; some take only one,
	and some take two.  Each instruction must be given the correct
	number of operands, and what sorts of operands an instruction
	can take depends on the instruction.  Each instructions falls
	into one of 19 patterns, though.  A description of the various
	types of operands referred to will follow.

	1)	No operands.  Instructions falling into this class are:

		BPT	CLNVC	CLZC	RESET	SENV	SETI	SEZVC
		CCC	CLNZ	CLZV	RTI	SENVC	SETL	WAIT
		CFCC	CLNZC	CLZVC	RTT	SENZ	SEV
		CLC	CLNZV	HALT	SCC	SENZC	SEVC
		CLN	CLV	IOT	SEC	SENZV	SEZ
		CLNC	CLVC	MFPT	SEN	SETD	SEZC
		CLNV	CLZ	NOP	SENC	SETF	SEZV

	2)	One general-addressing operand.  Instructions falling
		into this pattern are:

		ADC	CLR	DECB	MFPI	NEGB	SBCB	TSTB
		ADCB	CLRB	INC	MFPS	ROL	STFPS	TSTSET
		ASL	COM	INCB	MTPD	ROLB	STST	WRTLCK
		ASLB	COMB	JMP	MTPI	ROR	SWAB
		ASR	CSM	LDFPS	MTPS	RORB	SXT
		ASRB	DEC	MFPD	NEG	SBC	TST

		Note, though, that the operand of JMP is not allowed to
		be a register.

	3)	One operand, which must be a general-purpose register.
		The only instruction in this class is RTS.

	4)	One operand, which must be a constant from 0 through 7.
		The only instruction in this class is SPL.

	5)	One operand, which is a target to branch to; this
		target must be within approximately 128 instructions of
		the branch.  Instructions falling into this pattern
		are:

		BCC	BGE	BHIS	BLOS	BNE	BVC
		BCS	BGT	BLE	BLT	BPL	BVS
		BEQ	BHI	BLO	BMI	BR

	6)	Two operands, the first being a general-purpose
		register and the second an general-addressing operand.
		Instructions falling into this pattern are JSR and XOR,
		but note that the second operand for JSR is not allowed
		to be a register.

	7)	Two operands, the first being a general-addressing
		operand and the second a general-purpose register.
		Instructions falling into this pattern are ASH, ASHC,
		DIV, and MUL.

	8)	Two operands, both being general-addressing operands.
		Instructions falling into this pattern are:

		ADD	BICB	BISB	BITB	CMPB	MOVB
		BIC	BIS	BIT	CMP	MOV	SUB

	9)	Two operands, the first being a general-purpose
		register and the second being a target to branch to;
		the target must be before the instruction and cannot be
		farther than approximately 64 instructions back.  The
		only instruction in this class is SOB.

	10)	One operand, which must be a constant from 0 through
		377 (255.).  The instructions in this class are EMT and
		TRAP.

	11)	One operand, which must be a constant from 0 through 77
		(63.).  The only instructions in this class is MARK.

	12)	One operand, which must be a single-precision
		floating-point general-addressing operand.  The
		instructions in this class are ABSF, CLRF, NEGF, and
		TSTF.

	13)	Two operands, the first being a floating-point register
		from F0 to F3 and the second being a single-precision
		floating-point general-addressing operand.  The
		instructions in this class are STCDF and STF.

	14)	Two operands, the first being a single-precision
		floating-point general-addressing operand and the
		second being a floating-point register from F0 to F3.
		The instructions in this class are:

		ADDF	DIVF	LDF	MULF
		CMPF	LDCFD	MODF	SUBF

	15)	Two operands, the first being a floating-point register
		from F0 to F3 and the second being a
		(non-floating-point) general-addressing operand.  The
		instructions in this class are STCDI, STCDL, STCFI,
		STCFL, and STEXP.

	16)	Two operands, the first being a (non-floating-point)
		general-addressing operand and the second being a
		floating-point register from F0 to F3.  The
		instructions in this class are LDCID, LDCIF, LDCLD,
		LDCLF, and LDEXP.

	17)	One operand, which must be a double-precision
		floating-point general-addressing operand.  The
		instructions in this class are ABSD, CLRD, NEGD, and
		TSTD.

	18)	Two operands, the first being a floating-point register
		from F0 to F3 and the second being a double-precision
		floating-point general-addressing operand.  The
		instructions in this class are STCFD and STD.

	19)	Two operands, the first being a double-precision
		floating-point general-addressing operand and the
		second being a floating-point register from F0 to F3.
		The instructions in this class are:

		ADDD	DIVD	LDD	MULD
		CMPD	LDCDF	MODD	SUBD

	where the following terms have the following meanings:

	general-addressing operand
		One of the following:
			gpr
			(gpr)
			(gpr)+
			@(gpr)+
			-(gpr)
			@-(gpr)
			expression(gpr)
			@expression(gpr)
			#expression
			@#expression
			expression
			@expression
		where gpr means general-purpose register.

	general-purpose register
		One of R0, R1, R2, R3, R4, R5, R6, R7, SP, or PC.  No
		whitespace is allowed in a register name.

	constant
		An expression whose value is within the indicated
		range.

	target to branch to
		An expression designating an address to branch to.

	single-precision floating-point general-addressing operand
	double-precision floating-point general-addressing operand
		One of the following
			fpr
			(gpr)
			(gpr)+
			@(gpr)+
			-(gpr)
			@-(gpr)
			expression(gpr)
			@expression(gpr)
			#expression
			@#expression
			expression
			@expression
		where gpr means general-purpose register and fpr means
		floating-point register.

	floating-point register
		One of F0, F1, F2, F3, F4, or F5.  In some cases, F4
		and F5 are not allowed.

expression

	An expression formed from numeric constants, symbols (which
	produce their values when used in expressions), in the usual
	way with the following set of operators:

		+	(binary) addition
		-	(binary) subtraction
		*	(binary) multiplication
		/	(binary) division
		+	(unary) no-op
		-	(unary) negation
		~	(unary) bitwise complement
		%FASI	(unary) convert floating-point to integer by
			reinterpreting the bits, not by converting the
			value
		%IASF	(unary) convert integer to floating-point by
			reinterpreting the bits, not by converting the
			value
		%FIX	(unary) convert floating-point to integer by
			converting the value and (currently) rounding
		%ROUND	(unary) convert floating-point to integer by
			converting the value and rounding
		%TRUNC	(unary) convert floating-point to integer by
			converting the value and truncating

	where parentheses ( ) or < > can be used to override the
	precedence rules of the binary operators.  All unary operators
	come before their operand, and all of them bind tighter than
	any binary operator.

	Numeric constants are of two types.  Floating-point constants
	consist of a mantissa part, containing one or more digits and
	possible a decimal point, optionally followed by an exponent
	consisting of one of the letters e, E, d, or D, an optional
	sign, and a decimal exponent, except that if there is no
	decimal point, or if there are no digits after the decimal
	point, the exponent portion must be present.  Integer constants
	are basically strings of digits.  The set of legal digits
	changes, depending on the base; there are four ways to specify
	the base:

		- Explicitly, by writing the base in decimal and
		  enclosing it in { } and placing it before the rest of
		  the number.  For example, {8}100 is the number
		  sixty-four.

		- The traditional way of specifying decimal, with a
		  trailing period.  Thus, 100. is one hundred.

		- With a prefix.  If the number begins with 0o or 0O,
		  it is taken in base 8; if 0t or 0T, base 10; and if
		  0x or 0X, base 16.  (But see the note on the next
		  paragraph.)

		- By default.  There is at all times a notion of the
		  default base; this base is used for numbers that do
		  not otherwise have a base specified.  It is the value
		  of the reserved symbol .base and can be changed by
		  assigning to .base with an assignment.  .base can
		  take on any value from 2 through 36; if the value is
		  greater than 16, the prefix notation for specifying
		  bases is disabled.  In bases above 10, the digits are
		  alphabetic letters; case is ignored.  The default
		  default base is 8.

The listing file optionally generated consists of each line of assembly
source code, prefixed with the value of . in six-digit octal and a
colon.  If the line came from a .INCLUDE file, a number is prefixed to
indicate the depth of nesting.  If anything is assembled into memory as
a result of the line, the assembled data follow.  (If the .LIST
directive is used to disable listing, an ellipsis is printed to
indicate the omitted lines.)

If you think the assembler does not conform to the above, I'd like to
hear about why, because if it doesn't it's a bug (though it may be a
bug in the description rather than the assembler :-).

					der Mouse

			old: mcgill-vision!mouse
			new: mouse@larry.mcrcim.mcgill.edu