## Slide 1
Red Hat Linux 5.2 on Alpha
Fred Deady

## Slide 2: Words To The Wise
“Installing Red Hat Linux on an Alpha system is slightly more complex than installing Red Hat Linux/Intel, mostly due to differences in machine architecture, and the variety of different models supported. In general, the main steps to a successful install are...”
From Alpha Installation Addendum Section 1.3

## Slide 3: Differences In Installation
Different Kit
SRM (System Reference Manual) vs ARC (Advanced RISC Console) vs AlphaBios
fdisk (BSD or Linux fdisk) vs Disk Druid
WEB Browser

## Slide 4: System Options ARC / ALPHABIOS
Family/Model Aliases MILO Kernel Boot
============= ======= ===== ====== =========
AS 600 ALCOR xlt-alcor alcor.gz alcor.img
AS 500 5/5xx BRET xlt-alcor alcor.gz alcor.img
AS 250 4/* M3 avanti xl.gz xl.img
AS 255 4/* LX3+ avanti xl.gz xl.img
PWS 433a or 433au MIATA miata miata.gz miata.img
PWS 500a or 500au MIATA miata miata.gz miata.img
PWS 600a or 600au MIATA miata miata.gz miata.img
Table Provided By Jay Estabrook

## Slide 5: System Options SRM
Family/Model Aliases Kernel Boot
============= ======= ====== =========
AS 1000 5/xxx MIKASA mikasa-s-5.gz mikasa-s-5.img
AS 1000A 5/xxx NORITAKE noritake-s-5.gz noritake-s-5.img
AS 600 ALCOR alcor-s.gz alcor-s.img
AS 800 5/xxx CORELLE noritake-s-5.gz noritake-s-5.img
AS 4000 DURANGO rawhide-s.gz rawhide-s.img
AS 4100 DODGE rawhide-s.gz rawhide-s.img
AS 1200 TINCUP rawhide-s.gz rawhide-s.img
AS 2100 5/xxx SABLE sable-s-5.gz sable-s-5.img
AS 2000 5/xxx SABLE sable-s-5.gz sable-s-5.img
Table Provided By Jay Estabrook

## Slide 6: Disk Setup
fdisk (DOS) or BSD - SRM Must Be BSD
BSD Style
  Create c Partition As Full Disk
  Create a Partition As Type Swap (128MB <)
  Offset Start Of Partition by 1-3 Cylinders
  Create b Partition As Type ext2
  At End of Install Use writeboot To Write Boot File

## Slide 7: BOOT TERMS
Boot Disks MILO, Boot, and Ramdisk
MILO (Mini Loader) Must Be On A DOS Partition
  Firmware That Sets Up The System For Booting
  Loads The Linux Kernel
  Not For SRM
aboot
  Writes Boot Block And Allows Booting From Disk
  SRM

## Slide 8: Where To Go For Help
www.linux.org
www.alphalinux.org
www.redhat.com
www.linuxmall.com
www.compaq.com/alphaserver/linux/