## Slide 1
IPv6 IP - The Next Generation Technology Update
Robert Watson
Compaq Computer Corporation
Digital European Technical Center
Sophia Antipolis, France
Tel: +33.4.92.95.51.42
WatsonRob@digital.com
DECUS US FALL 98
Wednesday 7th Oct 1998
1400-1520 Session Code: UN117
0930-1050 Session Code: NE018
Notes: 23
25
SLIDE 31.

## Slide 2: What is IPv6? Why is it needed? What is it’s Status?

## Slide 3: IP : The Internet Protocol
The “Language” of the Internet : IP
IP(v4) : 4th Version of the Internet Protocol
20+ Years Old
Incredibly Successful
Showing its Age

## Slide 4: Are there Problems to Solve?
1. Running out of Internet addresses ...
  Stops Internet growth for existing users
  Prevents use of the Internet for new users
  Internet Routing today is inefficient for ISPs and NAPs
2. System Management
  Labour intensive, complex, slow & error prone
  Need dynamic configuration for users (Mobile especially)
3. Security
  Data security needs have grown beyond the IPv4 infrastructure.
4. Bandwidth Reservation / Resource Metering
  e.g. video conferencing and other high bandwidth applications
  Need to schedule bandwidth for select time
  Pay or Charge only for what is used

## Slide 5: IPng (IP Next Generation) & IPv6 History
August 1990
  Projections indicated that the Internet Class B Address Space would be exhausted by March of 1994
Early 90’s: Short Term “Fixes” for IP Address Space
  CIDR : Classless Inter-Domain Routing
  Knock-On Impact on Routing Tables
1991 - 1992 : Work Starts on New Protocols
  More than 6 Different proposals were developed and presented
1993 :IETF formed an IPng working group
  To select the new protocol by consensus
1995 : IPv6 Selected
1996 : 6Bone started - First “real” IPv6 network http://www.6bone.net
1997 : First “real” Products
1998 : First “real” Deployments?

## Slide 6: IPv4 versus IPv6 Key Features
665,570,793,348,866,943,898,599 IPv6 Addresses / m2 of the Earth Surface
IPv4
IPv6

## Slide 7: IPv6 - Radical Internet Surgery
Every link must support of at least ~1500 bytes
Fragmentation at Routers is NOT permitted
Addressing
  All nodes must be able to create a Link-Local Address
  IPv6 addresses come from Providers not IANA
  You will no longer OWN your IP addresses like today
  IPv6 supports the dynamic renumbering
  No More Broadcast
  IPv6 requires Multicast Support and allows Anycast Addressing
Destination Options can alter a node’s Addressing State
Flow Label in the IP Header
Congestion Experienced bits in the IP Header (Still under discussion)
Notes: 16

## Slide 8: Myth or Reality Is IPv6 really going to happen? Good Question!
Check Out the
IPv6 Protocol in development since 6 years
Public domain ‘test’ network since 2 year
There are lots of “clever” solutions for IPv4 problems
IPv6 maybe part of the solution
What’s the Industry doing?

## Slide 9: IPv6 TODAY : 6Bone
A Public Testbed for IPv6 and it’s related protocols
To Assist in the Evolution and Deployment of IPv6
IPv6 Sites are connected to each other
  over IPv4 (IPv6 tunnelled in IPv4)
  over (some) native IPv6 links

## Slide 10: IPv6 TODAY Growing World-wide
302 Registered IPv6 Sites on the 6Bone (August 1998)
  US and Canada 95 (87) Sites
  Europe 160 (128) Sites
  Asia Pacific 43 (32) Sites
  Latin America 1 (0) Sites
  Counties 35 (32)
  Registered Contacts 326 (226)
  ( ) Values in March 1998

## Slide 11: IPv6 TODAY 35 Countries on the 6Bone
http://www.6bone.net/6bone_countries.html
AT-Austria
AU-Australia
BE-Belgium
BG-Bulgaria
BR-Brazil
CA-Canada
CH-Switzerland
CN-China
CZ-Czech Republic
DE-Germany
DK-Denmark
ES-Spain
FI-Finland
FR-France
GB-Great Britain
GR-Greece
HK-Hong Kong
HU-Hungary
IE-Ireland
IT-Italy
JP-Japan
KR-Korea
KZ-Kazakhstan
LT-Lithuania
MX-Mexico
NL-Netherlands
NO-Norway
PL-Poland
PT-Portugal
RO-Romania
RU-Russian Federation
SE-Sweden
SG-Singapore
SI-Slovenia
SK-Slovakia
TW-Taiwan
US-United States

## Slide 12: IPv6 TODAY 28+ Implementations on the 6Bone
HOST Implementations
Compaq’s OpenVMS
Compaq’s Digital UNIX
FTP Software Win95
Hitachi NR60
IBM AIX
Inria BSD
Linux
SICS HP-UX
Sun Solaris
UNH for BSD
NRL for BSD
WIDE Hydrangea for BSD
WIDE ZETA for BSD
WIDE v6d
Router Implementations
Bay
Cisco
Cabletron
Fujitsu LR550
Hitachi NR60
Inria BSD
Linux
Merit MRT
NRL for BSD
Telebit
WIDE Hydrangea for BSD
WIDE ZETA for BSD
WIDE v6d

## Slide 13: Technical Changes
IPv6 Header
  Design Philosophy
  IPv6 Extension Headers
Extension Header
Header Performance Enhancements

## Slide 14: IPv4 Header 20 octets + options : 13 fields, including 3 flag bits
0 bits
31
Ver
IHL
Total Length
Identifier
Flags
Fragment Offset
32 bit Source Address
32 bit Destination Address
4
8
24
16
Service Type
Options and Padding
Time to Live
Header Checksum
Protocol
Removed
Changed

## Slide 15: IPv6 Header 40 Octets, 8 fields
0
31
Version
Class
Flow Label
Payload Length
Next Header
Hop Limit
128 bit Source Address
128 bit Destination Address
4
12
24
16

## Slide 16: IPv6 Extension Headers
Hop-by-Hop Options **
  Jumbo Payload
Routing **
Fragmentation
Destination Options
  Mobile Binding Update
  Anycast Address Dynamic Update
Authentication (RFC 1826)
Encapsulating Security Payload (RFC 1827)
No Next Header
** A Router is likely to need to process only these Extension Headers

## Slide 17: Extension Headers
IPv6 Header
Next = TCP
TCP Header
IPv6 Header
Next = Routing
TCP Header
Routing Hdr
Next = TCP
IPv6 Header
Next = Routing
TCP Header
Routing Hdr
Next = Frag
Application Data
Application Data
Fragment Hdr
Next = TCP
Data
Frag

## Slide 18: IPv6 Header Performance Wins Layout
Fixed Size IPv6 Header
  Unlike IPv4 - Options not limited at 40 bytes
Fewer fields in basic header
  faster processing of basic packets
64 Bit Alignment Header/Options
Efficient option processing
  option fields processed only when the option present
  Processing of most options limited performed only at destination

## Slide 19: IPv6 Header Performance Wins Processing
Remove Checksum from Network Layer
  Datalinks are more reliable these days
  Upper Layer (e.g. TCP, UDP, ICMPv6) Checksums are now Mandatory
No Fragmentation in the network
  More router cycles available for forwarding packets
  Easier to implement in Silicon
  Easy for Layer 3 Switching of IP

## Slide 20: IPv6 Addressing Architecture

## Slide 21: IPv6 Address Scope
Link-Local
Site-Local
Global
Scope
  Link Local
  Site Local
  Global
  RFC 2373

## Slide 22: IPv6 Addresses
Unicast
  The address for a Single Interface
Multicast
  The address of a Set of Interfaces
  A packet is delivered to ALL interfaces identified by this address
  Predefined
    All Nodes, All Routers, DHCP Server/Relay-Agent, Solicited-Node)
Anycast
  The address of a Set of Interfaces
  A packet is delivered to ONE OF the interfaces identified
  IPv6 Mobile Anycast address

## Slide 23: Text Representation of Addresses
Basic Format
  8 groups of 16 bit Hex Values Separated by :
    5F15:ABCD:1234:5678:9ABC:0123:4567:89AB
    1080:0:0:0:8:800:200C:417A
Compressed Format
  Suppress Leading 0’s
  :: Replaces multiple groups of 0’s
  Only one :: permitted per address
    FF01:0000:0000:0000:0000:0000:0000:43
    becomes FF01:0:0:0:0:0:0:43
    becomes FF01::43

## Slide 24: IPv6 Address Structure
3FFE:0301:DEC1::
Prefix
0A00:2BFF:FE36:701E
Interface ID
Prefix Representation 3FFE:0301:DEC1::/64
An IPv6 Address is formed from a combination of the:
Notes: .

## Slide 25: Aggregatable Global Unicast Address Structure
Interface ID
SLA ID
NLA ID
TLA ID
FP
3
13
32
16
64
(001 + 1FFE)
3FFE
0301:DEC1
0000
0A00:2BFF:FE36:701E
3FFE:0301:DEC1:0000:0A00:2BFF:FE36:701E
FP = Format Prefix
TLA = Top-Level Aggregation Identifier
NLA = Next-Level Aggregation Identifier
SLA = Site-Level Aggregation Identifier
Public Topology
Site Topology
Address format proposed for IPv6 nodes connected to the Internet
  Designed to support address aggregation

## Slide 26: EUI-64 Based Interface ID
08
00
2B
36
1E
70
IEEE 48Bit MAC Address
Company ID
Manufacturer Data
08
00
2B
36
1E
70
FF
FE
Expand to an EUI-64
0A
00
2B
36
1E
70
FF
FE
Invert the Global Bit
IPv6 Interface ID’s based on EUI-64
    Used on UniCast and AnyCast Address
    With Format Prefix range 001 thru 111
  Constructed from a Global Token
    e.g. IEEE 48bit MAC Address
    With the “global” bit inverted

## Slide 27: Renumbering
Renumbering IPv6 Hosts is easy
  Add a new Prefix to the Router
  Reduce the Lifetime of the old prefix
  As nodes depreciate the old prefix the new Prefix will start to be used for new connections
Network Renumbering Issues
  How often will this happen?
  How quickly will this happen?
  Impact on DNS
    Addresses in DNS need to be updated following renumbering
  Long lived TCP connections
    Should they survive renumbering of the source or destination host?

## Slide 28: Comparison with IPv4
Neighbor Discovery =
IPv4 ARP + ICMP Router Discovery + ICMP Redirect
Provides improvements over IPv4:
  Router Discovery is part of the base protocol set
  Router advertisements carry link-layer addresses
  Router advertisements carry prefixes for a link
  Router advertisements enable Address Autoconfiguration.
  Routers can advertise an MTU for hosts to use on the link
  Neighbor Unreachability Detection is part of the base
  Placing address resolution at the ICMP layer makes it possible to use standard IP authentication and security mechanisms

## Slide 29: DNS changes for IPv6
RFC 1886 DNS Extensions to support IP version 6
DNS AAAA records
  New Resource Record Type to store IPv6 Address
New Domain
  Support Lookups based on IPv6 Address
  Inverse lookup (Address -> Hostname)
    Rooted at IP6.INT.
    <nibble>.<nibble>....IP6.INT.

## Slide 30: Dynamic Update to DNS
RFC2136
Provides the ability for hosts and servers to dynamically update resource records
  Security is Important!
    DNS now has Secure Records!
  Dynamic DNS can be used for both IPv4 and IPv6

## Slide 31: DNS AAAA Record : New Proposal
The DNS name and address record can be distributed based on the canonical parts of the address for IPv6
  e.g. a DNS name like foo@company.country
  Really has 2 DNS zones associated it : country & company
Each zone has its own record for the name and is defined as a DNAME record
  When one wants the IPv6 address for foo@company.country you must request the entry for .country and the address for machine foo at .company
  and concatenate the records to obtain the actual IPv6 address
Advantages
  Separates “who you are” from “where are you connected to”
  Easy renumbering e.g. when changing ISP

## Slide 32: IPv6 - IPv4 Interworking

## Slide 33: IPv4 Address Mapping
IPv4-Compatible IPv6 Address
  refers to an IPv6/IPv4 node that supports automatic tunneling
    Reachable using the IPv4 Routing Infastructure
  0000:0000:0000:0000:0000:0000:0000:<IPv4 Address>
  ::12.22.33.44
IPv4-Translatable IPv6 Address
  refers to an IPv6-capable node that does not support automatic tunneling
    Reachable using the IPv4 Routing Infastructure
  0000:0000:0000:0000:0000:FFFF:0000:<IPv4 Address>
  ::FFFF:0:10.21.32.43
IPv4-Mapped IPv6 Address
  a node that is not IPv6-capable
    Reachable using the IPv4 Routing Infastructure
  0000:0000:0000:0000:0000:0000:FFFF:<IPv4 Address>
  ::FFFF:10.21.32.43

## Slide 34: Hybrid IP Stacks
IPv6
IPv4
TCP
RFC 1933
IPv6
TCP
TCP
IPv4
IPv4 Applications
  Restricted to IPv4 Addresses
Communication with IPv4 Hosts
  Hybrid Stacks

## Slide 35: Automatic Tunnel (1)
Source Host A
IPv4 B
IPv6 B
Data
Destination Host B
IPv6/v4
IPv6/v4
IPv4 only
Router R1
Router R2
IPv4 B
IPv6 B
Data
IPv6 B
Data
IPv4
Network
IPv6 only
IPv6
IPv4

## Slide 36: Automatic Tunnel (2)
Source Host A
IPv4 B
IPv6 B
Data
IPv6/v4
Destination Host B
IPv6/v4
IPv4 only
Router R1
Router R2
IPv4
Network
IPv4 only

## Slide 37: Configured Tunnel
IPv6 B
Data
Source Host A
IPv4 R2
IPv6 B
Data
Destination Host B
IPv6/v4
IPv4/v6
Router R1
Router R2
IPv6 B
Data
IPv4
Network
IPv6 only
IPv6 only

## Slide 38: IPv6 ’ification of IPv4 Applications
Informational RFC 2133 gives changes to socket library for IPv6
Design goals
  Minimal changes
  IPv4/IPv6 transparency
What’s Changed?
  Data Structure
  sockaddr_in becomes sockaddr_in6
  Name to Address Translation
    gethostbyname & gethostbyaddr Still Exists
    gethostbyname2 Added to support new Address Family

## Slide 39: Other ways of getting There from Here

## Slide 40: IPv4/IPv6 Interworking Tools
Network Address Translation (NAT)
  Manipulates Addresses
  Blocks use of IPv4 / IPv6 End-to-End Security
  Breaks current Mobile-IP Mechanism
Application Layer Gateways (ALG)
  Requires knowledge of applications which use addresses
  New Applications may require ALG changes
  Unpredictable Application Failure
Translators
  Complex : but under consideration
No-NAT
  A new Suggestion

## Slide 41: NAT: Network Address Translation
Advantages of NAT
  Requires no changes on host or internal routers
  no need to train network administrator on new protocols
Disadvantages of NAT
  Performance hit
    NAT router / gateway has to rewrite addresses
    update transport checksums and applications data
  NAT box needs prior knowledge
    all address-carrying applications and protocols
    Impact on new application introduction
  Cannot use more than one site entrance/exit router
  Breaks IP mobility, end-to-end security
  Single point of failure
But despite all this - NAT is widely use today!

## Slide 42: SIT vs SIIT
SIT
  Is for dual IPv4/IPv6 hosts
  Which need to interoperate with both dual and IPv4-only hosts
  Both IPv4 and IPv6 addresses are assigned to the dual stack hosts
SIIT
  As the pool of globally unique IPv4 addresses becomes smaller and the Internet grows larger
  there will probably be a strong need to take advantage of the large IPv6 address space while avoiding that every new node has to have a permanently assigned IPv4 address
  SIIT solves this dilemma

## Slide 43: Stateless IP/ICMP Translator (SIIT)
SIIT specifies a mechanism by which IPv6-only nodes can inter-operate with IPv4-only nodes
  By having the IPv6-only nodes acquire a temporary IPv4 address
  The IPv4 address is used as an IPv4-compatible IPv6 address
  The packets travel through a stateless IP/ICMP translator
  The stateless IP/ICMP translator will
    translate the packet headers between IPv4 and IPv6
    translate the addresses in the headers between IPv4 addresses on one side and IPv4-compatible or IPv4-mapped IPv6 addresses on the other side

## Slide 44: No-NAT An alternative to the traditional NAT
IPv4 Host looks up
the IPv4 address of the target
which currently has only IPv6 address
IPv6
IPv6
The
Internet
DHCPv6
Server
DNS
Server
IPv4 Host
IPv4 Network
IPv6 Host
No-NAT capable DNS finds AAAA IPv6 Address
Signals DCHPv6 to “reconfigure” the target
DCHPv6 reconfigures target
with temporary IPv4 address
Direct end-to-end IPv4 Communication
SECURE End-to-End IPv4 Path

## Slide 45: Mobile IPv6

## Slide 46: Mobile IPv6 Node Terminology
“Home Agent”
Correspondent
Node
“Home”
“Mobile” Node
“At Home”
“Home Address”
IPv6 Mobile Node
Home Agent
Correspondent Node
“Mobile” Node
“On the Road”

## Slide 47: Mobile IPv6
“Home Agent”
Correspondent
Node
“Home”
Normal Communication
“Mobile” Node
“At Home”
“Home Address”
“Mobile” Node
“On the Road”
“Care-Of Address”
Binding
Update
Mobile Node
  Establishes Home Address
  Leaves Home Network
  Auto Configures Care-of Address
  Sends Binding Update to Home Agent

## Slide 48: Mobile IPv6
“Mobile” Node
“On the Road”
“Home Agent”
Correspondent
Node
Normal Communication
“Home”
“Home Address”
“Care-Of Address”
Packets Sent to Home Address...
  Delivered to Home Network Using standard IP routing
  Intercepted by Home Agent
  Encapsulated, delivered via tunnel to Care-of address

## Slide 49: Mobile IPv6
“Home Agent”
Correspondent
Node
“Home”
Binding
Update
Direct Communication
to “Care of” Address
Mobile Node
  Sends Binding Update to all Correspondents
    Packets may be sent direct to Care-of Address
    Use Routing Header (Intermediate Routing Point)
“Mobile” Node
“On the Road”

## Slide 50: What happens when... A Mobile Node is actually Moving!
Mobile Nodes can be
  Stationary
    but currently not at Home
  Moving
    from one foreign link to another
When Moving from Link to Link
  Acquire a new Care-Of address when arriving on a new Link
  Inform their “Home Agent” and all current “Correspondents” of the new Care-Of Address
  Optionally inform a router near the previous Care-Of address of their new location so as to catch in-flight packets to the old Care-Of address

## Slide 51: Comparison with IPv4
Mobile IPv6 is fully integrated into the rest of IPv6
No “Foreign Agent”
  IPv6 Neighbor Discovery and Address Autoconfiguration allow hosts to operate in any location without any special support
No single point of failure (Home Agent)
More Scalable : Better Performance
  All Links are IPv6 Mobile-ready from Day-one
  Less traffic through Home Link
  Not dependent on one or two busy Home Agents
  Traffic Optimisation - Less redirection / re-routing
  Most packets to a mobile node are tunneled
    IPv4 makes use of encapsulation
Relies on mandatory parts of the base protocols

## Slide 52: Can IPv6 be used Today?

## Slide 53: IPv6 Today?
IPv6 is a proposed replacement for IPv4
  IPv6 Solves many of the problems caused by the IPv4 success
  and more...
Will the whole Internet get upgraded any time soon?
  No way!
Are some “green field” sites considering use of IPv6
  Yes!
Will bits of IPv6 appear in production use soon?
  Almost certainly Yes
Parts of IPv6 are HERE today
  and offer useful features for TODAY’s networks

## Slide 54: Core specs to Draft Standards
The IPv6 core specs that have moved to draft standard
As of IETF August 1998
  IPv6 Base Protocol Specification and Architecture
  IPv6 Internet Control Messages Protocol
  IPv6 Path MTU Discovery
  IPv6 Neighbor Discovery for Hosts and Routers
  IPv6 Stateless Address Autoconfiguration

## Slide 55: Where are we now?
IPv6 is "cooked"
The core specifications achieved Draft Standard status
Will most likely move to Full Standards
Check in 6 months from now (Feb 1999)
What will happen then?
  Great Question
  Many people are trying to predict the future
Actual Progress
  The first two ISPs to announce IPv6 Network Access Points (NAPS) on their networks were MCI USA and UUNET UK

## Slide 56: What are the IPv6 Carrots?
Increased Address Space
Performance
  Optimised for 64bit architecture
  Better Host and Router Internet Platform Performance
Plug and Play
  Address Autoconfiguration (Stateless and Stateful)
  Dynamic Renumbering of Networks
Security
  Mandated Standard
  Integrated & Flexible.
  Authentication and Encryption

## Slide 57: Deploying New Workgroups
The
Internet
IPv4/IPv6
Drop in some IPv4/IPv6
Hybrid Servers
IPv6
IPv6
IPv6
IPv6
IPv6
IPv6
IPv6
IPv6
Then add in IPv6 Workstations
and Clients at will
IPv6
IPv6
IPv6
IPv6
IPv6
IPv6

## Slide 58: Tunnels can be used to Link Expanding IPv6 Intranets
IPv6 nodes in different Intranets can be
linked by IPv6 over IPv4 Tunnels
The
Internet
IPv6
IPv6
IPv6
IPv6
IPv6
End to End IPv6 Security

## Slide 59: Putting the IT Director back in control
IPv6 Address Scope
  Some addresses are GLOBAL
  Others are Link or Site LOCAL
  Addressing Plan also controls network access
Configuration Policy Control
  Stateless
  Stateful (DHCPv6)
Routers Dictate the Configuration Policy
  Router Managers are “in control” of the network
  Routers also dictate MTU size for the Link

## Slide 60: Security
IPv4 relies on ‘add on’ Security
  There’s no network level security
IPv6 Provides Network Layer security
  Standardised and Mandated
  Authentication
  Encryption
Notes: 11

## Slide 61: IPv6 Security Native Network Layer Security
IPv6 mandates the ability to do end-to-end network layer security
  Protects DHCP
  Protects DNS
  Protects IPv6 Mobility
  Protects End-to-End traffic over IPv4 networks

## Slide 62: Next wave of IPv6 Standards
Focus on Transition and Interoperation IPv4:
  DHCPv6 (should be proposed standard by Oct 98)
  RIPng (proposed standard now)
  BGP4 for IPv6 (enroute to proposed standard)
  IPv6 Mobility (proposed standard by Oct 99)
  Router Renumbering (enroute to proposed standard)
  DNS AAAA Record (enroute to proposed standard)
  Multicast Listener Discovery (enroute to proposed standard)
  OSPF for IPv6 (proposed standard in process)
  IPv6 Header Compression (enroute to proposed standard)

## Slide 63: Who can help you get there?
(this is the marketing bit!)

## Slide 64: Compaq + Alpha + 64 bits + DIGITAL UNIX & OpenVMS
IPv6 family of protocols optimised for 64 bits
  Addresses are 128 bits long (two 64 bit words)
  Alpha is 64 bit processor
  64 bit implementation offers faster routing than 32 bit systems
Notes: 21

## Slide 65: Compaq + Alpha + 64 bits + DIGITAL UNIX & OpenVMS
Some IPv6 features compute-intensive (e.g. authentication and encryption)
  Alpha world’s fastest processor
  Ideal server platform for secure applications such as finance, defense, law enforcement, E-commerce, or medical records
Notes: 23

## Slide 66: Compaq + Alpha + 64 bits + DIGITAL UNIX & OpenVMS
IPv6 enables demanding real-time applications (e.g. audio and video conferencing)
  AlphaServer is world’s fastest server
  64 bit hardware and software enable Very Large Memory (VLM) applications for fast response time (e.g. Oracle video server)
Notes: 24

## Slide 67: Compaq IPv6 Pointers and Contacts Everything you need for IPv6
Compaq IPv6 Home Page http://www.digital.com/info/ipv6/
Technical Journal (Vol 3 No 8) http://www.digital.com/dtj
Prototypes running today
  IPv6 for Compaq’s Alpha DIGITAL UNIX - DIGITAL UNIX V4.0d
  IPv6 for Compaq’s Alpha DIGITAL OpenVMS - OpenVMS V7.1 & V7.2
  See the IPv6 Home Page for prototype access information
Compaq IPv6 Contacts:
  UNIX Business, Dave Carter dcarter@zk3.dec.com
  UNIX Engineering, Jim Bound bound@zk3.dec.com
  OpenVMS Business, Bette Ruyffelaert ruyffelaert@mail.dec.com
  OpenVMS Engineering, Matt Muggeridge matt.muggeridge@digital.com

## Slide 68
Compaq Computer Corporation
© 1998
Notes: 23
25
SLIDE 31.