- 1 -







                                        FLY8

                                  Flight Simulator

                                  _E_y_a_l _L_e_b_e_d_i_n_s_k_y

                              eyal@ise.canberra.edu.au






            11..  IInnttrroodduuccttiioonn
            This program is a flight simulator. It puts more emphasis on
            the dynamics than on the cosmetics: just wire-frame. It  can
            run on any machine but a 386DX is the minimum for any decent
            performance. A fast video controller is a boon as  the  pro-
            gram,  when  running  on a 386DX/40Mhz, spends 70-80% of its
            time pushing pixels. On non-intel machines you can  try  and
            see if it is fast enough...
            The  program  was  written  for  fun.  I borrowed ideas from
            everywhere and hope to hear some more. The basic  design  is
            based  on  a  program  I wrote more than 20 years ago at uni
            (the Technion). I had an excellent coach (Danny Cohen) and I
            still have fond memories of those times. But now my computer
            has more than 24Kbytes of memory! so Fly8 is  written  in  C
            (Fly8  was the name of the last version of the original pro-
            gram dated 12-JAN-1974, it was written in PDP15  assembly  -
            macro15 - for a VT15 graphics processor).
            The actual purpose of the program was to give me an opportu-
            nity to experiment with various aspects  of  flight  simula-
            tion, but mostly with (1) the HUD symbology (or, more gener-
            aly, with man-machine interaction) and (2) the  studying  of
            basic  aerodynamics (as well as general real time simulation
            techniques). This explains why there are so many HUD options
            and  such a proliferation of flight dynamics models, as well
            as why the simulation parameters are user definable as input
            files at run time. Of course, the experimental nature of the
            program means that it must be distributed in source form.
            On the  PC  the  basic  screen  drawing  uses  the  standard
            Microsoft  graphics library. It is OK but not very fast; the
            main advantage is that it will support most video  adapters.
            The  fast  graphics  driver was built from the routines from
            DJGPP with much personal additions. The flight dynamics  was
            influenced  by  an SGI program I saw and ACM. The timer rou-
            tines come from a microsoft journal article, the  user-input
            routine (notice how you can use arrow keys etc? use up-arrow
            to retrieve history.. I will document it one day) comes from
            DDJ (or was it CUJ? author name is Bob Bybee). Well, I avoid
            re-inventing wheels unless it is fun. The  program  compiles


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2



            with Microsoft C, Borland C, gcc on a friends Amiga, Sun and
            Linux and I hope on other platforms; it  is  written  to  be
            portable.  It runs under MSDOS, MSWindows, Amiga and unix/X-
            Windows.
            What? what? WHAT? you want to see some action? OK. just skip
            to the next chapter then come back.
            The full set of commands is detailed in the 'commands' chap-
            ter. Here we will look at the program areas in general.
            There are two rather distinct kinds  of  commands  that  one
            uses:  commands  that drive (fly) the game and commands that
            configure, set options and so on (which are used  with  less
            urgency).  It  was  attempted  to get the important commands
            into the keyboard (a one keystroke command) while the others
            go  into  the  main menu system (accessed with the Esc key).
            Some of the urgent commands may bring up a  menu  which  you
            may ignore if you know the keystokes.
            The  urgent commands will control the vehicle flight and the
            other subsystems (radar, HUD, HDD, weapons etc.).  You  will
            notice  early that the program lacks the traditional instru-
            ment panel: it is intended to be driven  from  the  HUD  and
            other digital displays.
            The vehicle is also driven by a pointing device (a mouse or,
            preferably, a joystick). It will run off the keypad when you
            have  no such device.  The pointer is used only for steering
            control although the buttons  can  be  mapped  to  auxiliary
            functions (by default both 'fire').
            The  display area is typicaly divided into the main view and
            a number of secondary Head Down Displays (HDD).  The  design
            has  a dozen or so on board instruments that generate visual
            data; you select which ones should  be  displayed  on  which
            HDD.  The main view is what you see through the cockpit. The
            HUD can be overlaid onto this view (as is the  case  with  a
            real  plane).  Other  data may also be shown here for conve-
            nience.
            One other instrument is designated as an alternate main view
            (use  the 'v' command to see it). The 'windows' menu handles
            the screen format and configuration.
            The program generates various messages  as  it  goes  along,
            these  will  appear at the bottom of the main view and stack
            up. Each message has a time-out for deletion but you can use
            'c'  to  clear the lot. When the program needs user input it
            will open a prompt line at the very bottom of the main  view
            (in  magenta  color)  where your data will show. You can use
            the normal editing keys while entering data here -  previous
            entries  are  accessible with the up/down arrows. See 'input
            line editing' later.
            You may find some of the commands/options  strange  (if  not
            outright  insane);  this  will  be  related  to  my taste or
            (mostly) to much history and quick fixing that did not  com-
            pletely  settle  yet.  I have looked at other programs (like
            F3, JF2, ACM and SGI f.s.) but this was after the first ver-
            sion of this program was finished, so some good ideas missed
            the bus this time. In the future I hope to polish  the  user
            interface  (especialy  after  other people get to use it and
            express an opinion).


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _3



            Being as the program is still evolving you  will  find  some
            areas less complete than others. I hope that there is enough
            of it to make it useful. I expect to see  contributions  (of
            ideas  and  code)  from  other  people;  I  will continue to
            develop the program (at least for a while) and would like to
            see it take it's own path in life [heavy stuff :-)].



            22..  QQuuiicckk ssttaarrtt
            In  this  chapter the symbol '@' is used to denote the Enter
            key. This will give you a quick feel for what the program is
            like.  With the program installed, type
                 ffllyy --zz55
            This  starts  the program in a demo setting and is useful to
            see if all is OK and also great as a screen blanker :-)
            If the fly.ini options are correct then your plane will take
            off  and  start  looking  for action. Some messages are dis-
            played during startup - these will disappear after  a  short
            while.  The  screen will show a simple view of the runway, a
            ground grid (in gray) and an overlaid HUD.
            If there is no picture, try hitting 'Enter'. Then try  'Esc'
            'x'  'y'.  If  no  luck then reboot (I guess). Now check the
            fly.log file which may have an error message in it.  It  was
            found  that  with  some  accelerator cards the program hangs
            (don't know why, I use the MicroSoft C graphics library  and
            most  advanced cards should emulate VGA). Try installing the
            correct video VESA bios.
            Do not run this program in a  dos  window  of  MSWindows  or
            OS/2,  use  the MSWindows version for MSWindows (although it
            probably will work fine, there is a chance of  locking  your
            machine up by not doing so).
            The scene will include you and 5 other planes (drones). Your
            auto-pilot will track and shoot the drones. As they are shot
            down,  new  ones  take  off.  To  take control back from the
            autopilot hit Shift-C. Now use  the  joystick  (or  whatever
            input device you choose) to fly the plane. One mouse or joy-
            stick button shoots (same as F1). When the target is in  the
            correct  position  the autopilot will shoot (unless you tell
            it not to with 'k'). The idea is to fly your plane  so  that
            the  target  is inside the aiming reticle (the small circle)
            and then shoot. A SHOOT cue will flash when your aim is cor-
            rect.
            You  may  want  to know the current settings (like throttle,
            flaps   etc.)    Turn   on   the   'misc'    display    (Esc
            hud/options-2/misc).  The  'Esc' key activates the menu sys-
            tem. most selections can be used as a short sequence of  the
            associated letters; the last sequence can be entered as Esc-
            u-2-m-Esc. The hud menu is also directly  available  as  the
            'u' command.
            This  how  you  fly  the plane: moving the joystick sideways
            will start the plane rolling. The further you move the stick
            the faster the roll. Once you center the stick the roll will
            stop. In order to fly level you  need  to  roll  either  way
            untill you are level and then center the stick.


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _4



            Moving  the  stick  away  from you will puch the nose of the
            plane DOWN, pulling the stick back will pull  the  nose  up.
            When  the  stick  is  centered  the plane will maintain it's
            climb angle.
            So far we roll and pitch but we did not yet turn.  In  order
            to turn one needs to use both controls. To turn right, first
            roll to the right, then pull the plane 'up'; at  this  point
            'up' is actualy 'right'. Remember that the joystick controls
            the plane relative to itself (the pilot if you wish) and NOT
            relative  to  the ground. Once you turn in the desired dirc-
            tion you can roll left to resume level  flight  in  the  new
            heading.
            Because  the plane has weight, if you roll and start turning
            the plane will also start falling down (the wings no  longer
            support  the  full  weight of the plane) so a realistic turn
            will call for a moderate roll and not a full 90 degrees. The
            harder you will pull the stick, the faster you will turn and
            the larger roll you should execute to maintain level  during
            the turn.
            You  probably  do  not want more instructions at this 'quick
            start' section, not to mention that I never  flown  a  plane
            and  am not qualified for much in the way of flight instruc-
            tion. Any volunteers for writing a flight manual chapter.
            Knowing how to fly the plane is not enough, you also need to
            know  how  to  partcipate  in  the game (fight). Actualy, in
            order to start winning you will need to be able to fly with-
            out  thinking,  you  will  need your logic powers to control
            your situation and plan your moves.   Your  strategy  is  to
            avoid  being hit and try and kill all enemy planes. There it
            is, as simple as can be. I wonder why people fill books with
            chat about Basic Flight and Air Combat Maneuvering :-)
            Now  a  quick look at controlling other equipment. For take-
            off, release the wheel brakes (b) and set full throttle  (1)
            or  even  light the afterburner (a few hits on the '.' key).
            You may want to set the flaps (a few ']',  then  reset  with
            '[') but it is not necessary. At a speed of 150-200 pull the
            nose up gently (not more than 10-15 degrees)  and  wait  for
            takeoff.  After you gain some high (but rather soon) retract
            the landing gear (g). There you are in the air. Do not try a
            sharp  turn  too  soon as you may loose altitude and hit the
            ground, unless you are exoerienced with this sort of  thing.
            To  land,  reduce  speed and approach the runway as a steady
            descent. Just before touchdown reduce  the  descent  to  the
            bare  minimum (don't forget to lower the landing gear (g) in
            time but not too early).  Once  on  the  ground  engage  the
            speed-brakes (+) and reverse (just hit 3 until you have -100
            power showing). When your speed is  low  enough  engage  the
            wheel  brakes  (b) and towards the end idle your engines (0)
            and release the speed brakes (+). Once you are stationary on
            the  ground  with the engine idle your fuel will start to be
            replaced and finally your wepons will be replaced  and  your
            damage will be reset.
            When flying, use 'r' to switch the radar on and off, use 'w'
            to select your weapon and use 'v' to switch to a map view of
            the  world (with you at the center) and back to normal view.


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _5



            This should do you for starters.
            While we are here, do 'Esc' 'i' 'Enter'. Some  numbers  will
            show  at  the top of the screen. The first is the total time
            (in milliseconds) for one frame, the second  is  the  video-
            drawing time. If the total time goes over 100 often then you
            should buy a faster machine (actually, if it is  the  second
            numbers  that dominates, a faster video card may be a better
            investment). If it stays under 60-70 then all is fine.
            On MSDOS, if you have a TsengLab ET4000 based card then  try
            running
                 ffllyy ddvvggrrffaasstt::eett44kk VVggrreett44kk mm880000xx660000xx225566 zz55
            and if it works you will notice the speedup. Other cards are
            supported but only the ET4000 and S3 got any testing. Follow
            the instructions in the readme for other cards. The standard
            Microsoft  library  does  not  do  double  buffering   above
            640x350x16  (even  in  C8);  don't  know why - the memory is
            there. You may wish to edit the  file  'fly.ini'  with  your
            preferred  setup  so that you will not need to specify it in
            the future.

            To exit hit 'Esc' 'x' and 'y'.



            33..  IInnssttaallllaattiioonn
            On most environments all you need to do is unpack  the  dis-
            tribution  archive  into your prefered directory and you are
            set. Refer to the README file for specific instructions, you
            will  peobably want to enable support for your graphics card
            (on MSDOS).



            44..  CCoommmmaannddss RReeffeerreennccee
            Fly8 commands are one keystroke each but  some  expect  some
            data  or options to follow, which may bring up a prompt or a
            menu.
            Some commands are used only when the 'keypad' is selected as
            the  pointing  device for flying. Otherwise the commands are
            grouped here by their physical location and organized alpha-
            betically.
            The  program  usually  runs  with  the NumLock engaged which
            means that the keypad keys duplicate the digits 0 through  9
            and the period '.'.
            There  is  no  current facility to redefine the usage of the
            keys but the keyboard macros can be of use here.  See  under
            F7/F8.


            44..11  AAllpphhaabbeettiicc KKeeyyss
            Most  commands  toggle  their  function  on/off,  some cycle
            through modes.
            A         select aiming reticle mode.  (cycles)   [obsolete]
                      This  is  used for experimenting with various LCOS
                      formulae and will be gone once it settles down. At


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _6



                      this  point  the  calculations are based on linear
                      motions, it should be modified to  follow  an  arc
                      instead.  The  setting  is  shown  as  'Mn' in the
                      'modes' screen in the 'radar' part.
                      0    no acceleration correction
                      1    0.5 second correction
                      2    1.0 second correction
                      3    t/2 seconds  correction  (t=time  to  impact)
                           (default)
                      4    t*t/2 seconds correction
            b         Wheel  brakes (toggle). Can be applied at any time
                      but only effective when on the ground. In  reality
                      these  should  not  be operated at high speed (use
                      speed brakes and reverse thrust for  initial  slow
                      down).
            c         Clear text area. By now there is no text area any-
                      more. The only messages expected are the  'paused'
                      and  'resumed'  which may litter the screen.  This
                      command also removes all outstanding messages.
            C         Chase the locked target (toggle) This is the auto-
                      pilot mode. If there is no target (or the radar is
                      turned off) then the plane will wander around  the
                      airport  perimeter.  If  there  are ground targets
                      then these will  be  chased  and  the  plane  will
                      crash!  This mode is activated by the command line
                      option '-z'. If the  kill-mode  is  enabled  ('k')
                      then the auto-pilot will fire at the target.
            D         Descend the parachute. After you eject it may take
                      a while to get to the ground.  You  can  pass  the
                      time  by  looking  around (use the arrow and F5/F6
                      zoom keys), or you can jump to the  landing  phase
                      with  this  command. If you land before your plane
                      crashes then you will have to wait (a WAIT  notice
                      will be shown).
            E         Eject.  If  your  plane is not dead, your ejecting
                      will send it crashing.
            f         Select radar target-acquisition mode (cycle). Con-
                      trols the manner by which the radar selects a tar-
                      get as explained later in the relevant chapter.
            g         Landing gear up/down (toggle). You can't raise the
                      gear while on the ground.
            h         Help (also ?)
            i         Intelligence:  identify  all visible targets (tog-
                      gle) This is what makes this program  better  than
                      the real thing... in this mode all visible targets
                      are identified even when outside of the HUD  area.
                      You need to have HUD data mode enabled to get info
                      about the targets.
            j         Radar sees only real pilots (ignores drones) (tog-
                      gle).  The  program can generate drones for target
                      practice. If you want the radar  to  ignore  these
                      and  only  show  (and select) real planes then use
                      this command.  There are other  pilots  only  when
                      you are networked.



            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _7



            k         Kill-  auto shoot when ready (toggle). When a tar-
                      get is in range and in correct position the  auto-
                      pilot  will  flash  a  SHOOT cue. In this mode the
                      selected weapon will be fired at this  point.  The
                      radar  must  be  active  with a locked target (you
                      should see a piper).
            l         Lock target (toggle) The radar can operate in  two
                      modes,  either  it  continuously  selects a target
                      according to  the  designated  target  acquisition
                      mode or it stays locked on the current one. In the
                      locked mode, the first  selected  target  will  be
                      locked on and no more searching will be done. When
                      not locked the target designator will be shown  as
                      a  broken  box.  You  can  use the un-lock command
                      (usually attached to one of the buttons and to the
                      space-bar)  to  release  the  current  target  and
                      acquire a new one.
            m         Show  general  program   status.   (toggle)   This
                      replaces  the numerous mode indicators that planes
                      have.
            o         Observer  select.  See  the  world  from   another
                      object's  point  of  view.  Also useful for just a
                      list of the objects. The list of  current  objects
                      is  presented.  Hit  Enter  to  abort or select an
                      object. The selection 'c' will return you to  your
                      controlled  plane.  'l' will select your target as
                      the view object (if there is  a  target).  In  the
                      list,  piloted  planes  have a 'c' and your target
                      has an 'l'. Note that you cannot use this  command
                      if  networking is active. Also as objects come and
                      go, by  the  time  you  select  an  object  (by  a
                      sequence  number in the list) it may have moved up
                      the list - you end up with the wrong  object.  The
                      command is not considered important enough to make
                      it any more robust.
            O         As 'o' but also shows minor objects.
            p         Pause. Will not work when net is active  (toggle).
                      The  "Pause"  or  "Resumed" message tells you what
                      the new state is. As the prompt is in  text  mode,
                      in  some  implementation it will not clear, so use
                      'c'.
            q         Quiet (sound) mode. (cycle) Sets the sounds  level
                      to one of the following. Note that the independent
                      'aural alarm' option can be used to turn the  nag-
                      ging alarms on/off.
                      0    no sound.
                      1    only shoot/hit/alarms sounds (default).
                      2    all  sounds  and  effects.  For  now the only
                           effect is the engine noise.
            r         Activate radar (toggle)
            S         resupply plane: full stores and fuel,  reset  dam-
                      age.
            u         Hud configuration. see 'hud commands' later. Iden-
                      tical to the main menu 'hud' function.



            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _8



            v         Select normal/alternate view (toggle). Will  bring
                      the  designated alternate instrument into the main
                      view. The alternate view is  defined  through  the
                      window  configuration  menu. Note the view name at
                      the top right corner of the screen.
            w         Select weapon (cycle).
            W         Remove all weapon  stores.  The  plane  manoeuvres
                      better  this  way.  You can still use the weapons,
                      the counters will just go negative.
            x         Calibrate pointer. Mainly for joystick. center  it
                      and then hit x.


            44..22  SSyymmbbooll KKeeyyss
            These  are  the  rest  of the keys on the main keyboard. For
            clarity each key's name is spelled out. If it  is  allocated
            then the function follows.
              [back del]
              [escape]               invoke the menu system
              [space]                release radar lock
            ` [grave accent]
            - [hyphen]               see keypad '-'
            = [equals sign]
            \ [back slash]           used to reset the trim to nill.
            [ [l-bracket]            less flaps
            ] [r-bracket]            more flaps
            ; [semicolon]
            ' [quote]
            , [comma]
            . [period]               see keypad '.'
            / [slash]                see keypad '/'
            ~ [tilde]
            ! [bang]                 shell  to  system.  May not restore
                                     isome  environment  parameters  and
                                     pallette.   Use  'exit'  to resume.
                                     Now implemented on windowed enviro-
                                     ments.
            @ [at symbol]
            # [hash]
            $ [dollar]
            % [percent]
            ^ [caret]
            & [ampersand]
            * [asterisk]             see keypad '*'
            ( [l-paren]              less wheel brakes.
            ) [r-paren]              more wheel brakes.
            _ [underdash]
            + [plus]                 see keypad '+'
            | [pipe]
            { [l-brace]              less spoilers
            } [r-brace]              more spoilers
            : [colon]
            " [double quote]
            < [less than]            less speed brakes.



            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _9



            > [greater than]         more speed brakes.
            ? [question mark]        help


            44..33  KKeeyyppaadd
            The  keypad  is a collection of keys that replicate the main
            keyboard.  These are described as three groups by  function.
            The following keys surround the numerical keypad and are not
            affected by the Shift key.
            -                   view right (+45 degrees)
            *                   view ahead
            /                   view left (-45 degrees)
            +                   air brakes (toggle). Note that the  air-
                                brake  takes time to deploy, it's status
                                is shown on the control panel in percent
                                of full extension.
            (Enter)             unallocated
            The rest of these keys must have NumLock on.
            These  first  four  keys  respond only if the keypad is your
            pointing device.
            8 (up)              pitch (pull nose) up
            2 (down)            pitch (push nose) down
            6 (right)           roll right
            4 (left)            roll left
            The following commands extend all pointing devices capabili-
            ties:
            5 (center)          center ailerons and elevetors, like cen-
                                tering the joystick. Useful when using a
                                mouse (or trackball): will move the ref-
                                erence point to where the  mouse  is  at
                                this moment.
            7 (Home)            stop  rolling.  Levels  the  plane.  For
                                quiche eaters.
            9 (PdUp)            more (+5%) power
            3 (PdDn)            less (-5%) power
            1 (End)             mil (dry) (100%) power
            0 (Ins)             zero (0%) power
            . (Del)             after burner up (+1 unit which is 20% of
                                full scale)


            44..44  SSppeecciiaall kkeeyyss
            These  keys are a group of six on most keyboard but can also
            be duplicated using the Shift key  and  a  numerical  keypad
            key.
            PageUp              level (heading 0, pitch 0, roll 0)
            PageDn              reset coordinates to zero (back to base)
            Home                unallocated
            End                 unallocated
            Insert              unallocated
            Delete              unallocated






            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_0



            44..55  FFuunnccttiioonn kkeeyyss
            The function keys are normally used in plain mode (no Shift,
            Alt  or  Ctrl).  When  the menu is on the up-front, the left
            column ten selections are accessible with F1-F10  while  the
            right column uses AltF1-AltF10.
            F1        shoot.  Usually  also mapped the mouse left button
                      and both joystick buttons.
            F2        rudder left
            F3        rudder center
            F4        rudder right
            F5        zoom in (more detail, narrower view,  eye  further
                      from window).
            F6        zoom  out  (less detail, wider view, eye closer to
                      window).
            F7        Macro/HotKey definition.  Any key can be used  for
                      a macro name (except F7/F8). If you define a macro
                      for a HotKey (CTRL-A thru CTRL-Z) then it  can  be
                      played  back  with  one  keystroke. Other keys are
                      played using the F8 key.  If you use a Macro  dur-
                      ing  recording then the Macro will be recorded. If
                      you later re-define this Macro then it will affect
                      any  other  Macros  that  uses  it.   During macro
                      expansion there is a limit of 16 levels  of  nest-
                      ing.  There is no capability for Macros definition
                      editing.
                      define              F7<macro-key><keystrokes>F7
                                          If the key is already  defined
                                          then you are warned of the re-
                                          definition.  You may abort  at
                                          any stage (F8F8) and the orig-
                                          inal definition  will  remain.
                                          If you hit F8 during recording
                                          then  you  are   prompted   by
                                          Abort/Cont/Quote? to which you
                                          may respond by F8  (abort  the
                                          recording),  F7 (ignore the F8
                                          and continue recording) or any
                                          other  key  (the  key  will be
                                          recorded with the F8 expecting
                                          it to be another macro).
                      delete              F7<macro-key>F7
                                          It is not possible to record a
                                          null macro.
            F8        F8<macro-key>
                      HotKey play         <HotKey>
                                          Hot  keys  are   from   CTRL-a
                                          through CTRL-z.
            F9        unallocated
            F10       unallocated
            F11       unallocated
            F12       unallocated






            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_1



            44..66  AALLTT kkeeyyss
            ALT-Arrows: see below.
            The other keys are unallocated.


            44..77  CCTTRRLL kkeeyyss
            CTRL-Arrows: see below.
            CTRL-A thru CTRL-Z are reserved for user defined HotKeys.
            The other keys are unallocated.


            44..88  AArrrrooww kkeeyyss
            up                  turn gaze (head) down
                                All turns by 5 degrees
            down                turn gaze (head) up
            left                turn gaze (head) left
            right               turn gaze (head) right
                                use '*' to restore normal front view.
            CTLup               trim nose down.
            CTLdown             trim nose up.
            CTLright            trim rudder right.
            CTLleft             trim rudder left.
            ALTup               debug (varies).
            ALTdown             debug (varies).
            ALTright            debug (varies).
            ALTleft             debug (varies).



            55..  MMeennuuss
            A menu has a list of options, each associated with a key and
            a function.  To select a function use the  Up/Dn  arrows  to
            highlight  it  and  then Enter, or directly press the corre-
            sponding key. When on the up-front, the  associated  letters
            are  NOT  shown but are recognized; use the F-keys to select
            left column functions and AltF-keys for  the  right  column.
            See under HDD later.
            Menus  can  be nested, in which case the previous selections
            are listed first (in a  staggered  fasion  and  highlighted)
            followed  by  the current menu. The selected option is high-
            lighted (white) while the others are displayed in gray.
            The Esc key brings up the top menu  but  later  is  used  to
            abort a menu.  During menu navigation use these keys:
            Esc                 aborts the menu
            Enter               accept the current selection option
            UpArrow             select previous option
            DnArrow             select next option
            other               select the corresponding option
            If  a  command  is  invalid (top/bottom of list or undefined
            option) then a beep is emited and the keystroke is  ignored.
            The  menu system is changing rapidly so the following may be
            incomplete.
            Some other commands may pop up a  menu,  in  which  case  it
            behaves  in a similar way.  If you have the up-front instru-
            ment active then the menus will appear on it rather than  on


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_2



            the  main menu. This is a stupid attempt to make your inter-
            action look similar to what happens in a modern fighter.  It
            is  often the case that the pilot has a panel which can dis-
            play about 10 alpha-numeric words in bright white  (daylight
            readable).  These  will  usually use special LEDs and a more
            elaborate font than the 7-seg digits (9 segment?). There are
            pushbuttons  beside  these  words. The words are arranged in
            two columns, each with 5 words, with 5 buttons on the  right
            and  5 on the left. As you press a button new information is
            displayed.  Other planes use a real CRT but still  have  the
            5-buttons  arrangement  (mostly  on all four sides, totaling
            20).  In Fly8 the up-front device has two columns of  words,
            each  column  can show 10 words, each word can be 10 charac-
            ters long. There are 10 buttons on the left (F1 through F10)
            and  10 on the right (AltF1 through AltF10).  Use these keys
            to make selections. You can still  use  the  normal  command
            letters  (if  you know them, as they are not displayed here)
            as well as move about with the Up/Down keys:  a  small  dash
            between the key number and the text identifies the currently
            selected option.


            55..11  TToopp MMeennuu
            Exit           quit the program
                           confirm with 'y' on subsequent menu
            Help           toggles the help screen on/off
            Pointer        select pointing device
            Screen         screen options.
            Windows        set windows configuration
            Info           select stats info level
            Emit           create some random objects or remove them
            Hud            configure HUD
            Net            networking commands
            Options        set global program options
            Auto           selects some autopilot modes
            Debug          set debug modes


            55..22  PPooiinntteerr MMeennuu
            A list of all available pointing devices is offered.  Select
            one. All systems have a keypad device, most have a mouse and
            the PC has a joystick.  You will be asked to specify pointer
            options  -  read  about it later in the command line options
            section.


            55..33  SSccrreeeenn MMeennuu
            Screen.Colors  set some colors.
            Screen.Stereo  select a stereo mode
            Screen.Dbl Buff set buffering mode to double/single. A  mes-
                           sage  is  posted  on  the  new  mode.  Double
                           buffering is not supported  in  all  environ-
                           ments  and in all modes, and in some cases it
                           may  be  significantly  slower  than   single
                           buffering.


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_3



            Screen.Blanker toggle  screen blanker mode. Borders and some
                           fixed data are not shown in blanker mode.
            Screen.Load font This [obsolete] function will  load  a  new
                           text font. Text fonts are not used anymore by
                           the program.
            Screen.Font show This [obsolete] function will  display  the
                           current  text  font as 16 lines of 16 charac-
                           ters each.
            Screen.HUD pos select it the  HUD  is  focused  at  infinity
                           (default) or on the HUD face.


            55..44  SSccrreeeenn..CCoolloorrss MMeennuu
            A  set of colors is listed. Select one for modification. You
            will then be presented with a number of adjustment options:
            Brighter       intensify the color
            Darker         reduce color intensity
            New            set color to a desired RBG value
            Restore        restore color to original value


            55..55  SSccrreeeenn..SStteerreeoo MMeennuu
            select a mono/stereo mode:
            Screen.Stereo.Mono standard mono mode
            Screen.Stereo.S'Scopic side by side stereoscopic images
            Screen.Stereo.RedBlue red/blue  composite   (needs   colored
                           glasses)
            Screen.Stereo.Alternate alternating left/right images (needs
                           shutter glasses and '-s' command line option)
            Screen.Reverse toggle  reverse-stereo  mode  (swap  Left and
                           Right images)
            Screen.Paralax set stereo inter-occular  distance.  Initialy
                           set  to  12  units.  Each  unit is 1meter/256
                           (about 4mm).


            55..66  WWiinnddoowwss MMeennuu
            A number of window configurations are offered. This  defines
            how  the  screen  is  split  into main and auxiliary display
            areas. After the selection the screen remains active so that
            you can select the 'configure' option immediately.
            Windows.text   a  square  window  is used for graphics and a
                           side bar is reserved for text. This  mode  is
                           obsolete.
            Windows.full   the whole screen is one window
            Windows.landscape a wide main view with three windows below
            Windows.portrait a  square  main  view  with a column of two
                           windows on the right
            Windows.square a square main view with  a  column  of  three
                           square windows on the right
            Windows.wide   a  wide  main  view  with four square windows
                           below
            Windows.configure define which instrument  is  displayed  in
                           each  window.  The  first  response will be a
                           number shown in each window and a mode listed


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_4



                           under it. A prompt will ask you to select the
                           window to be configured, then  the  Configure
                           menu will let you assign an instrument to it.
                           This  process  will  be  repeated  until  you
                           respond  with 'Enter' or 'Esc' to the prompt.


            55..77  WWiinnddoowwss..CCoonnffiigguurree MMeennuu
            The plane has a number of on-board instruments, each one has
            a  visual  representation  that  can  be shown on one of the
            active displays.  This  menu  is  used  for  defining  which
            instrument is to be shown on each of the displays. Configur-
            ing the main display  (usually  numbered  0)  defines  which
            instrument will be used as the alternate view.
            front          this is a forward looking camera.
            none           designates the HDD as unassigned
            rear           a rear viewing camera
            map            a  map of the area from above with you at the
                           center and north is up.
            radar          as 'map' above but the plane's current  head-
                           ing is the 'up' direction. Gives better situ-
                           ation awareness.
            target         a target following camera.
            pan            another target following camera that is  less
                           stable (more real?)
            gaze           a  view  of  my  plane  from a fixed relative
                           point
            chase          a view of my plane from a point  that  chases
                           my path.
            follow         as  'chase'  but  the  view  is  always level
                           (never rolls).
            hud            this is the raw HUD display
            up-front       an alphanumeric display used for pilot inter-
                           action
            misc           misc digital data and warning display.


            55..88  IInnffoo MMeennuu
            Select  the  stats info level. This info is shown on the up-
            front HDD but can (optionally) be overlaid on the main view.
            Info.off       do not overlay 'info' on the main view
            Info.on        do overlay 'info' on the main view
            Info.none      no info
            Info.timing    only basic timing will be shown.
            Info.stats     timing and internal stats are shown, used for
                           program testing.
            Info.game      timing and basic info for a game are shown.

                           The second line will show (in  order):
                           --   time from start of game (in seconds).
                           --   number of targets present (both standard
                                targets and ground targets)
                           --   number of weapons used in total
                           --   number of hits scored



            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_5



                           The third line will show:
                           --   score (counting down!)
                           --   plane speed (meters/sec).
            The  basic 'timing' data, which is always the first line, is
            a list of millisecond durations for:
            --    total time of frame
            --   graphics drawing (display list -> screen)
            --   3D transformations (world -> display list)
            --   objects simulation (old world -> new world)
            --   other visual calculation (hud, text, sky etc.)
            --   vertical sync wait (if double buffering)
            --   total minus the rest; will include the  auxiliary  win-
                 dows time and network disturbance.


            55..99  EEmmiitt MMeennuu
            Various objects can be created with this menu. These objects
            are used as targets.
            Emit.target    create one random target
            del            delete all targets
            Emit.gtarget   create one random ground target
            del            delete all ground targets
            Emit.box       create one random box. Boxes are  cubes  that
                           hop around which can be shot down.
            del            delete all boxes
            Emit.del tgts  delete all targets, ground targets and boxes.
            Emit.drone     create one random plane (drone)
            del            delete all drones. This  will  also  set  the
                           number of automatic drones to zero.
            Emit.drones    specify  how  many drones should be automati-
                           cally maintained in the air.  Whenever one is
                           lost another one takes off.
            Emit.killers   specify  how  many  of  the  drones should be
                           killers. These will be set to Chase and  Kill
                           mode.


            55..1100  HHUUDD MMeennuu
            Various aspects of the HUD can be set. Each option is either
            set, reset or toggled. The default is to toggle  the  option
            but  the  first  three menu items can be used to change this
            mode. This menu can be accessed from the main menu  as  well
            as  directly  with  the 'u' command. The following selection
            appear on some of the sub-menus:
            0 turn off          turn option off
            1 turn on           turn option  on
            2 toggle            toggle option on/off
            This top level menu will bring  up  a  number  of  sub-menus
            which are described further down this doco.
            HUD.off             turn  the  HUD off. When turned off, the
                                radar symbols will still show.  This  is
                                a  feature of the game which is not like
                                the real thing; it allows  you  to  play
                                with  a  very  clean view. Not only will
                                the radar  stuff  still  show,  but  the


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_6



                                symbols  will now move freely across the
                                full screen rather than  being  confined
                                to the HUD area. To get rid of the reti-
                                cle/TDB use the 'parts' menu.
            HUD.on              turn the HUD on
            HUD.type            Select HUD style.  Although  the  styles
                                are named after planes, each plane actu-
                                aly displays many  styles  depending  on
                                the mode of operation.
            HUD.parts           The  HUD  has many components. This sub-
                                menu allows  you  to  choose  which  are
                                included in the HUD display. Selecting a
                                HUD type will automatically adjust these
                                to what is appropriate for that style.
            HUD.options 1       This (and the next) selection allows you
                                to set some parameters which modify  the
                                appearance  of  the  HUD. The most often
                                used ones are in this sub-menu  and  the
                                rest are in the next.
            HUD.options 2       See description of "options 1" above.
            HUD.radar           This  will configure the radar symbology
                                on the HUD.
            HUD.ils             Will let you select the ILS  beacon.  In
                                the future there should be a more elabo-
                                rate NAV facility instead.


            55..1111  HHUUDD..ttyyppee MMeennuu
            Fly8 supports a number of HUD styles. The name  of  the  hud
            does not necessarily correspond with the plane type but this
            is what I found on the various videos that I saw. If anybody
            has  more  knowledge or can provide other detail PLEASE feel
            free to advice me.
            HUD.type.Classic This one I made up before seeing  any  real
                           HUD. The basic data is laid close to the edge
                           and  leaved  most  of  the  area  free   from
                           obstruction.  My original aiming reticule was
                           8 dots in a circle but I discontinued  it  in
                           favour  or  the  more common piper style. The
                           numerals on the pitch ladder  do  not  rotate
                           and  the fast font is used. On a slow machine
                           this hud (especially in low detail) will per-
                           form much faster that any other.
            HUD.type.FA18  This  HUD does not use tapes for the altitude
                           and speed. The pitch ladder is narrower  than
                           usual  and slanted toward the horizon. A good
                           feature is the fact  that  the  pitch  ladder
                           stays  always in view: if the velocity vector
                           goes off the screen (easily done on the FA-18
                           which has no trouble flying at high AOAs) the
                           pitch ladder adopts (temporarily) the  water-
                           line  mark.  Another  feature  is the closure
                           speed which is shown under the  piper  rather
                           than  on a radar ranging scale. Optionally, a
                           pendulum (or what do you  call  it?)  can  be


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_7



                           displayed  which  shows  you  your roll angle
                           with good resolution up to 45 Degrees  either
                           way.  This  is  a wide angle hud - 20 degrees
                           side to side.
            HUD.type.F16   This HUD uses simple  scales  (no  baseline).
                           The heading scale can be at the top or at the
                           bottom.
            HUD.type.F15   This HUD is probably used for air to  air  on
                           other planes. The speed scale is upside-down.
                           The heading scale can be set to two different
                           positioned at the top.


            55..1122  HHUUDD..ppaarrttss MMeennuu
            The  various  HUD  symbols  can be individually selected for
            display.
            HUD.parts.ladder Select pitch ladder (and related)  options.
            HUD.parts.altitude Show altitude scale (or box).
            HUD.parts.speed Show speed scale (or box).
            HUD.parts.heading Show heading scale.
            HUD.parts.gnd ptr Only  for  the FA18 style, show the pendu-
                           lum.
            HUD.parts.border Show the HUD border (in gray color).
            HUD.parts.vv   Show the plane's velocity vector. A must  for
                           accurate flying.
            HUD.parts.vw   This  activates  a  mode  that the FA18 uses:
                           when the vv goes off screen, a waterline mark
                           will  appear  and  the  pitch  ladder will be
                           drawn around it.  This way the  ladder  never
                           goes  completely  off screen (which can often
                           happen when flying at high AOAs).
            HUD.parts.plus Show a 'plus'  sign  at  the  center  of  the
                           screen.
            HUD.parts.pointer Show  a  small  (red) mark that tracks the
                           joystick  (or  mouse  or  whatever   pointing
                           device you  use).
            HUD.parts.beta Show the sideslip angle (beta) on FA18 style.
            HUD.parts.Xbreak Show the Xbreak symbol if at risk  of  hit-
                           ting the ground.
            HUD.parts.Xgrid Show  the warning grid if at risk of hitting
                           the ground. This is a  red  grid  which  will
                           overlay the ground if you fly too low.


            55..1133  HHUUDD..ooppttiioonnss 11 MMeennuu
            These options modify some aspects of the HUD appearance.
            HUD.options1.heading The  heading  scale  shows  the  planes
                           heading. The numbers  displayed  are  in  the
                           range  000-350  in  increments  of  10.  This
                           option selects between  showing  the  full  3
                           digits  of  using  an  abbreviated  form. The
                           abbreviated form will only show the  top  two
                           digits  (09 for 90 and 27 for 270). The Clas-
                           sic HUD style will show the full  number  but
                           without the leading zeros.


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_8



            .HUD.options1.knots Internally all data is stored in meters.
                           This option requests  that  all  numbers  use
                           knots/feet  (as  appropriate)  instead. It is
                           the default for the standard HUDs.
            HUD.options1.top This will further modify the heading scale.
                           The scale will show at the top or at the bot-
                           tom depending on this option.  For  the  FA18
                           HUD style, this option will cause a base-line
                           to be drawn under the scale (the  scale  will
                           stay at the top regardless).
            HUD.options1.fine For  some  of  the scales this option will
                           show more detail. The standard detail  is  to
                           show  a  tick  every 5 units. The fine detail
                           will show a tick every two units.
            HUD.options1.xfine This is a further refinement of the above
                           'fine'  level  and  will show a tick for each
                           scale unit.
            HUD.options1.big [obsolete]The  name  is  completely  wrong.
                           This option defines the style of the ticks on
                           the scales (for some of the HUDs  only).  The
                           usual  way  is  to have the ticks go from the
                           base-line to the outside. In the 'big'  style
                           the  scale  will  be  along the edge with the
                           ticks towards the inside.
            HUD.options1.scale This defines the number  of  units  along
                           the scale. This affects only the Classic HUD.
                           The more units, the longer the scales.
            HUD.options1.area The HUD has  a  fixed  area  (measured  in
                           field-of-view  degrees).  You  can alter this
                           size. Note that although the HUD size changes
                           when you zoom in/out, it still keeps the same
                           FOV. This option defines how many degrees are
                           from  the  center to the edge of the HUD (all
                           HUDs are square).


            55..1144  HHUUDD..ooppttiioonnss 22 MMeennuu
            These options modify some aspects  of  the  HUD  appearance.
            These are the less used options.
            HUD.options2.a alarm Enable  aural  alarms.  If you hate the
                           GLIMIT beeps etc. then  use  this  option  to
                           turn these alarms off.
            HUD.options2.v alarm This  will  Enable/disable  the  visual
                           alarms that show on the HUD.
            HUD.options2.panel Request to show the panel HDD on the main
                           window.  This  will  show at the bottom right
                           side as digital  flight  data  (and  as  some
                           indicators at the top left).
            HUD.options2.font Select  the font for the stroke characters
                           used on the screen
            HUD.options2.fontsize Select the stroke font size. A size of
                           8 means 'use the default' and all other sizes
                           are relative to 8. The default is  calculated
                           from the screen resolution.



            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _1_9



            55..1155  HHUUDD..rraaddaarr MMeennuu
            The  radar  symbology  on  the  HUD is controlled with these
            options.
            HUD.radar.corner Radar target data can be at the bottom-left
                           corner  of  the  HUD or can follow the target
                           designator.
            HUD.radar.data Request to show target data.
            HUD.radar.distance Request to show target distance in  intel
                           mode (mainly used in the radar/map modes).
            HUD.radar.name Request  to  show  target  type in intel mode
                           (mainly used in the radar/map modes).
            HUD.radar.accvect Show target acceleration vector as a  hand
                           inside the reticle piper.
            HUD.radar.reticle Show aiming reticle piper.
            HUD.radar.target Show the target designator.
            HUD.radar.ross Use  Ross's  method  for  the aiming reticle.
                           This mode will show a small box in  front  of
                           the  target where it is expected to be when a
                           bullet hits it. If you  aim  the  reticle  at
                           this  box  and  shoot then you should hit the
                           target.
            HUD.radar.limit Unlike real HUDs, the radar symbols  can  be
                           displayed  all  over  the  screen rather that
                           just inside the HUD area. 'limit' will  spec-
                           ify which way it should be.
            HUD.radar.thick This  is  an experimental option to draw the
                           radar reticle thicker.
            HUD.radar.hidetgt When active, if the TD box  is  under  the
                           reticle  then  it  is  not  shown.   This de-
                           clutters the area of interest.


            55..1166  NNeett MMeennuu
            Some of the requests in this menu will need you to  identify
            a  player.  A  numbered list of players is displayed and you
            should select one by entering their number. If you Enter '*'
            then  you will select 'all' of them. If you give a null then
            you secl 'none'. If there is only one player then it wil  be
            selected  automatically.   A message 'no net' means that the
            program was started withou the net option (or  possibly  all
            net  connections  are  inaccessible).  A message 'no player'
            may be displayed which means that there are  no  players  in
            the  needed  status  (eg.  you try to 'quit' but you are not
            currently playing with anyone).
            Net.ping       find out who else is playing.  A  message  is
                           broadcasted  and for each responding player a
                           message is displayed.
            Net.play       join another player's game (or all players)
            Net.quit       stop playing with a player. If there are more
                           than  one  players  then you will be asked to
                           choose.
            Net.message    send a message to a player (or all). You will
                           later  be  notified how long it took the mes-
                           sage to reach each player and return a  noti-
                           fication.


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_0



            Net.accept     accept  a  player's request to play with you.
                           Used in response to the Requesting message.
            Net.decline    decline a player's request to play with  you.
                           Used in response to the Requesting message.
            Net.always accept automatically accept any requests to play.
            Net.always decline automatically  decline  any  requests  to
                           play.
            Net.manual reply do   not   automatically   respond  to  any
                           requests to play.


            55..1177  OOppttiioonnss MMeennuu
            Options.Version show program version and compile  date/time.
            Options.Smoke  set/clear  smoke  generation.  Damaged planes
                           and craters  will  smoke  if  the  option  is
                           enabled.
            Options.Font   show  current stroke font. It is displayed if
                           large on the center of the screen.
            Options.Modes  show current program modes setting  (same  as
                           'm' command)
            Options.Sky    paint blue sky in views.
            Options.Gravity enable  gravity  (default). Will affect bul-
                           lets path.
            Options.Instruments show a rudimentary set of instruments.
            Options.Play Blues [sound debug] No  simulator  is  complete
                           without  it.  Actually used to test the sound
                           generation logic which for now is operational
                           only on the PC.
            Options.Verbose set  verbose  mode.  At  the moment it means
                           that when using the 'u' command you will  not
                           be  shown the long list of commands (the menu
                           will not show but it is active!).
            Options.Net Stats display network statistics  (same  as  'n'
                           command).
            Options.Limited Will  limit  the  ammunition  to the takeoff
                           quantity. Normally you have limitless ammo.
            Options.No stall This option reduced the effectiveness of  a
                           stall. Good for early practice.


            55..1188  AAuuttoo MMeennuu
            Auto.Flaps     Enables the flaps Control Augmentation System
                           (CAS). This will give you better turn perfor-
                           mance by adding flaps (or leading edge flaps)
                           when needed).
            Auto.Elevators This will enable the  CAS  which  limits  the
                           Elevators  sensitivity at high speed to avoid
                           excessive load. A Stability Augmentation Sys-
                           tem  (SAS)  is being added which will improve
                           dynamic  pitch  stability  by   taking   some
                           authority over the elevators.
            Auto.Rudder    Enable the rudder SAS and CAS.





            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_1



            55..1199  DDeebbuugg MMeennuu
            Debug.debug    Enable  the general debug mode. Some programs
                           will display internal data when in this mode.
                           Thie  changes a lot and cannot be documented.
            Debug.gp w     General purpose debug option W is  controlled
                           by  this option. It is used for debugging and
                           cannot be documented here, see  if  there  is
                           anything in the readme.
            Debug.gp x     As above for option X.
            Debug.gp y     As above for option Y.
            Debug.gp z     As above for option Z.



            66..  CCoommmmaanndd LLiinnee EEddiittiinngg
            When  a  command  needs to receive a parameter which is more
            than one keystroke it uses a line input facility. It  allows
            you  to  use history and editing. You can use the arrow keys
            and insert/delete keys to move about and edit your response.
            The  up/down  keys  will retrieve history.  Finally you will
            need to press Enter for the program to accept the input. The
            history queue has 20 entries. If you key the start of a line
            and hit PgUp then a search will be done for a previous entry
            with the same beginning.



            77..  AAuurraall IInnddiiccaattoorrss
            Sound  is  used to inform and warn. The sounds at the moment
            are simple tones or tone sequences.
            A short beep when:
                 --   you fire
                 --   you hit or a plane crash
                 --   the radar selects a target
                 --   a menu selection is invalid
                 A low beep when:
                      --   landing
                      --   taking off
                      --   landing gear status is changed
                      Two repeating tones for:
                           --   Emergency alarm (pull-up, eject etc.)
                           --   Warning alarm (stall, g-limit etc.)
                           Repeating scales when:
                                --   target practice has ended



            88..  VViissuuaall IInnddiiccaattoorrss
            These are highlighted words flashed onto the HUD. They  vary
            in size and blink rate.
            WAIT           You ejected and landed but your plane did not
                           yet crash. This one does not  relate  to  the
                           HUD, all the others only show when the HUD is
                           on.



            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_2



            STALL          You are flying the plane too slow to maintain
                           lift  or you are turning too sharply at a too
                           high angle of attack.
            GLIMIT         You exceeded the maximum acceptable  G  force
                           of  your  body  (+9G to -3G), or you exceeded
                           the 10G plane structure limit.
            FUEL           You have less than 10% fuel  left.  The  less
                           fuel  you have the faster the message blinks,
                           then it finally stays on.
            PULL UP        You are about to hit the  ground  unless  you
                           pull  the plane up immediately. If the danger
                           is higher then a red ground grid  is  flashed
                           to  give  the pilot better orientation (there
                           is not enough scenery to build proper  visual
                           awareness).
            EJECT          The  plane is damaged beyond control. Shift-E
                           to eject.



            99..  TThhee PPllaannee
            This chapter explains in detail how planes  are  handled  in
            this program.
            The  plane is controlled by your pointing device, preferably
            a joystick.  The basic  controls  will  have  the  following
            effect:
            Left/right  controls  will cause the plane to roll. The roll
            will continue while the controls are engaged. When the  joy-
            stick  is  centered the rolling will stop and the plane will
            stay in the current situation. If  you  want  to  fly  level
            after rolling to the right then you will have to do the fol-
            lowing:
                 --   roll right (the horizon will roll left).
                 --   stop rolling (the horizon will  stay  at  a  fixed
                      angle).
                 --   roll left (horizon rolling back to the right).
                 --   stop rolling (when the horizon is level).
                 As  the plane has momentum, the response is not immedi-
                 ate and you will have to get a feel for it.
                 To start climbing you will pull the  stick  toward  you
                 until the climb angle is what you want and then release
                 the stick. The plane will continue climbing  until  you
                 push  the nose down for level flight. If you are rolled
                 over to one side then the pulling will cause the  plane
                 to  turn into that side. If you are upside-down and you
                 pull the stick then you will start  descending  towards
                 the  ground. In other words: the up/down controls (ele-
                 vators) are used for  any  change  of  direction,  both
                 left/right and up/down.
                 To  turn  right,  first roll right, then pull the stick
                 until the desired heading is reached, then release  the
                 elevators and roll back to level flight. Of course, due
                 to gravity and plane dynamics any change  in  situation
                 will  probably  cause  the plane to move in a direction
                 slighly different from what the controls suggest -  you


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_3



                 should  learn  to compensate for this. The flight-path-
                 marker (the little circle with three wings)  tells  you
                 where  the plane is heading and this is hardly ever the
                 direction where your plane is pointed at.
                 To control your engine you set the  throttle  with  the
                 9/3  keys. The throttle can be set to between -100% and
                 100%. Reverse setting only works on  the  ground.  Each
                 keystroke is 5% change. The 1 key will set the throttle
                 to 100% and the 0 key to 0%. The planes speed will pick
                 up slowly (depends on the planes weight and the engines
                 power). You can engage the after-burner  with  the  '.'
                 key.  To  slow  down  you may use the speed brakes ('+'
                 key).
                 About the AfterBurner: light it with '.' (will also set
                 throttle to 100%). Then each '.' or '3' (power-up) will
                 add a notch. Each '9' (power-down) will take it down  a
                 notch.  There are five steps (say 20% each). The throt-
                 tle display will show '103' for '100% +  AB3',  105  is
                 full  AB.  The  engine display will show thrust in % of
                 mil thrust (full AB is about 150%-160%). If you use '1'
                 (max  throttle)  or  '0' (idle engine) the ab is turned
                 off. NOTE that AB5 uses about 6 times as much  fuel  as
                 MIL for 60% extra power!
                 Note that with the PC keyboard and the NumLock engaged,
                 the above keys appear in a logical order.
                 The Classic plane is an over-simplified vehicle. It has
                 no  momentum  and  no  aerodynamics characteristics, it
                 goes where you point it and is a good way  to  get  the
                 hang  of  the controls. It will never crash either (you
                 can fly underground of course). But don't get too  used
                 to  it,  the  real  planes handle very differently (the
                 Classic is more  like  a  weightless  spaceship  of  an
                 arcade-game).



            1100..  TThhee HHeeaadd UUpp DDiissppllaayy
            The program displays a number of HUD styles. These are named
            according to a plane type but this is just because  I  first
            saw  this  HUD  on  a video tape dedicated to that plane. In
            reality each plane has a number of HUD modes. You can change
            the  HUD  style through the hud menu regardless of the plane
            type.
            The HUD is a piece of glass that is positioned at  an  angle
            in front of the pilot. The pilot looks through it to see the
            front view from the cockpit and at the same time  a  reflec-
            tion  of  a  video screen is seen (this CRT is in the 'dash-
            board' facing up). The dual-image is  similar  to  when  one
            looks  outside  through a window at night and sees a reflec-
            tion of some part of the room as well as  the  outside.  The
            HUD  can be displayed by itself on one of the auxiliary HDDs
            (sometimes refered to as the 'HUD repeater'), which is  use-
            ful when the HUD optics is not operational (damaged).
            In  practice,  the  HUD  is a flat image superimposed on the
            front view, and it uses a special (usually green but you can


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_4



            change  this)  color.  It  does not cover the full field-of-
            view.
            The image projected onto  the  HUD  contains  two  kinds  of
            information.  One type is data that the pilot will otherwise
            have to look for in some cockpit  instruments  (thus  taking
            his  eye  off  the  outside  scene); this is simply a way of
            putting the most  important  information  if  front  of  the
            pilot.  An  example is the display of plane speed. The other
            kind is information directly related to  the  outside  image
            and  meaningfull  only  in  relation  to  it, for example: a
            bounding box is displayed such that it coincides with a vis-
            ible target that the radar is locked on.
            The  prominent  features  on  the HUD are a number of scales
            which are usually diaplayed along the  edge.  Sometimes  the
            detail  of  the  scales  can  be  controlled in three levels
            through the Hud menu (see there).
            The HUD symbols will relate to flight data or  to  auxiliary
            systems (weapons, radar, fuel etc.). The data related to the
            flying of the plane is described first.


            1100..11  HHeeaaddiinngg
            Your compass. It will be shown as a  horizontal  ruler  that
            moves  as  you  turn.  The  current heading is marked with a
            'tick' or a 'V'. It can be at the top or at  the  bottom  of
            the  HUD  (Top  option  in Hud menu). North is 360, South is
            180, East is 90 and West 270. Some modes  do  not  show  the
            trailing  zero (270 is shown as 27) and NO, there is no sup-
            port for radians or other units...


            1100..22  AAllttiittuuddee
            Your height above sea level, a vertical ruler at  the  right
            edge  of  the  HUD.  It  may  be accompanied by a second bar
            (immediately to its left) that shows your  climb/fall  rate.
            This ruler moves up and down as the plane moves, the current
            altitude is to be read at the 'tick'  in  its  middle.  High
            altitudes  show in thousands (with a possible decimal point)
            while low ones will show exact. The FA-18  style  HUD  shows
            the  altitude in a box at the right side of the HUD with the
            climb rate above it. Some HUDs will show a radar-range scale
            adjacent  to  (and  to the left of) the altitude scale. This
            will indicate the distance to the  target  (the  full  scale
            range  is  shown  just  above  this scale) as a sliding tick
            while the target closure speed is shown inside the tick.
            Climb rate is in meters (or feet) per minute!


            1100..33  SSppeeeedd
            Your speed is shown as a ruler at the left edge of the  HUD,
            a tick marks the current value. The FA-18 style HUD shows it
            in the left box. Some HUDs do not  show  the  trailing  zero
            while others show have the scale run from top to bottom.
            This information may be in meters/kmh of feet/knots (use the
            Hud Knots  command  to  toggle).  The  F16/FA18  default  to


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_5



            feet/knots.


            1100..44  PPiittcchh llaaddddeerr
            The  orientation of the plane is displayed as a ladder, each
            step relates to a different pitch. The steps are always par-
            allel  to  the  horizon.  Each  step is marked with a number
            which is your pitch angle (90 degrees is straight up, -90 is
            down  and  zero  is  level).  The step's angle represent the
            planes roll. When you are upside-down the steps are too,  as
            you  roll  the  steps turn in the opposite way to follow the
            horizon. The negative-pitch steps (when you are going  down)
            are dashed while the positive ones are solid. Small winglets
            at the tips of the steps point toward the ground. The  zero-
            pitch  step  is  larger and is your artifical horizon if you
            cannot see the real one. The FA-18 style  HUD  tries  a  bit
            harder  by  bending  the steps toward the ground: the higher
            your pitch the larger the slant. It also shows a small  cir-
            cle  at  the straight up/down directions (the down one has a
            cross through it).
            Although the pitch ladder follows the horizon  (meaning  the
            zero-step  is on the horizon) there is some freedom in where
            on the horizon  to show it. Unless you disable the  velocity
            vector  (flight path) marker (see below), the ladder will be
            centered on it. This means that at a high  angle  of  attack
            the pitch ladder may be out of view (as will the vv).
            In  the  case of the FA18, if the vv goes out of view then a
            waterline marker will appear at the center of the HUD (it is
            a  W  marker  in a fixed position) and the ladder will shift
            (smoothly) toward it. Once the vv is back in view the ladder
            will return to it and the waterline mark will disappear (the
            transitions take about two seconds maximum). The FA18 ladder
            shows  an  extra-long  zero-step  while  the landing gear is
            down.


            1100..55  VVeelloocciittyy VVeeccttoorr
            A plane rarely moves straight ahead due to gravity and aero-
            dynamic  forces.  This  marker  (sometimes called the 'plane
            marker') is a tiny circle with wings on either side  and  at
            the  top (it is a stylized shape of a plane from behind). At
            any time, this marker shows you where the plane is  heading.
            You will most of the time use this marker as a reference for
            flying the plane. The center of the view is  rather  useless
            for flying (you can bring up a cross-hair with the 'u+' com-
            mand) but can be  helpful  in  aiming  the  cannon  (in  the
            absence of the aiming reticle).
            The Classic plane always goes ahead, so the vv will be fixed
            at the center of the HUD. By default it will  not  be  shown
            for this plane.


            1100..66  WWaatteerrlliinnee mmaarrkk
            This  is a 'W' that shows in the straight ahead point on the
            front view (this is not always the physical  center  of  the


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_6



            HUD).  It comes on whenever the landing gear is lowered. The
            FA-18 HUD shows it whenever the Velocity Vector  is  outside
            the HUD.


            1100..77  RRaaddaarr SSyymmbboollooggyy
            When the radar is active, some symbols related to its opera-
            tion are displayed. The main features are the target  desig-
            nator box and the aiming reticle (the Piper).


            _1_0_._7_._1  _T_a_r_g_e_t _d_e_s_i_g_n_a_t_o_r
            This is a square that is centered on the target. If the tar-
            get is not locked then the box will have only  corners.  The
            target  should  be  visible inside the box, unless it is off
            screen. When off screen, the box has a '+' through it and it
            crawls  along  the  HUD edge showing you the direction where
            the target is. If the target is actualy behind you then  the
            '+' is replaced with an 'X'.


            _1_0_._7_._2  _A_i_m_i_n_g _R_e_t_i_c_l_e
            If  a  target  is close enough (within weapon range) then an
            aiming reticle appears.  The reticle is  a  circle  with  12
            ticks.  Each tick represent a distance of 1000 to the target
            and the range is marked with a tick  that  moves  along  the
            inside  edge  of  the  reticle. A tick at 11 o'clock means a
            distance of 11,000 etc. You should fly the plane so that the
            center  of the reticle (has a dot) is on the target and then
            shoot (actually,  the  cannon/radar  computer  will  display
            'shoot' above the reticle when you have a good aim). If this
            sounds simple it is because it is a  simple  procedure;  the
            problem  is  that  in order to get the target in the reticle
            you will NOT be flying the  plane  directly  toward  it.  In
            practice you forget about where the plane should go and play
            a game of follow-the-target with the reticle (just  try  and
            not hit the ground).
            The  F16  will  also  show  a 'hand' inside the circle which
            indicates the direction and magnitude of the target acceler-
            ation (this one is very jiterry at times). You can turn this
            hand on/off with the Hud menu "acc vect" command.
            The FA18 HUD shows the closure speed outside the lower right
            side  of the reticle. The F15/F16 shows the same information
            on the radar range scale (beside the altitude) marked with a
            large  '>'  symbol.  The closure speed measures how fast you
            are catching up (positive) with the target.
            However, in order to complicate the situation we  have  some
            variations possible:
            There  is an alternate piper: Ross's reticle. This is a dif-
            ferent aiming method altogether. A square reticle  is  shown
            with only the corners visible. It is ahead of your target at
            all times on its projected position. You  have  to  aim  the
            piper  at  the  box and then shoot. With this one you do not
            care where  the  real  target  is  because  the  aiming  box
            replaces  it.  The  piper will be fixed at the center of the


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_7



            HUD.  You may want to turn off the  target  designator  with
            'ut'.
            The target designator and aiming reticle are part of the HUD
            display, however you may choose to ignore this  and  request
            that  these  use  the  full  screen. Use the 'uL' command to
            limit these to inside the hud area or use the whole  screen.


            _1_0_._7_._3  _R_a_d_a_r _R_a_n_g_e
            The radar measures the distance and relative (closure) speed
            of the target. The range is shown as an extra scale  on  the
            right  side  on  the  HUD  while  the closure speed is shown
            beside the '>' mark on it. The FA18 HUD does not  show  this
            scale  but  shows  the  closure speed under the piper with a
            'Vc' mark.


            _1_0_._7_._4  _D_i_g_i_t_a_l _d_a_t_a
            When a target is selected, some digital information  may  be
            displayed  (it  can be disabled by the hud/radar menu). This
            data shows at the left bottom corner of the HUD and has  the
            following items:
                 --   distance to target (units or k's with one decimal)
                 --   closure speed (meters/knots)
                 --   time to meet (seconds with one decimal).
                 --   target type or pilot name
                 When the target is in range the time  shown  is  bullet
                 time-to-impact rather than plane flight time.
                 If  the  Corner  option  is not selected (uC) then this
                 data will show under the target designator box. If  the
                 target  is  too  close  to the bottom then the data may
                 show above it.
                 If you activate the Intel mode  (i)  then  all  visible
                 targets  get a box with the following data (the MAP and
                 RADAR diplays always have this mode):
                      --   distance to target (units  or  k's  with  one
                           decimal)
                      --   target type or pilot name
                      You  can  use  'un'  to disable the display of the
                      second line.

            1100..88  OOtthheerr FFeeaattuurreess
            In addition to the above features, the HUD may show the fol-
            lowing:
            The  FA18  type HUD shows as standard, on the left low edge,
            the angle of attack (aoa), the mach number and  the  pilot's
            vertical  Gs.  The  selected weapon (and available units) is
            displayed at the low center of the HUD.
            The F15/F16 HUD shows the aoa at the  top  right  above  the
            altitude  scale.  The weapon selected is shown at the top of
            the data list ('XXX' means none selected)






            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_8



            1111..  TThhee IILLSS
            The Instrument Landing System (ILS) is a  system  that  pro-
            vides enough information about your approach to guide you to
            the touchdown point with great  accuracy.  The  system  com-
            prises  two  separate  facilities:  the Localizer beam which
            tells you how well you are aligned with the runway  and  the
            Glide  Path  beam  which monitors your descent rate. The two
            components measure your approach error and display it as two
            bars.
            The  Localizer  deviation  bar is a vertical line that moves
            accross the HUD and indicates which way of the correct  line
            you  are.  If the bar is left of center then this means that
            you are to the right of the Localizer beam,  so  you  should
            correct  your approach to the left. When the bar is right of
            center you will need to move to the right too. You are  cor-
            rectly  aligned when the bar is at the center. You can judge
            the bar's position by noting the number of ticks  along  the
            horizontal  bar.  The larger middle one is where you want to
            be. The bar is at full deflection when  your  error  is  2.5
            degrees.
            The Glide Path deviation bar is a horizontal line that indi-
            cates where the correct descent line  is.  If  the  line  is
            above  center  then  the  you  should be flying higher (your
            descent is too rapid or you are descending toward a point on
            the  ground  too  short of the runway); you should gain some
            height or reduce your descent angle. In the same  way,  when
            the line is below HUD center you are above the correct path.
            The bar is at  full  deflection  when  your  error  is  0.75
            degrees.
            Note  that  the ILS system does not know where you are head-
            ing, it just tells you how close  you  are  to  the  correct
            approach path. The system does not even know if you are com-
            ing or going! So make sure that you approach the runway from
            the correct end or the ILS Localizer deviation bar will show
            reverse reading and the Glide Path will direct you  to  land
            at the far end of the runway.
            Real  ILS systems have very narrow beams and will only oper-
            ate when you are reasonably aligned. These systems will tell
            you  when  you  are  out of range. The one in Fly8 is active
            within a radius of about 25 kilometers around the runway.
            When the ILS is operating a marker along the  heading  scale
            will  direct  you  to  the  airport;  use it for the general
            approach but then identify the correct runway carefully.
            To select the desired runway use the  ILS  menu  and  choose
            from  the list.  There are now two airports (A is home and B
            is for the drones) and each has two runways: 18 (approach at
            heading 180) and 27 (approach at 270).  You can turn the ILS
            off and it will still remember the last active runway  which
            will be offered when you use the command again.



            1122..  RRaaddaarr aanndd ttaarrggeettss
            The  radar  in  this program does NOT try to simulate a real
            radar. The real thing has many types and modes of operation.


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _2_9



            This one just cheats to get its data.
            When  enabled  ('r')  the radar measures distance, direction
            and speed of possible targets.
            In the basic mode, the radar constantly selects the  closest
            target.  This may cause it to 'jump' between targets as they
            change distance. You can put  the  radar  in  'locked'  mode
            ('l')  which  will  make it stick to the selected target. In
            this mode, when a target is destroyed,  the  nearest  target
            will  be  selected  and  stay locked. Use 'l' to release the
            lock (or you can turn the radar off/on with 'rr').
            There are 3 other acquisition modes controlled  by  the  'f'
            command.
            0         pick closest target (old way, as described above).
            1         3.3deg circle: boresight. Only targets inside  the
                      small circle are detected.
            2         20deg  circle:  HUD.  Any  target inside the large
                      circle (which covers most  of  the  HUD  area)  is
                      detected.
            3         5.3deg  wide  by  60deg  high:  vertical.  Targets
                      inside the narrow band (+-5.3 degrees wide but  60
                      degrees tall) are detected.
            In  modes 1-3, a target is highlighted when it is within the
            designated area. The limits of the modes 1-3  are  drawn  on
            the HUD.
            If  you  are  in  locked mode then the first detected target
            will immediately be locked, otherwise you will have  to  hit
            'l'  to  lock  the highlighted target. Only when a target is
            locked you get the aiming reticle (if it is close enough).
            It should be made clear that the 'locked' mode is  set/reset
            by  you with the 'l' command. Once engaged, there is no need
            to lock on targets because the first  one  to  qualify  will
            immediately be locked on. If you want then to select another
            target then use 'l' to release the target and then later 'l'
            to lock on the new one.
            Once  a  target  is locked, the selection markings disappear
            and the piper shows.
            A target is identified with a box around it (the target des-
            ignator).   When  the  target  is  out of view the box has a
            large '+' crossing it which changes to a large 'X' when  the
            target is actually behind you.
            If  you  issue Shift-C then the plane will chase the current
            target (there must be one or  the  plane  will  just  patrol
            round  the  runway).  Use the 'k' command to allow automatic
            firing ('k' works even when not in Chase mode, and is useful
            if  you want to practice the chase and let the auto-pilot do
            the shooting).
            When the reticle goes off-screen it gets a '+' inside it.
            You can shoot at various objects. Use the emit menu to  cre-
            ate these objects.
            When  you  hit  something it gets damaged and fragments fall
            off. When enough damage is done  the  object  is  officially
            HIT.  It  blinks  red/white  and  starts  falling toward the
            ground. Practice targets are  destroyed  immediately.  These
            fragments are lethal and can hit any other object!  Normally
            you can fly through any object EXCEPT a bullet  -  so  don't


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _3_0



            stay  behind a broken plane or you may be hit by the falling
            fragments.



            1133..  NNeettwwoorrkkiinngg
            As others said before, playing with oneself is fun  but  you
            don't  make as many friends (they said you'll go blind too).
            The program will let you play with others using a variety of
            communication  media.  Once  networked,  objects  are shared
            between the players. The number of players is  only  limited
            by the capability of the network medium.
            Below  here, numeric parameter values can be given in C for-
            mat, i.e. if it starts with 0x it is hex, starts with  0  is
            octal, else it is decimal.
            At the bottom of the pile is the PC to PC serial connection.
            Only two players can combine in this way. You can choose two
            drivers for this:
                 --nnccoomm..NN::bbaauudd::ppaarriittyy::bbiittss::ssttoopp::xxmmooddee::iinnbbuuff::oouuttbbuuff
            Direct  control  over the com port. It can handle any speed,
            but slow machines will drop charaters if you  go  too  fast.
            Slow machines should NOT use output buffering.
            Positional parameters:
            N              com port number: 1...4
            parity         e, o or n
            bits           8
            stop           1
            xmode          xon or xoff; do not specify!
            inbuf          4000 is enough. experiment.
            outbuf         very  little  needed  if  at  all.  Very fast
                           machines will benefit from output  buffering,
                           slow  ones will choke unless the baud rate is
                           low. At 115200 most machines cannot cope with
                           output buffering.
            Other  parameters  can  follow,  the  parameter name MUST BE
            GIVEN:
            irqN           irq number (use 4/3 as usual)
            baseNNN        port hardware  address  (use  0x3f8/0x2f8  as
                           usual)
            Example:
                 --nnccoomm..22::111155220000::nn::88::11::::44000000::::iirrqq33::bbaassee00xx22ff88
            Note that no 'xmode' was given and no 'output buffering'.
            If you prefer, you can use SLIP when you have SLIP8250:
                 sslliipp88225500 00xx6655 --hh SSLLIIPP 33 00xx0022ff88 3388440000 1100000000
                 ffllyy88 --rr --nnsslliipp..11::00xx6655
            This is the same as
                 ffllyy88 --rr --nnsslliipp..11
            because the driver will then be searched for.
            Slip is not too fast, you need both machines to be 386DX for
            full speed and even then it is touch and go. It does no out-
            put buffering.
            If  you  have  a  'real' network then install your favourite
            packet driver and do
                 ffllyy88 --rr --nnppkktt..11::00xx6655
            In this mode you can have as many players as you  wish.  The


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _3_1



            program  talks  packet level. It uses packet type 0x5a5a. In
            the future there may be support for IP level  or  more  (but
            not soon).
            OK,  you  started  the  program  with  networking. It really
            enjoys it but then it is a computer. You want  to  enjoy  it
            too.  Here  is  how.  The Net menu has a set of commands for
            managing your connections with other players.
            P         This is a broadcast ping to all players. All other
                      programs  will  respond with their identification.
                      Now you know who is active on the net. How do  you
                      tell  who's who? the parameter -Nxxx supplies your
                      handle (nickname, etc.) and you will be  known  by
                      it in this game.
            Y         Request  to  play with another player. If there is
                      only one then the program will go ahead and estab-
                      lish connection. Otherwise you will be prompted to
                      select a player from a list. To have  the  program
                      know  who  is  playing  you should have used the P
                      command first.
            Q         Quit playing. If there are more players  then  you
                      will  get a list to choose from. An empty response
                      will assume you want to quit all players.
            M         Send a message to a player.  Right  now,  an  echo
                      message  will also be sent and the turnaround trip
                      time (in milliseconds) will be shown. This time is
                      end-to-end including program delay.
            When  you  exit  the  program it will automatically quit all
            players and notify the net of your exit.
            If long delays are observed then a player may  be  automati-
            cally  timed out. You will see messages about this. Use Y to
            re-establish contact.  Proper use of Q and Y  will  let  you
            pop  out of sight in danger and re-join in a more favourable
            position...
                 IMPORTANT NOTE: the comms at this point is one-on-
                 one.  If  you  connect to three other players then
                 they all show in your world and you show in  their
                 but  they  do  not  know of each other unless they
                 establish connections too. If a  group  plays  and
                 each  one  joins  with  a global 'Y' then everyone
                 will know about everyone else.
            There  is  a  need  for  proper   'game'   management   (co-
            ordination),  now  completely  lacking. Once on the net, you
            can accept/decline a player and you can quit a player  ('Q')
            that  you  do  not  wish  to play with. See the net menu for
            details.



            1144..  CCoommmmaanndd lliinnee ooppttiioonnss
            The program accepts options at start up from three  sources,
            in order:
            Init file
                      A  file (by default 'fly.ini') is read which has a
                      list of options. Each  option  is  on  a  separate
                      line.  A  hash  '#' starts a comment line, a blank


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _3_2



                      delimits  the  line  (but   leading   blanks   are
                      skipped).  The file is searched for in the current
                      directory, then in your home directory (using  the
                      HOME  variable)  then in each directory along your
                      PATH.  You can explicitly nominate a file  as  the
                      first  parameter  on  the  command  line (the only
                      parameter accepted without a preceding hyphen).
            FLY8 environment variable
                      This variable, if defined, is a list of  semicolon
                      separated options.
            Command line
                      Finally  the  command  line  options are accepted,
                      each must be preceded by a hyphen.
            All options can be defined in all sources. The command  line
            looks like this:
                 ffllyy88 IIIInniiFFiillee LLLLooggFFiillee FFFFiilleessDDiirr MMMMaaccooFFiillee XXNNaavvFFiillee YYLLaannddFFiillee
                      PPPPllaanneeTTyyppee DDDDrroonneeTTyyppee ppPPooiinnttiinnggDDeevviiccee
                      ddVViiddeeooDDrriivveerr mmVViiddeeooMMooddee VVVViiddeeooMMooddeessFFiillee ffFFoonntt
                      bbnn qq ll vv zzNNDDrroonneess ttTTiimmeeLLiimmiitt ssPPoorrttIIOO
                      BBLLiinneeBBuuffffeerrSSiizzee rr NNHHaannddllee nnNNeettPPoorrtt

            The options are as follows:
            IIniFile       Specifies  the  name  of  an  init  file. The
                           default is 'fly.ini'. The  file  is  searched
                           for  in  the  current  directory, then in the
                           home dir (uses HOME env. var.) then the  PATH
                           directories  are checked. Only the first file
                           found is used. This option can only  be  used
                           on the command line.
            LLogFile       name  of log file. Default is 'fly.log'. This
                           option can only be used the command line.
            MMacroFile
                           name of keyboard macros file.  This  file  is
                           read  at  program  startup and written during
                           shutdown. default is 'fly.max/fly.mac']
            XNavFile
                           name  of  the  nav  data  file.  Default   is
                           fly.nav.
            YLandFile
                           name   of  the  landscape  file.  Default  is
                           fly.lnd.
            FFilesDir
                           directory where  the  support  files  (*.prm,
                           *.vxx  etc.)  are  found.  Default is current
                           directory.
            pPointer       The pointing device can be  one  of:  keypad,
                           mouse,  astick,  bstick  (but check your spe-
                           cific platform). It can have options as  fol-
                           lows  [each  option  is one byte, see example
                           later]:
                           1  [pn]   set x coord direction to [p]ositive
                                     or [n]egative.
                           2  [0-3]  set  x  coord  analog function (see
                                     below)



            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _3_3



                           3  [pn]   set y coord direction to [p]ositive
                                     or [n]egative.
                           4  [0-3]  set  y  coord  analog function (see
                                     below)
                           5  [0-9]  set  left  button   function   (see
                                     below)
                           6  [0-9]  set   right  button  function  (see
                                     below)
                           7  [0-9]  set  x  coord  sensitivity   (mouse
                                     only)
                           8  [0-9]  set   y  coord  sensitivity  (mouse
                                     only)
                           9  [01]   1 means read joystick twice

                           The analog functions are:
                           0         right/left turn
                           1         up/down turn

                           The logical functions are:
                           0         power up
                           1         power down
                           2         reset  (set  flight  direction   to
                                     straight north)
                           3         return to origin (set x,y,z=0)
                           4         stop (set speed=0)
                           5         fire
                           6         rudder left
                           7         rudder right
                           8         stable (stop turning)
                           9         rudder to center
                           10        flaps
                           11        spoilers
                           12        level: cancel roll
                           13        air brakes
                           14        gnd brakes
                           15        gear

                           Example  of  pointer parameter (read the list
                           bottom to top):


















            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _3_4



                            112233445566778899 <<--ppoossiittiioonn
                           pppp00pp1155ii000000==aassttiicckk
                           ^^^^^^^^^^^^^^^^^^^^
                           ||||||||||||||||||||
                           ||||||||||||||||||++---- rreeaadd jjooyyssttiicckk oonnccee
                           ||||||||||||||||++------ nnoo rreeaaddiinngg ddeellaayy
                           ||||||||||||||++-------- ((uunnuusseedd))
                           ||||||||||||++---------- bbuuttttoonn 22 iiss ''uunnlloocckk''
                           ||||||||||++------------ bbuuttttoonn 11 iiss ''ffiirree''
                           ||||||++++-------------- ppoossiittiivvee ccoonnttrrooll
                           ||||||            ooff uupp//ddoowwnn ffrroomm sseeccoonndd
                           ||||||            jjooyyssttiicckk iinnppuutt
                           ||++++------------------ ppoossiittiivvee ccoonnttrrooll
                           ||              ooff lleefftt//rriigghhtt ffrroomm ffiirrsstt
                           ||              jjooyyssttiicckk iinnppuutt
                           ++---------------------- tthhiiss iiss tthhee ''ppooiinntteerr'' ppaarraammeetteerr

            PPlaneType and DDroneType
                           The plane and drone type. Drone type defaults
                           to  plane  type.  Current types are F15, F16,
                           FA18 and Simple.  You  can  create  your  own
                           types.
            dVideoDriver
                           the software video driver. These vary between
                           machines.
                           MSDOS     grqc  (deflault)  or  grt4k  (tsen-
                                     glab4000 only!)
                           MSWIN     grmswin
                           UNIX      grx
                           AMIGA     gramiga
            VVideoModesFile
                           the   xxx.vmd   file   to  use.  [default  is
                           'fly.vmd']. This file defines  the  available
                           videomodes.
            mVideoMode
                           the  display  video  mode. This is one of the
                           modes defined in the .vmd file you use.
            fFont          name of text font file. (tsenglab4000 only!).
                           [default is '6x8.fnt']
            bn             screen configuration.
            r              activate net.
            NHandle        You will be known as 'Handle'.
            nNetPort       Network  access  through driver 'NetPort'. At
                           the moment only MSDOS has network support.
            q              No sound
            l              add some landscaping (very rudimentary)
            v              verbose (not used)
            zNDrones       screen-blanker mode (with 'NDRONES'  drones).
                           Equivalent   to   setting   the  screen  mode
                           'blanker' and  the  emit  function  'y'  with
                           'NDrones' number.
            sPortIO        Sega  glasses port address (com1 is 3f8, com2
                           is 2f8 etc.) Only in MSDOS version.
            tTimeLimit
                           time limit in seconds (use in batch demos).


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _3_5



            BLineBufferSize
                           number  of  segments  in  the  display  list.
                           Default is 5000.



            1155..  FFiilleess
            fly.ini
                           This  file serves as an extension to the com-
                           mand line options.  The  command-line  option
                           -I can set a user selected file name.
            fly.log
                           This  file  logs the activity of the program,
                           problem messages and final  stats.  The  com-
                           mand-line  option  -L can set a user selected
                           file name.
            fly.mac
                           This file is  read  at  program  startup  and
                           written  at program shutdown.  It is the list
                           of keyboard macros. Use the 'mac2max' program
                           to  list  the  contents  of this file. At the
                           moment there is no macro editor so you should
                           use the redefine-macro for updating. The com-
                           mand-line option -M can set a  user  selected
                           file  name.  It  is  easier  to  maintain the
                           fly.max (see  later)  manually,  the  fly.mac
                           file may be removed in the future.
            fly.max
                           This  is  a  text file which defines the key-
                           board macros. If  present  then  it  is  read
                           instead  of  the  fly.mac  file.  However, on
                           exit, it is NOT overwritten but  the  fly.mac
                           IS.  Use  the  program mac2max to convert the
                           fly.mac file to a text format.
            fly.nav
                           Lists the navigation waypoints which have ILS
                           beacons.  Should  really  be  merged with the
                           landscape file. Maybe one day. It is  created
                           from the fly.nac file using an awk script (in
                           the 'parms' directory).
            fly.lnd
                           Defines the contents of the landscape. It  is
                           created  from  the  fly.lnc file using an awk
                           script (in the 'parms' directory).
            *.vxx
                           These files define the shape  of  the  corre-
                           sponding objects.
            *.prm
                           These  files define the behaviour of the cor-
                           responding plane type. The files MUST  reside
                           in  the  current  directory. They are created
                           from the *.prc text  files  (in  the  'parms'
                           directory).
            fly.vmd
                           This  file  defines  the  parameters  for the


            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r




                                       _P_a_g_e _3_6



                           available video modes. In  windowed  environ-
                           ments  this  is  the startup mode and you can
                           then resize  the  window.   The  command-line
                           option  -V can set a user selected file name.
                           The readme should itemize the available  mode
                           files for the different environments.



            1166..  AAcckknnoowwlleeddggeemmeennttss
            Ross Johnson (rpj@ise.canberra.edu.au)
                           Ideas,   testing,  networking  know-how,  X11
                           help. Doco typesetting and review.
            Mike Taylor
                           Amiga and Windows ports.



            1177..  MMiisscc NNootteess
            When you eject ('E') you will find yourself on a  parachute.
            When  you land, you will move to a new plane. You can accel-
            erate the descent with 'd' but if  the  plane  did  not  yet
            crash  then  you  will (have to) wait on the ground until it
            crashes and a new one is provided.
            The IBMPC uses a timer chip with three counters. Fly8  reads
            counter  0 to get high resolution interval timing and writes
            counter 2 to generate speaker sound. Counter 0 is often  set
            to  the wrong mode by various programs (some examples: Land-
            mark 1.14 sets the mode to 3 while version 2.00 sets  it  to
            2)  .  The standard is mode 3, but it is sometimes set to 2.
            Fly8 needs to have the timer in the standard mode or it gets
            bad timing information.
            The  program  'gettimer' will report the current mode. If it
            is 36 or b6 then the mode is correct.  The  usual  bad  mode
            will  show  34  or b4 (the mode is the last digit divided by
            two).
            The program settimer will set the timer to mode 3.



            1188..  KKnnoowwnn PPrroobblleemmss
            o    On a 486DX50 the serial driver fails at 115200  but  is
                 ok at 57600.  Output buffering at high speed looses the
                 comms. It is now fixed  with  a  kludge  in  the  comms
                 driver.
            o    On  fast machines attempting to read the joystick twice
                 in a row produces unexpected results. A  special  delay
                 option was introduced to get around this problem.
            o    The  stroke  character generator will not handle stroke
                 sizes above 128 pixels. May be a  problem  if  you  try
                 running at very high resolutions (say 1600x1200).






            _V_e_r_s_i_o_n _0_._9_9                _F_L_Y_8            _F_l_i_g_h_t _S_i_m_u_l_a_t_o_r








                                 Table of Contents



            1. Introduction .......................................... 1
            2. Quick start ........................................... 3
            3. Installation .......................................... 5
            4. Commands Reference .................................... 5
               4.1 Alphabetic Keys ................................... 5
               4.2 Symbol Keys ....................................... 8
               4.3 Keypad ............................................ 9
               4.4 Special keys ...................................... 9
               4.5 Function keys .................................... 10
               4.6 ALT keys ......................................... 11
               4.7 CTRL keys ........................................ 11
               4.8 Arrow keys ....................................... 11
            5. Menus ................................................ 11
               5.1 Top Menu ......................................... 12
               5.2 Pointer Menu ..................................... 12
               5.3 Screen Menu ...................................... 12
               5.4 Screen.Colors Menu ............................... 13
               5.5 Screen.Stereo Menu ............................... 13
               5.6 Windows Menu ..................................... 13
               5.7 Windows.Configure Menu ........................... 14
               5.8 Info Menu ........................................ 14
               5.9 Emit Menu ........................................ 15
               5.10HUD Menu ......................................... 15
               5.11HUD.type Menu .................................... 16
               5.12HUD.parts Menu ................................... 17
               5.13HUD.options 1 Menu ............................... 17
               5.14HUD.options 2 Menu ............................... 18
               5.15HUD.radar Menu ................................... 19
               5.16Net Menu ......................................... 19
               5.17Options Menu ..................................... 20
               5.18Auto Menu ........................................ 20
               5.19Debug Menu ....................................... 21
            6. Command Line Editing ................................. 21
            7. Aural Indicators ..................................... 21
            8. Visual Indicators .................................... 21
            9. The Plane ............................................ 22
            10.The Head Up Display .................................. 23
               10.1Heading .......................................... 24
               10.2Altitude ......................................... 24
               10.3Speed ............................................ 24
               10.4Pitch ladder ..................................... 25
               10.5Velocity Vector .................................. 25
               10.6Waterline mark ................................... 25
               10.7Radar Symbology .................................. 26
                   10.7.1 Target designator   26
                   10.7.2 Aiming Reticle   26
                   10.7.3 Radar Range   27
                   10.7.4 Digital data   27
               10.8Other Features ................................... 27
            11.The ILS .............................................. 28



                                          i








            12.Radar and targets .................................... 28
            13.Networking ........................................... 30
            14.Command line options ................................. 31
            15.Files ................................................ 35
            16.Acknowledgements ..................................... 36
            17.Misc Notes ........................................... 36
            18.Known Problems ....................................... 36


















































                                         ii