DECtalk


                          Applications Support Library
                                Reference Manual






        This document describes a  support  library  for  DECtalk  which
        should  simplify  application  development for the DECtalk DTC01
        speech output terminal.

                   Document compiled Mon Feb 20 14:38:06 1984





        UNIX is  a  trademark  of  Bell  Telephone  Laboratories.   RSX,
        RSTS/E,  RT11  and  VMS  are  trademarks  of  Digital  Equipment
        Corporation.

        Touch-Tone is a tradmark of AT&T.
        Unix is a trademark of Bell Telephone Laboratories.














                                   CHAPTER 1

                                  INTRODUCTION




        DTLIB is a runtime support library for  programs  written  in  C
        programs  which  mediates  access  to  the  DECtalk DTC01 speech
        output terminal.

        It may  be  compiled  to  run  on  Vax/VMS  native  mode  (using
        Vax-11C),  Vax/VMS  compatibility  mode,  RSX11-M,  RSX11M-PLUS,
        P/OS, and RSTS/E, using Decus C.

        It may also be compiled for Unix V7M and 4.2BSD systems.

        The I/O support modules have not been implemented on RT11.

        To use DTLIB, your application program must include the dectlk.h
        header  file  with all compilations.  The loadable image must be
        linked with the DTLIB library.


                 File name conventions and RSTS/E restrictions

            Although referred to as "DTLIB" in  this  document,  the
            supplied  VMS  command  files  build VDTLIB.OLB (Vax/VMS
            native) and XDTLIB.OLB (Vax/RSX-compatibility mode).

            Decus C supports both RSX-11M and RT11  environments  on
            RSTS/E.   Only  the  RT11  environment  runs  on RSTS/E.
            While this would not be difficult  to  change,  it  will
            require edits to several modules in the library.  If you
            are using some other compiler on RSX-11M or RSTS/E,  you
            may  need  to  modify  the support libraries, CX.OLB and
            RSTSLB.OBJ.


        To run  the  DECtalk  library  on  RT11,  you  must  modify  the
        DTOPEN.C,  DTCLOS.C,  DTIOGE.C, and DTIOPU.C modules to use RT11
        specific services, such as the multi-terminal driver.

        When attaching DECtalk to a computer, you should check that  the
        terminal  line  supports the XOFF/XON protocol.  The easiest way
        to do this is to configure the terminal line as  if  it  were  a

        DECtalk Applications Support Library                     Page 1-2
        Reference Manual


        VT100 video display terminal.

        On the PRO-350, these routines assume that the DECtalk host port
        is  connected  to  the  PRO  printer  port (TT2:), using a BCC05
        printer cable.  The software  may  also  be  used  with  DECtalk
        connected to the hard-wired communications port (XK0:).

        You can test that DECtalk is properly  connected  by  copying  a
        text  file  to  that port, using the operating system COPY (PIP)
        utility.



        1.1  A sample program

        The  following  program  is   perhaps   the   simplest   DECtalk
        application.  It speaks a brief message:

        #include        <stdio.h>
        #include        "dectlk.h"

        main()
        {
                DECTALK         *dt;

                if ((dt = dt_open("TT2:")) == NULL)
                    perror("TT2:");
                else {
                    dt_talk(dt, "Hello world, this is DECtalk.");
                    dt_sync(dt);
                    dt_close(dt);
                }
        }

        The program opens the DECtalk terminal (attached  to  TT2:)  and
        speaks  a message.  It then delays until the message is heard by
        the listener and closes the device.



        1.2  Answering the phone

        The above program is adequate only  when  the  DECtalk  user  is
        "local"  to  the  device  itself.   This  would be the case in a
        factory  warning  system   or   a   computer-aided   instruction
        application.

        In many other situations, the DECtalk user  will  interact  with
        DECtalk and your application by dialing a telephone number.  You
        must then command DECtalk to answer the phone,  to  accept  data
        entered  via  the telephone keypad, and then to hangup the phone
        when the call is complete.  A suitable "top-level" program would
        then be as follows:

        DECtalk Applications Support Library                     Page 1-3
        Reference Manual


        #include        <stdio.h>
        #include        "dectlk.h"

        main()
        {
                register DECTALK        *dt;    /* Dectalk device     */
                register int    retries;        /* Initializations    */
                register int    ncalls;         /* Completed calls    */

                retries = 0;
                ncalls = 0;
                if ((dt = dt_open("TT2:")) == NULL) {
                    perror("TT2:);              /* Can't open device  */
                    exit(IO_ERROR);             /* Exit program       */
                }
                dt_trap();                      /* Catch CTRL/C abort */
                while (dt_init(dt)) {           /* One-time setup     */
                    dt_dcs(dt, P2_MODE, MODE_SQUARE, -1);
                    retries++;                  /* Count attempts     */
                    while (dt_answer(dt, 1)) {  /* Answer the phone   */
                        if (process(dt)) {      /* Do user process    */
                            ncalls++;           /* User ran ok,       */
                            retries = 0;        /* Clear retry count  */
                        }
                        dt_hangup(dt);          /* Hangup the phone   */
                        if (dt_abort)           /* Check interrupt    */
                            goto finis;         /* Error exit         */
                    }
                    if (dt_abort)               /* CTRL/C interrupt?  */
                        goto finis;             /* Error exit         */
                    if (retries > 2) {          /* Confused?          */
                        printf("Too many retries\n");
                        break;
                    }
                }
        finis:  dt_abort = FALSE;               /* Restart output     */
                dt_reset(dt);                   /* Hangup DECtalk     */
                dt_put(dt, 0);                  /* Force out buffer   */
                dt_close(dt);                   /* Close up DECtalk   */
        }

        The above program fragment attempts to recover  from  transitory
        "line   glitches"  by  allowing  error  returns  from  the  user
        process() and from dt_answer().  If, however, dt_answer()  fails
        twice in a row, the program aborts.  It also establishes "CTRL/C
        trapping" which will allow the developer to  abort  the  program
        without losing log files.

        Note also that "square-bracket" phonemic mode is turned on  when
        the terminal is initialized.

        The essential flow of the above program (without error  recovery
        or interrupt processing) may be seen as follows:

        DECtalk Applications Support Library                     Page 1-4
        Reference Manual


        #include        <stdio.h>
        #include        "dectlk.h"

        main()
        {
                register DECTALK        *dt;    /* Dectalk device     */

                if ((dt = dt_open("TT2:")) == NULL) {
                    perror("TT2:);              /* Can't open device  */
                    exit(IO_ERROR);             /* Program fails      */
                }
                if (dt_init(dt)) {              /* One-time setup     */
                    while (dt_answer(dt, 1)) {  /* Answer the phone   */
                        process(dt);            /* Do user process    */
                        dt_hangup(dt);          /* Hangup the phone   */
                    }
                }
                dt_close(dt);                   /* Close up DECtalk   */
        }




        1.3  The User Process

        When the phone is answered, the  main  program  described  above
        will   call   an  application-specific  subroutine.   This  will
        generally have the following control flow:

        1.  Welcome the user to the application.

        2.  Enable the telephone keypad.

        3.  Ask for a command (enabling keypad timeouts to recover  from
            a disconnection).

        4.  Process the command and  continue  to  process  commands  as
            needed.

        5.  Eventually, finish the application and return  to  the  main
            program  (which  will  hangup  the phone and prepare for the
            next caller).

        The following code  fragment  illustrates  a  very  simple  test
        program that echos the user's key presses:

        DECtalk Applications Support Library                     Page 1-5
        Reference Manual


        #include        <stdio.h>
        #include        "dectlk.h"

        process(dt)
        register DECTALK        *dt;
        {
                register char   c;              /* Keypad character   */
                char            work[30];       /* For echo message   */

                dt_talk(dt, "Welcome to DECtalk");
                if (!dt_keypad(dt, TRUE))       /* Enable keypad      */
                    return (FALSE);             /* Error occurred     */
                for (;;) {                      /* Do forever...      */
                    c = dt_inkey(dt, 15);       /* Get a key          */
                    if (!dt_isvalid(c))         /* Check for timeout  */
                        return ((c == 'T') ? TRUE : FALSE);
                    sprintf(work, "You pressed %c%c", c, VT);
                    dt_talk(dt, work);
                    if (c == '*') {             /* Make '*' special   */
                        dt_timeout(dt, 0);      /* No timeouts now    */
                        dt_talk(dt, "Long message...");
                    }
                }
        }

        Note that the "long  message"  turns  off  timeouts.   If  still
        "alive",  DECtalk  will respond to the timeout message within 15
        seconds.  If the hardware has been disconnected,  the  operating
        system  timeout  will  occur in a minute or so (depending on the
        operating system), which will eventually cause an  error  return
        from the program.

        Because the user may press buttons when you don't  expect  them,
        it  is  very  important  to  call  dt_inkey()  to  read from the
        Touch-tone keypad.  Dt_inkey() contains  a  "type-ahead"  buffer
        and  understands timeouts.  It either returns a single character
        corresponding to the keypad button or a  character  representing
        an unusual situation:

          T A timeout occurred (and timeouts were enabled at the time).

          H The DECtalk hardware hung up the phone.  (This  is  required
            under certain circumstances in certain countries.)

          E An  operating  system  error  (probably  hardware   timeout)
            occurred.

          X An illegal escape sequence was  received.   This  may  be  a
            communication line problem.

        See the documentation of dt_inkey() for further details.

        DECtalk Applications Support Library                     Page 1-6
        Reference Manual


        1.4  Some Other Tricks

        This section contains a few other coding hints.



        1.4.1  Transmitting Phonemic Text

        The examples assume that  most  applications  will  use  "square
        bracket"  mode to transmit phonemic text and voice commands.  If
        this is not suitable, the program will have  to  format  a  more
        complex escape sequence as follows:

                dt_cmd(dt, P2_PHOTEXT, -1);
                dt_talk(dt, ":np :ra 180 hh'ehlow.");
                dt_st(dt);

        A similar sequence  would  be  needed  to  load  DECtalk's  user
        dictionary.



        1.4.2  Managing Keypad Timeout

        When your program requests information from the telephone  user,
        it  is  essential  that  you  use  some  form of timeout so your
        program won't hang if the caller  disconnects.   The  dt_inkey()
        routine is the recommended way to read from the keypad:

                key = dt_inkey(dt, timeout);

        You can use different  timeouts  for  different  parts  of  your
        program.   For example, the following code fragment reads a user
        password (which may contain one to six digits) from the  keypad.
        It has a long timeout for the first character and short timeouts
        for successive characters:

                dt_talk(dt, "Please enter your password");
                dt_talk(dt, NULL);
                timeout = 10;
                for (i = 0; i < 6; i++) {
                    key = dt_inkey(dt, timeout);
                    if (!dt_isvalid(key))
                        break;                  /* Assume timeout    */
                    password[i] = key;          /* Save the key      */
                    timeout = 2;                /* Short time now    */
                }
                password[i] = EOS;              /* Terminate entry   */

        On exit from the loop, The password string will contain the data
        entered.   If  password[0]  is  EOS,  nothing was entered before
        timeout.

        DECtalk Applications Support Library                     Page 1-7
        Reference Manual


        1.4.3  Stopping in Mid-stream

        If you are sending a long stream of text to the  user,  you  may
        want  to  allow  a  keypad button press to stop the speech.  The
        following subroutine takes an array of  strings  to  be  spoken.
        The  array  is  terminated by a NULL entry.  It returns FALSE if
        nothing was pressed (and everything was transmitted to DECtalk),
        or  TRUE  if something was pressed.  (Your program reads the key
        by calling dt_inkey().

        To restart cleanly after a  TRUE  return,  your  program  should
        retransmit a voice definition "[:np]" before anything else.

            int
            dt_speak(dt, strings)
            register DECTALK    *dt;
            register char       **strings;
            {
                dt_timeout(dt, 0);
                while (*strings != NULL) {
                    dt_talk(dt, *strings++);
                    dt_msg(dt, P2_IX_QUERY, -1, -1, R2_IX_QUERY, -1);
                    if (dt_iskey(dt)) {
                        dt_dcs(dt, P2_STOP, -1, -1);
                        return (TRUE);
                    }
                }
                return (FALSE);
            }

        The module does the following:

        1.  Disables keypad timeouts.

        2.  For each string in the string array...

        3.  Transmit the string to DECtalk (dt_talk()).

        4.  Transmit an Index Query  operation  (dt_msg()).   This  will
            read  data  from  DECtalk  and,  as a side-effect, store any
            keypress in the internal type-ahead buffer.

        5.  Check whether there is anything  in  the  type-ahead  buffer
            (dt_inkey()).  If so,

        6.  Stop speaking (dt_dcs()) and return TRUE.

        7.  If nothing is in the type-ahead buffer,  continue  with  the
            next   string   or   return  FALSE  when  all  strings  were
            transmitted.


        DECtalk Applications Support Library                     Page 1-8
        Reference Manual


        1.4.4  Reading Names from the Keypad

        Touch-Tone keypads transmit a unique code when  each  button  is
        pressed.   DECtalk  transmits  an Ascii character for each code.
        However,  an  application  designer  may  want   to   tell   the
        application's  user  "Press  the Y key for Yes and the N key for
        No.", or may need to compare text from the keypad with  commands
        or  usernames  which  are  encoded  in ordinary Ascii text.  The
        following function tests whether a keypad text string  (as  read
        from  DECtalk)  matches a text word in alphabetic Ascii.  As you
        can see, it assumes that the '7' button is labelled  "PQRS"  and
        the '9' button is labelled "WXYZ".

        Note:  the strchr() function returns NULL if the second argument
        (a  character)  was  not  one  of  the  characters  in the first
        argument string.  On some Unix systems, the  function  is  named
        "index".  It is comparable to the Basic-Plus INSTR() function.

        static char *btext[] = {
                                "2ABCabc",      "3DEFdef",
                "4GHIghi",      "5JKLjkl",      "6MNOmno",
                "7PQRSpqrs",    "8TUVtuv",      "9WXYZwxyz",
        };
        int
        buttontest(kptext, match)
        register char   *kptext;        /* Button format      */
        register char   *match;         /* ASCII format       */
        {
                extern char     *strchr();
                for (;;) {
                    if (*kptext == *match) {
                        if (*kptext == '\0')
                            return (TRUE);
                    }
                    else if (*kptext < '2' || *kptext > '9'
                          || strchr(btext[*kptext - '2'],
                                *match) == NULL)
                        return (FALSE);
                    text++;
                    match++;
                }
        }




        1.4.5  Speaking numbers or strings

        Financial applications ("bank balance by  phone")  may  want  to
        speak  numbers  twice,  once  as a "normal number" and once as a
        string of digits so  the  listener  can  copy  them  down.   The
        following  Basic-Plus  subroutine  takes  a  string  of text and
        expands it to one-letter  words.   Using  it,  a  program  would
        generate a message such as:

        DECtalk Applications Support Library                     Page 1-9
        Reference Manual


            Your balance is $1425.92, that is one four
            two five point nine two.


        3000    !*                                            &
                !*      F N e x p a n d $ ( t e x t $ )       &
                !*                                            &
                !* Expand a string into its component bytes.  &
                !* Note that this would be useful in a "bank  &
                !* by phone" application to speak a number,   &
                !* digit by digit, so the caller could copy   &
                !* it down.  If the input is "12.3", the      &
                !* output will be " 1 2 point 3".  Note the   &
                !* leading blank.                             &
                !*                                            &
                def* FNexpand$(text$)                         &
                \ q$ = ""                       ! Output work &
                \ for q% = 1% to len(text$)     ! For each,   &
                    \ q1$ = mid(text$, q%, 1%)  ! Locate byte &
                    \ q1$ = "point" if q1$ = '.'              &
                    \ q1$ = "minus" if q1$ = '-'              &
                    \ q1$ = "dollar sign" if q1$ = '$'        &
                    \ q$ = q$ + " " + q1$       ! Store byte  &
                \ next q%                       ! Do 'em all  &
                \ FNexpand$ = q$                ! That's it   &
                \ fnend                                       &

        Note that certain  bytes  are  "spelled  out"  to  override  the
        DECtalk built-in library.

        It is a simple matter to rewrite this in  C  and/or  extend  the
        list of "special case" bytes.



        1.5  Summary

        The above examples should be sufficient to  help  you  past  the
        initial confusion that every programmer feels when faced with an
        unfamiliar device.

        Although the library may appear to have a complex structure, the
        major control flow is relatively simple:

        DECtalk Applications Support Library                    Page 1-10
        Reference Manual


                             Application Program
                                     |
            +----+----+--------+-----+---+--------+-------+-------+
            |    |    |        |         |        |       |       |
        dt_inkey | dt_init dt_answer dt_hangup dt_talk dt_open dt_close
         |   |   |    |       |  |       |        |
         |   +-+-+    |       |  +---+---+        |
         |     |      |       |      |            |
         | dt_timeout |       |   dt_phone        |
         |     |      |       |      |            |
         |     +------+-------+------+            |
         |                    |                   |
         |                  dt_msg     dt_dcs     |
         |                  | | |        |        |
         +------+-----------+ | +----+   |        |
                |             |      |   |        |
             dt_read       dt_save  dt_pesc       |
                |                      |          |
                |                      |          |
             dt_gesc                   +----+-----+
                |                           |
             dt_get                      dt_put
                |                           |
             dt_ioget                    dt_ioput


        Library modules communicate with DECtalk by one of three general
        paths:

        1.  They speak text by calling dt_talk() or dt_put().

        2.  They send escape sequences by calling dt_dcs() or dt_pesc().

        3.  They send  DECtalk  control  sequences  that  will  generate
            replies by calling dt_msg().

        4.  They receive keypad characters by calling dt_inkey().

        As should be expected, there are a few special cases  to  handle
        unusual circumstances.

        Also,  the  library  does  not  address   the   need   to   load
        dictionaries, send phonemic text using escape sequences, or test
        DECtalk hardware status.

        DECtalk Applications Support Library                    Page 1-11
        dectlk.h        DECtalk Library Header File


        1.6  DECtalk Library Header File             _______ _______ ______ ____



                                  ************
                                  * dectlk.h *
                                  ************



        NAME:   dectlk.h -- DECtalk Library Header File

        SYNOPSIS:

                #include "dectlk.h"

        DESCRIPTION:

                This file is included in the compilation of all  modules
                that  use  the DECtalk applications library.  It defines
                common  ASCII  characters,   DECtalk   escape   sequence
                parameters,  library  globals,  and  the  DECTALK buffer
                structure.

        CONFIGURATION:

                You can  edit  dectlk.h  to  enable  debugging  code  by
                defining the DT_DEBUG flag as follows:

                    #define DT_DEBUG 1

                This changes the primary input and  output  routines  so
                that  they  become  capable  of  logging  all characters
                transmitted to and from the DECtalk device.

        GLOBALS:

                The library provides two global flags which are used  as
                follows:

                dt_abort        This is set non-zero by  an  intercepted
                                CTRL/C   trap   (if   you   have  called
                                dt_trap()).  When set, no  I/O  will  be
                                performed,  and library subroutines will
                                exit as quickly as possible.

                dt_debug        This  may  be   set   non-zero   by   an
                                applications  program  to  enable  debug
                                printouts.  Note that the  library  must
                                have been compiled with DT_DEBUG defined
                                in order to  compile  in  the  necessary
                                print calls.

        ERROR CODES:

        DECtalk Applications Support Library                    Page 1-12
        dectlk.h        DECtalk Library Header File


                The library may return the following error codes.  These
                are  all less than zero, and consequently cannot be part
                of the ASCII character set:

                DT_ERROR        An operating-system error.
                DT_TIMEOUT      An input operation did not complete in
                                the required (operating-system) time.
                IO_ERROR        An error exit code for the exit()
                                library routine.  The value is selected
                                as appropriate for the particular
                                operating system.

        ROUTINES IMPLEMENTED AS MACROS:

                Certain frequently routines may be implemented as macros
                (if  macro  expansion  is  supported by the particular C
                compiler).  These are as follows:

                dt_iskey(dt)        TRUE if data is currently stored in
                                    the keypad type-ahead buffer.
                dt_isvalid(c)       TRUE if the character is a valid
                                    keypad character.  Note:  evaluation
                                    of the argument must not have
                                    side-effects.  I.e., you must not
                                    write dt_isvalid(*p++).
                dt_ptest(dt,r3)     Phone test, TRUE if the current
                                    reply is R2_PHONE, R3.
                dt_offhook(dt)      Phone test, TRUE if the current
                                    reply is R2_PHONE, R3_PH_OFFHOOK.
                dt_onhook(dt)       Phone test, TRUE if the current
                                    reply is R2_PHONE, R3_PH_ONHOOK.
                dt_istimeout(dt)    Phone test, TRUE if the current
                                    reply is R2_PHONE, R3_PH_TIMEOUT.
                dt_phone(dt,p3,p4)  Send a phone message.
                dt_eol(dt)          Send "end of line" and force output
                                    to DECtalk.

        GENERAL DEFINITIONS:

                The following variables are defined:

                EOS             End of string
                FALSE           For TRUE/FALSE testing
                TRUE            For TRUE/FALSE testing

        ASCII CHARACTERS:

                The following C0 control characters are defined:

                  NUL   STX   ETX   BEL    BS    VT   LS1
                  LS0   XON  XOFF   CAN   SUB   ESC   DEL

                The following C1 control characters are defined:

        DECtalk Applications Support Library                    Page 1-13
        dectlk.h        DECtalk Library Header File


                  SS2   SS3   DCS OLDID   CSI    ST   OSC
                   PM   APC  RDEL

                The  following  DECtalk-specific  parameters  are   also
                defined.

                CSI_DA_PRODUCT  The DECtalk product identification code.
                DCS_F_DECTALK   The DECtalk specific device control
                                sequence (DCS) final character.
                P1_DECTALK      All DCT01 DCS sequences transmit this
                                for their first (P1) parameter.
                R1_DECTALK      All DCT01 DCS replies transmit this for
                                the first R1 reply parameter.

                The P2 and P3 parameters  select  the  specific  DECtalk
                command.

                P2_PHOTEXT      Speak phonemic text.
                P2_STOP         Stop speaking.
                P2_SYNC         Synchronize.
                P2_SPEAK        Enable/disable speech.
                P2_INDEX        Index text.
                P2_IX_REPLY     Index with reply.
                P2_IX_QUERY     Return last spoken index.
                P2_DICT         Load user dictionary.
                P2_PHONE        Telephone control.
                P2_MODE         Synthesis mode control.
                P2_LOG          Local terminal log control.
                P2_TERMINAL     Local terminal control.

                The  telephone  control  command  takes  an   additional
                parameter to specify the specific telephone action.

                P3_PH_STATUS    Return a status report.
                P3_PH_ANSWER    Answer on P4 rings.
                P3_PH_HANGUP    Hangup the phone.
                P3_PH_KEYPAD    Enable keypad data entry.
                P3_PH_NOKEYPAD  Disable keypad data entry.
                P3_PH_TIMEOUT   Send a timeout report if no data entered
                                in P4 seconds if P4 is greater than
                                zero;  disable timeouts if P4 is zero.
                P3_PH_TONE      Dial out using tones.
                P3_PH_PULSE     Dial out using pulses.

                Several P2 commands return messages to the host:

                R2_IX_REPLY     Reply to P2_IX_REPLY.  R3 contains the
                                last index processed.
                R2_IX_QUERY     Reply to P2_IX_QUERY.  R3 contains the
                                last index processed.
                R2_DICT         Reply to P2_DICT.  R3 contains the
                                dictionary entry status code.
                R2_PHONE        Reply to P2_PHONE.  R3 contains the
                                telephone status.

        DECtalk Applications Support Library                    Page 1-14
        dectlk.h        DECtalk Library Header File


                The  following  R3  parameters  are  returned  after   a
                P2_PHONE command.

                R3_PH_ONHOOK    Telephone is hung up (inactive).
                R3_PH_OFFHOOK   Telephone is answered (active).
                R3_PH_TIMEOUT   No data was entered by the telephone
                                user within the required number of
                                seconds.
                R3_PH_TOOLONG   A telephone number to dial is too long.

                The following R3 parameters are returned after a P2_DICT
                command:

                R3_DI_LOADED    Dictionary entry was loaded.
                R3_DI_NOROOM    The user dictionary is full.
                R3_DI_TOOLONG   The dictionary entry is too long.

                The following codes are used to  control  host-requested
                self test (DECTST):

                TEST_POWER      Rerun power up test.
                TEST_HDATA      Host data link loopback test.
                TEST_HCONTROL   Host line control test.
                TEST_LDATA      Local line data test.
                TEST_SPEAK      Speak a canned message.

                The following status codes are returned by the  extended
                DSR sequence:

                DSR_OK          No errors detected.
                DSR_COMFAIL     Communication failure.
                DSR_INBUFOVER   Input buffer overflow.
                DSR_DECNVRFAIL  Last restore from non-volatile memory
                                failed.
                DSR_PHONEME     Incorrect phoneme entered.
                DSR_PRIVATE     DECtalk DCS parameter error.
                DSR_DECTSTFAIL  Last DECTST self-test failed.

                The following flags configure the P2_LOG command:

                LOG_TEXT        Log spoken text.
                LOG_PHONEME     Log generated phonemes.
                LOG_RAWHOST     Log all characters received from host
                                without change.
                LOG_INHOST      Log all characters received from host in
                                "visible" format.
                LOG_OUTHOST     Log all output to host in visible
                                format.
                LOG_ERROR       Log error messages.
                LOG_TRACE       Log commands in mnemonic form.

                The following flags are for the P2_TERMINAL command:

                TERM_HOST       Send text entered from the local

        DECtalk Applications Support Library                    Page 1-15
        dectlk.h        DECtalk Library Header File


                                terminal to the host.
                TERM_SPEAK      Speak text entered from the local
                                terminal.
                TERM_EDITED     Line-edit text entered from the local
                                terminal.
                TERM_HARD       Use hard-copy edit conventions.
                TERM_SETUSPEAK  Speak SETUP dialog.

                The following flags are for the P2_MODE command:

                MODE_SQUARE     [ ] bracket phonemic text.
                MODE_ASKY       Use single-letter phonemic alphabet.
                MODE_MINUS      Pronounce '-' as "minus".

                The following flags are for the dt_splice() function.

                SPLICE_SPEAK   DECtalk speaks text if set.
                SPLICE_LOG     Text sent to DECtalk is sent to the
                                terminal (P2_LOG, LOG_RAWHOST).
                SPLICE_TERM    The terminal may send text to DECtalk
                                (P2_TERM, TERM_HOST).

        ESCAPE SEQUENCE DATA BUFFER:

                All information needed  to  generate  and  parse  escape
                sequences  is  contained in the SEQUENCE data structure.
                It is configured by the following size constants:

                SEQ_INTMAX      Maximum number of intermediate
                                characters.
                SEQ_PARMAX      Maximum number of parameters.

                It contains the following components:

                short state     Processing state or introducer character
                                to send.
                char final      Final character in sequence.
                char private    Private introducer character or 'X' to
                                indicate an error.
                short param[]   Private parameters (unsigned);  param[0]
                                contains the number of parameters.
                char inter[]    Intermediate characters;  inter[0]
                                contains the number of intermediates.

        DECTALK DATA BUFFER DEFINITION:

                All  information  needed  by  the  DECtalk  applications
                library is contained in the DECTALK data structure which
                is created by dt_open() and freed by dt_close().  It  is
                configured by the following parameters:

                PEND_SIZE       Maximum number of keypad characters that
                                may be typed-ahead.  Additional
                                characters are discarded.

        DECtalk Applications Support Library                    Page 1-16
        dectlk.h        DECtalk Library Header File


                IN_BUFLEN       Size of the operating system input
                                buffer.
                OUT_BUFLEN      Size of the operating system output
                                buffer.

                The data buffer contains the following information:

                DECTALK *link   Chains together all active units.
                short unit      Operating system I/O channel.
                short timeout   Current timeout value
                short flag      Speech and dtsplice flags.
                short pend_fc   Bytes in pending buffer.
                short pend_fp   Index to free byte in pending buffer.
                short pend_ep   Index to next byte to return from
                                pending buffer.
                char *in_ptr    Input buffer pointer.
                char *in_end    Input buffer end.
                char *outptr    Output buffer free pointer.
                SEQUENCE send   Last DCS sequence sent.
                SEQUENCE reply  Last DECtalk reply received.
                SEQUENCE seq    Look-ahead for string terminator
                                processing.
                char *device    Remember dtopen() device name for debug
                                printouts.
                char pend[]     Type-ahead buffer.
                char inbuff[]   Input buffer.
                char outbuff[]  Output buffer.
                struct sgtty stty_save Terminal characteristics block
                                (Unix).
                FILE *fildes    File descriptor (RSX).
                struct iosb iosb I/O status block (RSX).
                QIOPARM parm     QIO parameter block (RSX).  (RSX only).
                int pos_xk       TRUE if POS XK:  driver (RSX only).

                The flag entry values are set  and  cleared  internally.
                It should not be changed by application programs.

                _FLAG_SPEAK     Set if DECtalk is speaking.
                _FLAG_LOG       Set if LOG RAWHOST is set.
                _FLAG_TERM      Set if TERM HOST is set.


        DECtalk Applications Support Library                    Page 1-17
        dt_answer      Answer the Telephone


        1.7  Answer the Telephone             ______ ___ _________



                                 *************
                                 * dt_answer *
                                 *************



        NAME:   dt_answer -- Answer the Telephone

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_answer(dt, nrings)
                DECTALK         *dt;    /* Device descriptor    */
                int             nrings; /* Number of rings      */

        DESCRIPTION:

                Hangup the phone (by calling dt_hangup()) and answer the
                phone after the specified number of rings.

                Return TRUE if successful, FALSE if in error.


        DECtalk Applications Support Library                    Page 1-18
        dt_close       Terminate DECtalk Operation


        1.8  Terminate DECtalk Operation             _________ _______ _________



                                  ************
                                  * dt_close *
                                  ************



        NAME:   dt_close -- Terminate DECtalk Operation

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_close(dt)
                DECTALK         *dt;    /* DECtalk device       */

        DESCRIPTION:

                Close the DECtalk channel  and  free  all  buffers.   No
                error is returned.


        DECtalk Applications Support Library                    Page 1-19
        dt_cmd Send DCS w/o String Terminator


        1.9  Send DCS w/o String Terminator             ____ ___ ___ ______ __________



                                   **********
                                   * dt_cmd *
                                   **********



        NAME:   dt_cmd -- Send DCS w/o String Terminator

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_cmd(dt, p2, p3)
                DECTALK         *dt;    /* Device descriptor    */
                int             p2;     /* P2_... parameter     */
                int             p3;     /* P3_... parameter     */

        DESCRIPTION:

                This  routine  sends  a  DCS  command  to  the   DECtalk
                terminal.   The  string terminator is not sent.  This is
                needed to send phonemic text or telephone dial commands.

                The p2 or p3  parameter  may  be  -1  if  it  is  to  be
                ommitted.

                A phonemic text sequence would be sent as follows:

                    dt_cmd(dt, p2, p3);
                    dt_talk(dt, "hh'ehlow.");
                    dt_st(dt);


        DECtalk Applications Support Library                    Page 1-20
        dt_dchar       Dump One Character Visibly


        1.10  Dump One Character Visibly              ____ ___ _________ _______



                                  ************
                                  * dt_dchar *
                                  ************



        NAME:   dt_dchar -- Dump One Character Visibly

        SYNOPSIS:

                #include        <stdio.h>

                dt_dchar(c, iov)
                int             c;      /* Character to dump    */
                FILE            *iov;   /* File to write to     */

        DESCRIPTION:

                The  character  is  formatted  into  a   visible   Ascii
                "Datascope" format and the resulting text written to the
                indicated file.

                Note  that  this  routine  is  independent  of   DECtalk
                definitions.

                Output is via the C standard library.  If the dump is to
                a terminal, it is unbuffered.


        DECtalk Applications Support Library                    Page 1-21
        dt_dcs Send a DECtalk DCS Command


        1.11  Send a DECtalk DCS Command              ____ _ _______ ___ _______



                                   **********
                                   * dt_dcs *
                                   **********



        NAME:   dt_dcs -- Send a DECtalk DCS Command

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_dcs(dt, p2, p3, p4)
                DECTALK         *dt;    /* Device descriptor    */
                int             p2;     /* P2_xxx parameter     */
                int             p3;     /* P3_PH_xxxx parameter */
                int             p4;     /* timeout or rings     */

        DESCRIPTION:

                This routine sends a DECtalk DCS control sequence  using
                the p2, p3, and p4 parameters.

                Note that the Pn parameters are -1 if they are not sent.

                No errors are possible.


        DECtalk Applications Support Library                    Page 1-22
        dt_dial        Dial the Telephone


        1.12  Dial the Telephone              ____ ___ _________



                                  ***********
                                  * dt_dial *
                                  ***********



        NAME:   dt_dial -- Dial the Telephone

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_dial(dt, p3, numb, wait, msg)
                DECTALK         *dt;    /* Device descriptor    */
                int             p3;     /* P3_PH_xxxx parameter */
                char            *numb;  /* Number to dial       */
                int             wait;   /* See below            */
                char            *msg;   /* Announcement         */

        DESCRIPTION:

                This  routine  dials  the  DECtalk  telephone.   The  P3
                parameter  must  be  either  P3_PH_TONE  (tone  dial) or
                P3_PH_PULSE (pulse dial).

                For tone dialing, the number text may contain any  valid
                touch-tone   characters   ("0123456789*#ABCD")   or  the
                characters '!' (for a one second delay) or the '^' for a
                250 millisecond switch-hook flash.  All other characters
                are ignored.

                If pulse dialing is selected, only the digits,  '!'  and
                '^' are interpreted.

                Note that the telephone  will  not  be  hung  up  before
                dialing if it is offhook when the command is issued.

        CALL PROGRESS DETECTION:

                DECtalk cannot tell  if  or  when  someone  answers  the
                phone.   The  only way to do this is to speak a message,
                such as "This is DECtalk, please press any button on the
                keypad."  and  wait  some limited time for the person to
                press the button.  The wait and msg  parameters  provide
                this capability.

                If wait is less than or equal to zero,  DECtalk  returns
                without  attempting  to verify that someone has answered

        DECtalk Applications Support Library                    Page 1-23
        dt_dial        Dial the Telephone


                the phone.  The return will be  TRUE  if  the  phone  is
                offhook.

                If wait is greater than zero, it specifies the number of
                seconds  to  wait for a response, and msg is the message
                to speak.  (If msg is NULL, the sample text shown  above
                will  be  used.)  The  message  is repeated continuously
                until either the alloted time has elapsed or a button is
                received.   dt_dial()  then returns TRUE if the phone is
                offhook, as above.

                To cause DECtalk to silently wait for a message,  use  a
                zero-length string ("").  Note, however, that an audible
                message is required by some public telephone systems.

                When DECtalk  returns  after  call  progress  detection,
                keypad data entry and keypad timeout will be disabled.


        DECtalk Applications Support Library                    Page 1-24
        dt_drain       Drain Pending Input


        1.13  Drain Pending Input              _____ _______ _____



                                  ************
                                  * dt_drain *
                                  ************



        NAME:   dt_drain -- Drain Pending Input

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_drain(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                Absorb  any  type-ahead  characters.   No   errors   are
                possible.

        NOTE:

                On some unix systems the I/O control function is  stored
                in  the  <sgtty.h>  system  library  header,  while,  on
                others, it is stored on <ioctl.h>.  You may have to edit
                this file accordingly.

                The distributed sources are  correct  for  Unix  V7M  as
                implemented on the DEC Professional 350.

                On unix systems, dt_drain()  will  also  cancel  pending
                output.    This   may  cause  DECtalk  to  receive  word
                fragments or partial escape sequences.


        DECtalk Applications Support Library                    Page 1-25
        dt_dump        Dump Escape Sequence Buffer


        1.14  Dump Escape Sequence Buffer              ____ ______ ________ ______



                                  ***********
                                  * dt_dump *
                                  ***********



        NAME:   dt_dump -- Dump Escape Sequence Buffer

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectk.h"

                int
                dt_dump(what, seq)
                char            *what;  /* Explanation          */
                SEQUENCE        *seq;   /* Buffer to dump       */

        DESCRIPTION:

                The  requested  escape  sequence   buffer   is   written
                (visibly) to the standard output file.

                If what is not NULL, it is written as an identifier.

                Output is via the C standard library.

                For example,

                    #include <stdio.h>
                    #include "dectlk.h"

                    DECTALK *dt;
                    extern DECTALK *dt_open();
                    ...
                        /*
                         * Open a DECtalk device,
                         * request phone status and
                         * dump returned status sequence.
                         */
                        dt = dt_open("kb2:");
                        dt_phone(dt, P2_PH_STATUS, -1);
                        dt_dump("status", &dt->reply);


        DECtalk Applications Support Library                    Page 1-26
        dt_eol Write End of Line to DECtalk


        1.15  Write End of Line to DECtalk              _____ ___ __ ____ __ _______



                                   **********
                                   * dt_eol *
                                   **********



        NAME:   dt_eol -- Write End of Line to DECtalk

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_eol(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                An "end of line" is written to DECtalk and the operating
                system  executive  service  is called to cause the local
                output buffer to be written to the terminal.

                No value is returned.

                This routine is needed on operating systems that enforce
                "line   wrap-around"   on  terminal  devices.   It  also
                improves the appearance of debugging logs.


        DECtalk Applications Support Library                    Page 1-27
        dt_gesc        Read Escape Sequence or Character


        1.16  Read Escape Sequence or Character              ____ ______ ________ __ _________



                                  ***********
                                  * dt_gesc *
                                  ***********



        NAME:   dt_gesc -- Read Escape Sequence or Character

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_gesc(dt, sec)
                DECTALK         *dt;    /* Device descriptor    */
                char            sec;    /* O.S. timeout value   */

        DESCRIPTION:

                Read an escape sequence or keypad character.

                dt_gesc() interprets a stream of 7- or 8-bit  characters
                including   escape   sequences  adhering  to  the  coded
                representations of ISO 646, ISO 2022, and ISO 6429  with
                extensions  to  the  DCS  introducer  as required by DEC
                Standard 138.

                The function dt_gesc() recognizes ESC, CSI, and DCS, and
                processes characters following each of these introducers
                until a complete sequence is encountered.  In  the  case
                of  DCS,  control  returns to the caller after the final
                character of the DEC Standard 138 introduction sequence,
                but  before  the  first  data  character  of  the device
                control string.

                When  sandwiched  between  the  application  and  a  get
                character  function (dt_get()), dt_gesc() transforms the
                input stream from a character  stream  to  a  stream  of
                tokens   consisting  of  characters,  escape  sequences,
                control sequences, and DCS introduction sequences.  When
                any of the recognized sequence types is encountered, the
                function value returned is that of ESC, CSI, or DCS, and
                the interpretted body of the sequence is returned in the
                seq structure.  The caller may treat dt_gesc() similarly
                to  getchar(),  ignoring  the  returned structure in all
                cases except when the returned function  value  is  ESC,
                CSI, or DCS.

                An additional function performed by  dt_gesc()  is  that

        DECtalk Applications Support Library                    Page 1-28
        dt_gesc        Read Escape Sequence or Character


                all  C1  control  functions received in their 7-bit form
                are returned to the caller in  their  8-bit  form,  thus
                eliminating  the  need  for  the  caller  to  process C1
                control functions in their (7-bit) escape sequence  form
                and  enforcing  the  equivalence  of the 7-bit and 8-bit
                forms of the C1 control functions.   The  function  also
                enforces the sequence cancellation effect of the SUB and
                CAN control characters.

                The dt_gesc() function calls the user-supplied  dt_get()
                (read  one character) function as many times as required
                to complete an escape  sequence,  control  sequence,  or
                Digital  standard  DCS  introduction  sequence.   In the
                passed data structure, it returns the  final  character,
                intermediate characters, and parameter values.

                Since 7-bit operation is a compatible  subset  of  8-bit
                operation, there is -- normally -- no distinction in the
                dt_gesc() function between the  two  environments.   The
                DECtalk  library,  however,  enforces  a  7-bit external
                environment.  Also,  dt_get()  may  return  two  special
                values,    DT_ERR    and    DT_TIMEOUT,    to   indicate
                operating-system errors and communication line  timeouts
                respectively.

                Because  C0  control  characters  may  be  embedded   in
                sequences,  and must be interpretted as if they occurred
                before  the  sequence  in  the  stream,  the   dt_gesc()
                function  retains  internal  state  information  in  the
                sequence  data  structure  from  call  to   call.    The
                seq.state value is zero on return to indicate a complete
                escape sequence.  If non-zero, it contains the  sequence
                introducer.

                If the "seq.state" element is  zero,  dt_gesc()  assumes
                that  the remainder of the data structure is invalid and
                that there is no data being retained from a prior  call.
                A non-zero value for the "seq.state" element indicates a
                particular internal state (ESC, CSI, or  DCS)  that  the
                parser should assume on the next call.

                Intermediate    characters    and    parameter    values
                interpretted  up  to  the  occurrence  of  the  embedded
                control character are also stored in the  returned  data
                structure and also should not be altered by the caller.

                Escape sequence syntax errors are indicated  by  setting
                the  seq.private  parameter  to  'X'  (which  is  not  a
                possible private parameter).

                If the  dt_gesc()  function  encounters  more  than  the
                allowed  maximum  number of intermediate characters, the
                returned  data  structure  indicates   that   one   more
                intermediate  character  was  received than allowed.  Of

        DECtalk Applications Support Library                    Page 1-29
        dt_gesc        Read Escape Sequence or Character


                course, characters after the maximum are not stored.

                If the  dt_gesc()  function  encounters  more  than  the
                allowed   maximum   number   of  parameters,  the  extra
                parameters are ignored and the returned  data  structure
                indicates  that the allowed maximum number of parameters
                was received.

                After  each  call  to  dt_gesc()  the  dt->seq  SEQUENCE
                contains the following information:

                seq.state       zero to indicate complete sequence.
                seq.final       the sequence final character
                seq.private     private parameter character:
                                EOS, <, =, >, ?, or X for errors.
                seq.param[0]    the number of parameter values
                                (0:SEQPARMAX)
                seq.param[n]    (unsigned) the n'th parameter value
                seq.inter[0]    the number of intermediate characters
                                (0:SEQINTMAX+1)
                seq.inter[n]    (char) the n'th intermediate character.

                In general, the intermediate and final characters should
                be taken as a whole to determine the action.  It is easy
                to  ignore  sequences   with   too   many   intermediate
                characters  since  the  returned  number of intermediate
                characters will not match any action function.

                To simplify the  code,  this  module  doesn't  test  for
                overly  large  parameter  values  and  assumes  that all
                overflow errors are due to invalid escape sequences.


        DECtalk Applications Support Library                    Page 1-30
        dt_get Read one Character from DECtalk


        1.17  Read one Character from DECtalk              ____ ___ _________ ____ _______



                                   **********
                                   * dt_get *
                                   **********



        NAME:   dt_get -- Read one Character from DECtalk

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_get(dt, sec)
                DECTALK         *dt;    /* Device descriptor    */
                int             sec;    /* O.S. timeout param.  */

        DESCRIPTION:

                One character is read from the  DECtalk  terminal  line.
                The  sec parameter enables operating-system timeout;  it
                is zero if no timeout is needed.

                dt_get() returns the character or an error code:

                DT_ERROR            An  operating   system   error   (or
                                    <CTRL/C> interrupt) was received.

                DT_TIMEOUT          The sec parameter was  non-zero  and
                                    no  character  was  received  in sec
                                    seconds.

                If DT_DEBUG is #defined when the library is compiled and
                the  global dt_debug is set non-zero (by the application
                program),  the  character  received  is  logged  to  the
                standard output device.


        DECtalk Applications Support Library                    Page 1-31
        dt_hangup      Hangup the telephone


        1.18  Hangup the telephone              ______ ___ _________



                                 *************
                                 * dt_hangup *
                                 *************



        NAME:   dt_hangup -- Hangup the telephone

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_hangup(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                Hangup the telephone connected to DECtalk.  Return  TRUE
                if successful, FALSE if an error


        DECtalk Applications Support Library                    Page 1-32
        dt_init        DECtalk Initialization Routine


        1.19  DECtalk Initialization Routine              _______ ______________ _______



                                  ***********
                                  * dt_init *
                                  ***********



        NAME:   dt_init -- DECtalk Initialization Routine

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_init(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                Initialize the DECtalk terminal on the channel opened on
                dt.

                Return TRUE  if  the  device  initialized  successfully.
                Return FALSE on failure.

        NOTE:

                This  routine  turns  off  "local  mode"  so  a  logging
                terminal  does  not inadvertently send a response to the
                "who are you" escape sequence.


        DECtalk Applications Support Library                    Page 1-33
        dt_inkey       Read a Telephone Keypad Character


        1.20  Read a Telephone Keypad Character              ____ _ _________ ______ _________



                                  ************
                                  * dt_inkey *
                                  ************



        NAME:   dt_inkey -- Read a Telephone Keypad Character

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_inkey(dt, sec)
                DECTALK         *dt;    /* Device descriptor    */
                int             sec;    /* Seconds to wait      */

        DESCRIPTION:

                This routine  reads  a  telephone  keypad  button.   The
                application  program  has  previously enabled the keypad
                (by calling dt_keypad(dt, TRUE)).  dt_inkey() will  call
                dt_timeout() to enable or disable timeouts.

                If sec is non-zero,  it  will  indicate  the  number  of
                seconds to wait for a keypad response.  If zero, it will
                turn off keypad timeouts.  The operating-system  timeout
                (needed   to   catch   hardware  or  communication  line
                problems) will be set to four times the  timeout  value,
                plus an operating-system specific additional timeout.

                dt_inkey() returns a character as follows:

                0123456789*#ABCD    A valid keypad button.   (Note  that
                                    "ABCD"  may  be generated by certain
                                    keypad phones.)

                E                   An operating-system error.

                T                   Keypad timeout.

                X                   Badly parsed escape sequence.

                H                   Unexpected telephone hangup.

                The 'H' code is received if the DECtalk device hangs  up
                the  phone  (as  may  be  required by specific telephone
                system requirements).

        DECtalk Applications Support Library                    Page 1-34
        dt_ioget       Read one Character from DECtalk


        1.21  Read one Character from DECtalk              ____ ___ _________ ____ _______



                                  ************
                                  * dt_ioget *
                                  ************



        NAME:   dt_ioget -- Read one Character from DECtalk

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_ioget(dt, sec)
                DECTALK         *dt;    /* Device descriptor    */
                int             sec;    /* O.S. timeout param.  */

        DESCRIPTION:

                One character is read from the  DECtalk  terminal  line.
                The  sec parameter enables operating-system timeout;  it
                is zero if no timeout is needed.

                dt_ioget() returns the character or an error code:

                DT_ERROR            An  operating   system   error   (or
                                    <CTRL/C> interrupt) was received.

                DT_TIMEOUT          The sec parameter was  non-zero  and
                                    no  character  was  received  in sec
                                    seconds.

                If DT_DEBUG is #defined when the library is compiled and
                the  global dt_debug is set non-zero (by the application
                program),  the  character  received  is  logged  to  the
                standard output device.

                dt_ioget()  is  the  operating-system   specific   input
                routine.   It  is the only routine to read data from the
                DECtalk terminal line.

        NOTE:

                On vms, an  internally-used  routine,  dt_vmsread(),  is
                also defined.  Application programs should not call this
                routine.

                This module contains specific code for Unix 4.2BSD.  The
                makefile for the library should #define BSD_42.

        DECtalk Applications Support Library                    Page 1-35
        dt_ioput       Write one Character to DECtalk


        1.22  Write one Character to DECtalk              _____ ___ _________ __ _______



                                  ************
                                  * dt_ioput *
                                  ************



        NAME:   dt_ioput -- Write one Character to DECtalk

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_ioput(dt, byte)
                DECTALK         *dt;    /* Device descriptor    */
                char            byte;   /* Character to write   */

        DESCRIPTION:

                If the argument character is zero, or the output  buffer
                is  full,  the output buffer contents are written to the
                DECtalk device.

                If the argument character is non-zero, it is  stored  in
                the output buffer for subsequent transmission.

                By buffering characters  internally,  the  load  on  the
                operating  system  is  significantly reduced.  Note that
                the input routine (dt_get(), dt_ioget()) will flush  the
                output  buffer  before attempting to read any data.  The
                "speak" routine,  dt_talk(),  also  flushes  the  output
                buffer.

                No data is returned.  Errors are fatal.

                dt_ioput()  is  the  operating-system  specific   output
                routine.   It  is  the only routine to write data to the
                DECtalk terminal line.


        DECtalk Applications Support Library                    Page 1-36
        dt_iskey       Test for type-ahead


        1.23  Test for type-ahead              ____ ___ __________



                                  ************
                                  * dt_iskey *
                                  ************



        NAME:   dt_iskey -- Test for type-ahead

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_iskey(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                This routine (which  may  be  implemented  as  a  macro)
                returns  TRUE  if any characters have already been typed
                by the telephone  user  or  if  an  asynchronous  status
                message (such as timeout) was received.


        DECtalk Applications Support Library                    Page 1-37
        dt_istimeout   Test Phone Reply for Keypad Timeout


        1.24  Test Phone Reply for Keypad Timeout              ____ _____ _____ ___ ______ _______



                                ****************
                                * dt_istimeout *
                                ****************



        NAME:   dt_istimeout -- Test Phone Reply for Keypad Timeout

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_istimeout(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                This routine (which may be implemented as a macro) tests
                the  result of a dt_phone() message.  It returns TRUE if
                the current reply is the DECtalk phone reply with the R3
                parameter equal to R3_PH_TIMEOUT.


        DECtalk Applications Support Library                    Page 1-38
        dt_isvalid     Test for Valid Keypad Character


        1.25  Test for Valid Keypad Character              ____ ___ _____ ______ _________



                                 **************
                                 * dt_isvalid *
                                 **************



        NAME:   dt_isvalid -- Test for Valid Keypad Character

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_isvalid(c)

        DESCRIPTION:

                This routine (which  may  be  implemented  as  a  macro)
                returns TRUE if the argument character is one of

                    0123456789#*ABCD


        DECtalk Applications Support Library                    Page 1-39
        dt_keypad      Enable or Disable the Telephone Keypad


        1.26  Enable or Disable the Telephone Keypad              ______ __ _______ ___ _________ ______



                                 *************
                                 * dt_keypad *
                                 *************



        NAME:   dt_keypad -- Enable or Disable the Telephone Keypad

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_keypad(dt, flag)
                DECTALK         *dt;    /* Device descriptor    */
                int             flag;   /* TRUE to enable       */

        DESCRIPTION:

                Enable the telephone keypad if the flag is TRUE, disable
                it if FALSE.

                Returns TRUE if successful.  If FALSE, the telephone may
                have been hung up.


        DECtalk Applications Support Library                    Page 1-40
        dt_msg Send a DECtalk Command with Reply


        1.27  Send a DECtalk Command with Reply              ____ _ _______ _______ ____ _____



                                   **********
                                   * dt_msg *
                                   **********



        NAME:   dt_msg -- Send a DECtalk Command with Reply

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_msg(dt, p2, p3, p4, r2, r3)
                DECTALK         *dt;    /* Device descriptor    */
                int             p2;     /* P2_xxxx parameter    */
                int             p3;     /* P3_PH_xxxx parameter */
                int             p4;     /* timeout or rings     */
                int             r2;     /* R2_xxxx parameter    */
                int             r3;     /* R3_xxxx parameter    */

        DESCRIPTION:

                This routine sends a DECtalk DCS control sequence  using
                the  p2,  p3,  and  p4  parameters.  It then reads a DCS
                reply from DECtalk, returning TRUE if it matches the  r2
                and r3 calling parameters.

                If p2 is -1, no sequence is sent;  but a  DCS  reply  is
                read and tested.

                Note that the Pn and Rn parameters are -1  if  they  are
                not sent or checked respectively.

                Returns TRUE if  successful.   If  FALSE,  something  is
                funny.

                Note:  dt_msg() saves  user  keypad  characters  in  the
                type-ahead buffer.


        DECtalk Applications Support Library                    Page 1-41
        dt_offhook     Test Phone Reply for Offhook


        1.28  Test Phone Reply for Offhook              ____ _____ _____ ___ _______



                                 **************
                                 * dt_offhook *
                                 **************



        NAME:   dt_offhook -- Test Phone Reply for Offhook

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_offhook(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                This routine (which may be implemented as  a  macro)  is
                used  to  test  the  result of a dt_phone() message.  It
                returns TRUE if the current reply is the  DECtalk  phone
                reply with the R3 parameter equal to R3_PH_OFFHOOK.


        DECtalk Applications Support Library                    Page 1-42
        dt_onhook      Test Phone Reply for Onhook


        1.29  Test Phone Reply for Onhook              ____ _____ _____ ___ ______



                                 *************
                                 * dt_onhook *
                                 *************



        NAME:   dt_onhook -- Test Phone Reply for Onhook

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_onhook(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                This routine (which may be implemented as  a  macro)  is
                used  to  test  the  result of a dt_phone() message.  It
                returns TRUE if the current reply is the  DECtalk  phone
                reply with the R3 parameter equal to R3_PH_ONHOOK.


        DECtalk Applications Support Library                    Page 1-43
        dt_open        Connect to DECtalk Terminal


        1.30  Connect to DECtalk Terminal              _______ __ _______ ________



                                  ***********
                                  * dt_open *
                                  ***********



        NAME:   dt_open -- Connect to DECtalk Terminal

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                DECTALK *
                dt_open(dev)
                char            *dev;   /* Terminal device name */

        DESCRIPTION:

                Perform operating-specific initializations  to  initiate
                communication  with  a DECtalk device.  (This routine is
                similar to fopen() for FILE devices.) If the open fails,
                return NULL;  else return a pointer to a data descriptor
                block  that  will  be  used  for   all   other   DECtalk
                operations.

                If  the  open  failed,  the  standard  library  perror()
                routine may be called to print error information.

                This routine does not communicate with DECtalk.

                For  example,  the  following  sequence  opens  DECtalk,
                checks  that  it  is  responding,  sets "square-bracket"
                mode, and speaks a message:

                    #include <stdio.h>
                    #include "dectlk.h"

                    DECTALK *dt;
                    ...
                    main() {
                        if ((dt = dt_open("kb2:")) == NULL) {
                            perror("kb2:");
                            printf("Can't open DECtalk\n");
                        }
                        else if (!dt_init(dt))
                            printf("Can't initiate DECtalk\n");
                        else {
                            dt_dcs(dt, P2_MODE, MODE_SQUARE, -1);
                            dt_talk(dt, "Hello world.");

        DECtalk Applications Support Library                    Page 1-44
        dt_open        Connect to DECtalk Terminal


                            dt_sync(dt);
                            dt_close(dt);
                            printf("Success.\n");
                        }
                    }


        DECtalk Applications Support Library                    Page 1-45
        dt_pesc        Transmit Escape Sequence


        1.31  Transmit Escape Sequence              ________ ______ ________



                                  ***********
                                  * dt_pesc *
                                  ***********



        NAME:   dt_pesc -- Transmit Escape Sequence

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"


                dt_pesc(dt, seq)
                DECTALK         *dt;    /* Device descriptor    */
                SEQUENCE        *seq;   /* What to transmit     */

        DESCRIPTION:

                Compile  an  appropriate  escape   sequence   from   the
                parameter  buffer.   This is similar to putchar() except
                when seq->state is ESC, CSI, or DCS.   In  these  cases,
                the  function generates an appropriate sequence from the
                passed   data   structure.     dt_pesc()    calls    the
                user-supplied  dt_put()  to output each character.  This
                version of the code enforces 7-bit output.

                No value is returned.


        DECtalk Applications Support Library                    Page 1-46
        dt_phone       Send a Phone Message


        1.32  Send a Phone Message              ____ _ _____ _______



                                  ************
                                  * dt_phone *
                                  ************



        NAME:   dt_phone -- Send a Phone Message

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_phone(dt, p3, p4)
                DECTALK         *dt;    /* Device descriptor    */
                int             p3;     /* P3_PH_xxxx parameter */
                int             p4;     /* timeout or rings     */

        DESCRIPTION:

                This routine (which may be implemented as a macro) sends
                a  DECtalk  phone  message  (i.e.,  the  p2 parameter is
                P2_PHONE).

                p3 and p4 should be given as -1 if no parameter is to be
                sent.

                It then reads the status reply and returns TRUE  if  the
                r1   and  r2  parameters  are  R1_DECTALK  and  R2_PHONE
                respectively.  The application program should then  test
                for offhook/onhook as appropriate.

                Returns TRUE if  successful.   If  FALSE,  something  is
                funny.


        DECtalk Applications Support Library                    Page 1-47
        dt_ptest       Test Phone Reply


        1.33  Test Phone Reply              ____ _____ _____



                                  ************
                                  * dt_ptest *
                                  ************



        NAME:   dt_ptest -- Test Phone Reply

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_ptest(dt, r3)
                DECTALK         *dt;    /* Device descriptor    */
                int             r3;     /* R3_PH_xxxx parameter */

        DESCRIPTION:

                This routine (which may be implemented as  a  macro)  is
                used  to  test  the result of a dt_phone() message.  The
                parameter is a R3_PH_...  reply value.  It returns  TRUE
                if  the  current reply is a DECtalk phone reply with the
                specified R3 parameter.


        DECtalk Applications Support Library                    Page 1-48
        dt_put Write one Character to DECtalk


        1.34  Write one Character to DECtalk              _____ ___ _________ __ _______



                                   **********
                                   * dt_put *
                                   **********



        NAME:   dt_put -- Write one Character to DECtalk

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_put(dt, c)
                DECTALK         *dt;    /* Device descriptor    */
                int             c;      /* Character to write   */

        DESCRIPTION:

                One character is written to the DECtalk  terminal  line.
                No value is returned.

                If DT_DEBUG is #defined when the library is compiled and
                the  global dt_debug is set non-zero (by the application
                program),  the  character  written  is  logged  to   the
                standard output device.


        DECtalk Applications Support Library                    Page 1-49
        dt_read        Read Sequence or Character


        1.35  Read Sequence or Character              ____ ________ __ _________



                                  ***********
                                  * dt_read *
                                  ***********



        NAME:   dt_read -- Read Sequence or Character

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_read(dt, sec)
                DECTALK         *dt;    /* Device descriptor    */
                char            sec;    /* O.S. timeout value   */

        DESCRIPTION:

                Read an escape sequence or keypad character.  Ignore any
                characters  between  the  DECtalk  final  and the string
                terminator.  Return the character read or  the  sequence
                introducer.


        DECtalk Applications Support Library                    Page 1-50
        dt_reset       DECtalk Soft Reset


        1.36  DECtalk Soft Reset              _______ ____ _____



                                  ************
                                  * dt_reset *
                                  ************



        NAME:   dt_reset -- DECtalk Soft Reset

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_reset(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                Send a "soft reset"  escape  sequence.   No  errors  are
                possible.


        DECtalk Applications Support Library                    Page 1-51
        dt_save        Save User Type-ahead


        1.37  Save User Type-ahead              ____ ____ __________



                                  ***********
                                  * dt_save *
                                  ***********



        NAME:   dt_save -- Save User Type-ahead

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_save(dt, c)
                DECTALK         *dt;    /* Device descriptor    */
                char            c;      /* Character to save    */

        DESCRIPTION:

                If c is a keypad character, save it  in  the  type-ahead
                buffer and return TRUE, else return FALSE.

                If the current reply is a timeout and nothing is  stored
                in the type-ahead buffer, save 'T' and clear the timeout
                flag.  This is necessary as a timeout  sequence  may  be
                returned in the middle of a message/reply sequence.

                This  routine  should  not  be  called  by   application
                programs.


        DECtalk Applications Support Library                    Page 1-52
        dt_splice      Manage Local Terminal


        1.38  Manage Local Terminal              ______ _____ ________



                                 *************
                                 * dt_splice *
                                 *************



        NAME:   dt_splice -- Manage Local Terminal

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_splice(dt, flag)
                DECTALK         *dt;    /* Device descriptor    */
                int             flag;   /* Required state       */

        DESCRIPTION:

                dt_splice() allows control over a terminal connected  to
                DECtalk's  "local"  port.   Note  that the terminal must
                correctly process ANSI escape sequences.   Specifically,
                it  must  ignore  any  escape  sequence  that it doesn't
                understand.

                The flag parameter may have the following  (bit-encoded)
                values:

                SPLICE_SPEAK     Speak subsequent text, if set.  Do not
                                speak text if not set.  Initially zero.
                SPLICE_LOG       Text sent to DECtalk is sent (in raw
                                mode) to the local terminal if set.
                                Initially not set.
                SPLICE_TERM      Text typed on the local terminal is
                                sent to DECtalk if set.  Initially not
                                set.

                The  bits  would  normally  be  set   and   cleared   in
                combination.  For example:

                    dt_splice(dt, SPLICE_SPEAK);

                Speak text, don't log it, ignore text typed on the host.

                    dt_splice(dt, SPLICE_LOG | SPLICE_TERM);

                Stop speaking text, transmit text from/to  the  attached
                terminal.


        DECtalk Applications Support Library                    Page 1-53
        dt_st  Send String Terminator


        1.39  Send String Terminator              ____ ______ __________



                                   *********
                                   * dt_st *
                                   *********



        NAME:   dt_st -- Send String Terminator

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_st(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                This routine sends a String Terminator to DECtalk.  This
                is  needed  to terminate phonemic text or telephone dial
                commands.

                A phonemic text sequence would be sent as follows:

                    dt_cmd(dt, p2, p3);
                    dt_talk(dt, "hh'ehlow.");
                    dt_st(dt);


        DECtalk Applications Support Library                    Page 1-54
        dt_sync        Synchronize with DECtalk


        1.40  Synchronize with DECtalk              ___________ ____ _______



                                  ***********
                                  * dt_sync *
                                  ***********



        NAME:   dt_sync -- Synchronize with DECtalk

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_sync(dt)
                DECTALK         *dt;    /* Device descriptor    */

        DESCRIPTION:

                The program delays until all text sent  to  DECtalk  has
                been spoken.

                Returns TRUE if  successful.   If  FALSE,  something  is
                funny.


        DECtalk Applications Support Library                    Page 1-55
        dt_talk        Speak One Line of Text


        1.41  Speak One Line of Text              _____ ___ ____ __ ____



                                  ***********
                                  * dt_talk *
                                  ***********



        NAME:   dt_talk -- Speak One Line of Text

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_talk(dt, text)
                DECTALK         *dt;    /* Device descriptor    */
                char            *text;  /* What to say          */

        DESCRIPTION:

                This function sends a line of text to DECtalk.

                dt_talk(dt,  NULL)  flushes   DECtalk   by   sending   a
                vertical-tab sequence.


        DECtalk Applications Support Library                    Page 1-56
        dt_test        Test a DECtalk Reply


        1.42  Test a DECtalk Reply              ____ _ _______ _____



                                  ***********
                                  * dt_test *
                                  ***********



        NAME:   dt_test -- Test a DECtalk Reply

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_test(dt, r2, r3)
                DECTALK         *dt;    /* Device descriptor    */
                int             r2;     /* R2_xxx parameter     */
                int             r3;     /* R3_xxx parameter     */

        DESCRIPTION:

                This routine checks the last reply received from DECtalk
                against  the  model.  r3 is -1 to ignore it.  It returns
                TRUE if the reply is  a  properly-parsed  DECtalk  reply
                sequence, or FALSE on any failure.


        DECtalk Applications Support Library                    Page 1-57
        dt_timeout     Enable or Disable Keypad Timeout


        1.43  Enable or Disable Keypad Timeout              ______ __ _______ ______ _______



                                 **************
                                 * dt_timeout *
                                 **************



        NAME:   dt_timeout -- Enable or Disable Keypad Timeout

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_timeout(dt, sec)
                DECTALK         *dt;    /* Device descriptor    */
                int             sec;    /* Timeout in seconds   */

        DESCRIPTION:

                If sec is non-zero,  timeouts  are  being  enabled;   if
                zero, they are being disabled.

                Enable keypad timeouts if sec is non-zero and  there  is
                no  data  in the type-ahead buffer (and timeouts are not
                already enabled).

                Disable timeouts if they are enabled and sec is zero, or
                any  data  is  in  the type-ahead buffer (even if sec is
                non-zero).

                Before enabling timeouts, DECtalk is synchronized.

                Returns TRUE if successful.  If FALSE, the telephone may
                have been hung up.


        DECtalk Applications Support Library                    Page 1-58
        dt_tone        Send DTMF Tones


        1.44  Send DTMF Tones              ____ ____ _____



                                  ***********
                                  * dt_tone *
                                  ***********



        NAME:   dt_tone -- Send DTMF Tones

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                dt_tone(dt, msg)
                DECTALK         *dt;    /* Device descriptor    */
                char            *msg;   /* Announcement         */

        DESCRIPTION:

                This routine sends the msg text string as a tone dialing
                sequence.   If  the  telephone was on-hook when dttone()
                was  called,  it  will  be  returned  to   the   on-hook
                condition.   Note,  this  routine  may  not work to your
                satisfaction  in  countries  which   require   automatic
                announcement  messages  on  automatically  dialed calls.
                See  your   DECtalk   programmer's   manual   for   more
                information.

                For  message  text  may  contain  any  valid  touch-tone
                characters ("0123456789*#ABCD") or  the  characters  '!'
                (for  a  one  second  delay)  or  the  '^'  for  a   250
                millisecond switch-hook flash.  All other characters are
                ignored.

                Note that the telephone  will  not  be  hung  up  before
                dialing if it is offhook when the command is issued.


        DECtalk Applications Support Library                    Page 1-59
        dt_trap        Trap <CTRL/C> Interrupts


        1.45  Trap <CTRL/C> Interrupts              ____ ________ __________



                                  ***********
                                  * dt_trap *
                                  ***********



        NAME:   dt_trap -- Trap <CTRL/C> Interrupts

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                dt_trap()

        DESCRIPTION:

                Set the global dt_abort flag if the user types  <CTRL/C>
                at  the command terminal.  (On Unix, this is interpreted
                as  catching  the  INTERRUPT  signal,   which   is   not
                necessarily  <CTRL/C>,  and  which  may  be generated by
                running the "kill" system program.

                When the interrupt is received, pending I/O is cancelled
                (on those operating systems where this makes sense).

                If dt_abort is set TRUE when the interrupt is  received,
                the program aborts.

                No error is returned.


        DECtalk Applications Support Library                    Page 1-60
        dt_visible     Generate Visible Representation


        1.46  Generate Visible Representation              ________ _______ ______________



                                 **************
                                 * dt_visible *
                                 **************



        NAME:   dt_visible -- Generate Visible Representation

        SYNOPSIS:

                char            work[12]; /* Output buffer      */

                char *
                dt_visible(c, work)
                int             c;      /* Character to dump    */
                char            work[]; /* Work buffer          */

        DESCRIPTION:

                A visible  Ascii  representation  of  the  character  is
                stored  in the work buffer.  A pointer to the end of the
                output string is returned.

                Note  that  this  routine  is  independent  of   DECtalk
                definitions (except that it knows about the DT_ERROR and
                DT_TIMEOUT error codes).


        DECtalk Applications Support Library                    Page 1-61
        dtdemo  Sample Main Program


        1.47  Sample Main Program              ______ ____ _______



                                   **********
                                   * dtdemo *
                                   **********



        NAME:   dtdemo -- Sample Main Program

        SYNOPSIS:

                dtdemo [-d] [-t terminal] [-m max_time]

        DESCRIPTION:

                This is a sample "answer the phone"  main  program.   It
                calls  a  user-written  subroutine,  process()  when the
                phone is answered.  This subroutine should  return  TRUE
                when  the call has completed successfully and FALSE when
                the call completes in error.  The main program will hang
                up the phone before starting the next call.

                The following options are supported:

                -d          Enable debug logs.
                -t device   The DECtalk terminal is connected to this
                            terminal line.
                -m seconds  Hangup the phone after the specified number
                            of seconds.  (Default is 180 seconds or 3
                            minutes.) -m#0 disables the hangup.

                On Unix and VMS, an environment variable,  DECTALK,  may
                be  used  to specify the DECtalk terminal line.  On VMS,
                this would be set by the DCL ASSIGN command as follows:

                    $ ASSIGN terminal DECTALK

                On P/OS, the DECtalk device  must  be  attached  to  the
                PRO-350 printer port for the software to work correctly.
                P/OS V1.7 is required.

                The user-written process subroutine should be defined as
                follows:

                    int
                    process(dt, max)
                    DECTALK     *dt;    /* DECtalk device       */
                    int         max;    /* -m parameter         */


        DECtalk Applications Support Library                    Page 1-62
        sample  Sample Application


        1.48  Sample Application              ______ ___________



                                   **********
                                   * sample *
                                   **********



        NAME:   sample -- Sample Application

        SYNOPSIS:

                #include        <stdio.h>
                #include        "dectlk.h"

                int
                process(dt, max)
                DECTALK         *dt;    /* DECtalk device       */
                int             max;    /* Seconds to run demo  */

        DESCRIPTION:

                This module contains source for the user-written "sample
                application".   See  the  documentation for dtdemo.c for
                details.














                                   APPENDIX A

                              DTLIB LIBRARY INDEX



        The following is a keyword in context index to the DTLIB runtime
        library.   The entry in the left-hand column is the title of the
        routine in the main library documentation.


        dt_answer                              Answer the telephone     
        sample                          Sample application              
        dt_dump           Dump escape sequence buffer                   
        dt_inkey            a Telephone Keypad Character            Read
        dt_gesc             escape sequence or character            Read
        dt_read               Read sequence or character                
        dt_isvalid       Test for valid keypad character                
        dt_get                        Read one character from DECtalk   
        dt_ioget                      Read one character from DECtalk   
        dt_ioput                     Write one character to DECtalk     
        dt_put                       Write one character to DECtalk     
        dt_dchar                      Dump one character visibly        
        dt_dcs              Send a DECtalk DCS command                  
        dt_msg                  Send a DECtalk command with reply       
        dt_open         terminal               Connect to DECtalk       
        dt_trap                          Trap <CTRL/C> Interrupts       
        dt_dcs                  Send a DECtalk DCS command              
        dt_cmd          terminator        Send DCS w/o string           
        dt_get              one character from DECtalk              Read
        dt_ioget            one character from DECtalk              Read
        dt_sync               Synchronize with DECtalk                  
        dt_eol            Write End of Line to DECtalk                  
        dt_ioput              one character to DECtalk             Write
        dt_put                one character to DECtalk             Write
        dt_dcs                          Send a DECtalk DCS command      
        dt_close                     Terminate DECtalk Operation        
        dt_msg          reply           Send a DECtalk command with     
        dt_init         routine                DECtalk initialization   
        dectlk.h        file                   DECtalk library header   
        dt_test                         Test a DECtalk reply            
        dt_reset                               DECtalk soft reset       
        dt_open                     Connect to DECtalk terminal         
        dt_dial                                Dial the telephone       
        dt_keypad       Keypad       Enable or Disable the Telephone    
        dt_timeout                   Enable or disable keypad timeout   

        DECtalk Support Library (DTLIB)                                 Page A-2
        Support Library Index


        dt_drain                               Drain pending input      
        dt_tone                           Send DTMF tones               
        dt_dump         buffer                 Dump escape sequence     
        dt_dchar        visibly                Dump one character       
        dt_keypad       Telephone Keypad       Enable or Disable the    
        dt_timeout      timeout                Enable or disable keypad 
        dt_eol                           Write End of Line to DECtalk   
        dt_pesc                       Transmit escape sequence          
        dt_dump                           Dump escape sequence buffer   
        dt_gesc         character         Read escape sequence or       
        dectlk.h                library header file              DECtalk
        dt_visible      Representation         Generate Visible         
        dt_hangup                              Hangup the telephone     
        dectlk.h               DECtalk library header file              
        dt_init                        DECtalk initialization routine   
        dt_drain                 Drain pending input                    
        dt_trap                  Trap <CTRL/C> Interrupts               
        dt_keypad        Disable the Telephone Keypad          Enable or
        dt_inkey              Read a Telephone Keypad Character         
        dt_isvalid              Test for valid keypad character         
        dt_timeout           Enable or disable keypad timeout           
        dt_istimeout      Test phone reply for keypad timeout           
        dectlk.h                       DECtalk library header file      
        dt_eol                    Write End of Line to DECtalk          
        dt_talk                      Speak one line of text             
        dt_splice                       Manage Local Terminal           
        dtdemo                          Sample main program             
        dt_splice                              Manage Local Terminal    
        dt_phone                  Send a phone message                  
        dt_offhook        Test phone reply for Offhook                  
        dt_get          DECtalk           Read one character from       
        dt_ioget        DECtalk           Read one character from       
        dt_ioput                         Write one character to DECtalk 
        dt_put                           Write one character to DECtalk 
        dt_dchar                          Dump one character visibly    
        dt_talk                          Speak one line of text         
        dt_onhook         Test phone reply for onhook                   
        dt_close             Terminate DECtalk Operation                
        dt_keypad       Keypad          Enable or Disable the Telephone 
        dt_gesc           Read escape sequence or character             
        dt_read                  Read sequence or character             
        dt_timeout      timeout         Enable or disable keypad        
        dt_drain                         Drain pending input            
        dt_phone                        Send a phone message            
        dt_ptest                          Test phone reply              
        dt_offhook                        Test phone reply for Offhook  
        dt_istimeout    timeout           Test phone reply for keypad   
        dt_onhook                         Test phone reply for onhook   
        dtdemo                     Sample main program                  
        dt_inkey        Character              Read a Telephone Keypad  
        dt_gesc         character              Read escape sequence or  
        dt_get          DECtalk                Read one character from  
        dt_ioget        DECtalk                Read one character from  
        dt_read         character              Read sequence or         

        DECtalk Support Library (DTLIB)                                 Page A-3
        Support Library Index


        dt_msg            DECtalk command with reply              Send a
        dt_test                 Test a DECtalk reply                    
        dt_ptest                    Test phone reply                    
        dt_offhook                  Test phone reply for Offhook        
        dt_istimeout                Test phone reply for keypad timeout 
        dt_onhook                   Test phone reply for onhook         
        dt_visible            Generate Visible Representation           
        dt_reset                  DECtalk soft reset                    
        dt_init                 initialization routine           DECtalk
        sample                                 Sample application       
        dtdemo                                 Sample main program      
        dt_save                                Save user type-ahead     
        dt_cmd          terminator             Send DCS w/o string      
        dt_tone                                Send DTMF tones          
        dt_st                                  Send String Terminator   
        dt_dcs          command                Send a DECtalk DCS       
        dt_msg          with reply             Send a DECtalk command   
        dt_phone                               Send a phone message     
        dt_pesc                Transmit escape sequence                 
        dt_dump                    Dump escape sequence buffer          
        dt_read                           Read sequence or character    
        dt_gesc                    Read escape sequence or character    
        dt_reset                       DECtalk soft reset               
        dt_talk                                Speak one line of text   
        dt_st                             Send String Terminator        
        dt_cmd                    Send DCS w/o string terminator        
        dt_sync                                Synchronize with DECtalk 
        dt_keypad        Enable or Disable the Telephone Keypad         
        dt_inkey        Character       Read a Telephone Keypad         
        dt_answer                   Answer the telephone                
        dt_dial                       Dial the telephone                
        dt_hangup                   Hangup the telephone                
        dt_splice                 Manage Local Terminal                 
        dt_open             Connect to DECtalk terminal                 
        dt_close        Operation              Terminate DECtalk        
        dt_st                      Send String Terminator               
        dt_cmd             Send DCS w/o string terminator               
        dt_test                                Test a DECtalk reply     
        dt_iskey                               Test for type-ahead      
        dt_isvalid      character              Test for valid keypad    
        dt_ptest                               Test phone reply         
        dt_offhook      Offhook                Test phone reply for     
        dt_istimeout    keypad timeout         Test phone reply for     
        dt_onhook       onhook                 Test phone reply for     
        dt_talk              Speak one line of text                     
        dt_timeout           or disable keypad timeout            Enable
        dt_istimeout          reply for keypad timeout        Test phone
        dt_tone                      Send DTMF tones                    
        dt_pesc                                Transmit escape sequence 
        dt_trap                                Trap <CTRL/C> Interrupts 
        dt_save                      Save user type-ahead               
        dt_iskey                      Test for type-ahead               
        dt_save                           Save user type-ahead          
        dt_isvalid                    Test for valid keypad character   

        DECtalk Support Library (DTLIB)                                 Page A-4
        Support Library Index


        dt_visible                    Generate Visible Representation   
        dt_dchar            Dump one character visibly                  
        dt_cmd                        Send DCS w/o string terminator    
        dt_eol          DECtalk                Write End of Line to     
        dt_ioput        DECtalk                Write one character to   
        dt_put          DECtalk                Write one character to